## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 03
History of Computing: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
03-Computer_Architecture-History_of_Computing.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 03. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: what informatics is; the von Neumann architecture; RISC and an open ISA. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: Boolean algebra (Lecture 08). A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
No listing in Lecture 03: this deck gives you the program to run
2
The complete program: code/l03.S, 94 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The program of this lecture is ~/arc12/code/l03.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l03.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: The complete program: l03.S (1 of 5)
# ARC12 Computer Architecture - Lecture 03: History of Computing
# l03.S: the stored program: a program that reads one of its own instructions as data
#
# On the screen: a row of 32 lamps showing 0x00130313, the machine code of addi t1,
# t1, 1, and a green square: the word read is the one expected.
# Build: python3 -m prg32 cartridge build l03.S --portable \
# --entry-prefix l03 --name l03 --out l03.prg32
.option norelax
.equ BLACK, 0x0000
.equ GREY, 0x4208
.equ YELLOW, 0xffe0
.equ GREEN, 0x07e0
.equ RED, 0xf800
.section .text
.global l03_init
.global l03_update
.global l03_draw
l03_init:
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l03.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 4: The complete program: l03.S (2 of 5)
l03_update:
ret
# One instruction of the program. For von Neumann's machine it is a number in
# the same memory as the data: the program can load it like any other word.
.option push
.option norvc # keep it 32 bits long: no compressed form
specimen:
addi t1, t1, 1
.option pop
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l03.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 5: The complete program: l03.S (3 of 5)
l03_draw:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li a0, BLACK
call prg32_gfx_clear
la t0, specimen # the ADDRESS of an instruction ...
lw s0, 0(t0) # ... and the instruction, read as DATA
mv a0, s0
li a1, 60
call lamps32 # show its 32 bits
li t0, 0x00130313 # what the assembler should have produced
li a4, RED
bne s0, t0, 1f
li a4, GREEN # equal: instructions are numbers
1: li a0, 152
li a1, 100
li a2, 16
li a3, 16
call prg32_gfx_rect
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l03.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 6: The complete program: l03.S (4 of 5)
# lamps32: show the 32 bits of a word as a row of lamps, bit 31 on the left.
# a0 = the word, a1 = y of the row. A lamp is yellow for 1, grey for 0.
lamps32:
addi sp, sp, -32
sw ra, 28(sp)
sw s0, 24(sp)
sw s1, 20(sp)
sw s2, 16(sp)
mv s0, a0 # the word
mv s1, a1 # y
li s2, 0 # lamp number, 0 on the left
1: li t0, 31
sub t0, t0, s2 # lamp i shows bit 31 - i
srl t1, s0, t0 # bring that bit down to bit 0
andi t1, t1, 1 # keep it, clear all the others
li a4, GREY # lamp off
beqz t1, 2f
li a4, YELLOW # lamp on
2: slli a0, s2, 3
add a0, a0, s2 # 9 * i
addi a0, a0, 16 # x = 16 + 9 * i
mv a1, s1
li a2, 8
li a3, 8
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l03.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: The complete program: l03.S (5 of 5)
call prg32_gfx_rect
addi s2, s2, 1
li t0, 32
blt s2, t0, 1b
lw s2, 16(sp)
lw s1, 20(sp)
lw s0, 24(sp)
lw ra, 28(sp)
addi sp, sp, 32
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l03.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: Run it: what you should see
On the screen
– a row of 32 lamps showing 0x00130313, the machine code of addi t1, t1, 1, and a green square: the word read is the one expected.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 9: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l03.S --portable \
--entry-prefix l03 --name l03 --out l03.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l03.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 10: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l03.S --portable \
--entry-prefix l03 --name l03 --architecture qemu \
--out l03-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l03-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 11: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l03.S --portable \
--entry-prefix l03 --name l03 --architecture esp32c6 \
--out l03-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l03-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 12: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l03; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 13: Exercises: paper first, then PRG32
TRY IT
1
Draw the four units of the von Neumann architecture and write, inside each, one thing of the program of Lecture 02 that lives or happens there
2
For each of these, say whether it is a new way of representing information or of prescribing operations: the abacus, the Jacquard loom, the Pascaline, Boole's algebra, the punched cards of the Analytical Engine, the stored program
3
Download two of the four retro games from the Store, or build them from examples/games; with the counters of the debugger find how many instructions each executes per frame, and compare
Expected result
Registers and ALU: addi executed. Memory: counter and the instructions themselves. Control unit: the fetch of each instruction. Input/output: the bar on the screen.
Notes: Three exercises, moving from paper to the machine. The first asks the student to draw the four units of the von Neumann architecture and to assign to each an element of the program of Lecture 02; it tests whether the architecture has become a working model rather than an abstract diagram. The second asks for six inventions to be classified as means of representing information or of prescribing operations; the stored program is the instructive case, since it unifies the two categories by representing the prescription itself. The third is experimental: the counters of the debugger are used to compare the number of instructions that two games execute per frame, a first quantitative look at the cost of a program. For the lecturer: Representing: abacus, Pascaline (digits as wheel positions), Boole's algebra. Prescribing: the Jacquard loom, the cards of the Analytical Engine, the stored program, which unifies the two: a program is itself represented information. The third exercise has no fixed answer: the counters depend on the game and on the moment.