## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 05
Number Representation: Integers: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
05-Computer_Architecture-Number_Representation_Integers.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 05. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: two's complement; base conversions; naturals and overflow; shifts as multiplications; sign and magnitude; signed or unsigned instructions; sign extension. USE NOW: the PRG32 runtime calls, the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The 5 listings of Lecture 05, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l05.S, 93 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The program of this lecture is ~/arc12/code/l05.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l05.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Hold LEFT and watch the number
steer_update:
...
call prg32_input_read # a0 = button mask
mv t0, a0
la t1, marker_x
lw t2, 0(t1) # t2 = marker_x, starts at 2
andi t3, t0, BTN_LEFT # is LEFT pressed?
beqz t3, 1f
addi t2, t2, -1 # one step to the left
1: sw t2, 0(t1)
...
# draw prints marker_x with prg32_console_hex32
1
Hold LEFT: the value shown goes 00000002, 00000001, 00000000 ...
2
... and then FFFFFFFF. Is it a bug?
3
Is 0xFFFFFFFF the number 4,294,967,295 or the number -1?
4
Both. It depends on how you read the bits: this lecture gives the rules
USE NOW · the PRG32 runtime calls
UNDERSTAND NOW · two's complement
Notes: The warm-up. The code reads the buttons, loads marker_x from memory, subtracts 1 if LEFT is pressed and stores the result back: the load-modify-store idiom of Lecture 02. Holding LEFT, the printed value runs 00000002, 00000001, 00000000, and then FFFFFFFF. Is this an error? Is FFFFFFFF the number 4,294,967,295, or minus one? The fourth callout anticipates the answer: both, depending on how the bits are interpreted. The remainder of the lecture develops the rules behind that sentence, and by its end the phenomenon should be fully explicable. UNDERSTAND NOW: two's complement. USE NOW: the PRG32 runtime calls (used, not studied, in this course). For the lecturer: Adapted from textbook lab 06-asm-state-and-input (step2_move.S) with SPEED 1 and a console print. Where to look: on the board and in QEMU the console is drawn on the screen, as 0x00000002 ... 0xffffffff; PRG32-QT does not draw the console, it collects it in its log, as 00000002 ... FFFFFFFF. Run it live before any theory, and write the students' guesses on the board.

## Slide 4: Properties of binary strings
Extension on the left with zeros does not change the value
– 5 = 101 = 00101
Multiplying by 2^k is a shift left by k positions
– 00101 x 2 = 01010: five becomes ten
Integer division by 2^k is a shift right by k positions
– 00101 / 2 = 00010: five becomes two, the remainder is lost
Shifts are much cheaper than multiplications: compilers use them whenever they can
# multiply by 4
slli t0, t0, 2
# divide by 2 (unsigned)
srli t0, t0, 1
# x * 10 = x*8 + x*2
slli t1, t0, 3
slli t2, t0, 1
add t0, t1, t2
UNDERSTAND NOW · shifts as multiplications
Notes: Three properties of binary strings, each with a practical use. Extending a number on the left with zeros leaves its value unchanged. Shifting left by k positions multiplies by 2^k: 00101, five, becomes 01010, ten. Shifting right by k positions divides by 2^k and discards the remainder. A shift is far cheaper in hardware than a general multiplication, and the code on the right shows the decomposition that compilers routinely apply: ten times x equals eight times x plus two times x, that is, two shifts and one addition. Shifts also underlie the fixed-point arithmetic of Lecture 06. UNDERSTAND NOW: shifts as multiplications. For the lecturer: You used slli t1, t1, 2 in Lecture 04 to multiply an array index by four. Shifts are also the basis of fixed-point arithmetic (Lecture 06).

## Slide 5: Negating a number
By definition -x is represented by 2^n - x
Method 1: complement every bit, then add 1
– 6 = 0110, complement 1001, plus one: 1010 = -6
Method 2: starting from the right, copy the bits up to and including the first 1, complement all the others
– 5 = 0101 gives 1011 = -5; 1 = 0001 gives 1111 = -1
Negating twice returns the original number, with one exception: the most negative number has no positive partner
# neg t0, t1 is a pseudo-instruction:
sub t0, zero, t1
# the same thing by hand:
not t0, t1 # complement
addi t0, t0, 1 # plus one
UNDERSTAND NOW · two's complement
Notes: Two methods change the sign of a two's complement number. The first complements every bit and adds 1: six, 0110, becomes 1001 and then 1010, minus six. The second, faster by hand, scans from the right, copies the bits up to and including the first 1, and complements all the others. The justification of the first method is algebraic: the complement of x equals (2^n - 1) - x, so adding 1 yields 2^n - x, the representation of -x. RISC-V needs no dedicated instruction: neg is a pseudo-instruction for sub from the register zero. One exception remains: the most negative number has no positive counterpart, and negating it returns the same pattern. UNDERSTAND NOW: two's complement. For the lecturer: Why method 1 works: the complement of x is (2^n - 1) - x, so adding 1 gives 2^n - x. The source slide described method 2 'from the left'; the rule scans from the right.

## Slide 6: The warm-up, explained
marker_x held 0; addi t2, t2, -1 moved one step back on a wheel with 2^32 positions
The register now holds thirty-two ones: 0xFFFFFFFF
Read as unsigned it is 4,294,967,295; read in two's complement it is -1
– the adder did the same thing in both cases
prg32_console_hex32 prints the pattern, not an interpretation: it is neither right nor wrong
The marker disappears because prg32_gfx_rect is asked to draw at a huge x, or at -1: off the screen either way
Lab 06, step 2: seven lamps for the button bits and a marker
UNDERSTAND NOW · signed or unsigned instructions
Notes: The warm-up can now be explained completely. The marker stood at 0, and addi with -1 moved it one step backwards on a circle of 2^32 positions, leaving thirty-two ones in the register. Read as unsigned, they denote 4,294,967,295; read in two's complement, -1. The printing routine displays the pattern and takes no position on its meaning. The marker disappears because it is drawn off screen under either interpretation. The processor did not err: the program lacked a decision about how its value was to be interpreted and constrained. UNDERSTAND NOW: signed or unsigned instructions. For the lecturer: Not a bug in the processor: a missing decision in the program. The fix is on the next slides.

## Slide 7: Signed or unsigned? You choose with the instruction
Operation | Signed | Unsigned | Why they differ
add, subtract | add, addi, sub | the same | two's complement: one adder for both
multiply (low word) | mul | the same | the low 32 bits do not depend on the sign
compare | slt, slti | sltu, sltiu | is 0xFFFFFFFF less than 0? yes if signed
branch | blt, bge | bltu, bgeu | the same question, as a jump
shift right | sra, srai | srl, srli | copy the sign bit, or insert zeros
load a byte | lb | lbu | sign extension or zero extension
divide, remainder | div, rem | divu, remu | magnitudes are read differently
UNDERSTAND NOW · signed or unsigned instructions
Notes: RISC-V registers carry no type: thirty-two bits are signed or unsigned only for the instruction that reads them. The table identifies where the two interpretations require different instructions. Addition, subtraction and the low half of a product are identical for both. Comparisons, branches, right shifts, byte loads and division come in pairs: slt and sltu, blt and bltu, sra and srl, lb and lbu, div and divu. The letter u in the mnemonic always denotes the unsigned variant. Selecting the wrong member of a pair is a classic and instructive error. UNDERSTAND NOW: signed or unsigned instructions. For the lecturer: RISC-V registers have no type. The same 32 bits are signed or unsigned only in the eye of the instruction that reads them.

## Slide 8: Keeping the marker on the screen
andi t3, t0, BTN_LEFT
beqz t3, 1f
addi t2, t2, -SPEED
1: andi t3, t0, BTN_RIGHT
beqz t3, 2f
addi t2, t2, SPEED
2:
bgez t2, 3f # x < 0 ? clamp to 0
li t2, 0
3: li t3, MAX_X # .equ MAX_X, 304
ble t2, t3, 4f # x > 304 ? clamp to 304
mv t2, t3
4:
sw t2, 0(t1) # one store, after all adjustments
1
bgez reads t2 as a signed number: it tests the sign bit
2
ble is a signed comparison too: -1 is less than 304. With bleu, 0xFFFFFFFF would be far greater
3
A game does not detect overflow after the fact: it keeps values inside a range where overflow cannot happen
4
-SPEED is an immediate: twelve bits in two's complement, from -2048 to +2047
UNDERSTAND NOW · signed or unsigned instructions
Notes: The corrected program keeps the marker on the screen. After the two possible displacements, bgez tests whether the position is greater than or equal to zero, interpreting it as a signed number, and if it is not, sets it to 0. ble then compares it with the maximum, 304, again as a signed number, and limits it accordingly. This technique is called clamping. The method deserves notice: a game does not detect overflow after the fact, but keeps its values within a range in which overflow cannot occur. A single sw at the end stores the adjusted value. UNDERSTAND NOW: signed or unsigned instructions. For the lecturer: Source: textbook lab 06-asm-state-and-input, step3_clamp.S. Ask what happens with bgeu or bltu instead: an instructive bug to try.

## Slide 9: Detecting overflow without flags
# unsigned: did the sum wrap around?
add t2, t0, t1 # t2 = t0 + t1 (modulo 2^32)
sltu t3, t2, t0 # t3 = 1 if the sum is smaller than
# an operand: a carry was lost
# signed: did the sign come out wrong?
add t2, t0, t1
slti t3, t1, 0 # t3 = 1 if t1 is negative
slt t4, t2, t0 # t4 = 1 if the sum is less than t0
bne t3, t4, overflow # they must agree
1
RISC-V has no carry flag and no overflow flag: fewer hidden states, a simpler processor
2
Unsigned: a sum that wrapped is always smaller than either operand
3
Signed: adding a negative number must make the sum smaller; adding a non-negative one must not
UNDERSTAND NOW · signed or unsigned instructions
Notes: Many processors provide a carry flag and an overflow flag; RISC-V provides neither, and overflow is detected by comparison. In the unsigned case, if the sum after add is smaller than one of the operands, the result has wrapped around, a condition that sltu tests in a single instruction. In the signed case, adding a negative number must decrease the sum and adding a non-negative one must not; if these two facts disagree, overflow has occurred. In terms of the number wheel, the first test detects the crossing at the top and the second the crossing at the bottom. The absence of flags is a deliberate design choice, discussed in Lecture 18. UNDERSTAND NOW: signed or unsigned instructions. For the lecturer: Both idioms are the ones suggested in the RISC-V specification. Compare with the wheel: sltu detects crossing the top, the signed test detects crossing the bottom.

## Slide 10: The complete program: l05.S (1 of 5)
# ARC12 Computer Architecture - Lecture 05: Number Representation: Integers
# l05.S: hold LEFT and watch a number go below zero
#
# On the screen: the 32 bits of marker_x as lamps. It starts at 2 (one lamp); each
# frame with LEFT held subtracts 1: after 2, 1 and 0 every lamp lights up, 0xFFFFFFFF,
# which is -1.
# Build: python3 -m prg32 cartridge build l05.S --portable \
# --entry-prefix l05 --name l05 --out l05.prg32
.option norelax
.equ BLACK, 0x0000
.equ GREY, 0x4208
.equ YELLOW, 0xffe0
.equ BTN_LEFT, 1
.section .text
.global l05_init
.global l05_update
.global l05_draw
l05_init:
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l05.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 11: The complete program: l05.S (2 of 5)
l05_update:
addi sp, sp, -16
sw ra, 12(sp)
call prg32_input_read # a0 = button mask
mv t0, a0
la t1, marker_x
lw t2, 0(t1) # t2 = marker_x, starts at 2
andi t3, t0, BTN_LEFT # is LEFT pressed?
beqz t3, 1f
addi t2, t2, -1 # one step to the left
1: sw t2, 0(t1)
lw ra, 12(sp)
addi sp, sp, 16
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l05.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 12: The complete program: l05.S (3 of 5)
l05_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, BLACK
call prg32_gfx_clear
call prg32_console_clear # the number in hexadecimal, on the console
la t0, marker_x # (the board and QEMU show it on the screen,
lw a0, 0(t0) # PRG32-QT in its log)
call prg32_console_hex32
la t0, marker_x # and the same number, bit by bit
lw a0, 0(t0)
li a1, 96
call lamps32
lw ra, 12(sp)
addi sp, sp, 16
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l05.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 13: The complete program: l05.S (4 of 5)
# lamps32: show the 32 bits of a word as a row of lamps, bit 31 on the left.
# a0 = the word, a1 = y of the row. A lamp is yellow for 1, grey for 0.
lamps32:
addi sp, sp, -32
sw ra, 28(sp)
sw s0, 24(sp)
sw s1, 20(sp)
sw s2, 16(sp)
mv s0, a0 # the word
mv s1, a1 # y
li s2, 0 # lamp number, 0 on the left
1: li t0, 31
sub t0, t0, s2 # lamp i shows bit 31 - i
srl t1, s0, t0 # bring that bit down to bit 0
andi t1, t1, 1 # keep it, clear all the others
li a4, GREY # lamp off
beqz t1, 2f
li a4, YELLOW # lamp on
2: slli a0, s2, 3
add a0, a0, s2 # 9 * i
addi a0, a0, 16 # x = 16 + 9 * i
mv a1, s1
li a2, 8
li a3, 8
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l05.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 14: The complete program: l05.S (5 of 5)
call prg32_gfx_rect
addi s2, s2, 1
li t0, 32
blt s2, t0, 1b
lw s2, 16(sp)
lw s1, 20(sp)
lw s0, 24(sp)
lw ra, 28(sp)
addi sp, sp, 32
ret
.section .data
marker_x: .word 2
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l05.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 15: Run it: what you should see
On the screen
– the 32 bits of marker_x as lamps. It starts at 2 (one lamp); each frame with LEFT held subtracts 1: after 2, 1 and 0 every lamp lights up, 0xFFFFFFFF, which is -1.
What to press
– hold LEFT for a few frames
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 16: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l05.S --portable \
--entry-prefix l05 --name l05 --out l05.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l05.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 17: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l05.S --portable \
--entry-prefix l05 --name l05 --architecture qemu \
--out l05-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l05-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 18: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l05.S --portable \
--entry-prefix l05 --name l05 --architecture esp32c6 \
--out l05-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l05-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 19: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l05; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 20: Exercises: paper first, then PRG32
TRY IT
1
Convert 2026 to binary, octal and hexadecimal; convert 0.1 to binary up to eight fractional bits
2
Write -100 on 8 bits in sign and magnitude and in two's complement
3
Compute on 8 bits in two's complement: 90 + 60, -90 - 60, 90 - 60. Which overflow?
4
In the clamp code replace bgez and ble with their unsigned versions, predict the behaviour, then run it
5
Write an update that adds 0x10000000 to a counter each frame and lights a red rectangle when the signed sum overflows
Expected result
On paper: 2026 = 0x7EA = 111 1110 1010. On PRG32: the red rectangle flashes once every sixteen frames, when the counter passes from 0x7... to 0x8...
Notes: Five exercises, three on paper and two on the machine. Convert 2026 and the fraction 0.1; write -100 in two representations; compute three eight-bit sums and determine which overflow. Then, in the clamping code, replace the signed branches by their unsigned counterparts and predict the behaviour before running it: the resulting error is instructive precisely because it is predictable. Finally, write an update that adds 0x10000000 at each frame and signals the signed overflow. The expected results are given in the green box, which should remain covered until one's own answers have been obtained. For the lecturer: 2026 = 3752 octal. -100: sign and magnitude 1110 0100, two's complement 1001 1100. 90 + 60 = 150 overflows; -90 - 60 = -150 overflows; 90 - 60 = 30 does not. 0.1 = 0.00011001(1001...).