## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 14
Elementary Machines: Registers and Buses: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
14-Computer_Architecture-Registers_and_Buses.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 14. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: shift registers; registers as flip-flops; buses and three-state gates. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: memory-mapped I/O (Lecture 15); memories and addresses (Lecture 15). A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The 2 listings of Lecture 14, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l14.S, 94 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The program of this lecture is ~/arc12/code/l14.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l14.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Send a byte one bit at a time
# a0 = the byte to send, most significant bit first
li t0, 8 # eight bits to go
1: srli t1, a0, 7 # bring bit 7 down to bit 0
andi t1, t1, 1 # t1 = the bit to put on the wire
... # drive the data line with t1,
... # then pulse the clock line
slli a0, a0, 1 # shift left: the next bit moves up
addi t0, t0, -1
bnez t0, 1b
1
The display and the sound chip of the kit are connected by a few wires, not by thirty-two
2
A word must therefore travel one bit after another: a serial transfer
3
The loop is a shift register in software: shift, take one bit, repeat
4
The ESP32-C6 has hardware that does exactly this, millions of times per second
UNDERSTAND LATER · memory-mapped I/O → Lecture 15
UNDERSTAND NOW · shift registers
Notes: The warm-up loop transmits a byte one bit at a time, most significant bit first. At each iteration the byte is shifted right by 7 and masked with 1, isolating its top bit; that bit would be placed on a data line and a clock line pulsed; the byte is then shifted left by one, so that the next bit moves into the top position. After eight iterations the whole byte has been sent. The loop is a shift register realised in software. The two elided lines would write to memory-mapped GPIO registers, a mechanism explained in Lecture 15. The chip of the kit contains dedicated hardware that performs the same operation millions of times per second. UNDERSTAND NOW: shift registers. UNDERSTAND LATER: memory-mapped I/O (studied in Lecture 15). For the lecturer: Written for this lecture. On the kit the display uses SPI and the amplifier I2S: both are serial buses driven by shift registers inside the chip. The two elided lines would write to memory-mapped GPIO registers (Lecture 15).

## Slide 4: Buses on the PRG32 kit
Connection | Kind | Lines | What travels on it
inside the ESP32-C6 | parallel | 32 data lines, address and control | instructions, data and register transfers
display (ILI9341) | serial, SPI | clock, data out, chip select, data/command | every pixel of every frame, bit by bit
sound amplifier | serial, I2S | bit clock, word select, data | audio samples, 22,050 per second
joystick and buttons | one wire per button | one input pin each | a decoded representation: one line per button
USB to the laptop | serial, differential pair | two data wires | the firmware and the debug console
UNDERSTAND NOW · buses and three-state gates
Notes: The buses of the kit. Within the chip the bus is parallel. The display is connected by SPI, a serial bus with a clock line, a data line, a chip-select line and a line distinguishing data from commands; every pixel of every frame travels across it bit by bit. The amplifier is connected by I2S, another serial bus, which carries 22,050 audio samples per second. The buttons use one wire each, a decoded representation. USB, also serial, carries the firmware and the debug console. The kit thus exemplifies the general trend stated in the lecture: parallel inside the chip, serial between chips. UNDERSTAND NOW: buses and three-state gates. For the lecturer: From the hardware description of the PRG32 repository (docs/hardware). Chip select is the CS of the small memory of the lecture deck: several devices can share the same serial bus because only the selected one listens.

## Slide 5: Shifts in RISC-V: a shift register in one instruction
slli and srli move all the bits of a register by a given number of positions, filling with zeros
srai fills with copies of the sign bit (Lecture 05)
sll, srl and sra take the amount from a second register
In hardware a shift by any amount in one step is done by a barrel shifter: layers of multiplexers, not a chain of flip-flops
The shifter is one of the units of the ALU of Lecture 11
# parallel to serial, LSB first
andi t1, a0, 1 # take bit 0
srli a0, a0, 1 # next bit
# serial to parallel, MSB first
slli a1, a1, 1 # make room
or a1, a1, t1 # insert bit
UNDERSTAND NOW · shift registers
Notes: The shift instructions move every bit of a register in a single step: slli and srli fill with zeros, srai with copies of the sign bit, while sll, srl and sra take the shift amount from a register. In hardware this is not a chain of flip-flops, which would require one clock pulse per position, but a barrel shifter, a combinational network of layers of multiplexers, and one of the units of the ALU. The code on the right shows the two conversions, parallel to serial and serial to parallel. UNDERSTAND NOW: shift registers. For the lecturer: A true shift register needs n clock pulses for n positions; the barrel shifter of the ALU is combinational and does it within one clock period.

## Slide 6: The complete program: l14.S (1 of 6)
# ARC12 Computer Architecture - Lecture 14: Elementary Machines: Registers and Buses
# l14.S: a byte sent one bit at a time, and rebuilt at the other end
#
# On the screen: top row: the eight bits of 0xA5 in the order in which they leave,
# most significant first (lit, dark, lit, dark, dark, lit, dark, lit). Bottom row: the
# byte rebuilt by the receiver. A green square says that it is equal to the byte sent.
# Build: python3 -m prg32 cartridge build l14.S --portable \
# --entry-prefix l14 --name l14 --out l14.prg32
.option norelax
.equ BLACK, 0x0000
.equ GREY, 0x4208
.equ YELLOW, 0xffe0
.equ GREEN, 0x07e0
.equ RED, 0xf800
.equ BYTE, 0xA5 # the byte to send: 1010 0101
.section .text
.global l14_init
.global l14_update
.global l14_draw
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: The complete program: l14.S (2 of 6)
l14_init:
ret
l14_update:
ret
# lamp: a0 = position 0 to 7, a1 = y, a2 = bit
lamp:
li a4, GREY
beqz a2, 1f
li a4, YELLOW
1: slli a0, a0, 5
addi a0, a0, 36 # x = 36 + 32 * position
li a2, 24
li a3, 24
tail prg32_gfx_rect
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: The complete program: l14.S (3 of 6)
l14_draw:
addi sp, sp, -32
sw ra, 28(sp)
sw s0, 24(sp)
sw s1, 20(sp)
sw s2, 16(sp)
sw s3, 12(sp)
li a0, BLACK
call prg32_gfx_clear
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: The complete program: l14.S (4 of 6)
li s0, BYTE # a0 of the slide: the byte to send
li s1, 0 # the receiver's shift register
li s2, 0 # how many bits have gone
1: srli t1, s0, 7 # bring bit 7 down to bit 0
andi s3, t1, 1 # s3 = the bit to put on the wire
mv a0, s2 # ... here the wire is a lamp:
li a1, 40 # position = the order of sending
mv a2, s3
call lamp
slli s1, s1, 1 # receiver: make room (serial to parallel)
or s1, s1, s3 # insert the bit
slli s0, s0, 1 # sender: shift left, the next bit moves up
andi s0, s0, 255 # (keep eight bits)
addi s2, s2, 1
li t0, 8 # eight bits to go
blt s2, t0, 1b
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 10: The complete program: l14.S (5 of 6)
li s2, 0 # show the byte that the receiver rebuilt
2: li t0, 7
sub t0, t0, s2
srl a2, s1, t0
andi a2, a2, 1
mv a0, s2
li a1, 100
call lamp
addi s2, s2, 1
li t0, 8
blt s2, t0, 2b
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 11: The complete program: l14.S (6 of 6)
li a4, RED # is it the byte that was sent?
li t0, BYTE
bne s1, t0, 3f
li a4, GREEN
3: li a0, 152
li a1, 150
li a2, 16
li a3, 16
call prg32_gfx_rect
lw s3, 12(sp)
lw s2, 16(sp)
lw s1, 20(sp)
lw s0, 24(sp)
lw ra, 28(sp)
addi sp, sp, 32
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 12: Run it: what you should see
On the screen
– top row: the eight bits of 0xA5 in the order in which they leave, most significant first (lit, dark, lit, dark, dark, lit, dark, lit). Bottom row: the byte rebuilt by the receiver. A green square says that it is equal to the byte sent.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 13: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l14.S --portable \
--entry-prefix l14 --name l14 --out l14.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l14.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 14: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l14.S --portable \
--entry-prefix l14 --name l14 --architecture qemu \
--out l14-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l14-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 15: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l14.S --portable \
--entry-prefix l14 --name l14 --architecture esp32c6 \
--out l14-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l14-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 16: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l14; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 17: Exercises: paper first, then PRG32
TRY IT
1
Draw a 4-bit serial-in, parallel-out shift register with D flip-flops, and fill in its contents over four clock pulses for the input 1, 0, 1, 1
2
Three registers share a common bus: write the enable and load signals needed to copy register B into register A
3
Complete the warm-up: write the loop that receives eight bits from a line and rebuilds the byte
4
On PRG32, show a byte as eight lamps and shift it left by one position every half second
5
Make the bit that leaves on the left come back in on the right (a rotation): a ring counter
Expected result
On PRG32: a pattern of lamps that walks to the left and, in the last exercise, goes round for ever.
Notes: Five exercises. Draw a 4-bit serial-in, parallel-out shift register and trace its content over four clock pulses. Write the enable and load signals that copy one register into another over a common bus. Complete the warm-up with the receiving loop, which reconstructs the byte. On PRG32, display a byte as eight lamps and shift it every half second. Finally, make the bit that leaves on one side re-enter on the other: a rotation, which in hardware is called a ring counter. For the lecturer: Exercise 3: slli a1, a1, 1 then or with the received bit, eight times. Exercise 5: srli t1, a0, 7; andi t1, t1, 1; slli a0, a0, 1; or a0, a0, t1; andi a0, a0, 255.