## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 19
Instructions and Interrupts
Instruction formats, the processor cycle, and how RISC-V handles exceptional events
“Why does the CPU never get any work done? Because it gets interrupted constantly.”
Anonymous joke about computer architecture
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Lecture deck. The listings, the complete program and how to test it are in the code deck:
19-Computer_Architecture-Instructions_and_Interrupts-Lab.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: The previous lecture described what a processor is made of; this one describes what it does. It has two halves. The first follows a single instruction: how it is encoded in 32 bits and which steps the processor takes to execute it. The second explains what happens when something more urgent than the current program arrives, a timer, a device or an error, so that the processor must suspend its work and resume it later. The two halves are connected: the interrupt is a modification of the very cycle the first half describes. The joke on the cover, as will become apparent, is nearly literally true. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: instruction formats; addressing modes; the processor cycle; interrupts and traps. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise. For the lecturer: The original deck used a 16-bit word machine for the fetch phase and the Motorola MC68000 for vectored interrupts and priorities. Both are replaced by RISC-V: the six instruction formats, the five classic stages, and the machine-mode trap mechanism (mtvec, mepc, mcause, mstatus, mret). A comparison slide keeps the 68000 as the historical counterpart.

## Slide 2: What you will be able to do by the end
1
Describe an instruction as an operation code and its operands, and name the kinds of operand
2
Decode a RISC-V instruction by hand, recognising its format and fields
3
Follow an instruction through the processor cycle: fetch, decode, execute, memory, write back
4
Explain what a pipeline is and why it makes a processor faster
5
Define interrupts, exceptions and traps, and list their causes
6
Describe what RISC-V does when a trap occurs and how the interrupted program resumes
Notes: Six learning outcomes. Describing an instruction as an operation code with operands. Decoding a RISC-V instruction by hand. Following an instruction through the five phases of the processor cycle. Explaining what a pipeline is and why it increases throughput. Defining interrupt, exception and trap, three terms that RISC-V uses with precision. And describing what the hardware does at a trap and how the interrupted program resumes.

## Slide 3: What an instruction is made of
Typical instructions of a processor
– data transfers between memory and registers
– arithmetic and logic operations
– instructions for the control of flow
– data transfers to and from input/output
An instruction is composed of an operation code, the opcode, and zero or more operands
Kinds of operand
– a constant: an immediate, explicit or implicit
– a memory location
– a register, explicit or implicit (the accumulator)
Instructions can have zero, one, two or three operands
UNDERSTAND NOW · instruction formats
Notes: Every processor provides four families of instructions: transfers between memory and registers, arithmetic and logical operations, control of flow, and input/output. An instruction consists of an operation code, the opcode, specifying what to do, followed by zero or more operands, specifying on what. An operand may be a constant written within the instruction, an immediate; a memory location; or a register. Some operands are implicit, as the accumulator is in an accumulator machine. Instructions have from zero to three operands. UNDERSTAND NOW: instruction formats. For the lecturer: In RISC-V the fourth family does not exist as such: devices are memory (Lecture 15). add has three operands, all registers; ret has none visible.

## Slide 4: The formats of RISC-V instructions
R: register to register (add, sub, and, sll, ...)
funct7
31
25
rs2
24
20
rs1
19
15
funct3
14
12
rd
11
7
opcode
6
0
I: immediates and loads (addi, andi, lw, jalr, ...)
immediate [11:0]
rs1
funct3
rd
opcode
S: stores (sw, sh, sb); B: branches, with the same shape
imm [11:5]
rs2
rs1
funct3
imm [4:0]
opcode
U: upper immediates (lui, auipc); J: jumps (jal), with the same shape
immediate [31:12]
rd
opcode
Six formats, all of 32 bits. The opcode is always in the same seven bits, and the register numbers rd, rs1 and rs2 are always in the same places: the processor can read them before it even knows which instruction it is.
UNDERSTAND NOW · instruction formats
Notes: The instruction formats of RISC-V. Every instruction is 32 bits long and divided into fields. In the R format, for register-to-register operations, there are three five-bit register numbers, rs1, rs2 and rd, and three fields that select the operation. In the I format the second source register is replaced by a 12-bit immediate. S and B, for stores and branches, split the immediate into two pieces. U and J carry a 20-bit immediate. The regularity is a design objective: the opcode always occupies the lowest seven bits and the register fields always the same positions, so decoding can begin before the format is known. The 16-bit compressed forms of the C extension are only named here; Appendix A of the textbook lists them. UNDERSTAND NOW: instruction formats. For the lecturer: Bits 31 down to 0, left to right (indices shown on the first row). B and J differ from S and U only in how the bits of the immediate are arranged. This regularity is the heart of the RISC idea; the generic 0-, 1-, 2- and 3-operand formats of the original deck are its ancestors.

## Slide 5: Addressing modes: where an operand is found
Mode | The operand is | RISC-V example
immediate | a constant inside the instruction | addi t1, t1, 1
register | the content of a register | add t2, t0, t1
base plus displacement | the memory word at register + constant | lw t1, 8(sp)
PC-relative | an address at a distance from the instruction itself | beq t0, t1, loop
memory indirect | the memory word whose address is in memory | not available: two loads
UNDERSTAND NOW · addressing modes
Notes: An addressing mode is a method of locating an operand. RISC-V provides four. Immediate: the operand is a constant within the instruction. Register: it is the content of a register. Base plus displacement: it is the memory word at the address formed by a register plus a constant, the only means of reaching memory. PC-relative: an address at a given distance from the instruction itself, used by branches. Memory-indirect addressing, in which the address itself resides in memory, does not exist: it requires two loads. This is the formal treatment promised in Lecture 02 when address and value were first distinguished. UNDERSTAND NOW: addressing modes. For the lecturer: RISC-V has only the first four. A CISC processor such as the MC68000 has a dozen, including memory-indirect and auto-increment modes. The example of the original deck, R3 := M[M[A]], becomes in RISC-V: lw t0, 0(t1) followed by lw t0, 0(t0). The 'operand assembly' phase of a CISC processor is the price of rich addressing modes.

## Slide 6: The phases of the cycle
Fetch
the instruction at the address in the PC is read from memory; the PC advances
Decode
the opcode is recognised; the registers named by the instruction are read
Execute
the ALU computes: a result, an address or a comparison
Memory
loads read the memory, stores write it; the others skip this phase
Write back
the result is written into the destination register
After a start-up phase, the bootstrap, the processor repeats this cycle for ever. In processors with rich addressing modes, a phase of operand assembly collects the operands before the execution.
UNDERSTAND NOW · the processor cycle
Notes: Five phases. Fetch: the instruction at the address in the PC is read from memory and the PC advanced. Decode: the opcode is recognised and the registers named in the instruction are read. Execute: the ALU computes a result, an address or a comparison. Memory: loads read memory, stores write it, and other instructions do nothing in this phase. Write back: the result is written into the destination register. After the initial bootstrap the processor repeats this cycle indefinitely. UNDERSTAND NOW: the processor cycle. For the lecturer: Algoritmo fondamentale del processore: inizializzazione, instruction fetch and decoding, operand assembly, execute. The five-phase version is the classic RISC formulation.

## Slide 7: The pipeline
clock cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
instruction 1 | IF | ID | EX | MEM | WB |  |  | 
instruction 2 |  | IF | ID | EX | MEM | WB |  | 
instruction 3 |  |  | IF | ID | EX | MEM | WB | 
instruction 4 |  |  |  | IF | ID | EX | MEM | WB
Five phases, five pieces of hardware: while one instruction executes, the next is decoded and a third is fetched
Each instruction still takes five cycles, but one completes at every clock cycle: five times the throughput
Superscalar processors put two or more pipelines side by side: more than one instruction per cycle
The main core of the ESP32-C6 has a four-stage pipeline
UNDERSTAND NOW · the processor cycle
Notes: If each phase has dedicated hardware, the phases of successive instructions can overlap. In the table each row is an instruction and each column a clock cycle: while the first instruction executes, the second is decoded and the third fetched. Each instruction still requires five cycles, but one completes every cycle: this is the pipeline, the principle of the assembly line, which increases throughput without reducing latency. Superscalar processors place several pipelines side by side, as Lecture 24 shows. The main core of the kit has a four-stage pipeline. UNDERSTAND NOW: the processor cycle. For the lecturer: Source slide: «Esempio di pipeline lineare a 5 stadi; superscalarità». IF instruction fetch, ID decode, EX execute, MEM memory, WB write back. Branches and dependences between neighbouring instructions complicate the picture (hazards): the subject of an advanced course.

## Slide 8: The problem with the simple cycle
If the processor only ever did fetch, decode, execute, some problems would arise
Interaction with the outside world through the I/O units would be inefficient: the program would have to keep asking
There would be no way to forcibly remove an application that enters an infinite loop by mistake
The operating system would have limited control over the system
j loop
a program stuck in an endless loop: who takes the processor away from it?
UNDERSTAND NOW · interrupts and traps
Notes: A processor that did nothing but fetch, decode and execute would face three problems. Communication with devices would be inefficient, since the program would have to interrogate each device repeatedly. A program trapped by mistake in an endless loop, such as the j loop on the slide, could never be removed. And the operating system would have little control over the machine. All three share one solution: a mechanism for taking the processor away from the running program. UNDERSTAND NOW: interrupts and traps. For the lecturer: Source slide: «Ciclo del processore semplificato»: bootstrap, fetch, operand assembly, execute.

## Slide 9: Interrupts
Definition
Exceptional events, usually asynchronous with respect to the execution of the program in progress, that require the attention of the processor.
RISC-V vocabulary: an interrupt comes from outside the program, at any moment: a timer, a device
An exception is caused by the instruction being executed: an illegal opcode, a forbidden address
A trap is the transfer of control to a handler that follows either of them
UNDERSTAND NOW · interrupts and traps
Notes: The definition: interrupts are exceptional events, usually asynchronous with respect to the executing program, that require the attention of the processor. RISC-V distinguishes three terms. An interrupt originates outside the program and may arrive at any moment: a timer, a device. An exception is caused by the instruction being executed: an illegal opcode, a forbidden address. A trap is the transfer of control to a handler, whatever its cause. Other architectures use these words less strictly, so the RISC-V usage is worth adopting for its clarity. UNDERSTAND NOW: interrupts and traps. For the lecturer: Interrupt o interruzioni. Older processors and the original deck call 'traps' the synchronous events and use 'interrupt' for everything; the RISC-V specification uses the three words precisely.

## Slide 10: The real processor cycle
bootstrap
fetch
decode and
execute
interrupt
pending?
no
trap: go to
the handler
yes
At the end of each instruction the processor checks whether any interrupt signal has occurred
If there is none, the processing returns to the fetch phase
If there is one, the processor passes to the supervisor state and starts executing a routine of the system
When the routine ends, the suspended program can resume as if nothing had happened
UNDERSTAND NOW · interrupts and traps
Notes: The real cycle. After the bootstrap the processor fetches, decodes and executes; then, at the end of every instruction, it checks whether an interrupt is pending. If none is, it returns to fetch. If one is, it takes the trap: it enters the privileged state and begins executing a system routine, the handler. When the handler completes, the suspended program resumes as though nothing had occurred. The two paths on the diagram should be followed; the short loop is the common case. UNDERSTAND NOW: interrupts and traps. For the lecturer: Ciclo del processore reale. In RISC-V 'supervisor state' is machine mode, and the first instruction fetched after the trap is the one at the address in mtvec.

## Slide 11: Possible causes of interruption
1
Periodic interrupt
A timer, for example every 10 ms: to share the processor among programs and to measure the time each one uses.
2
I/O interrupt
A peripheral reports its state, for example that it is ready to receive data, to synchronise with the processor.
3
Errors in the program
An instruction that does not exist or is privileged, a forbidden address: synchronous events, called exceptions.
4
Faults
Failures of the system detected by dedicated probes: power, temperature, memory errors.
5
Reset
Brings the whole system back to a known state.
6
Software interrupt
Generated by a program that needs a shared resource and asks the operating system to mediate: in RISC-V, the instruction ecall.
UNDERSTAND NOW · interrupts and traps
Notes: Six causes of interruption. A periodic interrupt from a timer, used to share the processor among programs. An I/O interrupt, by which a peripheral signals that it is ready. Program errors, such as an instruction that does not exist: these are the exceptions. System faults: power, temperature. Reset, which returns everything to a known state. And the software interrupt, by which a program requests a service from the operating system: in RISC-V, the instruction ecall. UNDERSTAND NOW: interrupts and traps. For the lecturer: The original deck lists arithmetic overflow among the program errors: in RISC-V integer overflow does not raise an exception (Lecture 05). ecall, environment call, is synchronous with the program that executes it.

## Slide 12: Handling an interrupt
1
Save the context, hardware part: at least the address at which to resume
2
Identify the cause of the interrupt
3
Jump to the entry point of the interrupt service routine (ISR)
4
Save the context, software part: the registers the routine is going to use
5
Serve the interrupt
6
If the interrupt allows it: restore the context, and resume the suspended program from the instruction that follows the last one executed
UNDERSTAND NOW · interrupts and traps
Notes: The general procedure in six steps. Save the context, hardware part: at minimum the address at which to resume. Identify the cause. Jump to the entry point of the interrupt service routine. Save the context, software part: the registers the routine will use. Serve the interrupt. Finally, restore the context and resume the suspended program at the instruction following the last one executed. The context is everything the interrupted program requires to find unchanged, and its preservation is what makes the interruption invisible. UNDERSTAND NOW: interrupts and traps. For the lecturer: Gestione delle interruzioni. The state to save and restore: PC, status, and the registers. Saving can be done partly or wholly in hardware or in software; RISC-V does the minimum in hardware. With several devices the processor must identify who interrupted and, for simultaneous requests, apply a priority.

## Slide 13: The registers of the trap mechanism
CSR | Written by | Content
mtvec | the firmware, once, at start-up | the address of the trap handler, and whether the vectored mode is used
mstatus | hardware and firmware | MIE, the global interrupt enable, and MPIE, its previous value
mie | the firmware | one enable bit for each source: software, timer, external
mip | the hardware | one pending bit for each source
mepc | the hardware, at each trap | the address of the interrupted instruction
mcause | the hardware, at each trap | one bit that says interrupt or exception, and a code for the cause
UNDERSTAND NOW · interrupts and traps
Notes: Six registers. mtvec, written once by the firmware, holds the address of the trap handler. mstatus contains MIE, the global interrupt enable, and MPIE, its previous value. mie holds one enable bit per source, mip one pending bit per source. mepc receives, at each trap, the address of the interrupted instruction. mcause receives the cause. The middle column deserves attention: some registers are written by the firmware to configure the mechanism, others by the hardware when a trap occurs. UNDERSTAND NOW: interrupts and traps. For the lecturer: Machine-mode control and status registers (Lecture 18). An interrupt is taken only if its bit is set in both mip and mie and MIE is 1.

## Slide 14: What the hardware does on a trap
1
mepc := the address of the interrupted instruction
2
mcause := the cause: top bit 1 for an interrupt, 0 for an exception, plus a code
3
mstatus: MPIE := MIE, then MIE := 0, so that further interrupts are disabled
4
the processor passes to machine mode
5
PC := the address in mtvec, or, in vectored mode and for interrupts, that address plus 4 times the cause
6
mret, at the end of the handler, undoes it: MIE := MPIE and PC := mepc
UNDERSTAND NOW · interrupts and traps
Notes: The actions of the hardware at a trap, in order. It writes into mepc the address of the interrupted instruction. It writes the cause into mcause. It copies MIE into MPIE and clears MIE, disabling further interrupts. It enters machine mode. It loads the PC with the address in mtvec. Nothing is saved on a stack: the general registers are left to the handler, consistently with the absence of hidden state noted in Lecture 18. The instruction mret, at the end of the handler, reverses everything: MIE recovers MPIE and the PC recovers mepc. UNDERSTAND NOW: interrupts and traps. For the lecturer: Nothing is pushed on a stack by the hardware: saving the general registers is left to the handler. This is the 'hardware context save' of the general scheme, reduced to two registers and one bit.

## Slide 15: The cause of a trap: mcause
Kind | Code | Cause
interrupt | 3 | machine software interrupt
interrupt | 7 | machine timer interrupt
interrupt | 11 | machine external interrupt: a device, through the interrupt controller
exception | 2 | illegal instruction
exception | 3 | breakpoint (ebreak): how a debugger stops a program
exception | 5, 7 | load or store access fault: a forbidden address
exception | 8, 11 | environment call (ecall) from user mode, from machine mode
UNDERSTAND NOW · interrupts and traps
Notes: The content of mcause. The top bit indicates whether the trap was an interrupt or an exception; the remaining bits are a code. The three interrupts, highlighted, are software, timer and external, that is, a device. Among the exceptions are illegal instruction, breakpoint, access fault on a load or store, and ecall. The same number may appear in both families with different meanings, which is why the top bit is needed. The breakpoint row explains how a debugger such as that of PRG32-QT halts a program. UNDERSTAND NOW: interrupts and traps. For the lecturer: The standard codes of the privileged specification; chips add their own. The same code 3 means different things for interrupts and exceptions: the top bit of mcause distinguishes them. With mtvec in vectored mode, a timer interrupt enters at base + 4 x 7.

## Slide 16: Interrupts on the PRG32 kit
A timer interrupts the processor a hundred times per second: the firmware uses it to keep time and to pace the frames
The display and sound peripherals interrupt when a block of data has been sent and the next is wanted
The Wi-Fi radio interrupts when a packet arrives: a cartridge can be uploaded while a game is running
Your init, update and draw are ordinary functions called by the firmware between one interrupt and the next
A cartridge stuck in a loop does not stop the interrupts: PRG32-QT ends the frame with an error; on the board a watchdog reports the stall, and you press reset
The PRG32 firmware menu
UNDERSTAND NOW · interrupts and traps
Notes: All of this takes place on the kit. A timer interrupts the processor a hundred times per second, and the firmware uses it to keep time and pace the frames. The display and the audio interrupt when they require more data. The radio interrupts when a packet arrives, which is why a cartridge can be uploaded while a game runs. The functions init, update and draw are ordinary functions executed between interrupts. And a cartridge caught in a loop does not stop the interrupts: PRG32-QT reports an error, and on the board a watchdog reports the stall. UNDERSTAND NOW: interrupts and traps. For the lecturer: The three problems of the simple cycle (inefficient I/O, runaway programs, limited control) and their solution, all visible on the kit. Checked against the firmware sources and configuration (not on a physical board): the cartridge runs natively inside the main task, in the same privilege mode as the firmware; FreeRTOS ticks at 100 Hz; the task watchdog (5 s, watching the idle task) only prints a warning on the serial port, because the panic option is off, so a stuck cartridge keeps the cartridge lock and the kit needs a reset. A cartridge that disabled interrupts would instead trip the interrupt watchdog (300 ms), which panics and restarts the chip. Run on PRG32-QT: an endless loop gives 'instruction budget exhausted', a write to mstatus gives 'unsupported CSR'. In PRG32-QT a breakpoint is the exception with code 3.

## Slide 17: Check your understanding
1
In which bits of a RISC-V instruction is the opcode?
A
the seven most significant
B
the seven least significant
C
bits 14 to 12
D
it depends on the format
2
During the fetch of an RV32 instruction that is not compressed, the PC is increased by:
A
1
B
2
C
4
D
32
Notes: For the first question one returns to the slide of the formats: one field occupies the same position in all four rows. For the second: addresses count bytes, and the question is how many bytes a 32-bit instruction occupies. For the lecturer: 1. Answer: B. Bits 6 to 0, in every format: the processor always knows where to look first. 2. Answer: C. Addresses count bytes and an instruction is four bytes long.

## Slide 18: Check your understanding
1
Which register holds the address at which an interrupted RISC-V program will resume?
A
ra
B
mtvec
C
mepc
D
mcause
2
Which of these is an exception rather than an interrupt, in RISC-V terms?
A
a timer expires
B
a key is pressed
C
an illegal instruction is fetched
D
a packet arrives from the network
Notes: For the first question, four registers are involved: one holds the address of the handler, one the cause, one the address at which to resume. ra belongs to procedure calls, not to traps. For the second, the definition applies: an exception is caused by the instruction being executed, whereas an interrupt arrives from outside at an arbitrary moment. Three of the four events originate outside the program. For the lecturer: 1. Answer: C. mepc, written by the hardware at the trap and used by mret. mtvec holds the address of the handler. 2. Answer: C. It is caused by the instruction being executed, synchronously; the others come from outside, at any moment.

## Slide 19: Glossary: English and Italian
English | Italiano | English | Italiano
operation code (opcode) | codice operativo | interrupt | interruzione
operand | operando | exception / trap | eccezione / trap
addressing mode | modo di indirizzamento | interrupt service routine | routine di servizio dell'interruzione
fetch / decode / execute | prelievo / decodifica / esecuzione | interrupt latency | latenza di interruzione
pipeline stage | stadio della pipeline | to mask an interrupt | mascherare un'interruzione
context | contesto | nesting | annidamento
Notes: Twelve terms. The operation code is the codice operativo; an addressing mode is a modo di indirizzamento. Fetch, decode and execute are prelievo, decodifica and esecuzione. The interrupt service routine is the routine that serves an interrupt. Interrupt latency is the delay between the request and the start of useful work. To mask an interrupt is to prevent its acceptance temporarily.

## Slide 20: Conclusions and reading
An instruction is an operation code and zero, one or more operands; in RISC-V it is always 32 bits, in six regular formats
A fixed length keeps the fetch simple: the PC advances by a constant, 4 for an instruction that is not compressed
The processor has a cycle: it fetches an instruction, decodes it, executes it, and writes the result
Exceptional events break the cycle: the processor saves where it was, serves the event and resumes
Interrupts can be enabled, masked and ordered by priority; RISC-V does it with a handful of registers and the instruction mret
Reading
– Patterson, Hennessy: Computer Organization and Design, RISC-V Edition, sections 2.5, 4.1-4.6 and 4.10
– The RISC-V Instruction Set Manual, volume II: Privileged Architecture
– Playing with RISC-V, chapter 4: PRG32-QT and its debugger
Notes: Five conclusions. An instruction is an operation code with its operands; in RISC-V it is always 32 bits long, in six regular formats, unless compressed. A fixed length keeps the fetch simple: the PC advances by a constant, 4 for an uncompressed instruction. The processor executes a cycle: fetch, decode, execute, write the result. Exceptional events interrupt the cycle: the processor records where it was, serves the event and resumes. Interrupts can be enabled, masked and prioritised, and RISC-V achieves all of this with a handful of registers and mret. The next lecture leaves the processor for the buses and the video card. Learning status, recap. UNDERSTAND NOW: instruction formats; addressing modes; the processor cycle; interrupts and traps. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise. For the lecturer: The original conclusions stated that 'the interrupt is a non-maskable signal': most interrupts can be masked; only a few cannot. Next lecture: buses and the video card.