## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 24
Beyond One Core: Superscalar RISC‑V, HPC, GPUs and FPGAs: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
24-Computer_Architecture-Superscalar_HPC_GPU_FPGA.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 24. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: the performance equation; superscalar processors; vector instructions; HPC and Amdahl's law; GPU and FPGA accelerators. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The 7 listings of Lecture 24, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l24.S, 72 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The program of this lecture is ~/arc12/code/l24.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l24.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: The loop that empties the map
la t0, grid
li t1, COLS*ROWS
1: sb zero, 0(t0) # one byte per turn of the loop
addi t0, t0, 1
addi t1, t1, -1
bnez t1, 1b
1
From new_game of Verm1: 960 bytes set to zero
2
Four instructions per byte: 3 840 instructions in all
3
One byte at a time, one instruction at a time
4
How many ways are there to make this faster?
UNDERSTAND NOW · the performance equation
Notes: The warm-up: the loop in new_game that clears the map, setting 960 bytes to zero. Each iteration executes four instructions: a byte store, the increment of the address, the decrement of the counter, and the branch back, for 3,840 instructions in all, one byte and one instruction at a time. On the kit it takes about 24 microseconds, and nothing requires it to be faster. It was chosen because it is small enough to be followed onto every class of contemporary machine. The lecture's question is: in how many distinct ways can it be made faster? UNDERSTAND NOW: the performance equation. For the lecturer: The processor cycle of Lecture 19. At best one instruction per clock cycle, and 160 million cycles per second on the kit: about 24 microseconds. Nobody needs this loop to be faster; it is small enough to follow onto every machine of today.

## Slide 4: What gets in the way: dependences
add t0, t1, t2 # i1
add t3, t0, t4 # i2 needs the t0 of i1: it must wait
lw t5, 0(t6) # i3 is independent: it could go now
beqz t3, skip # i4: which way? known only after i2
addi t5, t5, 1 # i5: executed, or not?
skip:
1
i2 cannot run beside i1: it uses its result
2
i3 depends on nobody: why should it wait?
3
After a branch the processor does not know what comes next
4
Real code is full of such chains: width alone is not enough
UNDERSTAND NOW · superscalar processors
Notes: What impedes parallel execution. The second instruction uses t0, which the first is still computing, so it cannot execute alongside it: a data dependence. The third depends on nothing, yet in an in-order processor it waits behind the second. The fourth is a branch: until it is resolved the processor cannot know whether the fifth must be executed, a control dependence. Real programs are full of such chains, so issue width alone does not deliver speed; the remedy is to let independent instructions overtake. UNDERSTAND NOW: superscalar processors. For the lecturer: Data dependences, control dependences. An in-order superscalar stalls at i2 and everything behind it waits. The remedy is to let i3 overtake.

## Slide 5: Register renaming: thirty-two names, many registers
# as written # as executed, after renaming
lw t0, 0(a0) lw p41, 0(a0)
addi t0, t0, 1 addi p42, p41, 1
sw t0, 0(a0) sw p42, 0(a0)
lw t0, 4(a0) lw p43, 4(a0) # a new t0
addi t0, t0, 1 addi p44, p43, 1
sw t0, 4(a0) sw p44, 4(a0)
1
The second half reuses the name t0, not its value
2
Renamed, the two halves share nothing
3
They can run at the same time, on different registers
4
The 32 registers you know are names; the chip has many more
UNDERSTAND NOW · superscalar processors
Notes: Register renaming illustrated. On the left, the code as written: two halves, each loading a word, incrementing it and storing it back, and both using t0. The second half reuses the name, not the value, which constitutes a false dependence. On the right, after renaming, each new value has its own physical register, so the two halves share nothing and can execute simultaneously. The thirty-two registers of the instruction set are names; the chip contains a few hundred physical registers. The register numbers on the slide are illustrative. UNDERSTAND NOW: superscalar processors. For the lecturer: A false dependence: the same name for two unrelated values. p41 to p44 are invented numbers of physical registers. A big core has a few hundred of them.

## Slide 6: The same loop, with vectors
la t0, grid
li t1, COLS*ROWS
vsetvli t2, t1, e8, m1, ta, ma # elements are bytes
vmv.v.i v0, 0 # a register full of zeros
1: vsetvli t2, t1, e8, m1, ta, ma # t2 = bytes of this turn
vse8.v v0, (t0) # store t2 bytes at once
add t0, t0, t2
sub t1, t1, t2
bnez t1, 1b
1
v0 is a vector register: many bytes wide
2
vsetvli asks: how many of the bytes left fit? The answer is in t2
3
vse8.v stores t2 bytes with one instruction
4
With 128-bit registers: 16 bytes per turn, 60 turns instead of 960
UNDERSTAND NOW · vector instructions
Notes: The same loop written with the vector extension. v0 is a vector register, many bytes wide, filled with zeros. In each iteration vsetvli asks how many of the remaining bytes fit in a register, and the answer is placed in t2. vse8.v stores that many bytes in a single instruction, and the address and the counter advance by t2. With 128-bit registers one iteration handles 16 bytes: 60 iterations instead of 960. The code never states the width of the registers, so the same binary is correct for any width, a property called vector-length agnosticism, which the test verifies at four widths. UNDERSTAND NOW: vector instructions. For the lecturer: The V extension, ratified in 2021. Not on the kit: the ESP32-C6 is RV32IMAC. The code never says how wide the registers are: it is vector-length agnostic, and the same binary uses 128, 256 or 1024 bits. Tested on QEMU at 128, 256, 512 and 1024 bits by tools/tests/vector_qemu.S.

## Slide 7: A sum, lane by lane
la t0, numbers
li t1, 16 # sixteen words to add
vsetvli t2, zero, e32, m1, ta, ma
vmv.v.i v1, 0 # v1 = partial sums, one per lane
1: vsetvli t2, t1, e32, m1, tu, ma
vle32.v v2, (t0) # load t2 words
vadd.vv v1, v1, v2 # add them, lane by lane
slli t3, t2, 2
add t0, t0, t3
sub t1, t1, t2
bnez t1, 1b
vsetvli t2, zero, e32, m1, ta, ma
vmv.s.x v3, zero
vredsum.vs v3, v1, v3 # add the lanes together
vmv.x.s a0, v3
1
vle32.v loads several words at once
2
vadd.vv adds register to register, lane by lane
3
At the end vredsum adds the lanes together
4
Sixteen numbers, 1 to 16: the result is 136
UNDERSTAND NOW · vector instructions
Notes: A sum computed lane by lane. A vector register holds several words, each in its own lane. vle32.v loads several words at once; vadd.vv adds two registers lane by lane, so that v1 accumulates as many partial sums as there are lanes. At the end vredsum reduces the lanes to a single number. With the sixteen numbers from 1 to 16 the result is 136. This is the parallel sum shown pictorially in Lecture 04, now expressed in instructions. UNDERSTAND NOW: vector instructions. For the lecturer: The parallel sum of Lectures 04 and 20, in RISC-V. tu, tail undisturbed, keeps the partial sums of the lanes that the last turn does not use. Tested on QEMU together with the previous listing.

## Slide 8: The map of Verm1, one thread per cell
// the kernel: this function runs once in every thread
__global__ void clear(unsigned char *grid, int n) {
int i = blockIdx.x * blockDim.x + threadIdx.x; // who am I?
if (i < n)
grid[i] = 0; // my cell, and only mine
}
// on the host: 4 blocks of 256 threads cover the 960 cells
clear<<<(960 + 255) / 256, 256>>>(grid, 960);
1
There is no loop: there are 960 threads
2
Each thread computes its own index and does one store
3
Threads come in blocks; the last ones find nothing to do
4
For 960 bytes the copies cost far more than the work
UNDERSTAND NOW · GPU and FPGA accelerators
Notes: The map of Verm1 cleared on a GPU, in CUDA C. The function marked as a kernel executes once in every thread. Each thread first determines its identity, its index i, from its block number and its position within the block; then, if the index lies within the map, it clears its own cell. There is no loop: there are 960 threads. The last line, executed on the host, launches four blocks of 256 threads. For 960 bytes the two memory copies cost far more than the work, so the example illustrates the programming model, not a gain; a GPU pays off only when data are large and the work per element is substantial. UNDERSTAND NOW: GPU and FPGA accelerators. For the lecturer: CUDA C, in its usual textbook form; not compiled for these slides. The point of the last callout is serious: a GPU pays off when the data are large and the work per element is real. Ask: for which size of map would it be worth it?

## Slide 9: The U-turn rule of Verm1, as hardware
// Lecture 12: opposite directions differ in bit 1 only
module uturn (
input wire [1:0] dir, // direction of the last step
input wire [1:0] want, // direction asked by the player
output wire refuse // 1 = this would be a U-turn
);
assign refuse = (dir ^ want) == 2'b10;
endmodule
1
Verilog: a language that describes circuits, not steps
2
assign is a wire, always true: there is no before and after
3
Two XOR gates and an AND with one inverted input
4
On the kit this rule took three instructions and three cycles
UNDERSTAND NOW · GPU and FPGA accelerators
Notes: The rule of Verm1 forbidding the U-turn, written as hardware in Verilog, a language that describes circuits rather than sequences of steps. The module has two two-bit inputs, the current direction and the requested one, and one output. The assign statement denotes a wire that holds continuously: the output is 1 when the XOR of the two directions equals binary 10. There is no before and after, only a combinational relation. On the kit the same rule took three instructions and three cycles; as hardware it answers in a fraction of a nanosecond, continuously. UNDERSTAND NOW: GPU and FPGA accelerators. For the lecturer: A hardware description language: Verilog, or VHDL. Not synthesised for these slides. The xor, li, beq of Part 2 become gates that answer in a fraction of a nanosecond, continuously. Ask the students to draw the circuit: refuse = (d1 xor w1) and not (d0 xor w0).

## Slide 10: Emptying the map of Verm1: 960 cells
Machine | How | Steps in time
The kit: ESP32-C6 | one byte per turn, one instruction per cycle | 3 840 cycles
Out-of-order RISC-V core | the same binary; several instructions per cycle, the branch predicted | a fraction of those cycles
RISC-V with vectors, 128 bits | 16 bytes per turn | 60 turns
GPU | 960 threads, one per cell | one launch, plus two copies
FPGA | 960 flip-flops with a common reset | one clock cycle
The first three rows are the same instruction set. The first and the third were run for these slides.
UNDERSTAND NOW · GPU and FPGA accelerators
Notes: Clearing the 960 cells of the map on five machines. On the kit: one byte per iteration, 3,840 cycles. On an out-of-order RISC-V core: the same binary, in a fraction of those cycles. With 128-bit vectors: 60 iterations. On a GPU: one launch of 960 threads, plus two copies. On an FPGA: 960 flip-flops with a common reset, cleared in one clock cycle. The work is identical; what differs is how much of it occurs simultaneously, and at what cost. The engineer's question is not which machine is fastest, but which is sufficient. UNDERSTAND NOW: GPU and FPGA accelerators. For the lecturer: The work is the same; what changes is how much of it happens at the same time. And the costs: the first row needs a two-euro chip and four lines of assembly; the last needs a hardware design. The engineer's question is never which is fastest, but which is enough.

## Slide 11: The complete program: l24.S (1 of 4)
# ARC12 Computer Architecture - Lecture 24: Beyond One Core
# l24.S: the loop that empties the map of Verm1, one byte at a time
#
# On the screen: a green square: the 960 bytes of the map, filled with ones by init,
# were all set to zero by the four-instruction loop of the lecture. A red square would
# mean that some byte survived.
# Build: python3 -m prg32 cartridge build l24.S --portable \
# --entry-prefix l24 --name l24 --out l24.prg32
.option norelax
.equ BLACK, 0x0000
.equ GREEN, 0x07e0
.equ RED, 0xf800
.equ CELLS, 960 # 40 columns by 24 rows
.section .text
.global l24_init
.global l24_update
.global l24_draw
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l24.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 12: The complete program: l24.S (2 of 4)
l24_init: # fill the map with ones, so that there is work to do
la t0, grid
li t1, CELLS
li t2, 1
1: sb t2, 0(t0)
addi t0, t0, 1
addi t1, t1, -1
bnez t1, 1b
ret
l24_update:
la t0, grid # the loop of the lecture
li t1, CELLS
1: sb zero, 0(t0) # one byte ...
addi t0, t0, 1 # ... the next address ...
addi t1, t1, -1 # ... one fewer to go ...
bnez t1, 1b # ... 960 times: 3840 instructions
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l24.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 13: The complete program: l24.S (3 of 4)
la t0, grid # count the bytes that are not zero
li t1, CELLS
li t3, 0
2: lbu t2, 0(t0)
add t3, t3, t2
addi t0, t0, 1
addi t1, t1, -1
bnez t1, 2b
la t0, left
sw t3, 0(t0)
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l24.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 14: The complete program: l24.S (4 of 4)
l24_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, BLACK
call prg32_gfx_clear
la t0, left
lw t1, 0(t0)
li a4, GREEN
beqz t1, 1f
li a4, RED
1: li a0, 136
li a1, 76
li a2, 48
li a3, 48
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
.section .data
left: .word 1
grid: .space CELLS
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l24.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 15: Run it: what you should see
On the screen
– a green square: the 960 bytes of the map, filled with ones by init, were all set to zero by the four-instruction loop of the lecture. A red square would mean that some byte survived.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 16: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l24.S --portable \
--entry-prefix l24 --name l24 --out l24.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l24.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 17: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l24.S --portable \
--entry-prefix l24 --name l24 --architecture qemu \
--out l24-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l24-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 18: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l24.S --portable \
--entry-prefix l24 --name l24 --architecture esp32c6 \
--out l24-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l24-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 19: The vector listings: test them on upstream QEMU
# from ~/arc12/tools/tests, with the RISC-V compiler on the PATH
riscv32-esp-elf-gcc -march=rv32imv_zicsr -mabi=ilp32 -nostdlib \
-nostartfiles -T link.ld -o v.elf vector_qemu.S
# the same binary, with vector registers of four different widths
for n in 128 256 512 1024; do
qemu-system-riscv32 -machine virt -cpu rv32,v=true,vlen=$n \
-bios none -kernel v.elf -nographic -display none
echo "vlen=$n: exit code $?"
done
1
The kit has no vector extension: these listings run on a bare emulated RV32 with V
2
Exit code 0: every check passed; any other value is the number of the failing check
3
The same binary passes with registers of 128, 256, 512 and 1024 bits
4
Use upstream QEMU here, not the Espressif fork
USE NOW · the PRG32 tools
Notes: The vector listings of this lecture cannot run on the kit, whose processor does not implement the V extension. They are therefore tested on a bare emulated RV32 processor: the commands build a single binary and execute it with four different vector lengths. The exit code is the result, zero meaning that every check passed, which also demonstrates that the code is independent of the vector length. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests (tools/tests/run_all.sh, step vectors). On macOS there is no timeout command: if a listing loops for ever, stop QEMU with Ctrl-A X.

## Slide 20: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l24; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 21: Exercises: paper first, then the machine
TRY IT
1
Fill in the Amdahl table for p = 0.95 and n = 10, 100, 1000
2
Draw the pipeline diagram of a three-wide processor for nine independent instructions with five stages
3
Rename the registers of the step-wrap code of Verm1, Part 2: which instructions could run in the same cycle?
4
Write the truth table stored in a four-input look-up table for refuse = (dir xor want) == 2
5
Build tools/tests/vector_qemu.S and run it on QEMU with vlen=128 and vlen=512: why does the same binary work?
Expected result
Amdahl, p = 0.95: 6.9, 16.8, 19.6. Nine instructions, three-wide: seven cycles. The look-up table has four ones out of sixteen entries.
Notes: Five exercises. Complete the Amdahl table for p = 0.95. Draw the pipeline diagram of a three-wide processor executing nine independent instructions. Rename the registers of a fragment of Verm1 and identify which instructions could execute in the same cycle. Write the truth table of a four-input look-up table implementing the U-turn rule. And build the vector test and run it on QEMU with two different vector widths, explaining why the same binary works in both cases. For the lecturer: QEMU: qemu-system-riscv32 -machine virt -cpu rv32,v=true,vlen=128; the build command is in tools/tests/README.md. The four ones of the table: (dir, want) = (0,2), (1,3), (2,0), (3,1).