## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 02
First Contact: RISC-V Assembly on PRG32
Registers, memory and the call: a running program before any theory
“Talk is cheap. Show me the code.”
Linus Torvalds, Linux kernel mailing list, 2000
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Notes: This is the first lecture in which you write a program, and it comes before any theory on purpose. In two hours you build four small cartridges, each a complete program that runs. You will not understand every detail today, and you are not expected to: the aim is to see registers, memory and a function call at work, so that the lectures that follow have something concrete to explain. The quotation sets the tone: less talk, more code. For the lecturer: New lecture for 2026/27. It is the 'play' turn of the spiral for the whole first half of the course: every later lecture points back to something typed here. The four steps are the verified steps of the textbook lab 05-asm-first-contact; run them live (labs/run.sh 05-asm-first-contact/stepN_....S first).

## Slide 2: What you will be able to do by the end
1
Build a cartridge from an assembly file and run it on PRG32
2
Say what a register is, and name the ones you will use every day
3
Call a framework function, passing arguments in registers
4
Keep a value in memory from one frame to the next: load, modify, store
5
Read one instruction as the 32-bit number it really is
6
List the questions this program raises: the rest of the course answers them
Notes: Six things you will be able to do at the end. The first four are practical: build and run a cartridge, name the registers, call a function with its arguments, keep a value in memory between frames. The fifth is a change of point of view: an instruction is a 32-bit number. The sixth is the most important for the course: you will leave with a list of questions, and each of them is the subject of a later lecture. For the lecturer: Tell the students explicitly that they are not expected to understand everything today. Today is for seeing; the next lectures are for explaining.

## Slide 3
01
The machine
Thirty-two registers and a small repertoire of instructions.
Notes: Before typing, a look at the machine. A RISC-V processor is described by two things only: a set of registers and a repertoire of instructions. The next three slides present both, and the contract between your program and PRG32.

## Slide 4: The machine you are programming
1
32 registers
Each register holds one 32-bit value. The processor can compute only on values that are in registers.
2
Compute
An arithmetic or logic operation between registers: add, sub, and, or, xor, and their immediate forms such as addi.
3
Move
A transfer between a register and memory: lw loads a word, sw stores a word. Nothing else touches memory.
4
Jump
A change in which instruction runs next: branches such as beqz, calls and returns.
Notes: The whole machine in four cards. There are 32 registers, each holding one 32-bit value, and the processor can compute only on what is in them. There are three kinds of instruction. Compute: arithmetic and logic between registers, such as add or addi. Move: transfers between a register and memory, lw to load a word and sw to store one; nothing else touches memory. Jump: changes of the instruction that runs next. Everything a computer does is a long sequence of these three kinds. For the lecturer: That is very nearly the whole machine. The richness of computing comes not from a large instruction set but from combining a small one in long sequences.

## Slide 5: The registers you will actually use
Register | Name | Role | Preserved across a call?
a0 - a7 | arguments | values passed into a call; a0 also carries the return value | no
t0 - t6 | temporaries | scratch values | no
s0 - s11 | saved | values a call promises to preserve | yes
ra | return address | where ret jumps back to | no: save it yourself
sp | stack pointer | top of the stack, kept 16-byte aligned | yes
zero | zero | always reads as 0; writes are ignored | -
The roles come from an agreement, the calling convention (ABI), not from the hardware.
Notes: The registers have names that say how they are used. a0 to a7 carry the arguments of a call, and a0 carries the result back. t0 to t6 are temporaries, free to use and not preserved by a call. s0 to s11 are preserved. ra holds the return address, sp the top of the stack, and zero always reads as 0. Read the caption carefully: these roles are not built into the hardware. They are an agreement, the calling convention, and it is what lets your assembly and the C code of the framework call each other. For the lecturer: The roles are fixed not by the hardware but by an agreement: the calling convention, or ABI. Following it is what lets your assembly and the framework's C code call each other.

## Slide 6: The contract: three functions that you write
init
called once, when the cartridge starts: set up your state
update
called once per frame: read input, change the state
draw
called once per frame: turn the state into a picture
The firmware finds the three functions by name: a prefix that you choose, followed by _init, _update and _draw. That is the whole contract between your game and the machine.
Notes: The contract with PRG32 is three functions that you write. init is called once, when the cartridge starts, to set up the state. update is called once per frame, to read the input and change the state. draw is called once per frame, to turn the state into a picture. The firmware finds them by name: a prefix chosen by you, followed by _init, _update and _draw. Keep the division of labour in mind from the first day: update decides, draw shows.

## Slide 7
02
Your first cartridge
Four small steps, each one a complete program that runs.
Notes: Now the practice: four steps, each a complete program. Type them yourself; do not copy and paste. Typing forces you to read every character, and the mistakes you make while typing are the cheapest lessons of the course.

## Slide 8: Step 1: the smallest program that runs
# Assembly Lab 1: the smallest program that runs
.option norelax
.section .text
.global first_init
.global first_update
.global first_draw
first_init:
ret
first_update:
ret
first_draw:
ret
1
.option norelax keeps the layout of the cartridge predictable: every PRG32 example starts with it
2
.section .text says that what follows is executable code
3
.global makes a label visible to the firmware, which finds your functions by name
4
ret returns to the caller: three functions that do nothing, correctly
Notes: The smallest program that runs. .option norelax is a line with which every PRG32 example starts: it keeps the layout of the cartridge predictable. .section .text says that code follows. Each .global makes a label visible outside the file, so that the firmware can find the function by name. Then three functions, each made of the single instruction ret, which returns to the caller. The result is a black screen, and it is a success: the framework found your three functions, called them, and got control back. For the lecturer: Source: labs/05-asm-first-contact/step1_skeleton.S. Expected result: a black screen. The achievement is that the framework found the three functions, called them, and survived.

## Slide 9: Build it, run it
# 1. build a portable cartridge from one assembly file
python3 -m prg32 cartridge build step1_skeleton.S --portable \
--entry-prefix first --name step1 --out build/step1.prg32
# 2a. run it in QEMU on your laptop
python3 -m prg32 qemu upload build/step1.prg32
python3 -m prg32 qemu run
# 2b. or send it to a board, or to PRG32-QT, over the network
python3 -m prg32 esp32c6 upload-and-run build/step1.prg32 \
--url http://192.168.4.1 --slot cart0
Notes: Two commands that you will type hundreds of times. cartridge build turns the assembly file into a cartridge: --entry-prefix first is the prefix of your three functions, --out the name of the result. Then you run it: in QEMU with qemu upload and qemu run, or on a board or PRG32-QT with upload-and-run and the address of the host. For PRG32-QT on your own laptop the address is http://localhost:8080. The cartridge file is the same for all three. For the lecturer: Source: labs/run.sh. With PRG32_HOME set, the whole sequence is: labs/run.sh 05-asm-first-contact/step1_skeleton.S first . The cartridge file is byte-for-byte the same for QEMU, the board and PRG32-QT.

## Slide 10: Step 2: say hello
first_draw:
addi sp, sp, -16 # prologue: a 16-byte frame
sw ra, 12(sp) # save the return address
li a0, BLACK
call prg32_gfx_clear
li a0, 32 # x
li a1, 40 # y
la a2, title # address of the string
li a3, WHITE # foreground
li a4, BLACK # background
call prg32_gfx_text8
lw ra, 12(sp) # epilogue: restore ra
addi sp, sp, 16 # release the frame
ret
.section .rodata
title:
.asciz "HELLO PRG32"
Screenshot: this step, built and run on PRG32
The first argument goes in a0, the second in a1, and so on. li loads a number; la loads the address of a label.
Notes: The second step writes on the screen. Read first_draw in three parts. The first two lines make room on the stack and save ra. Then two calls: prg32_gfx_clear with the colour in a0, and prg32_gfx_text8 with five arguments in a0 to a4: x, y, the address of the string, foreground, background. Note the two ways of loading: li loads a number, la loads the address of a label. The last three lines restore ra, release the stack and return. The string itself is data, in the section .rodata. For the lecturer: Source: labs/05-asm-first-contact/step2_hello.S. The .equ lines (BLACK 0x0000, WHITE 0xffff) are omitted on the slide.

## Slide 11: Why save ra? The stack frame
call stores the address to come back to in ra
The function you call will use ra for its own calls, overwriting yours
So a function that calls another one saves ra first
– lower sp by 16 to make room
– store ra at 12(sp)
After the call, undo it in reverse order
– load ra back, raise sp by 16, then ret
Forgetting the pair is the classic first bug: the function returns to the wrong place
Stack memory after the prologue
caller's data
16(sp)
ra
12(sp)
free
8(sp)
free
4(sp)
free
0(sp)
sp
higher addresses
The stack grows downward: subtract from sp to allocate, add to release.
Notes: Why save ra? The instruction call writes into ra the address to return to. But the function you call may make calls of its own, and each of them overwrites ra. So a function that calls another must first save its own ra in memory: it lowers sp by 16 to make room, the stack frame, and stores ra at 12(sp). After the call it does the reverse. The drawing shows the frame: the stack grows towards lower addresses. Forgetting this pair of operations is the classic first bug: the function returns to the wrong place. For the lecturer: The convention requires sp to stay 16-byte aligned across calls, which is why the frame is 16 bytes even though only 4 are used. The stack is treated formally in the lectures on memory and on subroutines.

## Slide 12: Step 3: a value that survives between frames
first_update:
# A leaf function: it calls nothing,
# so it needs no stack frame.
la t0, counter # t0 = ADDRESS of counter
lw t1, 0(t0) # t1 = VALUE stored there (load)
addi t1, t1, 1 # one tick per frame (modify)
sw t1, 0(t0) # write it back (store)
ret
.section .data
counter: .word 0
1
counter is a label: it names a location in memory, in the .data section, holding one 32-bit word
2
la puts the ADDRESS of that location in t0
3
lw reads the VALUE at that address into t1; sw writes it back
4
The processor computes only in registers: load, modify, store
Notes: The third step keeps a value from one frame to the next. Registers do not survive between calls of update, so the value must live in memory. counter is a label: it names a location in the section .data that holds one word. The four instructions are the pattern of every variable: la puts the address of the location in t0; lw loads the value into t1; addi changes it; sw stores it back. Load, modify, store. Nothing changes on the screen yet: the counter ticks, but nobody draws it. For the lecturer: Source: labs/05-asm-first-contact/step3_counter.S. Nothing visible changes yet: the counter ticks but nobody draws it. Ask the class how they could prove that it is ticking (answer: the debugger of PRG32-QT, or the next step).

## Slide 13: Address or value? The crux of memory
Registers (inside the processor)
t0
address of counter
t1
41 then 42
Memory (.data section)
...
counter: 41
...
t0 points here
lw copies the contents
la t0, counter # t0 = WHERE the value lives
lw t1, 0(t0) # t1 = WHAT is stored there
addi t1, t1, 1 # change the copy in the register
sw t1, 0(t0) # memory still says 41 until this line
Using an address where a value belongs, or the reverse, is one of the most common beginner errors. Comment every register: ADDRESS or VALUE.
Notes: This slide separates two ideas that beginners confuse: the address and the value. After la, t0 contains where the counter lives. After lw, t1 contains what is stored there, 41 in the drawing. addi changes the copy in the register to 42, and memory still says 41 until sw writes it back. Follow the two arrows. A practical habit from the box on the right: in your comments, write for every register whether it holds an ADDRESS or a VALUE. It prevents the most common error of the first month. For the lecturer: A label names a location. la gives the location, lw gives the contents. This is how every variable in every program ultimately works; we return to it formally with addressing modes.

## Slide 14: Step 4: make the counter visible
la t0, counter
lw t1, 0(t0)
andi a2, t1, 255 # width = counter modulo 256
li a0, 32 # x
li a1, 60 # y
li a3, 8 # height
li a4, GREEN # .equ GREEN, 0x07e0
call prg32_gfx_rect
Screenshot: this step, built and run on PRG32
The bar grows from 0 to 255 pixels, then starts again. andi with 255 keeps only the low eight bits of the counter.
Notes: The fourth step makes the counter visible as a green bar. The value is loaded, and andi a2, t1, 255 keeps only its low eight bits, so the width goes from 0 to 255 and then starts again. The other registers are the arguments of prg32_gfx_rect: x, y, width, height and colour. Eight lines, and three later lectures are hidden in them: 255 written as 0xFF, andi used as a mask, and 0x07e0 that means green. Remember where you first saw them. For the lecturer: Source: labs/05-asm-first-contact/step4_bar.S (the lines added to first_draw). Three future lectures hide in these eight lines: 255 = 0xFF (positional notation), andi as a bit mask (Boolean algebra), 0x07e0 as a colour (information encoding).

## Slide 15
03
Reading what you wrote
The same program, seen as the processor sees it.
Notes: You have written a program; now read it as the processor does. The next slides classify the instructions you used, show which of them are shortcuts, open one instruction to look at its bits, and trace the program by hand.

## Slide 16: The instructions you have just used
Family | Instruction | What it does | Example
Arithmetic | add, sub | combine two registers | add t0, t1, t2
Logic | and, or, xor | bitwise operation on two registers | and t0, t1, t2
Immediate | addi, andi, ori, xori | one register and one small constant | addi t1, t1, 1
Memory | lw, sw | load or store a 32-bit word | lw t1, 0(t0)
Control | call, ret | go to a function and come back | call prg32_gfx_rect
Notes: Five families cover everything you have typed: arithmetic (add, sub), logic (and, or, xor), the immediate forms that take a small constant (addi, andi), memory (lw, sw) and control (call, ret). In every instruction the result goes in the first register named: add t0, t1, t2 puts t1 + t2 in t0. The base instruction set has about forty instructions, and you have already met a quarter of them. For the lecturer: The result goes in the first register. The base RISC-V integer instruction set (RV32I) has about forty instructions; you have already met a quarter of them.

## Slide 17: Pseudo-instructions: shortcuts the assembler expands
You write | The assembler emits | Meaning
li t0, 42 | addi t0, zero, 42 | load a constant
mv t0, t1 | addi t0, t1, 0 | copy a register
not t0, t1 | xori t0, t1, -1 | bitwise complement
la t0, counter | auipc t0, ... + addi t0, t0, ... | load the address of a label
ret | jalr zero, 0(ra) | jump to the address in ra
beqz t0, skip | beq t0, zero, skip | branch if t0 is zero
Notes: Some of the instructions you wrote do not exist in the processor: they are pseudo-instructions, shortcuts that the assembler expands. li t0, 42 becomes addi t0, zero, 42; mv is an addi with 0; ret is a jump to the address in ra; beqz is a comparison with the register zero. Notice how often zero appears in the middle column: a register that is always 0 lets a small instruction set do the work of a larger one. For the lecturer: A pseudo-instruction is not a separate hardware operation. The register zero is what makes many of them possible: a small instruction set, reused with care.

## Slide 18: One instruction is one 32-bit number
addi t1, t1, 1
000000000001
immediate
the constant 1
31
20
00110
rs1
t1 is x6
19
15
000
funct3
add
14
12
00110
rd
t1 is x6
11
7
0010011
opcode
register-immediate
6
0
0x00130313
Assembly is a readable spelling of machine code. The assembler translates each line into one 32-bit word; the processor reads the fields with logic circuits that we will design ourselves later in the course.
Notes: An instruction is a number. addi t1, t1, 1 is the 32-bit word 0x00130313, and the coloured strip shows its fields: twelve bits for the constant 1, five for the source register (t1 is register number 6), three that say "add", five for the destination, seven for the kind of instruction. You do not need to learn the format now. Keep the idea: assembly is a readable spelling of machine code, and the processor reads these fields with circuits that you will learn to design. For the lecturer: Check: 0000 0000 0001 | 00110 | 000 | 00110 | 0010011 = 0000 0000 0001 0011 0000 0011 0001 0011 = 0x00130313. Do not explain the formats now; the point is only that an instruction is data. Lecture 04 (digital information) and the lectures on the processor come back to this slide.

## Slide 19: PRG32-QT: a microscope for registers
Runs the same cartridge on your desktop, one instruction at a time
Stops between any two instructions and shows every register
Step through first_update and watch t0 and t1 change
Use the board when you want the truth about time, PRG32-QT when you want the truth about a register
The PRG32-QT debugger: source, registers, memory
Notes: PRG32-QT runs the same cartridge on your laptop and can stop between any two instructions, showing every register. Use it now on the third step: go to update, pause, and execute the four instructions of first_update one at a time, watching t0 and t1. Before each press, say aloud what will change. The last line is a rule to remember: the board tells the truth about time, PRG32-QT tells the truth about a register. For the lecturer: Demonstrate live: load step 3, break at first_update, single-step four times. Ask the students to predict each register before pressing the key.

## Slide 20: Trace it by hand: three frames of first_update
Frame | lw: t1 becomes | addi: t1 becomes | sw: counter becomes | Bar width (andi 255)
1 | 0 | 1 | 1 | 1
2 | 1 | 2 | 2 | 2
256 | 255 | 256 | 256 | 0
257 | 256 | 257 | 257 | 1
At frame 256 the counter keeps growing, but its low eight bits return to zero: the bar starts again.
Notes: A trace by hand: for each frame, write what each instruction leaves in t1 and in memory. In the first frames nothing surprising happens. Look at the highlighted row: at frame 256 the counter becomes 256, yet the width of the bar is 0, because andi with 255 keeps only the low eight bits, and 256 in binary is a one followed by eight zeros. Tracing by hand is slow and unglamorous, and it is the most useful debugging skill you will learn in this course. For the lecturer: The by-hand trace is the most valuable debugging skill of the course. 256 = 1 0000 0000 in binary: the low eight bits are all zero, so the bar restarts.

## Slide 21
04
What comes next
Every question raised here has a lecture that answers it.
Notes: The lecture ends by looking forward. What you typed has raised questions, and the next slide lists them with the lecture that answers each.

## Slide 22: Questions your program has already raised
You saw | The question | Answered in
0x07e0, 0xffff, 255 | Why do programmers write numbers in hexadecimal? | Lectures 04 and 05
a position below zero shown as 0xFFFFFFFF | How does a register hold a negative number? | Lecture 05
a ball that moves less than a pixel per frame | How do we represent fractions without an FPU? | Lecture 06
andi a2, t1, 255 | What does AND do to thirty-two bits at once? | Lectures 08 and 09
addi t1, t1, 1 | Which circuit actually adds two numbers? | Lecture 09: the adders
a pressed button is a 1 | What is a bit made of, physically? | Lecture 10
counter survives between frames | How does a circuit remember a bit? | Lectures 13 and 15
0x00130313 | How does the processor decode and execute it? | Lectures 18 and 19
three functions and a rectangle | Can I make a whole game out of this? | Verm1: 07, 12, 17, 22
Notes: Each row is something you saw today, the question it raises and where the answer is. Why hexadecimal? Lectures 04 and 05. How does a register hold a negative number? Lecture 05. What does AND do to thirty-two bits at once? Lectures 08 and 09. How does a circuit remember a bit? Lectures 13 and 15. How is 0x00130313 decoded and executed? Lectures 18 and 19. The last row is the project: from three functions and a rectangle, a whole game. Keep this table: it is the map of the course seen from your own program. For the lecturer: This is the forward map of the course. Keep a copy: each later deck opens by pointing at one of these rows. The last row is the project: Verm1 starts in Lecture 07 from exactly the skeleton of today.

## Slide 23: Check your understanding
After la t0, counter and lw t1, 0(t0), what does t0 hold?
A
The value of the counter
B
The address of the counter
C
Zero, because la clears the register
D
The return address
Notes: Apply the distinction between address and value. la loads the address of the label into t0; lw then uses t0 to find the location and copies its content into t1, without changing t0. So t0 still holds the address. If you chose "the value", go back to the slide with the two arrows. For the lecturer: Answer: B. la loads the address of the label; lw then reads the value stored at that address into t1.

## Slide 24: Check your understanding
A function that calls prg32_gfx_clear must save one register before the call. Which one?
A
a0, because it carries the argument
B
sp, because the stack moves
C
ra, because call overwrites it
D
t0, because it is temporary
Notes: The key is what call does: it writes the return address into ra. If your function has to return to its own caller afterwards, it needs the old ra, which the call has just overwritten. a0 is meant to be overwritten, sp is restored by the callee, and t0 is a temporary that nobody promised to keep. For the lecturer: Answer: C. call writes the return address in ra. The callee's own calls would overwrite it, so a non-leaf function saves ra on the stack and restores it before ret.

## Slide 25: Check your understanding
t1 holds 300. What does andi a2, t1, 255 leave in a2?
A
300
B
255
C
45
D
44
Notes: Do the calculation in binary. 300 is 256 + 44, that is a one in position 8 followed by the eight bits of 44. The mask 255 is eight ones: AND keeps the low eight bits and clears the rest. What remains is 44. Subtracting 255 from 300 gives 45, a tempting wrong answer: AND is not a subtraction. For the lecturer: Answer: D. 300 = 256 + 44 = 1 0010 1100 in binary. AND with 1111 1111 keeps the low eight bits: 0010 1100 = 44.

## Slide 26: Exercises on PRG32
TRY IT
1
Change the title string and its colour to yellow (0xffe0); run it again
2
Make the bar grow twice as fast, then four times as fast, changing one instruction only
3
Make the bar shrink instead of grow. What happens when the counter passes zero?
4
In PRG32-QT, single-step first_update and write down t0 and t1 after each instruction
5
Draw a second bar, in red, whose width is the counter modulo 64
Expected result
For exercise 3 the counter goes 0, then 0xFFFFFFFF: with andi 255 the bar jumps to 255 and shrinks. Keep the observation: Lecture 05 explains it.
Notes: Five exercises on your own cartridge; each is the seed of a later lecture. Change the text and its colour. Make the bar grow two or four times as fast by changing one instruction. Make it shrink, and observe what happens when the counter passes zero: the bar jumps to its full width, and Lecture 05 will explain why. Single-step first_update and write down the registers. Draw a second bar whose width is the counter modulo 64. Predict first, then run. For the lecturer: Hints: addi t1, t1, 2 or slli before andi for exercise 2; addi t1, t1, -1 for exercise 3; andi a2, t1, 63 for exercise 5. Each exercise is a seed for a later lecture.

## Slide 27: Glossary: English and Italian
English | Italiano | English | Italiano
register | registro | stack | pila (stack)
load / store | caricare / memorizzare | stack pointer | puntatore alla pila
address | indirizzo | return address | indirizzo di ritorno
immediate | immediato (costante) | calling convention | convenzione di chiamata
branch | salto condizionato | machine code | codice macchina
label | etichetta | cartridge | cartuccia
Notes: Twelve terms of this lecture, with the Italian used in class. Load and store are always seen from the processor: load brings a value from memory into a register, store sends it back. An immediate is a constant written inside the instruction itself. A branch is a jump that is taken only if a condition holds. The calling convention is the agreement on the roles of the registers. For the lecturer: The course is taught in Italian; slides, notes and textbook exist in English and in Italian, and the technical documentation of PRG32 is in English. This table is repeated, topic by topic, in every deck.

## Slide 28: Summary and reading
A RISC-V processor is thirty-two registers and a small set of instructions that compute, move and jump
A PRG32 game is three functions; arguments travel in a0 to a7; a function that calls another saves ra
Variables live in memory: la for the address, lw and sw for the value
An instruction is a 32-bit number; assembly is its readable spelling
Reading
– Playing with RISC-V, chapter 5: First Contact
– Patterson, Hennessy: Computer Organization and Design, RISC-V Edition, chapter 2
– PRG32 repository: docs/learn/tutorial_ascii_game.md
Notes: Four sentences contain the lecture. A RISC-V processor is thirty-two registers and a small set of instructions that compute, move and jump. A PRG32 game is three functions, with arguments in a0 to a7, and a function that calls another saves ra. Variables live in memory: la for the address, lw and sw for the value. An instruction is a 32-bit number, and assembly is its readable spelling. The next lecture steps back and tells the history that led to this machine. For the lecturer: Next lecture: the history that led to this machine.