## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 14
Elementary Machines: Registers and Buses
Word gates, registers, buses, three-state buffers, serial and parallel transfers
“Roads? Where we're going, we don't need roads.”
Dr. Emmett Brown, Back to the Future, Robert Zemeckis, 1985
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Notes: The previous lecture built a register out of flip-flops. This one asks how registers talk to each other: how a word goes from one to another, along which wires, and what happens when many registers share the same wires. The answers are the bus, the three-state buffer and the shift register. Doc Brown's line on the cover is ironic here: data do need roads, and a bus is exactly that. The warm-up starts from a fact about the kit: its display receives every pixel one bit at a time. For the lecturer: Spiral: the display of the PRG32 kit receives every pixel one bit at a time; the warm-up sends a byte serially in assembly, and the lecture builds the machines that do it in hardware.

## Slide 2: What you will be able to do by the end
1
Describe a register as a set of flip-flops with a common clock, and explain its load signal
2
Explain what a bus is, and compare dedicated buses with a common bus
3
Say why a common bus needs three-state buffers, and what high impedance means
4
Describe a shift register and its four combinations of serial and parallel input and output
5
Convert a datum from parallel to serial and back, in hardware and in RISC-V assembly
Notes: Five objectives. Describe a register as a set of flip-flops with a common clock and a load signal. Explain what a bus is and compare dedicated buses with a common bus. Say why a common bus needs three-state buffers and what high impedance means. Describe a shift register and its four combinations of serial and parallel input and output. And convert a datum from parallel to serial and back, in hardware and in assembly.

## Slide 3
01
Warm-up on the machine
One wire, eight bits.
Notes: The warm-up asks how to send eight bits along a single wire. Before reading the code, think of how you would dictate a number to someone over the phone, one digit at a time.

## Slide 4: Send a byte one bit at a time
# a0 = the byte to send, most significant bit first
li t0, 8 # eight bits to go
1: srli t1, a0, 7 # bring bit 7 down to bit 0
andi t1, t1, 1 # t1 = the bit to put on the wire
... # drive the data line with t1,
... # then pulse the clock line
slli a0, a0, 1 # shift left: the next bit moves up
addi t0, t0, -1
bnez t0, 1b
1
The display and the sound chip of the kit are connected by a few wires, not by thirty-two
2
A word must therefore travel one bit after another: a serial transfer
3
The loop is a shift register in software: shift, take one bit, repeat
4
The ESP32-C6 has hardware that does exactly this, millions of times per second
Notes: The loop sends a byte one bit at a time, most significant bit first. At each turn the byte is shifted right by 7 and masked with 1, which isolates its top bit; that bit would be put on a data line and a clock line pulsed; then the byte is shifted left by one, so that the next bit moves into the top position. After eight turns the whole byte has gone. The loop is a shift register in software. The chip of the kit contains hardware that does the same thing, millions of times per second. For the lecturer: Written for this lecture. On the kit the display uses SPI and the amplifier I2S: both are serial buses driven by shift registers inside the chip. The two elided lines would write to memory-mapped GPIO registers (Lecture 15).

## Slide 5
02
Word gates and registers
From one bit to a whole word.
Notes: First the building blocks at the scale of a word: the word gate, which acts on all the bits together, and the register.

## Slide 6: Word gates
A word is a vector V of n bits: V = (v0, v1, ..., v(n-1))
A word gate acts on all the bits of a word at once
With a control signal a, the word gate computes a AND v(i) for every i
– a = 1: the word passes unchanged; a = 0: every bit is forced to 0
It is n identical gates sharing one control input
The bitwise instructions and, or, xor of RISC-V are word gates thirty-two bits wide
n gates
one gate per bit, one control signal for all: the building block of every datapath
Notes: A word is a vector of n bits. A word gate is n identical gates that share one control input: with the control at 1 the word passes unchanged, with the control at 0 every bit is forced to 0. It is the natural extension of a gate from one bit to a word. The bitwise instructions of RISC-V are word gates thirty-two bits wide, and the multiplexer on words of Lecture 11 is built from them. For the lecturer: Porte di parola. The multiplexer on words of Lecture 11 is built from word gates.

## Slide 7: The register
A register is a device able to store a group of bits
In its simplest form: a group of flip-flops and a common synchronisation signal, a clock or an enable
Example: the 74273, an 8-bit register in one chip
– eight D flip-flops; one clock and one clear; inputs D0 to D7, outputs Q0 to Q7
Loading a register: the datum on its inputs is stored when the load signal is active, typically in step with the clock
In RISC-V each of the registers x1 to x31 is thirty-two such flip-flops
SN74LS273: eight D flip-flops with a common clock
Notes: A register stores a group of bits: in its simplest form it is a group of flip-flops with a common clock. The classic example in one chip is the 74273, with eight D flip-flops, one clock and one clear. Loading a register means storing the datum present on its inputs, and it happens when the load signal is active, normally in step with the clock. Each of the registers x1 to x31 of RISC-V is thirty-two such flip-flops. For the lecturer: Datasheet: ti.com/lit/ds/symlink/sn74ls273.pdf. The 7474 holds two D flip-flops with preset and clear. See Lecture 13 for the flip-flop itself.

## Slide 8
03
Buses
How data travel between registers.
Notes: A register by itself is of little use: its content must come from somewhere and go somewhere. The transfer between registers is the fundamental operation of a computer, and the paths along which it happens are the buses.

## Slide 9: Data transfers and the bus
Bus
A communication channel that lets the components of an electronic system exchange data by transmitting and receiving signals: the set of lines that carries a datum.
The transfer from a register X to a register Y is the fundamental operation of a computer's architecture
The name is a contraction of the Latin omnibus: for all
A bus of n lines carries a word of n bits in one step
Notes: A bus is the set of lines that carries a datum between the components of a system. The word comes from the Latin omnibus, "for all". A bus of n lines carries a word of n bits in one step. The transfer from a register X to a register Y is the elementary action from which everything else is built: almost every instruction you have written is, underneath, a short sequence of register transfers. For the lecturer: Almost every instruction of Lecture 02 is, at bottom, a sequence of register transfers.

## Slide 10: Two technical solutions
Dedicated buses
One set of lines for each possible transfer
Several transfers can happen at the same time
Efficient but expensive: the wires grow with the square of the number of registers
Common bus
A single path collects many potential transfers
Each time, one source and one destination are chosen
A transfer takes two steps: source to bus, bus to destination
Cheap and widespread; less efficient, because transfers cannot be simultaneous
Notes: Two ways of connecting registers. With dedicated buses each possible transfer has its own lines: several transfers can happen at once, but the wires grow with the square of the number of registers. With a common bus one path serves all the transfers: each time one source and one destination are chosen, and a transfer takes two steps, from the source to the bus and from the bus to the destination. It is cheap and widespread, at the price of doing one transfer at a time. For the lecturer: Intermediate solutions exist: several buses, each shared by a group of registers. Real processors use them.

## Slide 11: Parallel, serial and mixed transfers
Parallel: the n bits of the word travel together on n lines, in one step
Serial: the bits travel one after another on a single line, in n steps
Mixed: for example, serial on the byte: eight lines carry one byte at a time
Accessing a bus means reading from it or writing to it; buses come in very different physical sizes
Inside a chip buses are parallel; between chips and between machines they are today almost always serial
Bus lines on a printed circuit board
Notes: A transfer can be parallel, with the n bits travelling together on n lines in one step, or serial, with the bits travelling one after another on a single line in n steps, or a mixture, for example one byte at a time. Remember the last line: inside a chip buses are parallel; between chips and between machines they are today almost always serial, because at very high speed it is easier to keep one line clean than thirty-two lines in step. For the lecturer: USB, SATA, PCI Express, HDMI and Ethernet are all serial: at very high speeds it is easier to keep one fast line clean than to keep thirty-two lines in step.

## Slide 12: From bus to register, and from register to bus
bus A
register R
load c
From bus to register: the datum is loaded into R when the load signal c is active (a strobe, usually in step with the clock).
bus A
register R
buffer
enable c
From register to bus: the outputs of R reach the bus only while the enable signal c is active. What happens to the bus when it is not?
Notes: The two halves of a transfer on a common bus. On the left, from the bus to a register: the datum on the bus is loaded into R when the load signal is active. On the right, from a register to the bus: the outputs of R reach the bus through a buffer, and only while the enable signal is active. The question at the bottom leads to the next section: when the enable is not active, what must the output of the buffer be, so as not to disturb the bus? For the lecturer: Trasferimento dati su bus unico: caricamento di un registro (da bus a registro) and trasferimento da registro a bus.

## Slide 13
04
Three-state buffers
Sharing one wire without short circuits.
Notes: If several registers are connected to the same wire, all but one must stay out of the way. An ordinary gate cannot do it: its output is always either 0 or 1. A third possibility is needed.

## Slide 14: The three-state gate
If two registers drove the same wire, one with 0 and one with 1, the result would be a short circuit
A three-state output has a third condition besides 0 and 1: high impedance, written z
In high impedance the output is electrically disconnected: it neither drives nor loads the wire
An enable signal a decides: a = 1 the gate works normally, a = 0 the output is z
It is the most widespread technique for connecting several source registers to a common bus
a | x | y | output
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
0 | any | any | z
A three-state AND with an active-high enable: with a = 1 it is an ordinary AND; with a = 0 its output floats.
Notes: A three-state output has a third condition besides 0 and 1: high impedance, written z, in which the output is electrically disconnected from the wire. An enable input decides: when it is 1 the gate works normally, when it is 0 the output is z. The table shows it for an AND with enable: four rows of an ordinary AND, and a last row in which the output floats whatever the inputs. Electrically, both transistors of the output stage are switched off. For the lecturer: AND tristate; segnale di abilitazione in logica 1-attiva. Electrically, both output transistors are switched off.

## Slide 15: Enabling a bus
A three-state word gate between an enable signal a and a bus X gives a bus Y
Y reproduces X if a is active; otherwise all its lines are at high impedance: Y takes the neutral value
We say that Y is sustained by a three-state buffer
The GPIO pins of the ESP32-C6 work this way: each pin can be an output, or be released and used as an input
0, 1, z
three states: low, high and disconnected
Notes: Applied to a whole word, a three-state gate lets a bus through or disconnects it: when the enable is active the output bus reproduces the input bus; otherwise all its lines are at high impedance. The pins of the chip of the kit work in this way: each can be configured as an output, which drives the wire, or released and used as an input. The joystick pins are inputs; the display pins are outputs. For the lecturer: Tristate di parola. On the kit, the joystick pins are configured as inputs (their output buffers in high impedance) and the display pins as outputs.

## Slide 16: Connecting buses: the bus OR
register A
3-state
enable α
register B
3-state
enable β
register X
3-state
enable ξ
common bus Y
destination
registers
Several source registers are connected to one bus simply by joining their outputs, each through a three-state buffer
The condition: of the n sources that flow into the bus, at most one is enabled at a time. One active signal, the other n - 1 neutral
On the destination side, every register is connected to the bus and only the one whose load signal is active takes the datum
Choosing the source and the destination is the job of decoders, driven by the control unit
Notes: The complete scheme of a common bus. Each source register reaches the bus through a three-state buffer with its own enable. The rule is strict: at most one enable is active at a time, so that one source drives the bus and all the others are disconnected. On the other side every destination register is connected to the bus, and only the one whose load signal is active takes the datum. Choosing the source and the destination is the job of decoders driven by the control unit. For the lecturer: Collegamento di bus: OR di bus; trasferimento verso registri-destinazione. Inside modern chips long shared lines are usually replaced by multiplexers, which do the same selection without high-impedance states; between chips, three-state buses are still the rule.

## Slide 17
05
Shift registers
Registers that move their bits.
Notes: The last machine of the lecture is a register whose bits move: it is what turns a parallel word into a serial stream and back.

## Slide 18: Shift registers
Definition
A chain of one-bit memory cells connected to each other: at every clock pulse each bit moves from one cell to the adjacent one.
The shift can go in one fixed direction, or in a direction chosen by a control line (bidirectional registers)
They make reading and writing data in a system easier: they turn parallel data into serial data and back
Each cell is a D flip-flop whose input is the output of its neighbour
Notes: A shift register is a chain of one-bit cells in which, at every clock pulse, each bit moves to the adjacent cell. Each cell is a D flip-flop whose input is the output of its neighbour. The edge-triggered behaviour of the flip-flop is essential: with transparent latches a bit would run through the whole chain during a single clock pulse. The shift can be in a fixed direction or in a direction chosen by a control line. For the lecturer: Registri a scorrimento. Edge-triggered flip-flops are essential here: with transparent latches a bit would run through the whole chain in one clock pulse (Lecture 13).

## Slide 19: Four kinds of shift register
Serial in, serial out
F1
F2
...
FN
Serial in, parallel out
F1
F2
...
FN
Parallel in, serial out
F1
F2
...
FN
Parallel in, parallel out
F1
F2
...
FN
The same chain of flip-flops, with a common clock c; what changes is where the data enter and where they leave. Parallel in and parallel out with no shifting is the ordinary register.
Notes: The same chain of flip-flops gives four machines, according to where the data enter and leave. Serial in, serial out: a delay line. Serial in, parallel out: it collects bits arriving one at a time and presents the whole word. Parallel in, serial out: it takes a word and sends it out bit by bit. Parallel in, parallel out, with no shifting, is the ordinary register. The second and the third are the two ends of every serial connection. For the lecturer: SISO, SIPO, PISO and PIPO. The clock line is not drawn.

## Slide 20: Transfers between registers
Serial transfer: the serial output of one shift register feeds the serial input of another
– n clock pulses move a word of n bits; one wire is enough
Parallel transfer: the parallel outputs of one register feed the parallel inputs of another
– one clock pulse moves the whole word; n wires are needed
Time against wires: the same trade-off as dedicated against common buses
n pulses or n wires
moving a word of n bits costs either time or copper
Notes: Two ways of moving a word between registers. In a serial transfer the serial output of one shift register feeds the serial input of another: n clock pulses, one wire. In a parallel transfer the outputs of one register feed the inputs of another: one clock pulse, n wires. The phrase on the right is the trade-off of the whole lecture: moving a word of n bits costs either time or copper. For the lecturer: Trasferimento seriale (serial input, serial output) and trasferimento parallelo (parallel input, parallel output).

## Slide 21: Serial to parallel and back
Load
the datum of n bits is placed in parallel in the register R
Shift out
R is a shift register: the n bits leave one after another, in n successive steps
Travel
a single line carries them to the equipment downstream
Shift in
another register is loaded serially in n steps, rebuilding the datum bit by bit
Use
the rebuilt datum is passed on in parallel
This is the hardware of the warm-up. The display of the kit receives each pixel this way over SPI; the keyboard of Lecture 21 sends each key code this way.
Notes: A complete serial connection in five steps: the datum is loaded in parallel into a shift register; it is shifted out, one bit per step; the bits travel on a single line; at the other end a second shift register collects them, one per step; and the rebuilt word is passed on in parallel. This is the hardware of the warm-up, and it is how the display of the kit receives every pixel. Every serial standard, from the old serial port to USB, rests on a pair of shift registers. For the lecturer: Trasformazione serie-parallelo di un dato. UART, SPI, I2C, I2S and USB all rest on a pair of shift registers, one at each end.

## Slide 22: Registers with an address: a first memory
decoder
2-to-4
register 0 (3 bits)
register 1 (3 bits)
register 2 (3 bits)
register 3 (3 bits)
A1 A0
I2 I1 I0
O2 O1 O0
control: CS, RD, OE
Four registers of three bits: a memory of 4 words by 3 bits
Two address lines, A1 and A0, go to a decoder that selects one register
Three data inputs and three data outputs, shared by all the registers
Three control lines
– CS, chip select: the memory responds only when selected
– RD, read or write
– OE, output enable: three-state outputs, so that several memories can share one bus
Everything in it comes from Lectures 11, 13 and this one
Notes: Four registers of three bits and a decoder make a small memory. Two address lines choose, through the decoder, one of the four registers; three lines carry the data in and three carry them out. Three control lines complete it: chip select, so that the memory responds only when selected; a line that says read or write; and output enable, which controls three-state outputs so that several memories can share one bus. Nothing here is new: decoder, registers, three-state buffers. The next lecture scales it up. For the lecturer: Memoria 4 (registri) x 3 (bit): eight inputs (I0-I2, A0-A1, CS, RD, OE) and three outputs. The next lecture scales this up to the main memory.

## Slide 23
06
Back to the machine
Registers and buses on the kit.
Notes: Where are these machines on the kit and in the instructions you write? Two slides: the buses of the kit, and the shift instructions of RISC-V.

## Slide 24: Buses on the PRG32 kit
Connection | Kind | Lines | What travels on it
inside the ESP32-C6 | parallel | 32 data lines, address and control | instructions, data and register transfers
display (ILI9341) | serial, SPI | clock, data out, chip select, data/command | every pixel of every frame, bit by bit
sound amplifier | serial, I2S | bit clock, word select, data | audio samples, 22,050 per second
joystick and buttons | one wire per button | one input pin each | a decoded representation: one line per button
USB to the laptop | serial, differential pair | two data wires | the firmware and the debug console
Notes: The buses of the kit. Inside the chip the bus is parallel. The display is connected by SPI, a serial bus with a clock, a data line, a chip select and a line that distinguishes data from commands: every pixel of every frame travels on it bit by bit. The amplifier is connected by I2S, another serial bus, which carries 22,050 audio samples per second. The buttons use one wire each: a decoded representation. USB, serial as well, carries the firmware and the debug console. For the lecturer: From the hardware description of the PRG32 repository (docs/hardware). Chip select is the CS of the small memory on the previous slide: several devices can share the same serial bus because only the selected one listens.

## Slide 25: Shifts in RISC-V: a shift register in one instruction
slli and srli move all the bits of a register by a given number of positions, filling with zeros
srai fills with copies of the sign bit (Lecture 05)
sll, srl and sra take the amount from a second register
In hardware a shift by any amount in one step is done by a barrel shifter: layers of multiplexers, not a chain of flip-flops
The shifter is one of the units of the ALU of Lecture 11
# parallel to serial, LSB first
andi t1, a0, 1 # take bit 0
srli a0, a0, 1 # next bit
# serial to parallel, MSB first
slli a1, a1, 1 # make room
or a1, a1, t1 # insert bit
Notes: The shift instructions move all the bits of a register in a single step: slli and srli fill with zeros, srai with copies of the sign bit; sll, srl and sra take the number of positions from a register. In hardware this is not a chain of flip-flops, which would need one clock pulse per position, but a barrel shifter, a combinational network of layers of multiplexers, and it is one of the units of the ALU. The code on the right shows the two conversions between parallel and serial. For the lecturer: A true shift register needs n clock pulses for n positions; the barrel shifter of the ALU is combinational and does it within one clock period.

## Slide 26: Check your understanding
Why does a common bus need three-state buffers?
A
To make transfers faster
B
So that only the enabled source drives the lines
C
To store the datum on the bus
D
To convert serial data to parallel
Notes: Think of two outputs connected to the same wire, one at 0 and one at 1. A three-state buffer has nothing to do with speed, with storing or with conversion: it disconnects the sources that are not chosen. For the lecturer: Answer: B. Several sources share the same lines; all but one must be electrically disconnected (high impedance), otherwise two outputs would fight over the wire.

## Slide 27: Check your understanding
How many clock pulses does a serial transfer of a 32-bit word need?
A
1
B
5
C
32
D
64
Notes: One bit per clock pulse. The alternative, a parallel transfer, would take one pulse and thirty-two wires. For the lecturer: Answer: C. One bit per pulse: n pulses for n bits. A parallel transfer needs one pulse and n wires.

## Slide 28: Check your understanding
A memory has 10 address lines and 8 data lines. How many bits does it store?
A
80
B
1,024
C
8,192
D
10,240
Notes: Ten address lines select one word among 2 to the 10; each word has 8 bits. Multiply the two numbers. The first option multiplies the lines instead of using the power. For the lecturer: Answer: C. 2^10 = 1,024 words of 8 bits: 8,192 bits, that is 1 KiB.

## Slide 29: Exercises: paper first, then PRG32
TRY IT
1
Draw a 4-bit serial-in, parallel-out shift register with D flip-flops, and fill in its contents over four clock pulses for the input 1, 0, 1, 1
2
Three registers share a common bus: write the enable and load signals needed to copy register B into register A
3
Complete the warm-up: write the loop that receives eight bits from a line and rebuilds the byte
4
On PRG32, show a byte as eight lamps and shift it left by one position every half second
5
Make the bit that leaves on the left come back in on the right (a rotation): a ring counter
Expected result
On PRG32: a pattern of lamps that walks to the left and, in the last exercise, goes round for ever.
Notes: Five exercises. Draw a 4-bit serial-in, parallel-out shift register and follow its content over four clock pulses. Write the enable and load signals that copy one register into another on a common bus. Complete the warm-up with the receiving loop. On PRG32, show a byte as eight lamps and shift it every half second. Finally make the bit that leaves on one side come back on the other: a rotation, also called a ring counter. For the lecturer: Exercise 3: slli a1, a1, 1 then or with the received bit, eight times. Exercise 5: srli t1, a0, 7; andi t1, t1, 1; slli a0, a0, 1; or a0, a0, t1; andi a0, a0, 255.

## Slide 30: Glossary: English and Italian
English | Italiano | English | Italiano
word gate | porta di parola | three-state (tri-state) | a tre stati (tristate)
register | registro | high impedance | alta impedenza
bus | bus | shift register | registro a scorrimento
dedicated / common bus | bus dedicato / comune | serial / parallel transfer | trasferimento seriale / parallelo
load, strobe | caricamento, strobe | chip select | selezione del chip
Notes: Ten terms. Three-state, or tri-state, is a tre stati; high impedance is alta impedenza. A shift register is a registro a scorrimento. Load and strobe indicate the signal that makes a register take its input. Chip select is the line that chooses which device on a shared bus must respond.

## Slide 31: Conclusions and reading
Registers are an evolved form of memory with an elementary way of working
Reading and writing registers happens through buses of different kinds
For a common bus to work, three-state circuits are needed: 0, 1, and disconnected
Data can be transferred serially or in parallel; shift registers convert between the two
A decoder in front of a group of registers makes a memory: the subject of the next lecture
Reading
– Patterson, Hennessy: Computer Organization and Design, RISC-V Edition, appendix A
– Bucci: Architettura dei calcolatori elettronici, chapters on registers and buses
– PRG32 repository: docs/hardware/hardware.md
Notes: Five conclusions. A register is a form of memory with an elementary way of working. Registers are read and written through buses. A common bus needs three-state circuits: 0, 1 and disconnected. Data travel serially or in parallel, and shift registers convert between the two. And a decoder in front of a group of registers makes a memory, which is the subject of the next lecture. For the lecturer: Next lecture: memory.