## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 18
The Processor
Control unit, registers, stack and ALU: the general model, and RISC-V as the reference processor
“One Ring to rule them all...”
J. R. R. Tolkien, The Lord of the Rings, 1954-1955
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Notes: The last block of the course opens the machine that has been running your programs. This lecture presents the processor twice: first as a general model, valid for every processor, with its control unit, registers, stack and arithmetic unit; then as RISC-V, the processor you have programmed since the first days. Each abstract element of the model already has, for you, a familiar name. The ring of the quotation is the processor itself: the one component that commands all the others. For the lecturer: The original deck presented a general processor model and ended with the architecture of the Motorola MC68000. Here the general model is kept and RISC-V (RV32IMAC, as on the ESP32-C6 of the PRG32 kit) is the reference: the students have programmed it since the first days, so every abstract element has a name they already know.

## Slide 2: What you will be able to do by the end
1
Name the components of a processor: control unit, ALU, registers, links to memory and to input/output
2
Distinguish internal registers from machine registers, and general registers from special ones
3
Explain how a stack works and how RISC-V implements push and pop
4
Compare the accumulator, stack and general-register models on the same computation
5
Describe RISC-V as a load-store, general-register processor, and read the name RV32IMAC
6
Map every element of the general model onto the processor of the PRG32 kit
Notes: Six objectives. Name the components of a processor. Distinguish internal registers from machine registers, and general registers from special ones. Explain how a stack works and how RISC-V implements push and pop. Compare three models of processor, accumulator, stack and general registers, on the same computation. Describe RISC-V as a load-store, general-register processor and read the name RV32IMAC. And map every element of the model onto the processor of the kit.

## Slide 3
01
Warm-up on the machine
One line of a high-level language.
Notes: The warm-up takes one line of a high-level language, a sum of two variables, and writes it in RISC-V. Count the instructions, and notice which ones touch memory.

## Slide 4: z = x + y
la t0, x
lw t1, 0(t0) # bring x into a register
la t0, y
lw t2, 0(t0) # bring y into a register
add t3, t1, t2 # compute, between registers
la t0, z
sw t3, 0(t0) # take the result back to memory
.section .data
x: .word 5
y: .word 7
z: .word 0
1
Seven lines for one sum: memory is touched only by lw and sw
2
The arithmetic happens only between registers
3
Other processors do the same job with three instructions, or with one
4
Why is RISC-V made this way? To answer we need a model of the processor
Notes: To compute z = x + y the program loads x into a register, loads y into another, adds the two registers into a third, and stores the result in z. Seven lines for one sum. Memory is touched only by lw and sw; the arithmetic happens only between registers. Other processors do the same job with three instructions, or with one. Why is RISC-V made like this? To answer we need a model of what a processor is, and then a comparison between different ways of building one. For the lecturer: The load-modify-store cycle of Lecture 02, now seen as a design choice. Keep the three addresses in mind: the same computation returns in the comparison of the processor models.

## Slide 5
02
The processor
What it is made of.
Notes: First the anatomy: what a processor is made of, in general, and what corresponds to each part in RISC-V.

## Slide 6: The computer and its processor
An electronic computer is a numeric, automatic, stored-program system built with electronic circuits
Three subsystems: processor (CPU), main memory, input/output, connected by buses
The processor can execute only a set of instructions, from some tens to a few hundred, more or less complex
Machine language: the strings of bits that encode the instructions the circuits of a processor can execute
Instructions request
– transfers of information, inside the computer and to or from the I/O devices
– arithmetic and logic operations
Data and instructions of a program are stored in the main memory
CPU
central processing unit: the one ring that rules memory and input/output
Notes: A reminder and a definition. A computer has three subsystems, processor, main memory and input/output, connected by buses. The processor can execute only a fixed set of instructions, from a few tens to a few hundred, and machine language is the set of strings of bits that encode them. Instructions request two kinds of things: transfers of information and arithmetic or logic operations. Both programs and data are in the main memory. For the lecturer: RV32I, the base of RISC-V, has about forty instructions; with the M, A and C extensions of the kit, about a hundred encodings. The Motorola 68000 had fifty-six instruction types with many variants each.

## Slide 7: The processor: a reference model
CPU
control
network
PC
D
R0
R1
. . .
Rn-1
O1
O2
ALU
U
internal bus
MA
MB
RI
RU
link to memory
link to input/output
Control unit
– program counter (PC): the next instruction
– decoding register (D): the instruction being executed
– the control network that issues the commands
Machine registers R0 ... Rn-1
Arithmetic logic unit
– two operand registers O1 and O2, a result register U
Link to memory
– memory address (MA) and memory buffer (MB)
Link to input/output
– I/O buffer registers RI and RU
Notes: The reference model. The control unit contains the program counter, which holds the address of the next instruction, a decoding register, which holds the instruction being executed, and the network that issues the commands. The machine registers R0 to Rn-1 are those the programmer uses. The arithmetic logic unit has two operand registers and a result register. Two pairs of registers link the processor to the outside: MA and MB towards memory, RI and RU towards input and output. An internal bus connects everything. For the lecturer: Modello di riferimento. Although based on the same logical scheme, and so made of rather similar components, the processors on the market can be very different from one another.

## Slide 8: The model and RISC-V, side by side
Element of the model | In RISC-V | Seen by the programmer?
PC, program counter | pc, 32 bits | indirectly: branches, jumps and auipc use it
D, decoding register | the instruction register | no
R0 ... Rn-1, machine registers | x0 ... x31, thirty-two registers of 32 bits | yes: zero, ra, sp, t0, a0, s0, ...
O1, O2, U, registers of the ALU | the ALU inputs and output | no
MA, MB, link to memory | the address and data of a load or store | no
RI, RU, link to input/output | absent: devices are memory-mapped | -
status register with flags | absent: no condition codes | -
special registers | the control and status registers (CSR) | only by privileged software
Notes: Each element of the model, and what it is in RISC-V. The program counter is pc. The machine registers are x0 to x31, with the names you know. The registers of the ALU and those towards memory exist in the hardware but are invisible to the programmer. Two rows say "absent", and they are deliberate choices: there are no registers for input and output, because devices are memory-mapped, and there is no status register with flags. The special registers are the CSRs, reserved for privileged software. For the lecturer: The two 'absent' rows are deliberate simplifications of RISC-V, explained later in this lecture and in Lecture 15. The MC68000 of the original deck had all the elements of the model: eight data and eight address registers, a status register with condition codes, and separate interrupt circuitry.

## Slide 9: Internal registers and machine registers
Internal registers
– not directly visible to the programmer, and necessary for the processor to work: PC, MA, MB, D, O1, O2, U, ...
Machine registers
– they define the programming model; further divided into general registers and special registers
The processor handles three kinds of information: instructions, memory addresses and data
– the size of MA and PC depends on the size of the addresses
– the size of the ALU registers depends on the size of the data
In RV32 all three are 32 bits wide: one size for registers, addresses and instructions
RV32
registers of 32 bits, addresses of 32 bits, instructions of 32 bits
Notes: Two classes of registers. Internal registers are necessary for the processor to work but are not visible to the programmer: the program counter, the registers towards memory, those of the ALU. Machine registers define the programming model: they are the ones named in instructions. The processor handles three kinds of information, instructions, addresses and data, and each could have its own size. In RV32 all three are 32 bits wide, which makes the machine very regular. For the lecturer: Tipi di dato del processore. The '32' of RV32 is the width of the registers; RV64 has 64-bit registers and addresses and the same 32-bit instructions.

## Slide 10: How real processors differ from the model
In general
They may have a different, usually richer, set of general registers
The machine registers may be specific memory locations
The I/O section may be missing altogether, and be implemented by dedicated chips
Very simple arithmetic units can be extended by dedicated chips that improve the ALU
RISC-V on the PRG32 kit
Thirty-two general registers, in a bank inside the processor
No I/O section: peripheral controllers on the same chip, reached as memory
Optional extensions instead of extra chips: M adds multiply and divide
No F extension on the ESP32-C6: floating point would be done in software (Lecture 06)
Notes: Real processors differ from the model in several ways: more or fewer general registers, registers that are really memory locations, an input/output section that is missing and delegated to other chips, a simple arithmetic unit extended by dedicated chips. The right column says how RISC-V on the kit resolves each point: thirty-two registers in a bank, no I/O section, optional extensions instead of extra chips. The M extension adds multiplication and division; the floating-point extension is absent on the kit. For the lecturer: Il modello di processore. Historic example of a dedicated arithmetic chip: the 68881 floating-point coprocessor for the 68000 family, the 8087 for the 8086.

## Slide 11: Words or bytes: the length of machine words
Word processors
All the machine words have the same length
Sized on the longest piece of information
Awkward with data of intrinsically variable nature
RISC-V: every instruction is 32 bits (16 in the compressed form)
Character (byte) processors
The length of machine words is variable, a multiple of a byte
Well suited to the treatment of strings
Intel x86: instructions from 1 to 15 bytes
MC68000: instructions of one to five 16-bit words
Notes: How long is a machine word? In word processors all instructions have the same length, sized on the longest piece of information: RISC-V instructions are all 32 bits, or 16 in the compressed form. In character processors the length varies in multiples of a byte: x86 instructions go from 1 to 15 bytes. A fixed length wastes some space but makes decoding simple, which matters for speed. For the lecturer: Processore a voce o a caratteri. A characteristic parameter of a processor is the number of bits of its registers: the parallelism of internal transfers, 8, 16, 32 or 64 bits.

## Slide 12: User state and supervisor state
State | Who runs in it | What it may do | RISC-V name
supervisor | the operating system | every instruction of the instruction set | machine mode (M); supervisor mode (S) where there is a full operating system
user | a user program | everything except the privileged instructions | user mode (U)
The processor is in supervisor state when it executes the operating system, in user state when it executes a user program.
Notes: A processor has at least two states of operation. In supervisor state it runs the operating system and may execute every instruction. In user state it runs an ordinary program and may execute everything except the privileged instructions, those that could compromise the system. RISC-V calls them modes: machine mode, the most privileged and the only mandatory one, supervisor mode and user mode. The chip of the kit has machine and user. Passing from one to the other happens through the traps of the next lecture. For the lecturer: Stato utente o stato supervisore. RISC-V defines three privilege modes: M, the most privileged and the only mandatory one, runs firmware; S runs the kernel of an operating system such as Linux; U runs applications. The ESP32-C6 implements M and U. Changing mode happens through traps (Lecture 19).

## Slide 13
03
Registers
What they are for.
Notes: Registers deserve a closer look: how they are organised, what they are used for, which ones RISC-V has, and what replaces the flags that RISC-V does not have.

## Slide 14: Kinds of registers
A register can be specialised, or do several jobs
– specialised registers need specialised operation codes for the same operation on different banks
– concentrating several functions gives more internal complexity and more flexibility of use
Machine registers, different in number and often grouped in banks, can be organised
– as an addressable memory: a bank R, the register Ri
– as autonomous registers, each with its own name
RISC-V: one bank of thirty-two registers, addressed by 5 bits inside the instruction; the names t0, a0, sp are only conventions
Notes: Registers can be specialised or general. Specialised registers need different instructions for the same operation on different banks; general registers give more flexibility. They can be organised as a small addressable memory, a bank in which register number i is selected, or as separate registers with their own names. RISC-V chooses a single bank of thirty-two registers, each selected by five bits inside the instruction. The names t0, a0, sp are only conventions. For the lecturer: Tipologia dei registri. Special registers are used exclusively by the operating system: addressing aids, interrupt registers, memory limits. General addressable registers were, in some processors, the first locations of memory: the 'page zero' of the 6502.

## Slide 15: The functions of registers
Transit of data
– memory to register, register to register, register to memory: load, move, store
Accumulation of results
– needed for arithmetic and logic: R := (op) R, or R := R (op) X
Addressing
– finding the address of an operand: index registers, base registers
Stack pointers
– managing a stack implemented in memory
Indicators, or flags
– binary information about events: zero, sign, overflow, carry, illegal addresses or codes
– produced during the execution of an instruction, they can condition the following ones
Notes: Five functions of registers. Transit: carrying data between memory and registers. Accumulation: holding the operands and the results of arithmetic. Addressing: holding an address or part of one, as base and index registers do. Stack pointer: indicating the top of a stack in memory. Flags: single bits that record events such as zero, sign, overflow and carry, to condition later instructions. In RISC-V the general registers serve the first four functions; the fifth does not exist as a register. For the lecturer: Funzione dei registri. In RISC-V the first four functions are all served by the general registers; the fifth does not exist as a register.

## Slide 16: The thirty-two registers of RISC-V
Register | Name | Function, by convention | Register | Name | Function, by convention
x0 | zero | always 0 | x8 - x9 | s0 - s1 | saved
x1 | ra | return address | x10 - x11 | a0 - a1 | arguments, results
x2 | sp | stack pointer | x12 - x17 | a2 - a7 | arguments
x3 | gp | global pointer | x18 - x27 | s2 - s11 | saved
x4 | tp | thread pointer | x28 - x31 | t3 - t6 | temporaries
x5 - x7 | t0 - t2 | temporaries | pc | - | program counter (not in the bank)
Notes: The complete table of the registers of RISC-V, with numbers, names and roles. You have used most of them: zero, ra, sp, the temporaries t0 to t6, the arguments a0 to a7, the saved registers s0 to s11. Two are new: gp and tp, used by compilers and operating systems. The hardware treats x1 to x31 identically; only x0 is special. The roles come from the calling convention. The program counter is not in the bank. For the lecturer: The hardware treats x1 to x31 identically; only x0 is special. The roles come from the calling convention (Lecture 02). The MC68000 instead separated data registers D0-D7 from address registers A0-A7, with A7 as stack pointer.

## Slide 17: Flags: the status register, and its absence
Processors with a status register
Bit flags accessible from the program
Z zero, N negative, V overflow, C carry, sometimes parity
An instruction sets them; a later conditional branch tests them
MC68000: the condition code register; x86: the flags register
RISC-V: no flags
A branch compares two registers and jumps, in one instruction: beq, bne, blt, bge, bltu, bgeu
slt and sltu write the result of a comparison in a general register
Carry and overflow are computed when needed (Lecture 05)
Less hidden state: simpler pipelines, simpler interrupts
Notes: Many processors have a status register whose bits, the flags, record the outcome of the last operation: zero, negative, overflow, carry. An instruction sets them, and a later conditional branch tests them. RISC-V has none. A branch compares two registers and jumps, all in one instruction; slt writes the result of a comparison in an ordinary register; carry and overflow are computed when needed, as in Lecture 05. Less hidden state means a simpler processor and simpler interrupts. For the lecturer: Registro di stato. The original deck listed Z, N, P (positive), V, C and a parity bit.

## Slide 18: Special registers of RISC-V: the CSRs
Register | Name | What it holds
mstatus | machine status | the global interrupt enable and the previous privilege mode
mtvec | trap vector | the address of the routine that handles interrupts and exceptions
mepc | exception program counter | the address of the instruction that was interrupted
mcause | trap cause | a code that says why the trap happened
mie, mip | interrupt enable, interrupt pending | one bit per source of interrupt
Notes: The special registers of RISC-V are the control and status registers, CSRs: a separate bank, read and written only by privileged code with dedicated instructions. Five are worth knowing by name: mstatus, with the global interrupt enable; mtvec, the address of the routine that handles traps; mepc, the address of the interrupted instruction; mcause, the reason for the trap; and the pair mie and mip, with one bit per source of interrupt. The next lecture uses them all. For the lecturer: Control and status registers: a separate bank of up to 4,096 registers, read and written only with the instructions csrrw, csrrs and csrrc, and only by privileged code. They are the 'registers of the interrupts' of the general model, and the subject of Lecture 19.

## Slide 19
04
The stack
Last in, first out.
Notes: The stack is the data structure that makes subprograms and interrupts possible. You have used it since Lecture 02; here it is defined and compared across processors.

## Slide 20: The stack
An abstract data structure with two operations: push stores an element as the last of the pile, pop takes the last element away
It works always and only on the top: there is no need to say where to store or to fetch
It is used to set aside the contents of registers that must be freed to carry out a task, and to restore them afterwards: subprograms, interrupts
Implemented with a pointer, in memory or in a dedicated register, that indicates the position of the last element at every instant
Operations on the stack should check for overflow on a push and for an empty stack on a pop
LIFO
the last value pushed is the first one popped
Notes: A stack has two operations: push stores an element on top of the pile, pop removes the element on top. It always works on the top, so there is no need to say where: last in, first out. It is used to set aside the contents of registers that must be freed for a task and to restore them afterwards. It is implemented with a pointer that indicates the last element. Careful programs check for overflow on a push and for an empty stack on a pop. For the lecturer: LIFO, last in, first out. You have used it since Lecture 02 to save ra.

## Slide 21: Push and pop in RISC-V
memory
low addresses
(free)
(free)
-28
-17
739
43
bottom of the stack
sp
sp points to the last occupied location; the stack grows towards low addresses.
# push t0
addi sp, sp, -4 # make room
sw t0, 0(sp) # store on top
# pop t0
lw t0, 0(sp) # fetch the top
addi sp, sp, 4 # release it
Processor | Push
RISC-V | addi sp, sp, -4 and sw: two instructions
MC68000 | MOVE D0, -(SP): a pre-decrement addressing mode
Intel x86 | PUSH: a dedicated instruction
Notes: In RISC-V the stack pointer sp holds the address of the last occupied location, and the stack grows towards low addresses. A push is two instructions: subtract 4 from sp, then store on the new top. A pop is the reverse: load from the top, then add 4. The table compares three processors: RISC-V needs two instructions, the 68000 one instruction with a special addressing mode, x86 a dedicated instruction. In practice a RISC-V function allocates its whole frame once, as you have done since Lecture 02. For the lecturer: The values are those drawn in the original deck. RISC-V has no push and pop: a stack frame is allocated once per function, sixteen bytes at a time, and filled with ordinary stores (Lecture 02). The 68000 form MOVE (SP)+, D0 pops with a post-increment.

## Slide 22
05
Processor models
Where the operands live.
Notes: Where do the operands of an operation live? The answer distinguishes the great families of processors, and explains the seven lines of the warm-up.

## Slide 23: Four architectures of the processor
1
General registers
The processor has a set of registers REG0, REG1, ..., REGN-1 that can be used interchangeably.
2
Accumulator
All arithmetic, logic and comparison instructions have an implicit operand: one special register, the accumulator.
3
Stack
There are neither accumulators nor general registers, only the stack pointer; instructions work on the data on top of the stack.
4
Orthogonal
A single bank of general registers, some of which serve, when needed, as stack pointer or other special registers.
Notes: Four architectures. With general registers the processor has a set of interchangeable registers. With an accumulator, arithmetic instructions have an implicit operand, one special register. In a stack machine there are neither, only a stack pointer, and instructions work on the top of the stack. An orthogonal architecture has a single bank of general registers, some of which also serve as stack pointer or in other special roles. RISC-V is of this last kind. For the lecturer: Modello a registri generici, ad accumulatore, a stack; architetture ortogonali. The original definition of orthogonal mentions a status register too; RISC-V is orthogonal and has not even that.

## Slide 24: z = x + y in four processors
Model | Example | Program | Memory accesses
accumulator | Motorola 6809, MOS 6502 | LDA x ; ADD y ; STA z | 3
stack | Java virtual machine, WebAssembly | PUSH x ; PUSH y ; ADD ; POP z | 3, plus the stack itself
general registers, memory operands | MC68000, Intel x86 | MOVE x, D0 ; ADD y, D0 ; MOVE D0, z | 3
general registers, load-store | RISC-V | lw t1, x ; lw t2, y ; add t3, t1, t2 ; sw t3, z | 3
Notes: The sum of the warm-up in four machines. The accumulator machine: load x, add y, store z. The stack machine: push x, push y, add, pop z. A register machine with memory operands: move x into a register, add y to it, move the register into z. RISC-V: two loads, an add between registers, a store. The memory accesses are three in every case. What changes is the number of instructions and how much each one does: in RISC-V each does one thing only. For the lecturer: The same three accesses to memory everywhere: what changes is how many instructions there are and how complex each one is. In the register-memory model an instruction such as ADD y, D0 reads memory and computes; in the load-store model every instruction does one thing. Stack machines with the stack in memory are generally slower than general-register machines. lw t1, x is a shorthand the assembler accepts for the la and lw pair of the warm-up.

## Slide 25: RISC-V: a load-store, general-register processor
Instructions that work on registers are faster than those that work on memory locations: the most used data are kept in registers
Only loads and stores touch memory; every other instruction works register to register
Three operands: two sources and a destination, so that no value is destroyed unless you want it to be
Each instruction does one simple thing and has a fixed size: easy to decode, easy to execute in a pipeline
This is the meaning of RISC: reduced instruction set computer
load, compute, store
the rhythm of every RISC-V program, from the first counter to the last game
Notes: RISC-V is a load-store processor with general registers. Only loads and stores touch memory; every other instruction works from register to register, which is faster. Instructions have three operands, two sources and a destination, so that no value is destroyed unless you want it to be. Each instruction does one simple thing and has a fixed size, which makes it easy to decode and to execute in a pipeline. This is what RISC means. The seven lines of the warm-up are the price, and the simplicity of each line is the gain. For the lecturer: Register-to-register: [REGX] + [REGY] gives [REGZ]. The memory-to-register and register-to-memory forms of the original deck exist in CISC processors and are exactly what RISC gives up.

## Slide 26
06
The ALU and the whole picture
Notes: The last part puts the pieces together: the arithmetic unit seen from the processor, the block diagram of an RV32 processor, and the numbers of the chip of the kit.

## Slide 27: The arithmetic logic unit
It supervises the arithmetic and logic operations between operands
Physically included in the processor in elementary architectures; an independent apparatus in more complex ones
A widespread solution: a reduced arithmetic unit inside the processor, and independent apparatus for more sophisticated operations
Scheme: two input registers O1 and O2 for the operands, an output register U for the result
The operations depend on the data types and on their representation
– logical type, strings of characters, pointers, numbers in the various encodings of Lectures 05 and 06
Notes: The ALU carries out the arithmetic and logic operations between operands: it is the combinational machine of Lecture 11, with two inputs and one output. In simple architectures it is entirely inside the processor; in complex ones the most sophisticated operations are delegated to separate units. In RISC-V these units are the extensions: M for multiplication and division, F and D for floating point. For the lecturer: The ALU of Lecture 11, seen from the processor. In RISC-V the 'independent apparatus' are the extensions: M for multiplication and division, F and D for floating point.

## Slide 28: The architecture of an RV32 processor
PC
address of the
instruction
instruction
memory
fetch
decoder and
control unit
fields and
commands
register file
x0 - x31
32 x 32 bits
ALU
compute, or
form an address
data
memory
load, store
write back: the result returns to the register named by rd
next PC: PC + 4, or the branch target
Next to them, out of the main path: the bank of control and status registers, and the trap logic of Lecture 19. Compared with the MC68000 of the original deck there are no separate data and address registers, no condition code register and no effective-address register.
Notes: The block diagram of an RV32 processor, from left to right. The PC gives the address of the instruction. The instruction is fetched from memory. The decoder separates its fields and the control unit issues the commands. The register file provides the operands. The ALU computes, or forms an address. The data memory is read or written by loads and stores. Two paths go back: the result returns to the register named by rd, and the next value of the PC is PC plus 4 or the target of a branch. Every instruction you write travels along this path. For the lecturer: The classic single-cycle RISC-V datapath of Patterson and Hennessy, reduced to its blocks; instruction memory and data memory are the same address space, drawn twice for clarity. It replaces the slide 'Architettura del processore MC68000'.

## Slide 29: The processor of the PRG32 kit
Feature | ESP32-C6
Instruction set | RV32IMAC: base integer set, multiply and divide, atomics, compressed instructions
Main core | one 32-bit RISC-V core, up to 160 MHz, four-stage pipeline
Second core | a low-power RISC-V core, up to 20 MHz, for tasks that run while the main core sleeps
Privilege modes | machine and user
Floating point | none: no F or D extension
Memory | 512 KB of SRAM, 320 KB of ROM, external flash
On the same chip | Wi-Fi 6, Bluetooth, Thread and Zigbee radios; SPI, I2S, GPIO and timer peripherals
Notes: The processor of the kit, in numbers: instruction set RV32IMAC; one main core at up to 160 MHz with a four-stage pipeline, and a second low-power core; machine and user modes; no floating point; 512 KB of SRAM, 320 KB of ROM and an external flash; radios and peripherals on the same chip. A complete computer in a few square millimetres, for about two euros: processor, memory and input/output are all there, as in the model. For the lecturer: From the Espressif ESP32-C6 datasheet. A complete computer on a chip of a few square millimetres that costs about two euros: processor, memory and input/output are all there, as in the model of the first slides.

## Slide 30: Check your understanding
Which register of the general model has no counterpart in RISC-V?
A
the program counter
B
the status register with the flags
C
the stack pointer
D
the instruction register
Notes: Go back to the table that puts the model beside RISC-V and look for the rows marked "absent". One of them is among the options. For the lecturer: Answer: B. RISC-V has no condition codes: branches compare registers directly.

## Slide 31: Check your understanding
In RISC-V, which instructions can read or write the main memory?
A
all of them
B
add and sub
C
only loads and stores
D
only jumps
Notes: Remember the warm-up: which instructions touched memory, and which only registers? That is the definition of a load-store architecture. For the lecturer: Answer: C. It is a load-store architecture: lw, lh, lb, sw, sh, sb and their unsigned forms.

## Slide 32: Check your understanding
After addi sp, sp, -4 and sw t0, 0(sp), what has happened?
A
t0 was popped from the stack
B
t0 was pushed on the stack
C
the stack was emptied
D
sp was saved in t0
Notes: Follow the two instructions: the pointer moves down by one word, then a value is stored at the address it now holds. A value has been added on top of the stack. For the lecturer: Answer: B. The pointer moves down by one word and the value is stored on the new top: a push.

## Slide 33: Check your understanding
In an accumulator machine, the instruction ADD y means:
A
y := y + accumulator
B
accumulator := accumulator + [y]
C
push y, then add
D
y := accumulator
Notes: In an accumulator machine the accumulator is the implicit operand: it is one of the two addends and it receives the result. The operand written in the instruction is only read. For the lecturer: Answer: B. The accumulator is the implicit operand and the destination.

## Slide 34: Exercises: paper first, then PRG32
TRY IT
1
Write z = (a + b) - (c + d) for an accumulator machine, a stack machine and RISC-V; count instructions and memory accesses
2
Write push and pop of two registers, t0 and t1, keeping sp a multiple of 16 as the calling convention requires
3
For each register used in your last PRG32 program, say which function it serves: transit, accumulation, addressing, stack
4
In PRG32-QT, single-step a call and its return: watch pc, ra and sp, and the word saved on the stack
5
Find in the datasheet of the processor of your phone or laptop: instruction set, number of cores, clock, privilege levels
Expected result
On PRG32-QT: sp drops by 16 at the prologue and returns at the epilogue; ra holds the address after the call.
Notes: Five exercises. Write the expression z = (a + b) - (c + d) for an accumulator machine, a stack machine and RISC-V, counting instructions and memory accesses. Write push and pop of two registers keeping sp a multiple of 16. Classify the registers of your last program by function. Single-step a call and its return in PRG32-QT, watching pc, ra and sp. And look up the processor of your phone or laptop. For the lecturer: Accumulator: LDA a; ADD b; STA tmp; LDA c; ADD d; STA tmp2; LDA tmp; SUB tmp2; STA z. Stack: PUSH a; PUSH b; ADD; PUSH c; PUSH d; ADD; SUB; POP z. RISC-V: four loads, two adds, one sub, one store.

## Slide 35: Glossary: English and Italian
English | Italiano | English | Italiano
control unit | unità di controllo | accumulator | accumulatore
program counter | contatore di programma | stack pointer | puntatore allo stack
machine register | registro di macchina | status register, flags | registro di stato, indicatori
general / special register | registro generico / speciale | supervisor / user state | stato supervisore / utente
instruction set | insieme (set) di istruzioni | privileged instruction | istruzione privilegiata
Notes: Ten terms. The control unit is the unità di controllo. A machine register is one visible to the programmer. Flags are also called indicatori in Italian. Supervisor and user state are the two levels of privilege. A privileged instruction can be executed only in supervisor state.

## Slide 36: Conclusions and reading
The processor commands and controls, relying on the memory and on the input/output systems
Registers are storage locations that may be physically inside or outside the processor
The kinds of registers and the way they are used determine the model of processor: accumulator, stack, general registers
The ALU carries out the operations between operands
RISC-V is a load-store, general-register processor with no flags and no I/O instructions: few elements, each one simple
Reading
– Patterson, Hennessy: Computer Organization and Design, RISC-V Edition, chapters 2 and 4
– The RISC-V Instruction Set Manual, volume I: Unprivileged Architecture
– Stallings: Computer Organization and Architecture, chapters on processor structure and function
Notes: Five conclusions. The processor commands and controls, relying on memory and on input/output. Registers are storage locations, inside or outside the processor. The kinds of registers and their use determine the model: accumulator, stack, general registers. The ALU carries out the operations. And RISC-V is a load-store processor with general registers, no flags and no I/O instructions: few elements, each one simple. The next lecture follows an instruction through its whole life. For the lecturer: Next lecture: instructions and interrupts.