## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 06
Number Representation: Real Numbers
One's complement, excess-k, fixed point and IEEE 754 floating point
“I may count for little, it's true, said the One to the Zero, but what are you worth? Nothing: nothing at all.”
Trilussa, Nummeri, 1944
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Lecture deck. The listings, the complete program and how to test it are in the code deck:
06-Computer_Architecture-Number_Representation_Reals-Lab.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: The previous lecture treated integers; this one treats numbers with a fractional part. It begins from a concrete engineering problem: a ball must move by less than one pixel per frame, on a processor with no instructions for real numbers. The first solution, fixed point, uses nothing beyond integer arithmetic already understood. Floating point then emerges as the general solution, together with the standard to which essentially every computer conforms, IEEE 754. The lecture is thus organised as a progression from a specific constraint to a general theory, and back to the constraint. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: fixed point; one's complement and excess-k; IEEE 754 floating point; the name RV32IMAC. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise. Roadmap. Today's outcomes: (1) represent a real number in fixed point and compute with it using integer instructions; (2) decode an IEEE 754 single-precision number; (3) read the name RV32IMAC and say what the kit can and cannot compute in hardware. Builds on: only what Lecture 01 set up. Next: Lecture 07, Verm1, Part 1: A Head That Crosses the World. For the lecturer: Spiral: the lecture opens with a ball that must move less than one pixel per frame on a processor with no floating-point unit. Fixed point solves it; floating point is then presented as the general answer, with IEEE 754.

## Slide 2: What you will be able to do by the end
1
Encode signed integers in one's complement and in excess-k, and say what each is good for
2
Represent a fractional quantity in fixed point and compute with it using integer instructions
3
Explain mantissa, exponent and normalisation in floating point
4
Encode and decode a number in IEEE 754 single precision
5
Recognise zero, denormalised numbers, infinity and NaN
6
Say why the ESP32-C6 has no floating-point instructions and what PRG32 games do instead
Notes: Six learning outcomes. Two further encodings of signed integers, one's complement and excess-k, complete the previous lecture and are prerequisites for floating point. Fixed-point representation follows, which the course project will use. Then floating point: mantissa, exponent and normalisation, encoding and decoding in single precision, and the special patterns. The final outcome concerns the student's own kit: its processor has no floating-point instructions, and the student should be able to explain what programs do instead, and why.

## Slide 3: One's complement
Non-negative numbers, 0 <= x < 2^(n-1), are represented by themselves: X = x
Negative numbers are represented by X = 2^n - 1 - |x|
Range: from -(2^(n-1) - 1) to +(2^(n-1) - 1)
Zero has two representations, 0000 and 1111: 2^n - 1 numbers are represented, as in sign and magnitude
Why use it? Negating is trivial: complement every bit
– 6 = 0110 and -6 = 1001; 5 = 0101 and -5 = 1010; 1 = 0001 and -1 = 1110
-x = not x
the one's complement of a number is obtained by inverting all its bits
UNDERSTAND NOW · one's complement and excess-k
Notes: In one's complement a negative number is obtained by inverting every bit of its positive counterpart: 6 is 0110, -6 is 1001. Negation could not be simpler. The cost is that already paid by sign and magnitude: zero has two representations, 0000 and 1111, and the range is symmetric, from -7 to +7 on four bits. The RISC-V instruction not computes precisely the one's complement of a register, and the previous lecture showed that adding 1 to it yields the two's complement. UNDERSTAND NOW: one's complement and excess-k. For the lecturer: Also called diminished radix complement (complemento alla base diminuita). The bitwise not of RISC-V computes exactly this.

## Slide 4: Arithmetic in one's complement
No correction
3 +
-4 =
-1
0011 +
1011 =
1110
no carry out: the result is right
Two negatives
-2 +
-3 =
-5
1101 +
1100 =
1 1001 + 1 =
1010
carry out: add it back
Positive result
5 +
-2 =
3
0101 +
1101 =
1 0010 + 1 =
0011
carry out: add it back
The adder works modulo 2^n - 1: whenever there is a carry out of the most significant bit, 1 must be added to the result (end-around carry)
The correction is needed when both operands are negative, or when the operands have opposite signs and the sum is positive
An adder and a complementer are still enough, but the extra step and the double zero made two's complement win
UNDERSTAND NOW · one's complement and excess-k
Notes: Addition in one's complement uses an ordinary binary adder with one correction: when a carry leaves the most significant position, 1 must be added to the result, an operation known as the end-around carry. The first example requires no correction; in the second and third the outgoing carry is brought round and added. This extra step, together with the double zero, explains why two's complement, in which the outgoing carry is simply discarded, prevailed in the design of arithmetic units. UNDERSTAND NOW: one's complement and excess-k. For the lecturer: The source slides call the carry an 'overflow in the arithmetic of positive integers': it is the carry out of the natural-number adder, reinterpreted as the need for a correction.

## Slide 5: Excess-k (biased) representation
Every number is shifted upward by a constant k: X = x + k, typically k = 2^(n-1)
The order is preserved: if x1 > x2 then X1 > X2, so signed numbers compare as naturals
A sum must be corrected by subtracting k; multiplication and division are much more awkward than with complements
Preferred where only additions and comparisons are needed
It is the encoding of the exponent in floating-point numbers
X = x + k
on four bits with k = 8: the pattern 0000 means -8, 1000 means 0, 1111 means +7
UNDERSTAND NOW · one's complement and excess-k
Notes: In excess-k representation every number is displaced upwards by a constant: X = x + k. With four bits and k = 8, the pattern 0000 denotes -8, 1000 denotes zero and 1111 denotes +7. Its valuable property is order preservation: a larger number always has a larger pattern, so two signed values can be compared as though they were natural numbers. Arithmetic is less convenient, since every sum must be corrected by subtracting k. This is precisely the encoding of the exponent in floating-point formats, where fast comparison matters more than convenient addition. UNDERSTAND NOW: one's complement and excess-k. For the lecturer: Excess-8 on four bits: 0000 = -8, 1000 = 0, 1111 = +7. Compare with two's complement: the same range, with the most significant bit inverted.

## Slide 6: Four bits, five readings
Bits | Unsig. | Sign-m. | 1's c. | 2's c. | Exc.-8
0000 | 0 | +0 | +0 | 0 | -8
0001 | 1 | +1 | +1 | +1 | -7
0010 | 2 | +2 | +2 | +2 | -6
0011 | 3 | +3 | +3 | +3 | -5
0100 | 4 | +4 | +4 | +4 | -4
0101 | 5 | +5 | +5 | +5 | -3
0110 | 6 | +6 | +6 | +6 | -2
0111 | 7 | +7 | +7 | +7 | -1
Bits | Unsig. | Sign-m. | 1's c. | 2's c. | Exc.-8
1000 | 8 | -0 | -7 | -8 | 0
1001 | 9 | -1 | -6 | -7 | +1
1010 | 10 | -2 | -5 | -6 | +2
1011 | 11 | -3 | -4 | -5 | +3
1100 | 12 | -4 | -3 | -4 | +4
1101 | 13 | -5 | -2 | -3 | +5
1110 | 14 | -6 | -1 | -2 | +6
1111 | 15 | -7 | -0 | -1 | +7
Sign and magnitude and one's complement have two zeros (highlighted): 0000 and 1000, or 0000 and 1111
Two's complement and excess-8 cover the same range, -8 to +7, with a single zero
Only excess-k keeps the patterns in the same order as the numbers
UNDERSTAND NOW · one's complement and excess-k
Notes: The table of Lecture 05, extended by two columns: the same sixteen patterns read as unsigned, sign and magnitude, one's complement, two's complement and excess-8. Three observations. Sign and magnitude and one's complement each have two zeros, highlighted. Two's complement and excess-8 cover the same range, -8 to +7, and differ only in the leftmost bit. And excess-8 is the only column in which values increase monotonically from the top of the table to the bottom, which is the order-preservation property in visual form. UNDERSTAND NOW: one's complement and excess-k. For the lecturer: This table replaces the comparison picture of the source deck ('Numeri relativi: complementi').

## Slide 7: Numbers in fixed point
The integer part and the fractional part are stored side by side in one word
The position of the point is fixed and implicit: it is not stored, the program knows it
With f fractional bits the stored integer is X = x times 2^f, and the resolution is 2^-f
Each part uses one of the representations already seen: usually the whole word is two's complement
Notation Qm.f: m integer bits and f fractional bits, for example Q24.8
X = x 2^f
store the number multiplied by a power of two; shift right by f bits to get back the integer part
UNDERSTAND NOW · fixed point
Notes: In fixed point the integer and fractional parts occupy adjacent positions within one word, and the position of the binary point is fixed. It is stored nowhere: it is a convention known to the program. If f bits are reserved for the fraction, the word contains the number multiplied by 2^f, and the smallest representable increment, the resolution, is 2^-f. The notation Qm.f specifies the division of the bits: Q24.8 denotes 24 integer bits and 8 fractional bits. Arithmetic is ordinary integer arithmetic, with rescaling only where a product or quotient requires it. UNDERSTAND NOW: fixed point. For the lecturer: Fixed point is how games, audio and control software handle fractions on processors without a floating-point unit. It is also how money should be stored: integer cents.

## Slide 8: Rational numbers: the approximation error
The reals are dense: even in a limited interval, not every number can be represented
Approximation: each number is associated with the nearest representable one
– in Q24.8, 0.1 becomes 26/256 = 0.1015625: an error of about 1.6%
The approximation error is at most half of the resolution: 1/512 for eight fractional bits
Underflow: a number close to zero, but not zero, is represented by zero
In fixed point the absolute error is the same everywhere on the number line
1/256
the resolution of eight fractional bits: nothing smaller can be told apart from zero
UNDERSTAND NOW · fixed point
Notes: The real numbers are dense: between any two there are infinitely many others, so with a finite number of bits most of them cannot be represented, and each is replaced by its nearest representable neighbour. In Q24.8 the number 0.1 becomes 26/256, approximately 0.1016. The error never exceeds half the resolution. A value sufficiently close to zero rounds to zero, which is underflow, and which is why a speed of 0.001 pixels per frame would leave the ball motionless. In fixed point the absolute error bound is the same across the whole range. UNDERSTAND NOW: fixed point. For the lecturer: 0.1 x 256 = 25.6, rounded to 26. With SPEED_Q8 = 1 the ball moves 1/256 pixel per frame; a speed of 0.001 pixel per frame underflows to zero and the ball never moves.

## Slide 9: Real numbers in floating point
A real number x is represented by a pair (m, e) such that x = m times b^e
m is the mantissa, e the exponent, b the base
– the point floats: the exponent says where it is
Infinitely many pairs represent the same number
– 346.09801 = (346.09801, 0) = (346098.01, -3) = (0.034609801, 4)
Normalisation chooses a single representative
– the point goes right after the first significant digit: (3.4609801, 2)
x = m b^e
mantissa, base and exponent: the scientific notation of the laboratory, in binary
UNDERSTAND NOW · IEEE 754 floating point
Notes: A real number is represented as a pair: a mantissa m and an exponent e, such that x equals m multiplied by the base raised to e. This is the scientific notation of the physics laboratory, and the point "floats" because the exponent determines its position. Since the same number admits infinitely many such pairs, a canonical one is selected by normalisation: the point is placed immediately after the first significant digit, so 346.09801 becomes 3.4609801 with exponent 2. Normalisation guarantees uniqueness and maximises the number of significant digits retained. UNDERSTAND NOW: IEEE 754 floating point. For the lecturer: Scientific notation, in other words. Fixed point spends its bits on a fixed range; floating point spends some bits to say where the range is.

## Slide 10: Approximation: absolute and relative error
The absolute error is not constant: precision is very fine near zero and decreases as numbers grow
Near zero the maximum error is 0.001 x 10^-99
– 1.001 x 10^-99 minus 1.000 x 10^-99
Near the upper limit the maximum error is 0.001 x 10^99
– 9.999 x 10^99 minus 9.998 x 10^99
Absolute error: small on small numbers, large on large numbers
Relative error: constant along the whole axis
4 digits
the same number of significant digits everywhere: constant relative error, whatever the size of the number
UNDERSTAND NOW · IEEE 754 floating point
Notes: In floating point the spacing between consecutive representable numbers is not uniform: it is very fine near zero and coarse near the upper limit of the range. The absolute error therefore grows with the magnitude of the number. What remains approximately constant is the relative error, because every number carries the same number of significant digits, four in this example. Fixed point exhibits the opposite behaviour: constant absolute error, with relative error that becomes large near zero. The choice between the two is a choice of which error matters for the application. UNDERSTAND NOW: IEEE 754 floating point. For the lecturer: This is the opposite of fixed point, where the absolute error is constant and the relative error explodes near zero.

## Slide 11: IEEE 754 single precision: 32 bits
S
sign
1 = negative
31
E
exponent: 8 bits
excess-127
30
23
F
fraction: 23 bits
magnitude, after the hidden 1
22
0
value = (-1)^S x 1.F x 2^(E - 127)
The mantissa is in sign and magnitude: one sign bit and 23 bits of magnitude
A normalised binary mantissa always starts with 1: that bit is hidden, not stored, and one bit of precision is gained
The exponent is in excess-127, not 128: the true exponents go from -126 to +127
The patterns E = 0 and E = 255 are reserved: zero and denormalised numbers, infinity and NaN
UNDERSTAND NOW · IEEE 754 floating point
Notes: The IEEE 754 single-precision format divides 32 bits into three fields: one sign bit, eight exponent bits and twenty-three fraction bits, with the value given by the formula in the centre. Two design decisions deserve attention. A normalised binary mantissa always begins with 1, so that bit need not be stored: it is the hidden bit, which yields one additional bit of precision at no cost. And the exponent is stored in excess-127, the encoding of the previous section, so that floating-point numbers of the same sign can be compared as natural numbers. UNDERSTAND NOW: IEEE 754 floating point. For the lecturer: IEEE 754 dates from 1985 (revised 2008 and 2019). Before it, every manufacturer had its own format and programs gave different results on different machines.

## Slide 12: Worked example: -5.125 in IEEE 754
1
Convert the two parts: 5 = 101 and 0.125 = 1/8 = 0.001, so 5.125 = 101.001
2
Normalise: 101.001 = 1.01001 x 2^2
3
Sign S = 1; exponent E = 2 + 127 = 129 = 1000 0001
4
Fraction F = 01001 followed by zeros: the leading 1 is hidden
1
31
1000 0001
30
23
0100 1000 0000 0000 0000 000
22
0
1100 0000 1010 0100 0000 0000 0000 0000 = 0xC0A40000
UNDERSTAND NOW · IEEE 754 floating point
Notes: A complete worked example: -5.125. The integer and fractional parts are converted separately: 5 is 101 and 0.125 is 0.001, so the number is 101.001. Normalisation moves the point two places: 1.01001 times 2^2. The sign bit is 1. The exponent field is 2 + 127 = 129, that is, 1000 0001. The fraction field is 01001 followed by zeros, without the leading 1. Concatenating the three fields and regrouping by four bits gives 0xC0A40000. The example should be reproduced on paper and then repeated with a number of one's own choosing. UNDERSTAND NOW: IEEE 754 floating point. For the lecturer: Check the regrouping in nibbles: 1100 = C, 0000 = 0, 1010 = A, 0100 = 4, then zeros. Three slides of the source deck are merged here.

## Slide 13: IEEE 754 at a glance
 | Single precision | Double precision
Total bits | 32 | 64
Sign bits | 1 | 1
Exponent bits | 8 | 11
Fraction bits | 23 | 52
Exponent encoding | excess-127 | excess-1023
Exponent range | -126 ... +127 | -1022 ... +1023
Smallest normalised | 2^-126, about 1.2 x 10^-38 | 2^-1022, about 2.2 x 10^-308
Largest | about 2^128, 3.4 x 10^38 | about 2^1024, 1.8 x 10^308
Smallest denormalised | about 1.4 x 10^-45 | about 4.9 x 10^-324
Decimal digits | about 7 | about 16
UNDERSTAND NOW · IEEE 754 floating point
Notes: Single and double precision compared. Double precision uses 64 bits, with 11 exponent bits in excess-1023 and 52 fraction bits. Two rows are worth retaining as orders of magnitude: single precision provides about 7 significant decimal digits and a range reaching about 10^38; double precision about 16 digits and a range reaching about 10^308. The C types float and double correspond to these two formats on essentially every modern platform. UNDERSTAND NOW: IEEE 754 floating point. For the lecturer: Corrections to the source table: the double-precision exponent is in excess-1023 (not 1024), and the decimal ranges are about 10^38 and 10^308.

## Slide 14: IEEE 754: what the patterns mean
Kind | Sign | Exponent E | Fraction F | Value
Normalised | 0 or 1 | 0 < E < max | any pattern | (-1)^S x 1.F x 2^(E-bias)
Denormalised | 0 or 1 | all zeros | not zero | (-1)^S x 0.F x 2^(1-bias)
Zero | 0 or 1 | all zeros | all zeros | +0 or -0
Infinity | 0 or 1 | all ones | all zeros | +infinity or -infinity
Not a Number | 0 or 1 | all ones | not zero | NaN: an invalid result
UNDERSTAND NOW · IEEE 754 floating point
Notes: Not every pattern encodes an ordinary number. An exponent field strictly between its extremes denotes a normalised number. An exponent of all zeros denotes zero, if the fraction is also zero, or a denormalised number, which fills the gap around zero with gradually decreasing precision. An exponent of all ones denotes infinity, if the fraction is zero, or NaN, "not a number", the result of an invalid operation such as zero divided by zero. Two consequences are counter-intuitive and worth noting: there are two zeros, positive and negative, and NaN compares unequal to everything, itself included. UNDERSTAND NOW: IEEE 754 floating point. For the lecturer: Denormalised (subnormal) numbers fill the underflow gap around zero with gradually decreasing precision. 1/0 gives infinity; 0/0 and the square root of -1 give NaN. NaN is not equal to anything, itself included.

## Slide 15: Floating point on RISC-V, and on your kit
RISC-V with the F and D extensions
Thirty-two more registers, f0 to f31, for floating-point values
Instructions such as fadd.s, fmul.s, flw and fsw work on IEEE 754 numbers
fcvt.w.s converts to an integer, fcvt.s.w from an integer
Found on RISC-V processors for laptops, servers and supercomputers
The ESP32-C6: RV32IMAC
No F and no D: there are no floating-point instructions at all
A C program can still use float: the compiler calls software routines such as __addsf3
Each call costs tens to hundreds of integer instructions
PRG32 games use integers and fixed point: fast, exact enough, and visible in the debugger
UNDERSTAND NOW · IEEE 754 floating point
Notes: RISC-V supports floating point through two optional extensions, F for single precision and D for double, which add thirty-two registers, f0 to f31, and instructions such as fadd.s. The processor of the kit, RV32IMAC, implements neither. A C program may still use float, but each operation is then compiled into a call to a software routine costing tens or hundreds of integer instructions. This is why PRG32 games use integers and fixed point: they are fast, sufficiently precise for the purpose, and transparent in the debugger. UNDERSTAND NOW: IEEE 754 floating point. For the lecturer: The software routines implement exactly the algorithm of this lecture with shifts, masks and integer additions: a good reading exercise for the end of the course.

## Slide 16: Reading the name RV32IMAC
Letter | Extension | What it adds | On the ESP32-C6
RV32I | base integer set | 32-bit registers, add, logic, load and store, branches | yes
M | multiply and divide | mul, mulh, div, rem and their unsigned forms | yes
A | atomic | instructions for safe sharing between tasks | yes
C | compressed | 16-bit encodings of the most common instructions | yes
F | single precision | f0 to f31 and IEEE 754 single-precision instructions | no
D | double precision | IEEE 754 double-precision instructions | no
UNDERSTAND NOW · the name RV32IMAC
Notes: The name RV32IMAC can now be read letter by letter. RV32I is the base: 32-bit registers and the integer instructions. M adds multiplication and division. A adds atomic instructions, for safe sharing of data among concurrent tasks. C adds compressed, 16-bit encodings of the most frequent instructions. F and D, the floating-point extensions, are absent. This modularity is a central design principle of RISC-V: a small mandatory base and optional extensions, so that the same architecture can serve an inexpensive microcontroller and a supercomputer. UNDERSTAND NOW: the name RV32IMAC. For the lecturer: RISC-V is modular: a small mandatory base plus optional extensions. A microcontroller picks what it needs; this is one reason the same architecture scales from a two-euro chip to a supercomputer.

## Slide 17: Check your understanding
1
Which signed encoding keeps the bit patterns in the same order as the numbers?
A
Sign and magnitude
B
One's complement
C
Two's complement
D
Excess-k
2
In Q24.8 fixed point, which real number does the word 0x00000180 represent?
A
384
B
1.5
C
1.8
D
0.375
Notes: For the first question, one should consider what each encoding does to ordering. In sign and magnitude and in both complements, negative numbers have a leftmost 1 and therefore, read as patterns, follow the positive ones. Only an encoding that adds a constant to every number preserves the order. For the second, Q24.8 means that the word contains the number multiplied by 256. 0x180 is read as an integer and divided by 256; alternatively it is split directly into integer part 0x01 and fraction 0x80, that is, 128/256. For the lecturer: 1. Answer: D. In excess-k, X = x + k: a larger number always has a larger pattern. This is why it encodes floating-point exponents, which must be compared quickly. 2. Answer: B. 0x180 = 384; 384 / 256 = 1.5. Integer part 0x01, fraction 0x80 = 128/256 = 0.5.

## Slide 18: Check your understanding
1
Which real number is the IEEE 754 single-precision pattern 0x40400000?
A
2.0
B
3.0
C
4.0
D
0.75
2
In IEEE 754, an exponent field of all ones with a fraction of all zeros means:
A
zero
B
a denormalised number
C
infinity
D
NaN
Notes: For the first question, the leading hexadecimal digits are written in binary and the fields separated: one sign bit, eight exponent bits, then the fraction. The bias of 127 is subtracted from the exponent, and the hidden 1 restored in front of the fraction. For the second, the table of special patterns should be consulted. An exponent of all ones is reserved; the question is which of its two cases has a fraction of all zeros. For the lecturer: 1. Answer: B. 0100 0000 0100 0000 ...: S = 0, E = 1000 0000 = 128, F = 100...: 1.1 (binary) x 2^(128-127) = 1.5 x 2 = 3.0. 2. Answer: C. All ones in the exponent: infinity if the fraction is zero, NaN otherwise.

## Slide 19: Glossary: English and Italian
English | Italiano | English | Italiano
one's complement | complemento a uno (alla base diminuita) | mantissa / fraction | mantissa
excess-k (biased) | eccesso-k | exponent | esponente
fixed point | virgola fissa | normalisation | normalizzazione
floating point | virgola mobile | hidden bit | bit nascosto
single / double precision | singola / doppia precisione | denormalised | denormalizzato
rounding | arrotondamento | Not a Number (NaN) | non un numero (NaN)
Notes: Twelve terms. In Italian the decimal separator is the comma, so fixed point and floating point become virgola fissa and virgola mobile. Mantissa is the traditional term for the significant digits; the standard calls the stored part the fraction. The hidden bit is the leading 1 that is not stored. Denormalised numbers are also termed subnormal.

## Slide 20: Conclusions and reading
Integers have several representations: 8, 16, 32 or 64 bits, signed or unsigned, complements or excess
Fixed point stores a fraction as a scaled integer: constant absolute error, integer speed
Floating point stores mantissa and exponent: huge range, constant relative error
IEEE 754 is the universal standard for floating point, with special patterns for zero, infinity and NaN
On a processor without the F extension, fixed point is the natural choice
Reading
– Patterson, Hennessy: Computer Organization and Design, RISC-V Edition, section 3.5
– David Goldberg: What Every Computer Scientist Should Know About Floating-Point Arithmetic
– Playing with RISC-V, appendix: The PRG32 Runtime Interface (playfields and parallax)
Notes: Five conclusions. Integers admit several representations, chosen according to use. Fixed point stores a fraction as a scaled integer, with constant absolute error and the speed of integer arithmetic. Floating point stores mantissa and exponent, with an enormous range and approximately constant relative error. IEEE 754 is the universal standard, with special patterns for zero, infinity and NaN. On a processor lacking the F extension, fixed point is the natural choice. The next lecture is the first part of Verm1, in which the content of the last four lectures is put to work. Learning status, recap. UNDERSTAND NOW: fixed point; one's complement and excess-k; IEEE 754 floating point; the name RV32IMAC. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise. Closing thread: Without an F extension, fractions are integers with an agreed scale: Verm1 will move its head by fractions of a cell exactly this way. Next: the first part of the project. Exit ticket (two to four minutes, alone, on paper): 1. Read RV32IMAC letter by letter. A student writes fmul.s in a cartridge for the kit: what happens, and why does Verm1 move with fixed-point numbers? 2. In Q24.8, which real number does the word 0x00000180 represent? How do you add two Q24.8 numbers, and how do you multiply them? For the lecturer: Next: Verm1, part 1, where the first four lectures go to work in a real program. Then Boolean algebra.