## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 07
Verm1, Part 1: A Head That Crosses the World: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Verm1 reference implementation contributed by Giuseppe Coviello
Code deck. The concepts, the figures and the questions are in the lecture deck:
07-Computer_Architecture-Verm1_Part_1.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 07. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: the Verm1 project; the init, update, draw contract; a colour is a number; arrays in memory; .text, .rodata, .data; address, value, load, store; why ra is saved; shifts as multiplications; fixed point; pseudo-instructions; little-endian byte order. USE NOW: the PRG32 tools, the PRG32-QT debugger (used, not studied, in this course). UNDERSTAND LATER: instruction formats (Lecture 19). A slide without a badge is context: a story, an example, a question, an exercise. Roadmap. Today's outcomes: (1) build a cartridge from an empty file: a grid, a title and a moving head; (2) place constants and variables in the right section, .rodata or .data; (3) control a speed with a fixed-point accumulator. Builds on: the init, update, draw contract (Lecture 02); a colour is a number (Lecture 04); arrays in memory (Lecture 04); address, value, load, store (Lecture 02); why ra is saved (Lecture 02). Next: Lecture 08, Elements of Boolean Algebra. Bridge. In Lecture 02 step 2 saved ra on the stack before its calls, and lw t1, 0(t0) read a word at the address in t0. Today verm1_draw saves ra and verm1_update does not, and every variable of Verm1 is read with la and lw. Lecture 18 explains the stack and the calling convention; Lecture 19 names the addressing modes. Recall: Why does verm1_draw save ra while verm1_update does not?

## Slide 2: In this deck
1
The 8 listings of Lecture 07, one per slide: read the code, then the numbered remarks beside it
2
The program is your verm1.S; the reference is verm1/verm1_part1.S, 78 lines, shown here region by region
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The reference program is ~/arc12/verm1/verm1_part1.S; tools/tests/verm1_check.py builds it and plays it with a scripted player, and verm1_steps.py runs the intermediate checkpoints. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The reference program is ~/arc12/verm1/verm1_part1.S; tools/tests/verm1_check.py builds it and plays it with a scripted player, and verm1_steps.py runs the intermediate checkpoints. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Build and run
# 1. build the cartridge (from your PRG32 folder, toolchain active)
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --out ~/verm1/verm1.prg32
# 2. send it to PRG32-QT, running on the same computer
python3 -m prg32 esp32c6 upload-and-run ~/verm1/verm1.prg32 \
--url http://localhost:8080 --slot cart0
# or: in PRG32-QT, import the file verm1.prg32 and choose Run Cartridge
USE NOW · the PRG32 tools
Notes: A folder named verm1 is created in the home directory, and in it a single file, verm1.S, which will grow from part to part. The first command builds the cartridge; the second sends it to PRG32-QT, running on the same computer, and starts it. These two commands are identical in every tutorial, which is the point: the cost of trying an idea must be negligible. If localhost does not answer, the address shown on the Setup screen of PRG32-QT is used instead; alternatively, the file can be imported from the PRG32-QT menu. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Make a folder ~/verm1 and keep one file in it, verm1.S, that grows from part to part. PRG32-QT listens on port 8080 and shows its address on the Setup screen: use that address if localhost does not answer. The same cartridge runs on QEMU (python3 -m prg32 qemu upload, then qemu run) and on the board (--url http://192.168.4.1).

## Slide 4: Step 1: three functions that return
# verm1.S - my Verm1
.option norelax
.section .text
.global verm1_init
.global verm1_update
.global verm1_draw
verm1_init:
ret
verm1_update:
ret
verm1_draw:
ret
1
Type it, build it, run it: a black screen is the right answer
2
The prefix verm1 is the name you pass to --entry-prefix
3
init runs once; update and draw run once per frame
4
From now on: add one thing, run, look. Never two things at once
UNDERSTAND NOW · the init, update, draw contract
Notes: Step 1 is the skeleton of Lecture 02 with the prefix verm1: three global labels and three functions that merely return. It is typed, built and run. The correct result is a black screen, which demonstrates that the tools work and that the firmware locates the three entry points. A build failure at this stage indicates a problem with the installation, not with the program, and must be resolved before proceeding. The last callout states the methodological rule of the entire project: add one thing, run, observe; never two things at once, so that every failure has a single candidate cause. UNDERSTAND NOW: the init, update, draw contract. For the lecturer: The skeleton of Lecture 02. If the build fails here the problem is the installation, not the program: solve it before going on.

## Slide 5: Constants: colours and the grid
.option norelax
.equ BLACK, 0x0000 # RGB565 colours
.equ WHITE, 0xffff
.equ GREEN, 0x07e0
.equ CELL, 8 # a cell is 8 x 8 pixels
.equ COLS, 40 # 320 / 8 cells across
.equ ROWS, 24 # 192 / 8 cells down
.equ TOP, 8 # the top 8 pixels are the title line
.equ SPEED_Q8, 40 # 40/256 of a cell per frame (Q24.8)
.section .text
.global verm1_init
.global verm1_update
.global verm1_draw
1
Colours are RGB565 numbers: 0x07e0 is pure green
2
320 pixels across, 8 per cell: 40 columns
3
The top 8 pixels hold the title; 192 are left: 24 rows
4
.equ gives a name to a number: no memory is used
UNDERSTAND NOW · a colour is a number
Notes: These lines replace the beginning of the skeleton. Each .equ binds a name to a number and occupies no memory: the assembler merely substitutes the value wherever the name appears. Three colours are defined in RGB565. Then the geometry: a cell measures 8 by 8 pixels, so the 320-pixel width holds 40 columns; the top 8 pixels are reserved for the title, and the remaining 192 hold 24 rows. SPEED_Q8, the speed in fixed point, is used in step 3. Named constants make the program legible and its parameters easy to change in one place. UNDERSTAND NOW: a colour is a number. For the lecturer: Replace the skeleton's first lines with these. SPEED_Q8 is used in step 3.

## Slide 6: Variables and a string
.section .rodata
title: .asciz "VERM1"
.section .data
head_x: .word 5 # column of the head, 0 .. COLS-1
head_y: .word 12 # row of the head, 0 .. ROWS-1
step_q8: .word 0 # fraction of a step, in 1/256
1
.rodata holds constants: the title ends with a zero byte
2
.data holds variables: one 32-bit word each
3
The initial values are only a start: init will set them again
UNDERSTAND NOW · .text, .rodata, .data
Notes: This block is placed at the end of the file. The .rodata section holds what never changes: the title, a string terminated by a zero byte through .asciz. The .data section holds the variables, one 32-bit word each: the column of the head, its row, and the fraction of a step accumulated so far. The initial values written here are only a starting point; init assigns them again explicitly, for a reason given on the next slide. UNDERSTAND NOW: .text, .rodata, .data. For the lecturer: Put this at the end of the file. step_q8 is used in step 3.

## Slide 7: init: put the head in its place
verm1_init:
la t0, head_x
li t1, 5
sw t1, 0(t0) # the head starts in column 5 ...
la t0, head_y
li t1, 12
sw t1, 0(t0) # ... of row 12
la t0, step_q8
sw zero, 0(t0) # no fraction of a step yet
ret
1
la takes an ADDRESS, sw stores a VALUE there
2
init sets the start explicitly: never trust what memory contained
3
zero is the register that always reads 0
4
A leaf function: no calls, so no stack frame
UNDERSTAND NOW · address, value, load, store
Notes: verm1_init places the head in its starting position. For each variable the pattern is identical: la loads the address, li the value, and sw stores the value at the address. The accumulator step_q8 is cleared by storing the register zero directly. The function calls nothing, so it is a leaf and requires no stack frame. Why assign values that .data already contains? Because init may be invoked again to restart the game; the general principle is never to rely on the prior content of memory. UNDERSTAND NOW: address, value, load, store.

## Slide 8: draw: title and head
verm1_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, BLACK
call prg32_gfx_clear
li a0, 0 # x
li a1, 0 # y
la a2, title # address of the string
li a3, WHITE
li a4, BLACK
call prg32_gfx_text8
la t0, head_x
lw a0, 0(t0)
slli a0, a0, 3 # x = column * 8
la t0, head_y
lw a1, 0(t0)
slli a1, a1, 3
addi a1, a1, TOP # y = row * 8 + 8
li a2, CELL # width
li a3, CELL # height
li a4, GREEN
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Clear, write the title, draw one rectangle: three calls
2
Arguments travel in a0 to a4, in order
3
slli by 3 multiplies by 8: cell to pixel
4
draw makes calls, so it saves ra in a stack frame
UNDERSTAND NOW · why ra is saved
Notes: verm1_draw makes three calls: clear the screen, write the title, draw the head. It therefore saves ra in a stack frame on entry and restores it on exit, as in Lecture 02. The conversion from cell to pixels deserves attention: the column is loaded into a0 and shifted left by 3; the row is loaded into a1, shifted, and offset by TOP. The remaining arguments are width, height and colour. Arguments are passed in a0 to a4, in the order the callee expects them. UNDERSTAND NOW: why ra is saved; shifts as multiplications. For the lecturer: prg32_gfx_text8(x, y, string, foreground, background); prg32_gfx_rect(x, y, width, height, colour).

## Slide 9: Run it: a head on the grid
The title and the head. After step 3 the head will be moving: this picture was taken 64 frames into the finished Part 1
Expected now: the word VERM1 at the top left and a green square standing still in column 5, row 12.
Notes: Build and run. The word VERM1 should appear at the top left, and a stationary green square in column 5 of row 12. The screenshot on the slide was taken from the finished Part 1, so its head lies further to the right; the difference is expected. If the square is misplaced, the two shifts and the addition of TOP are the first things to check. For the lecturer: Screenshot produced by tools/tests/verm1_check.py from verm1/verm1_part1.S.

## Slide 10: update: accumulate, step, wrap
verm1_update:
la t0, step_q8
lw t1, 0(t0)
addi t1, t1, SPEED_Q8 # add a fraction of a cell
li t2, 256
blt t1, t2, 2f # less than one whole cell: wait
sub t1, t1, t2 # one cell done: keep the remainder
sw t1, 0(t0)
la t0, head_x
lw t3, 0(t0)
addi t3, t3, 1 # one cell to the right
li t4, COLS
blt t3, t4, 1f
li t3, 0 # past the right edge: back to column 0
1: sw t3, 0(t0)
ret
2: sw t1, 0(t0)
ret
1
Add the speed to the fraction; below 256, wait
2
At 256: subtract it, keep the rest, move one cell
3
Column 40 does not exist: back to column 0
4
Two exits: each stores what it changed
UNDERSTAND NOW · fixed point
Notes: verm1_update is best read in two halves. First the timer: step_q8 is loaded, the speed added, and the sum compared with 256. If it is smaller, control jumps to label 2, the accumulator is stored and the function returns: nothing moves in this frame. Otherwise 256 is subtracted, the remainder kept and stored. Then the step: head_x is loaded and incremented, and compared with COLS; if the column has reached 40 it is reset to 0, so the head re-enters from the left. The labels 1: and 2: are local labels, and 1f denotes "the next label 1, searching forward". UNDERSTAND NOW: fixed point. For the lecturer: blt compares signed numbers, which is right here: every value is small and positive. Local labels 1: and 2: are referred to as 1f and 2f, 'the next 1 or 2 forward'.

## Slide 11: Run it: the head crosses the world
TRY IT
1
Build and run: the head moves to the right, about five cells per second
2
Wait for the right edge: the head leaves at column 39 and returns at column 0
3
Change SPEED_Q8 to 8, then to 128, then to 256: predict the speed before you run
4
Change the starting row in init and the colour of the head
Expected result
The head crosses the forty columns in 256 frames, about eight and a half seconds at thirty frames per second, for ever.
Notes: Run it. The head moves to the right at about five cells per second, leaves at column 39 and reappears at column 0. The speed should then be varied, predicting the outcome before each run: with 8 the head is slow; with 128 it steps every two frames; with 256, once per frame. A larger value exposes a limitation of this program: update takes at most one step per frame, so speeds above 256 saturate. Discovering such a limit by prediction and experiment is exactly the habit the course aims to form. For the lecturer: With SPEED_Q8 = 256 the head moves one cell per frame; larger values still give one step per frame, because update takes at most one step: a limit worth discovering.

## Slide 12: What the listing shows: your code, as the assembler left it
verm1_update:
auipc t0, 0x0 # la t0, step_q8 is two instructions:
addi t0, t0, ... # t0 = address of step_q8
lw t1, 0(t0)
addi t1, t1, 40 # SPEED_Q8 is gone: only the number is left
addi t2, zero, 256 # li t2, 256
blt t1, t2, ...
sub t1, t1, t2
sw t1, 0(t0)
...
c.addi t3, 1 # addi t3, t3, 1 in a 16-bit form
...
c.jr ra # ret
1
Names are gone: labels became addresses, constants became numbers
2
Pseudo-instructions are expanded: la is auipc plus addi, li is addi from zero, ret is a jump to ra
3
Some instructions start with c.: the compressed 16-bit forms of the same instructions
4
The cartridge is loaded at address 0x40800000: every address you see starts there
UNDERSTAND LATER · instruction formats → Lecture 19
UNDERSTAND NOW · pseudo-instructions
Notes: The debugger does not display the source but what the assembler produced from it. Symbolic names have disappeared: labels have become addresses, and SPEED_Q8 has become the number 40. Pseudo-instructions have been expanded: la into auipc followed by addi, li into an addi from zero, ret into a jump through ra. Some instructions bear the prefix c.: these are the compressed 16-bit encodings of the same operations, the C of RV32IMAC. Recognising one's own program in this listing is a skill acquired with practice; the instruction formats behind it are studied in Lecture 19. UNDERSTAND NOW: pseudo-instructions. UNDERSTAND LATER: instruction formats (studied in Lecture 19). For the lecturer: Disassembly of verm1_update from verm1/verm1_part1.S (objdump, rv32imac), abridged; the exact offsets depend on the build. Instruction formats are the subject of Lecture 19; the compressed forms are only named there, and listed in Appendix A of the textbook.

## Slide 13: Run it: what you should see
On the screen
– the word VERM1 at the top left and a green head that crosses the grid from left to right, about five cells per second, and comes back in from column 0.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 14: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --out verm1.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run verm1.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 15: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --architecture qemu \
--out verm1-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload verm1-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 16: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --architecture esp32c6 \
--out verm1-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run verm1-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 17: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix verm1; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 18: Make it yours
TRY IT
1
Make the head move to the left: which instruction changes, and which comparison detects the edge?
2
Make it move downwards instead, wrapping from row 23 to row 0
3
Draw a second cell, in a darker green, one column behind the head: a first hint of a body
4
Write your own name next to the title, in a colour you computed by hand in RGB565
Expected result
Each change is a few lines. Keep a copy of the working Part 1 before you experiment: Part 2 starts from it.
Notes: Four modifications that make the program the student's own, each requiring a few lines. Make the head move leftwards: the addition becomes a subtraction, and the edge is detected from the sign of the result. Make it move downwards. Draw a second, darker cell behind the head. Write one's name beside the title, in a colour computed by hand. Before experimenting, a copy of the working Part 1 should be kept, since Part 2 starts from it. For the lecturer: Moving left: addi t3, t3, -1, then bgez t3 to skip the wrap, else li t3, COLS-1. The comparison is on the sign: Lecture 05. Darker green: 0x03e0.