## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 09
Elements of Boolean Algebra: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
09-Computer_Architecture-Boolean_Algebra_2.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 09. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: the adder; Boolean functions; canonical forms; minimisation, Karnaugh maps. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise. Roadmap. Today's outcomes: (1) write a function in canonical form from its truth table; (2) minimise a function of up to four variables with a Karnaugh map; (3) build a full adder and chain it into an n-bit adder. Builds on: only what Lecture 01 set up. Next: Lecture 10, Introduction to Electronics and Digital Electronics.

## Slide 2: In this deck
1
The 2 listings of Lecture 09, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l09.S, 107 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The program of this lecture is ~/arc12/code/l09.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l09.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: One-bit addition without add
# a0 and a1 hold one bit each: 0 or 1
# goal: compute a0 + a1, which needs two bits (0, 1 or 2)
xor t0, a0, a1 # low bit of the sum: 1 when the bits differ
and t1, a0, a1 # high bit, the carry: 1 when both are 1
# a0 a1 | t1 t0
# 0 0 | 0 0 0 + 0 = 0
# 0 1 | 0 1 0 + 1 = 1
# 1 0 | 0 1 1 + 0 = 1
# 1 1 | 1 0 1 + 1 = 2 (binary 10)
1
Two logic instructions add two bits: no arithmetic involved
2
The comment is a truth table with two outputs
3
This pair of gates is called a half adder
4
How do you find the gates when the table is given? That is today's method
UNDERSTAND NOW · the adder
Notes: The warm-up. The sum of two bits can be 0, 1 or 2, so the result requires two bits. xor produces the low bit, which is 1 when the inputs differ; and produces the high bit, the carry, which is 1 only when both inputs are 1. The comment beneath the code is a truth table with two outputs, whose four rows should be verified. This pair of gates has a name, the half adder. The final callout states the problem of the lecture: here the gates were supplied; how are they found when only the table is known? UNDERSTAND NOW: the adder. For the lecturer: Run it in PRG32-QT with the four input pairs. Lecture 05 said that an adder is all a processor needs for arithmetic; this is its first bit.

## Slide 4: A full adder, one gate per instruction
# a0 = A, a1 = B, a2 = Cin (each 0 or 1)
# result: a3 = S, a4 = Cout
xor t0, a0, a1 # t0 = A xor B
xor a3, t0, a2 # S = A xor B xor Cin
and t1, a0, a1 # t1 = A . B
and t2, t0, a2 # t2 = (A xor B) . Cin
or a4, t1, t2 # Cout = A . B + (A xor B) . Cin
1
Five instructions, five gates: the program is the schematic, read from left to right
2
Analysis: single-step it in PRG32-QT and fill in the truth table
3
Synthesis: you derived these gates from the table with the method of this lecture
4
With whole registers as inputs, the same lines work on all thirty-two bit positions at once
UNDERSTAND NOW · the adder
Notes: The full adder written as five instructions, one per gate: two xor for the sum, two and and one or for the outgoing carry. The program is the schematic, read from left to right, and it allows both problems of Lecture 08 to be practised. Analysis: single-step it in PRG32-QT for the eight input combinations and fill in the truth table. Synthesis: derive these gates from the table with the method of the lecture. With whole registers as inputs, the same five lines operate on all thirty-two bit positions at once, though without propagating carries between them; propagation is what the ripple-carry chain adds. UNDERSTAND NOW: the adder. For the lecturer: Suggested laboratory activity: loop over the eight input combinations and draw the two output bits as lamps, as in lab 06.

## Slide 5: The complete program: l09.S (1 of 6)
# ARC12 Computer Architecture - Lecture 09: Elements of Boolean Algebra
# l09.S: a full adder, one gate per instruction, on its eight input combinations
#
# On the screen: eight rows, one per combination of A, B and Cin (000 at the top):
# three lamps for the inputs on the left, then S and Cout on the right. It is the
# truth table of the full adder.
# Build: python3 -m prg32 cartridge build l09.S --portable \
# --entry-prefix l09 --name l09 --out l09.prg32
.option norelax
.equ BLACK, 0x0000
.equ GREY, 0x4208
.equ YELLOW, 0xffe0
.equ CYAN, 0x07ff
.section .text
.global l09_init
.global l09_update
.global l09_draw
l09_init:
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l09.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 6: The complete program: l09.S (2 of 6)
l09_update:
ret
# full_adder: a0 = A, a1 = B, a2 = Cin (each 0 or 1); result: a3 = S, a4 = Cout
full_adder:
xor t0, a0, a1 # t0 = A xor B
xor a3, t0, a2 # S = A xor B xor Cin
and t1, a0, a1 # t1 = A . B
and t2, t0, a2 # t2 = (A xor B) . Cin
or a4, t1, t2 # Cout = A . B + (A xor B) . Cin
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l09.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: The complete program: l09.S (3 of 6)
# lamp: a0 = column, a1 = row, a2 = bit (0 or 1), a3 = colour when the bit is 1
lamp:
li a4, GREY
beqz a2, 1f
mv a4, a3
1: slli a0, a0, 5
addi a0, a0, 60 # x = 60 + 32 * column
slli a1, a1, 4
slli t0, a1, 1
srli a1, a1, 1
add a1, a1, t0 # 40 * row ...
srli a1, a1, 1 # ... / 2 = 20 * row
addi a1, a1, 20 # y = 20 + 20 * row
li a2, 24
li a3, 14
tail prg32_gfx_rect # a tail call: rect returns to our caller
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l09.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: The complete program: l09.S (4 of 6)
l09_draw:
addi sp, sp, -32
sw ra, 28(sp)
sw s0, 24(sp)
sw s1, 20(sp)
sw s2, 16(sp)
li a0, BLACK
call prg32_gfx_clear
li s0, 0 # row = the three inputs as a number, 0 to 7
1: srli a0, s0, 2
andi a0, a0, 1 # A = bit 2 of the row
srli a1, s0, 1
andi a1, a1, 1 # B = bit 1
andi a2, s0, 1 # Cin = bit 0
call full_adder
mv s1, a3 # keep S and Cout: they are in a registers,
mv s2, a4 # which the next calls destroy
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l09.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: The complete program: l09.S (5 of 6)
li a0, 0 # column 0: A
mv a1, s0
srli a2, s0, 2
andi a2, a2, 1
li a3, YELLOW
call lamp
li a0, 1 # column 1: B
mv a1, s0
srli a2, s0, 1
andi a2, a2, 1
li a3, YELLOW
call lamp
li a0, 2 # column 2: Cin
mv a1, s0
andi a2, s0, 1
li a3, YELLOW
call lamp
li a0, 4 # column 4: S
mv a1, s0
mv a2, s1
li a3, CYAN
call lamp
li a0, 5 # column 5: Cout
mv a1, s0
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l09.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 10: The complete program: l09.S (6 of 6)
mv a2, s2
li a3, CYAN
call lamp
addi s0, s0, 1
li t0, 8
blt s0, t0, 1b
lw s2, 16(sp)
lw s1, 20(sp)
lw s0, 24(sp)
lw ra, 28(sp)
addi sp, sp, 32
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l09.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 11: Run it: what you should see
On the screen
– eight rows, one per combination of A, B and Cin (000 at the top): three lamps for the inputs on the left, then S and Cout on the right. It is the truth table of the full adder.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 12: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l09.S --portable \
--entry-prefix l09 --name l09 --out l09.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l09.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 13: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l09.S --portable \
--entry-prefix l09 --name l09 --architecture qemu \
--out l09-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l09-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 14: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l09.S --portable \
--entry-prefix l09 --name l09 --architecture esp32c6 \
--out l09-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l09-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 15: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l09; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 16: Exercises: paper first, then PRG32
TRY IT
1
Write the canonical forms P and S of the full adder outputs S and Cout
2
Minimise Cout with a Karnaugh map of three variables. How many gates do you save?
3
Minimise F = sum of m(0, 1, 2, 5, 8, 9, 10) with a map of four variables
4
Build NOT, AND and OR using NAND only, and check each with a truth table
5
Program the full adder on PRG32 and display S and Cout as lamps for the eight input combinations
Expected result
On paper: Cout = AB + ACin + BCin. On PRG32: eight pairs of lamps that reproduce the truth table of the full adder.
Notes: Five exercises. Write the canonical forms of the two outputs of the full adder. Minimise the outgoing carry with a three-variable map and count the gates saved. Minimise a four-variable function given as a list of minterms, remembering that the corners are adjacent. Construct NOT, AND and OR from NAND gates alone, verifying each by its truth table, which demonstrates functional completeness constructively. Then program the full adder on PRG32 and display its outputs as lamps for the eight input combinations. For the lecturer: Exercise 3: F = B'D' + B'C' + A'C'D (corners; top-left and bottom-left pairs with their neighbours; m1 with m5). Exercise 2: the canonical form of Cout has four minterms (3, 5, 6, 7); the map gives three clauses of two literals.