## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 13
Sequential Machines: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
13-Computer_Architecture-Sequential_Machines.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 13. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: finite-state machines; the clock; latches and flip-flops; registers as flip-flops. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise. Roadmap. Today's outcomes: (1) describe a finite-state machine with a state diagram; (2) explain the clock and why a circuit must settle within one period; (3) tell a latch from a flip-flop and build a register. Builds on: only what Lecture 01 set up. Next: Lecture 14, Elementary Machines: Registers and Buses.

## Slide 2: In this deck
1
The listing of Lecture 13: read the code, then the numbered remarks beside it
2
The complete program: code/l13.S, 65 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The program of this lecture is ~/arc12/code/l13.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l13.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: A game is a state machine
.equ TITLE, 0
.equ PLAY, 1
.equ OVER, 2
game_update:
...
call prg32_input_read # a0 = buttons: the INPUT
la t0, state
lw t1, 0(t0) # t1 = the present STATE
andi t2, a0, 0x10 # button A
li t3, TITLE
bne t1, t3, 1f
beqz t2, done # TITLE: stay until A is pressed
li t1, PLAY # TITLE --A--> PLAY
j store
1: li t3, OVER
bne t1, t3, done # PLAY is handled elsewhere
beqz t2, done # OVER: stay until A is pressed
li t1, TITLE # OVER --A--> TITLE
store:
sw t1, 0(t0) # the next state becomes the present state
done:
...
1
Pressing A starts the game from the title screen and returns to it from the game-over screen: the effect depends on the state
2
The state is one word in memory that survives from frame to frame
3
update computes the next state from the present state and the input
4
draw shows a different screen for each state: the output
UNDERSTAND NOW · finite-state machines
Notes: The warm-up: a game with a title screen, a playfield and a game-over screen. The variable state holds one of three values. game_update reads button A and the present state: in TITLE, pressing A leads to PLAY; in OVER, pressing A leads back to TITLE; otherwise nothing changes. The effect of A therefore depends on the state, which is the defining property of a state machine: update computes the next state from the present state and the input, the state persists in memory from frame to frame, and draw renders a screen for each state. The program anticipates every concept of the lecture. UNDERSTAND NOW: finite-state machines. For the lecturer: Written for this lecture; the textbook capstone game has the same structure. Bug to discuss: holding A on the OVER screen goes to TITLE and, one frame later, to PLAY. Fixing it requires remembering the previous value of the button: one more bit of state.

## Slide 4: The warm-up as a state diagram
UNDERSTAND NOW · finite-state machines
Present state | Input that changes it | Next state | Output (draw)
TITLE | A pressed | PLAY | the title screen
PLAY | lives = 0 | OVER | the playfield
OVER | A pressed | TITLE | the final score
Notes: The game of the warm-up drawn as a state diagram: three states, with A leading from TITLE to PLAY and from OVER to TITLE, and the exhaustion of lives leading from PLAY to OVER. The self-loops represent the cases in which nothing changes. The table below lists, for each state, the input that changes it, the next state and the output drawn. Drawing the diagram before writing the code is the most valuable design habit for a game, because it forces every transition to be considered explicitly. The diagram also reveals a defect discussed in the warm-up note: holding A on OVER passes through TITLE to PLAY, which only an additional bit of state can prevent. UNDERSTAND NOW: finite-state machines. For the lecturer: A Moore machine with three states: two bits of state would be enough, the program uses a whole word. Drawing the diagram before writing the code is the single most useful design habit for a game.

## Slide 5: The program counter: a register in a loop
PC
register, 32 bits
adder
+ 4
MUX
branch target
from the ALU
next PC
clock
branch taken?
The PC holds the address of the instruction being executed: it is the state that says where the program is
Next state: PC + 4 for a normal instruction, or the branch target when a branch is taken
Present state, combinational network, next state, clock: exactly the general architecture
With only the + 4 path it is a counter: the simplest finite-state machine
first_update of Lecture 02 was the same machine in software
UNDERSTAND NOW · registers as flip-flops
Notes: The program counter, PC, is the register holding the address of the instruction being executed. Its next value is computed by a small network: an adder yields PC + 4, the address of the following instruction, and a multiplexer chooses between that and the target of a branch. At each clock edge the next value becomes the present one. The structure is exactly the general architecture of a sequential machine. With only the +4 path it is a counter, the simplest of all state machines. UNDERSTAND NOW: registers as flip-flops. For the lecturer: The comparator of Lecture 11 produces 'branch taken?' for beq and bne. Instructions are 4 bytes apart; with the compressed extension the adder adds 2 for 16-bit instructions.

## Slide 6: The processor is a sequential machine
State
the program counter, the thirty-two registers, the memory
Input
the instruction at the address in the PC, and the data it reads
Next-state network
decoders, multiplexers and the ALU compute the new values
Clock edge
the registers named by the instruction take their new values
Executing a program is nothing but a long walk through the states of a very large finite-state machine, one clock edge at a time. Single-stepping in PRG32-QT shows that walk one state after another.
UNDERSTAND NOW · finite-state machines
Notes: The processor as a whole is a sequential machine. Its state comprises the program counter, the thirty-two registers and the memory. Its input is the instruction found at the address in the PC, together with the data it reads. The next-state network consists of decoders, multiplexers and the ALU, and at each clock edge the registers named by the instruction take their new values. Executing a program is a traversal of the states of a very large state machine, and single-stepping in PRG32-QT exhibits that traversal one state at a time. UNDERSTAND NOW: finite-state machines. For the lecturer: This is the bridge to the lectures on the processor: datapath (the combinational part and the registers) and control (itself a finite-state machine in multi-cycle and microprogrammed designs).

## Slide 7: The complete program: l13.S (1 of 3)
# ARC12 Computer Architecture - Lecture 13: Sequential Machines
# l13.S: a game is a state machine
#
# On the screen: one colour per state. Blue is TITLE: press A and the screen turns
# green, PLAY. (OVER, red, is reached only when a game ends: this warm-up has no game
# yet. Hold A on the red screen and you meet the bug discussed in the lecture.)
# Build: python3 -m prg32 cartridge build l13.S --portable \
# --entry-prefix l13 --name l13 --out l13.prg32
.option norelax
.equ TITLE, 0
.equ PLAY, 1
.equ OVER, 2
.section .text
.global l13_init
.global l13_update
.global l13_draw
l13_init:
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l13.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: The complete program: l13.S (2 of 3)
l13_update:
game_update:
addi sp, sp, -16
sw ra, 12(sp)
call prg32_input_read # a0 = buttons: the INPUT
la t0, state
lw t1, 0(t0) # t1 = the present STATE
andi t2, a0, 0x10 # button A
li t3, TITLE
bne t1, t3, 1f
beqz t2, done # TITLE: stay until A is pressed
li t1, PLAY # TITLE --A--> PLAY
j store
1: li t3, OVER
bne t1, t3, done # PLAY is handled elsewhere
beqz t2, done # OVER: stay until A is pressed
li t1, TITLE # OVER --A--> TITLE
store:
sw t1, 0(t0) # the next state becomes the present state
done:
lw ra, 12(sp)
addi sp, sp, 16
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l13.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: The complete program: l13.S (3 of 3)
l13_draw:
addi sp, sp, -16
sw ra, 12(sp)
la t0, state
lw t1, 0(t0)
la t0, colours # the OUTPUT depends on the state only:
slli t1, t1, 2 # a Moore machine
add t0, t0, t1
lw a0, 0(t0)
call prg32_gfx_clear
lw ra, 12(sp)
addi sp, sp, 16
ret
.section .rodata
colours: .word 0x001f, 0x07e0, 0xf800 # TITLE blue, PLAY green, OVER red
.section .data
state: .word TITLE
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l13.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 10: Run it: what you should see
On the screen
– one colour per state. Blue is TITLE: press A and the screen turns green, PLAY. (OVER, red, is reached only when a game ends: this warm-up has no game yet. Hold A on the red screen and you meet the bug discussed in the lecture.)
What to press
– press A
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 11: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l13.S --portable \
--entry-prefix l13 --name l13 --out l13.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l13.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 12: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l13.S --portable \
--entry-prefix l13 --name l13 --architecture qemu \
--out l13-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l13-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 13: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l13.S --portable \
--entry-prefix l13 --name l13 --architecture esp32c6 \
--out l13-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l13-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 14: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l13; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 15: Exercises: paper first, then PRG32
TRY IT
1
Draw the state diagram of a machine that outputs 1 when the last two inputs were both 1; write it as a Moore and as a Mealy machine
2
Complete the timing diagram of an SR latch for a given sequence of S and R, marking where it holds
3
Synthesise a counter modulo 3 (0, 1, 2, 0, ...) with two D flip-flops; what happens in the unused state?
4
Add a PAUSE state to the warm-up game, entered and left with the SELECT button, and draw the new diagram first
5
Fix the warm-up so that A must be released and pressed again: store the previous button state and react only to a 0 to 1 change
Expected result
On PRG32: four screens, and a held button that causes exactly one transition. The last exercise is edge detection in software: the program behaves like a flip-flop instead of a latch.
Notes: Five exercises. Design a machine whose output is 1 when the last two inputs were both 1, both as a Moore and as a Mealy machine, and compare the number of states required. Complete a timing diagram of an SR latch. Synthesise a modulo-3 counter with two D flip-flops, considering what should happen in the unused fourth state. Add a PAUSE state to the game of the warm-up, drawing the diagram first. And make button A act only on a new press: this is edge detection in software, used in Verm1 Part 3. For the lecturer: Exercise 1: Moore needs three states (no 1 seen, one 1 seen, two or more), Mealy two. Exercise 3: D1 = Q0, D0 = Q1'Q0' with state 11 as a don't-care, or designed to return to 00. Exercise 5: keep prev in memory; pressed_now = buttons AND NOT prev; then store buttons in prev.