## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 20
Buses and the Video Card: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
20-Computer_Architecture-Video_Card.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 20. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: the frame buffer; device controllers; buses and bandwidth; the video card; GPU and GPGPU. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise. Roadmap. Today's outcomes: (1) explain why devices sit behind controllers and how the processor talks to them; (2) compute the size of a frame buffer and the bandwidth of a video signal; (3) describe what a video card and a GPU do. Builds on: only what Lecture 01 set up. Next: Lecture 21, Input and Output.

## Slide 2: In this deck
1
The listing of Lecture 20: read the code, then the numbered remarks beside it
2
The complete program: code/l20.S, 32 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The program of this lecture is ~/arc12/code/l20.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l20.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: One pixel, please
li a0, 100 # x
li a1, 50 # y
li a2, 0xf800 # red, in RGB565
call prg32_gfx_pixel # ... where does it go?
# what the runtime does, in principle:
li t0, 320
mul t1, a1, t0 # y * 320
add t1, t1, a0 # + x = position in the frame
la t2, framebuffer
add t2, t2, t1 # ADDRESS of that pixel
sb t3, 0(t2) # store its palette index (one byte)
1
The screen is an array in memory, one element per pixel: the frame buffer
2
Drawing a pixel is a store instruction at address base + y x 320 + x
3
Nothing appears until the frame is sent to the display: prg32_gfx_present
4
On a PC these two jobs, keeping the frame and sending it to the monitor, belong to the video card
UNDERSTAND NOW · the frame buffer
Notes: The warm-up. The first four lines belong to the program: x in a0, y in a1, a colour in a2, and a call to prg32_gfx_pixel. The second half shows in principle, not as the literal source of the runtime, what is done with them: y is multiplied by 320, x added, the base address of the frame buffer added, and one byte stored there. The screen is thus an array in memory with one element per pixel, and drawing a pixel is a store instruction. Nothing appears until the frame is transmitted to the display. On a PC, holding the frame and transmitting it are the two functions of the video card. UNDERSTAND NOW: the frame buffer. For the lecturer: The second half is a sketch of the principle, not the source of the runtime: t3 stands for the palette index that the runtime derives from the RGB565 colour in a2. On the ESP32-C6 the PRG32 frame buffer is 320 x 200 bytes, one palette index per pixel (docs/hardware/ili9341.md).

## Slide 4: The complete program: l20.S (1 of 2)
# ARC12 Computer Architecture - Lecture 20: Buses and the Video Card
# l20.S: one pixel, please
#
# On the screen: a single red pixel at x = 100, y = 50 on a black screen. Look
# closely.
# Build: python3 -m prg32 cartridge build l20.S --portable \
# --entry-prefix l20 --name l20 --out l20.prg32
.option norelax
.section .text
.global l20_init
.global l20_update
.global l20_draw
l20_init:
ret
l20_update:
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l20.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 5: The complete program: l20.S (2 of 2)
l20_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0
call prg32_gfx_clear
li a0, 100 # x
li a1, 50 # y
li a2, 0xf800 # red, in RGB565
call prg32_gfx_pixel # ... where does it go?
lw ra, 12(sp)
addi sp, sp, 16
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l20.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 6: Run it: what you should see
On the screen
– a single red pixel at x = 100, y = 50 on a black screen. Look closely.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 7: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l20.S --portable \
--entry-prefix l20 --name l20 --out l20.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l20.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 8: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l20.S --portable \
--entry-prefix l20 --name l20 --architecture qemu \
--out l20-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l20-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 9: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l20.S --portable \
--entry-prefix l20 --name l20 --architecture esp32c6 \
--out l20-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l20-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 10: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l20; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 11: Exercises: paper first, then PRG32
TRY IT
1
Compute the memory for one 4K frame in True Color, and the bytes per second at 60 frames per second
2
The PRG32 display bus runs at 27 MHz: how long does it take to send 20 rows of 320 pixels at 16 bits per pixel?
3
Draw a diagonal line pixel by pixel with prg32_gfx_pixel in a loop
4
Fill the screen once with prg32_gfx_clear and once with 64,000 calls to prg32_gfx_pixel: compare the frame rates
5
Change one palette entry with prg32_palette_set every frame and watch every pixel that uses it change at once
Expected result
On paper: 24,883,200 bytes per frame, about 1.5 GB per second; 102,400 bits, about 3.8 ms. On PRG32: palette cycling animates the screen without redrawing a single pixel.
Notes: Five exercises. Compute the memory of a 4K frame in True Color and the bytes per second required at 60 frames per second. Compute how long the display bus of PRG32 takes to send 20 rows. Draw a diagonal line pixel by pixel. Fill the screen once with a single call and once with 64,000 calls, and compare the frame rates, which makes the cost of per-pixel calls quantitative. Finally, modify one entry of the palette at each frame: every pixel that uses it changes at once without being redrawn, which demonstrates the power of indirection that an indexed frame buffer provides. For the lecturer: The last exercise shows why indexed colour was loved by game programmers: one store changes thousands of pixels. API calls from the textbook appendix (prg32_palette_set, prg32_gfx_clear, prg32_gfx_pixel).