## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 20
Buses and the Video Card
From a byte in memory to a pixel on the screen; graphics processors and general-purpose computing on them
“...nothing is more serious than gaming...”
attributed to Jean Cocteau (1889-1963)
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Lecture deck. The listings, the complete program and how to test it are in the code deck:
20-Computer_Architecture-Video_Card-Lab.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: With this lecture the course leaves the processor and turns to its surroundings. The subject is the path of an image, from a number in memory to a point of light on the screen. Along the way two general ideas are encountered, the peripheral controller and the bus, together with one specific machine, the video card and its processor, the GPU. The kit has no video card at all, and for teaching purposes this is an advantage: every step that a card would conceal is performed by code that can be read, and its cost measured. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: the frame buffer; device controllers; buses and bandwidth; the video card; GPU and GPGPU. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise. Roadmap. Today's outcomes: (1) explain why devices sit behind controllers and how the processor talks to them; (2) compute the size of a frame buffer and the bandwidth of a video signal; (3) describe what a video card and a GPU do. Builds on: only what Lecture 01 set up. Next: Lecture 21, Input and Output. For the lecturer: Spiral: one call draws one pixel on PRG32; the lecture follows that pixel from the frame buffer to the display, then generalises to buses, video cards, GPUs and GPGPU. The kit has no video card: its processor does everything, which makes every step visible.

## Slide 2: What you will be able to do by the end
1
Explain what a peripheral controller is and why devices need synchronisation with the processor
2
Characterise a bus by width, speed and transfer rate, and list its advantages and limits
3
Describe the job of a video card: frame buffer, resolution, colour depth, output interface
4
Compute the memory a frame needs and the time it takes to send it over a bus
5
Explain what a GPU does and what general-purpose computing on GPUs is
Notes: Five learning outcomes. Explaining what a peripheral controller is and why devices must be synchronised with the processor. Characterising a bus by its width, speed and transfer rate. Describing the function of a video card: frame buffer, resolution, colour depth and output interface. Computing the memory a frame requires and the time needed to send it across a bus. And explaining what a GPU does and what it means to use it for general-purpose computation.

## Slide 3: Input/output devices
Peripherals are used for the interaction between the user and the system
They have limited autonomy: they are controlled and coordinated by the processor
They work asynchronously with respect to the processor, so synchronisation mechanisms are needed
– to know when an input datum will be available
– to know when an output device has finished producing its data
The terminal, the most common instrument of interaction, is made of two independent devices: the keyboard and the video
UNDERSTAND NOW · device controllers
Notes: Peripherals serve the interaction between the user and the system. They enjoy limited autonomy, being controlled and coordinated by the processor. And they operate asynchronously, at their own pace, so synchronisation mechanisms are required: to know when an input datum is available, and when an output device has completed its task. The terminal, the most common instrument of interaction, consists in fact of two independent devices, a keyboard and a display; it is the processor that copies to the display what arrives from the keyboard. UNDERSTAND NOW: device controllers. For the lecturer: Keyboard and video are not directly connected: the processor reproduces on the video what arrives from the keyboard (Lecture 21).

## Slide 4: Controllers
processor
memory
data bus, address bus, control
video
controller
monitor
USB
controller
keyboard,
mouse
storage
controller
disks
Peripherals are interfaced to the processor through dedicated controllers
The controller manages the communication between the device and all the other components, processor included
It presents a few registers on the bus: the processor reads and writes them like memory
Generally a controller signals the end of the operation in progress by raising a signal: an interrupt (Lecture 19)
The video card is the controller of the monitor
UNDERSTAND NOW · device controllers
Notes: A peripheral is never connected directly to the processor: a controller is interposed. In the diagram, processor and memory sit on the bus, and so do the controllers, each with its device on the far side. The controller manages the dialogue with the device and presents a few registers on the bus, which the processor reads and writes as memory, by the memory-mapped I/O of Lecture 15. When an operation completes, the controller typically raises an interrupt, as in the previous lecture. The video card is the controller of the monitor. UNDERSTAND NOW: device controllers. For the lecturer: On the ESP32-C6 the controllers (SPI, I2S, GPIO, USB) are on the same chip as the processor, and their registers are memory-mapped (Lecture 15).

## Slide 5: What characterises a bus
A bus is a communication channel shared by several units; its characteristics decisively influence the performance of the whole system
Width
– the number of bits of the data bus
Speed
– the working frequency of the bus; the number of bytes per clock cycle
Transfer rate
– megabytes transmitted per second: a 32-bit bus at 66 MHz carries 264 MB/s
A bus is a standard: signals, connectors and a protocol that all the units agree on
264 MB/s
32 bits at 66 MHz: width times frequency gives the transfer rate
UNDERSTAND NOW · buses and bandwidth
Notes: A bus is a communication channel shared by several units, and its characteristics determine the performance of the whole system. Its width is the number of bits of the data bus; its speed is the frequency at which it operates; their product is the transfer rate. A 32-bit bus at 66 MHz carries 4 bytes 66 million times per second, 264 megabytes per second. A bus is also a standard: signals, connectors and a protocol on which all the attached units agree. UNDERSTAND NOW: buses and bandwidth. For the lecturer: The example is the PCI bus: 4 bytes x 66 million cycles per second = 264 MB/s. Interface: the hardware module that encodes the data electrically or optically. Protocol: the higher-level description of how the dialogue takes place.

## Slide 6: Buses: advantages and disadvantages
Advantages
New devices can easily be added
Peripherals can be moved from one computer to another that uses the same bus
A single set of wires connects several peripherals
Low cost per byte transmitted
Disadvantages
The bandwidth of the bus limits the transfer speed
The maximum speed depends on the length of the bus
and on the number of devices connected to it
A shared resource: only one transfer at a time
UNDERSTAND NOW · buses and bandwidth
Notes: The merits and costs of buses. The advantages: new devices are added easily; a peripheral can be moved to another computer with the same bus; one set of wires connects many peripherals; the cost per byte transferred is low. The disadvantages: the bandwidth of the bus bounds the transfer speed; the maximum speed decreases as the bus grows longer and as more devices are attached; and, being shared, the bus carries only one transfer at a time, the limitation already observed for the common bus of Lecture 14. UNDERSTAND NOW: buses and bandwidth.

## Slide 7: Buses through the years
Bus | Kind | Used for | Today
ISA, EISA, VESA | parallel, 16 to 32 bits | expansion cards of early PCs | disused
PCI | parallel, 32 or 64 bits | expansion cards | replaced by PCI Express
AGP | parallel, dedicated port | the video card alone | replaced by PCI Express
PCI Express | serial, 1 to 16 lanes | video cards, fast storage | current: each generation doubles the speed
IDE (ATA), SCSI | parallel | disks | replaced by Serial ATA and NVMe
USB | serial | almost every external device | current: from 12 Mbit/s to tens of Gbit/s
SPI, I2C, I2S | serial, a few wires | chips on the same board | current: the buses of the PRG32 kit
UNDERSTAND NOW · buses and bandwidth
Notes: Forty years of buses in one table, best read by columns. The early buses, ISA, PCI, AGP for the video card alone, IDE and SCSI for disks, were parallel, with many wires side by side. Their successors, PCI Express, Serial ATA and USB, are serial: few wires, far higher speeds. This is the trend stated in Lecture 14, now documented historically. The last row is the kit: SPI, I2C and I2S are the small serial buses that connect chips on the same board. UNDERSTAND NOW: buses and bandwidth. For the lecturer: USB: universal serial bus. PCI: peripheral component interconnect. AGP: accelerated graphics port. IDE: integrated device electronics. ISA: industry standard architecture. SCSI: small computer system interface. PCMCIA and FireWire were in the original list. The move from parallel to serial is the lesson of Lecture 14.

## Slide 8: What a video card does
Its function: to send to the monitor the information to display
It translates the representation of the image produced by the processor into a format the monitor can show
It contains memory of its own, the video memory, which holds the frame: the frame buffer
Every time the screen must be redrawn, it reads the digital representation of the image and sends the monitor the signal for the colour of each pixel
It has processing capability of its own
UNDERSTAND NOW · the video card
Notes: The function of a video card is to supply the monitor with the information to be displayed. It translates the representation of the image produced by the processor into a form the monitor can render. It has a memory of its own, the video memory, which holds the frame, the frame buffer. At every refresh of the screen the card reads that memory and emits the signal encoding the colour of each pixel. It also has its own processing capability, which the last part of the lecture examines. UNDERSTAND NOW: the video card. For the lecturer: DAC: digital-to-analogue converter, needed for analogue monitors. On PRG32 the 'video card' is a region of RAM plus the SPI peripheral: no separate hardware at all.

## Slide 9: Analogue and digital monitors
CRT monitor, analogue input
The card converts the digital image into analogue signals
The conversion is done by a component called RAMDAC
VGA output (1987): designed for cathode-ray tubes
Problems: electrical noise, distortion, errors in placing the pixels
LCD monitor, digital input
The card adapts colours and resolution of the image
Provides local memory to use as a buffer
Supports graphics acceleration, for example 3D
DVI: each pixel of the output corresponds to one pixel of the screen, at its native resolution
UNDERSTAND NOW · the video card
Notes: Two generations of monitor. A cathode-ray monitor has an analogue input: the card must convert the digital image into analogue signals with a component called the RAMDAC, and noise and distortion enter along the cable. A liquid-crystal monitor has a digital input: the card adapts colours and resolution, and each output pixel corresponds exactly to one pixel of the panel. The conversion to analogue, and its defects, disappear, an instance of the advantage of digital representation argued in Lecture 10. UNDERSTAND NOW: the video card. For the lecturer: RAMDAC: random access memory digital-analog converter. DVI could also carry analogue VGA signals for compatibility.

## Slide 10: Video outputs
Interface | Year | Signal | Notes
VGA | 1987 | analogue | for CRT monitors; kept for years for compatibility
DVI | 1999 | digital (and analogue) | introduced with LCD monitors
HDMI | 2003 | digital | replaces the earlier standards; carries audio too
DisplayPort | 2006 | digital | video, audio and other data; also over USB-C connectors
SPI to a display controller | - | digital, serial | the PRG32 kit: an ILI9341 panel of 320 by 240 pixels
UNDERSTAND NOW · the video card
Notes: The outputs, in chronological order. VGA, analogue, for cathode-ray monitors. DVI, the first digital output, which arrived with LCD monitors. HDMI, digital, which also carries audio. DisplayPort, digital, which can also travel over USB-C connectors. The last row is the kit: the display is reached over an SPI bus, and the chip on the display module, an ILI9341, plays the role of the monitor electronics for a panel of 320 by 240 pixels, with its own memory for the frame. UNDERSTAND NOW: the video card. For the lecturer: High-Definition Multimedia Interface; Digital Visual Interface; Video Graphics Array. The ILI9341 is the chip on the display module: it has its own memory for the frame and drives the liquid crystals (Lecture 21).

## Slide 11: Resolution: the size of the pixel grid
Resolution | Pixels | Aspect ratio | Where
320 x 200 | 64,000 | 8:5 | Commodore 64, VGA games, the PRG32 viewport
640 x 480 | 307,200 | 4:3 | VGA
1024 x 768 | 786,432 | 4:3 | monitors of the 1990s
1920 x 1080 | 2,073,600 | 16:9 | Full HD
3840 x 2160 | 8,294,400 | 16:9 | 4K
The resolution determines the definition of the image, and how many pixels must be stored and sent for every frame.
UNDERSTAND NOW · the video card
Notes: Resolution is the size of the pixel grid, columns by rows. The table ranges from 320 by 200, 64,000 pixels, the resolution of the Commodore 64 and of the PRG32 viewport, to 4K, with more than eight million. The third column gives the aspect ratio, where the traditional 4:3 has given way to 16:9. Resolution determines the definition of the image, and also the number of pixels that must be stored and transmitted for each frame. UNDERSTAND NOW: the video card. For the lecturer: The table of the original deck also listed 800 x 600, 1280 x 1024 (5:4) and 1600 x 1200. The traditional 4:3 ratio has given way to the panoramic 16:9. The 4K row is new.

## Slide 12: Colour depth: bits per pixel
Depth | Colours | Bytes per pixel | Name
4 bits | 16 | 0.5 | standard VGA
8 bits | 256 | 1 | 256-colour mode: each value is an index into a palette
16 bits | 65,536 | 2 | High Color: RGB565
24 bits | 16,777,216 | 3 | True Color: 256 shades of each of red, green and blue
UNDERSTAND NOW · the video card
Notes: Colour depth is the number of bits per pixel. With 4 bits there are 16 colours; with 8 bits, 256, each value usually an index into a colour table, the palette; with 16 bits, 65,536, in the familiar RGB565 format; with 24 bits, more than sixteen million, with 256 levels for each primary. The memory required by a frame is the number of pixels times the bytes per pixel. PRG32 combines the two middle rows: an 8-bit frame buffer of indices and a palette of 256 RGB565 colours, trading colour freedom for memory. UNDERSTAND NOW: the video card. For the lecturer: In True Color every colour is obtained from 256 shades of each of the three additive primaries. PRG32 uses both middle rows: an 8-bit frame buffer of palette indices, and a palette of 256 RGB565 colours (Lecture 04).

## Slide 13: Following the pixel on PRG32
your code
prg32_gfx_pixel
frame buffer
320 x 200 bytes
in RAM
palette
256 entries
of RGB565
SPI bus
27 MHz,
serial, with DMA
display
ILI9341,
320 x 240
Quantity | Value
memory for one frame, one byte per pixel | 320 x 200 x 1 = 64,000 bytes
the same frame at two bytes per pixel | 128,000 bytes: a quarter of all the RAM of the chip
bits sent to the display for a whole frame | 64,000 pixels x 16 bits = 1,024,000 bits
time on the bus at 27 MHz | about 38 ms: at most some 26 full frames per second
Two engineering answers: an indexed frame buffer halves the memory, and only the rows that changed are sent.
UNDERSTAND NOW · the frame buffer
Notes: The path of a pixel on the kit, in five stages: the program, the frame buffer in RAM, the palette that maps an index to a colour, the SPI bus, the display. The table carries out the arithmetic. One frame at one byte per pixel occupies 64,000 bytes; at two bytes it would consume a quarter of the chip's RAM. On the bus each pixel travels as 16 bits, about a million bits per frame, or 38 milliseconds at 27 MHz. Two engineering responses follow: an indexed frame buffer, and transmitting only what has changed, which Verm1 Part 4 implements. UNDERSTAND NOW: the frame buffer. For the lecturer: Figures from the PRG32 repository (docs/hardware/ili9341.md): 64,000-byte 8-bit indexed frame buffer, 512-byte palette, default SPI clock of 27 MHz, DMA transfers and dirty-rectangle tracking. 1,024,000 / 27,000,000 = 37.9 ms. The FPS counter of the demo cartridges shows the result.

## Slide 14: Memory and bandwidth: the pressure on video hardware
The memory and the processor time needed by ever more demanding graphics, 3D video games above all, imposed a rapid evolution on video cards
As the definition of the images grows, so does the memory needed to represent a frame
The flow of data from the memory to the video card risks saturating the capacity of the bus
Two lines of attack
– more and more memory on the card itself: the video memory
– a wider or dedicated bus: AGP yesterday, PCI Express today
Several cards could even be connected together to share the work
4K, 60 Hz
8.3 million pixels x 3 bytes x 60 frames: about 1.5 GB of pixels every second
UNDERSTAND NOW · the video card
Notes: The same arithmetic at the scale of a PC explains the history of video hardware. Higher definition requires more memory per frame, and the stream of data towards the card threatens to saturate the bus. The two responses were more memory on the card itself and a wider or dedicated bus: AGP first, PCI Express today. The figure on the right conveys the scale: a 4K screen at 60 frames per second amounts to about one and a half gigabytes of pixels every second. UNDERSTAND NOW: the video card. For the lecturer: With AGP the graphics processor used part of the main memory through direct access. PCI Express (2004) replaced it with more bandwidth and more power. SLI (NVIDIA) and CrossFire (AMD) linked up to four cards; today a single card, or many cards in a server, are the rule.

## Slide 15: The graphics processing unit
The share of processor time spent computing images grew with the use of graphical interfaces
To relieve the CPU, video cards were given dedicated processors: GPUs
They accelerate
– raster graphics: copying blocks of pixels (blitting), operations on textures
– 3D graphics: transformations, texture mapping, lighting
Programs use them through libraries: OpenGL, Direct3D, and today Vulkan and Metal
A device driver adapts the software running on the CPU to the primitives offered by the GPU; what is not supported is emulated by the CPU, slowly
No GPU on the kit: every pixel is a store instruction
UNDERSTAND NOW · GPU and GPGPU
Notes: As graphical interfaces spread, computing images consumed a growing share of processor time. To relieve the CPU, video cards acquired dedicated processors, graphics processing units, which accelerate raster operations, such as copying blocks of pixels, and 3D graphics: transformations, textures, lighting. Programs reach them through libraries, and a device driver adapts the software to the primitives of each GPU. The kit has no GPU: a rectangle is a loop of stores executed by the RISC-V core, and its cost is directly observable. UNDERSTAND NOW: GPU and GPGPU. For the lecturer: On PRG32 there is no GPU: prg32_gfx_rect is a loop of store instructions executed by the RISC-V core. This is why the frame rate of a busy cartridge drops, and why the students can see the cost of every pixel.

## Slide 16: General-purpose computing on GPUs
Modern GPUs execute the same operation in parallel on whole matrices of pixels
GPGPU: using GPUs for applications of a general kind, not necessarily graphical
A very large number of simple cores per GPU: hundreds, thousands
Programming models: CUDA (NVIDIA) and OpenCL, an open standard
Scientific simulation, data analysis and, above all today, the training and use of neural networks run on GPUs
The same operation on many data at once
UNDERSTAND NOW · GPU and GPGPU
Notes: A GPU applies the same operation in parallel to whole matrices of pixels, and nothing requires those numbers to be pixels: GPGPU is the use of graphics processors for general computation. A GPU contains a very large number of simple cores and is programmed with models such as CUDA and OpenCL. Scientific simulation, data analysis and, above all today, the training and inference of neural networks run on GPUs. The picture recalls the parallel sum of Lecture 04: one operation applied to many data at once. Lecture 24 returns to this model of computation. UNDERSTAND NOW: GPU and GPGPU. For the lecturer: Compute Unified Device Architecture. The parallel sum of Lecture 04 is the simplest GPGPU example. The weather and marine models of the Department run on GPU clusters.

## Slide 17: Check your understanding
1
How much memory does a frame of 640 x 480 pixels need in True Color (24 bits)?
A
307,200 bytes
B
614,400 bytes
C
921,600 bytes
D
7,372,800 bytes
2
A 16-bit bus works at 50 MHz, one transfer per cycle. What is its transfer rate?
A
50 MB/s
B
100 MB/s
C
400 MB/s
D
800 MB/s
Notes: For the first question: the memory required by a frame is the number of pixels times the bytes per pixel. The pixels are computed first, then one recalls how many bytes 24 bits represent. For the second: the transfer rate is width times frequency, with the width converted to bytes before multiplying. For the lecturer: 1. Answer: C. 307,200 pixels x 3 bytes = 921,600 bytes. 2. Answer: B. 2 bytes x 50 million transfers per second = 100 MB/s.

## Slide 18: Check your understanding
1
In an 8-bit indexed frame buffer, the byte of a pixel contains:
A
its red component
B
its brightness
C
the position of its colour in a palette
D
its x coordinate
2
What is GPGPU?
A
A faster video output
B
Using graphics processors for non-graphical computation
C
A bus for video cards
D
A kind of video memory
Notes: For the first question "indexed" is the key word: the byte does not describe the colour but indicates where to find it. For the second, the acronym is expanded: its first two letters stand for "general-purpose". For the lecturer: 1. Answer: C. The byte is an index; the actual colour is looked up in a table of 256 entries, the palette. 2. Answer: B. General-purpose computing on graphics processing units.

## Slide 19: Glossary: English and Italian
English | Italiano | English | Italiano
peripheral | periferica | resolution | risoluzione
controller | controller (unità di controllo della periferica) | colour depth | profondità di colore
bus width | larghezza del bus | palette | tavolozza (palette)
transfer rate | velocità di trasferimento | video memory | memoria video
video card | scheda video | device driver | driver di periferica
Notes: Ten terms. A peripheral is a periferica; its controller retains the English name. Bus width and transfer rate are larghezza del bus and velocità di trasferimento. Colour depth is profondità di colore. A palette is a tavolozza, though programmers say palette. A device driver is the software that adapts programs to a specific device.

## Slide 20: Conclusions and reading
Input/output devices are a fundamental component of computers
Devices are managed by a controller that interfaces them to the bus
A bus is characterised by width, speed and transfer rate; its bandwidth is a limit to design around
Video cards make it possible to display graphics and text: a frame buffer, a resolution, a colour depth, an output
Their processors, the GPUs, are also used for high-performance computing
Reading
– Tanenbaum, Austin: Structured Computer Organization, chapters 2 and 3 (buses, displays)
– Playing with RISC-V, chapter 7: the graphics game
– PRG32 repository: docs/hardware/ili9341.md
Notes: Five conclusions. Input/output devices are a fundamental part of a computer. Each is managed by a controller that interfaces it to the bus. A bus is characterised by width, speed and transfer rate, and its bandwidth is a constraint that designs must respect. A video card displays graphics and text through a frame buffer, a resolution, a colour depth and an output interface. And its processors, the GPUs, are today used for high-performance computing. The next lecture covers the other input and output devices. Learning status, recap. UNDERSTAND NOW: the frame buffer; device controllers; buses and bandwidth; the video card; GPU and GPGPU. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise. Closing thread: Every rectangle drawn since Lecture 02 ended in a frame buffer that a controller sends to the screen many times a second. Next: the other devices: displays, keyboards, printers. Exit ticket (two to four minutes, alone, on paper): 1. Why is a device never connected directly to the processor? Say what its controller does and how the processor talks to it. 2. A screen of 320 x 200 pixels uses 16 bits per pixel and is redrawn 30 times per second. How much frame-buffer memory is needed, and how many bytes per second must reach the screen? For the lecturer: Next lecture: input and output devices.