## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 22
Verm1, Part 4: The Finished Game: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Verm1 reference implementation contributed by Giuseppe Coviello
Code deck. The concepts, the figures and the questions are in the lecture deck:
22-Computer_Architecture-Verm1_Part_4.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 22. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: quotient and remainder; characters and strings; fixed point; the calling convention; arrays in memory; finite-state machines; the frame buffer; the processor cycle. USE NOW: the PRG32 tools, the PRG32-QT debugger (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise. Roadmap. Today's outcomes: (1) turn a number into decimal digits with divu and remu; (2) draw only what changed, with a dirty flag; (3) finish the game: levels, sound, speed. Builds on: characters and strings (Lecture 04); fixed point (Lecture 06); the calling convention (Lecture 18); arrays in memory (Lecture 04); finite-state machines (Lecture 13). Next: Lecture 23, Verm1 on the Cartridge Store.

## Slide 2: In this deck
1
The 31 listings of Lecture 22, one per slide: read the code, then the numbered remarks beside it
2
The program is your verm1.S; the reference is verm1/verm1_part4.S, 565 lines, shown here region by region
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The reference program is ~/arc12/verm1/verm1_part4.S; tools/tests/verm1_check.py builds it and plays it with a scripted player, and verm1_steps.py runs the intermediate checkpoints. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The reference program is ~/arc12/verm1/verm1_part4.S; tools/tests/verm1_check.py builds it and plays it with a scripted player, and verm1_steps.py runs the intermediate checkpoints. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: The working loop, again
# 1. build the cartridge (from your PRG32 folder, toolchain active)
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --out ~/verm1/verm1.prg32
# 2. send it to PRG32-QT, running on the same computer
python3 -m prg32 esp32c6 upload-and-run ~/verm1/verm1.prg32 \
--url http://localhost:8080 --slot cart0
# or: in PRG32-QT, import the file verm1.prg32 and choose Run Cartridge
USE NOW · the PRG32 tools
Notes: The same two commands as always. Before anything is changed, Part 3 is run in debug mode and the telemetry recorded during a game: retired instructions, frames per second, late frames. These figures are the baseline of the measurement that concludes the lecture; without them no claim of improvement could be substantiated. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The same two commands. Before you start, run Part 3 in debug mode and write down what the telemetry shows during a game: retired instructions, frames per second, late frames. You will need the numbers in step 5.

## Slide 4: NEW to_decimal: divide by ten, three times
to_decimal: # a0 = value 0..999, a1 = address of 3 chars
li t0, 10
remu t1, a0, t0 # the units: the remainder of value / 10
addi t1, t1, 48 # 48 is the ASCII code of '0'
sb t1, 2(a1)
divu a0, a0, t0
remu t1, a0, t0 # the tens
addi t1, t1, 48
sb t1, 1(a1)
divu a0, a0, t0
remu t1, a0, t0 # the hundreds
addi t1, t1, 48
sb t1, 0(a1)
ret # a leaf function: no stack frame needed
1
Contract: a0 = value, a1 = where the 3 characters go
2
remu gives the digit, divu what is left
3
sb stores a byte: offsets 2, 1, 0 from a1
4
A leaf: only t registers, no frame at all
UNDERSTAND NOW · quotient and remainder
Notes: to_decimal states its contract in a comment: the value in a0, the address of three characters in a1. It performs the same operation three times: remu yields the remainder of division by ten, 48 is added to it, sb stores the byte, and divu leaves the quotient for the next round. The offsets are 2, 1 and 0, from units to hundreds. The function is a leaf: it calls nothing and uses only temporaries, so it needs no stack frame. Division instructions are slow on a small processor, tens of cycles each, but ten of them per step are negligible. UNDERSTAND NOW: quotient and remainder. For the lecturer: Values above 999 would show only their last three digits: a limit that no player will meet soon. The division instructions are slow, tens of clock cycles each on a small processor, and ten per step of the worm are nothing.

## Slide 5: CHANGED draw_score: two numbers, two texts
draw_score:
addi sp, sp, -16
sw ra, 12(sp)
la t0, score
lw a0, 0(t0)
la a1, score_txt
call to_decimal # the score, as three characters
li a0, 56
li a1, 0
la a2, score_txt
call draw_text
la t0, best
lw a0, 0(t0)
la a1, best_txt+5 # after the letters "BEST "
call to_decimal
li a0, 256
li a1, 0
la a2, best_txt
call draw_text
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Replace draw_score of Part 3: the marks go
2
The digits are written into a string in RAM
3
best_txt+5: skip BEST and the space, five characters
4
Then the string is drawn like any other
UNDERSTAND NOW · characters and strings
Notes: draw_score replaces that of Part 3. It calls to_decimal twice, once for the score and once for the best score, each time with an address within a string where the digits belong: best_txt+5 skips the word BEST and the following space. The two strings are then drawn like any other text. Because text is drawn with its background colour, the new digits overwrite the old ones without any need to clear them first. UNDERSTAND NOW: characters and strings. For the lecturer: score_txt and best_txt are strings in .data, not .rodata: the program writes into them. Text is drawn with its background colour, so new digits cover the old ones without clearing.

## Slide 6: CHANGED .data: the variables of Part 4
.section .data # variables: they live in RAM
state: .word TITLE
prev_btn: .word 0 # the buttons one frame ago
dir: .word 0
want: .word 0
step_q8: .word 0
score: .word 0
best: .word 0 # lost when the power goes
food_x: .word 0
food_y: .word 0
head_i: .word 0 # ring index of the head
length: .word 0 # number of cells of the worm
body_x: .space 256 # the ring: one byte per segment
body_y: .space 256
grid: .space COLS*ROWS # one byte per cell: 1 = worm
dirty: .word 2 # 0 nothing to draw, 1 a step, 2 everything
old_x: .word 0 # where the head was before the step
old_y: .word 0
erase_on: .word 0 # 1 if the tail left a cell
erase_x: .word 0
erase_y: .word 0
score_txt: .asciz "000" # filled in by to_decimal
best_txt: .asciz "BEST 000"
1
Replace the .data of Part 3
2
Two strings that the program fills in
3
dirty, old and erase: used in steps 3 and 4
UNDERSTAND NOW · characters and strings
Notes: The new .data section. Two strings that the program fills in, placed in .data rather than .rodata precisely because the program writes into them. Six new variables follow: dirty, the previous position of the head, and the cell to be erased. They are not used until the third step, but are typed now so that the section is written once. UNDERSTAND NOW: characters and strings. For the lecturer: Type all of it now. The six variables from dirty to erase_y are not used until step 3.

## Slide 7: Run it: digits
TRY IT
1
Build and run, press A: the top line reads VERM1 000 and, on the right, BEST 000
2
Play and eat: 001, 002, ...
3
Lose: on the game-over screen BEST shows your score
4
In the debugger find score_txt in memory and read its bytes: 30 30 33 00 after three meals
Expected result
The score and the best score in digits; everything else as in Part 3.
Notes: Build and run. The top line reads VERM1 000 and, on the right, BEST 000; each meal increments the first; on losing, BEST shows the score attained. In the debugger, score_txt can be inspected in memory: after three meals its bytes are 30 30 33 00, the characters produced by the student's own division. For the lecturer: This intermediate program, Part 3 with the new draw_score, to_decimal and .data, is built and run by tests/verm1_steps.py.

## Slide 8: CHANGED Constants: two speeds instead of one
.option norelax
.equ BLACK, 0x0000 # RGB565 colours
.equ WHITE, 0xffff
.equ GREEN, 0x07e0 # the head
.equ BODY, 0x03e0 # the body: a darker green
.equ RED, 0xf800 # the food
.equ CELL, 8 # a cell is 8 x 8 pixels
.equ COLS, 40
.equ ROWS, 24
.equ TOP, 8
.equ SPEED_MIN, 32 # 32/256 of a cell per frame at the start
.equ SPEED_MAX, 96 # the worm never goes faster than this
.equ BTN_LEFT, 0x01
.equ BTN_RIGHT, 0x02
.equ BTN_UP, 0x04
.equ BTN_DOWN, 0x08
.equ BTN_A, 0x10
.equ DIR_RIGHT, 0 # bit 0 = vertical, bit 1 = backwards
.equ DIR_DOWN, 1
.equ DIR_LEFT, 2
.equ DIR_UP, 3
.equ TITLE, 0 # the three states of the game
.equ PLAY, 1
.equ OVER, 2
1
SPEED_Q8 is replaced by a minimum and a maximum
2
32/256: one step every 8 frames at the start
3
96/256: three steps every 8 frames at most
UNDERSTAND NOW · fixed point
Notes: The constant SPEED_Q8 is replaced by two: a minimum of 32 and a maximum of 96. Both are fixed-point values in 256ths of a cell per frame, as in Part 2: 32 means one step every eight frames, 96 three steps every eight frames. UNDERSTAND NOW: fixed point. For the lecturer: Replace the constants of Part 3. Only the two SPEED lines differ.

## Slide 9: CHANGED play_update: a speed that grows
la t0, score
lw t3, 0(t0)
slli t3, t3, 2
addi t3, t3, SPEED_MIN # speed = 32 + 4 * score, in 1/256 of a cell
li t4, SPEED_MAX
ble t3, t4, 8f
mv t3, t4 # ... but never more than 96
8: la t0, step_q8
lw t1, 0(t0)
add t1, t1, t3 # add a fraction of a cell
li t2, 256
blt t1, t2, 6f # less than one whole cell: wait
sub t1, t1, t2
sw t1, 0(t0)
call step # one whole cell: move
j 7f
6: sw t1, 0(t0)
7: lw ra, 12(sp)
addi sp, sp, 16
ret
1
speed = 32 + 4 x score: a shift and an add
2
ble and mv: the smaller of speed and 96
3
The rest is the timer you know
4
The limit is reached at 16 points
UNDERSTAND NOW · fixed point
Notes: The timer at the end of play_update. The speed is 32 plus four times the score, computed with a shift by two positions and an addition. A comparison then retains the smaller of this value and the maximum. The rest is the familiar timer: the speed is added to an accumulator, and a step is taken whenever it exceeds 256. A quantity that follows a line and then remains at a bound is said to saturate, the same idea as the clamping of Lecture 05. UNDERSTAND NOW: fixed point. For the lecturer: Replace the timer at the end of play_update. A saturation: the value follows a line and then stays at the limit, like the clamp of the first laboratory. With fixed point the speed changes by a sixty-fourth of a cell per frame at each meal: no integer speed could be so fine.

## Slide 10: Run it: faster and faster
TRY IT
1
Build and run: the worm starts slower than in Part 3, and gains speed at every meal
2
Count the frames between two steps with the debugger at score 0: eight
3
Reach 16 points: the speed no longer changes
4
Try SPEED_MAX = 256, if you dare
Expected result
A slow start, one step every 8 frames, and a visible acceleration over the first meals.
Notes: Build and run: the worm starts more slowly than in Part 3 and accelerates at every meal. With the debugger, the frames between two steps at score zero can be counted: eight, as predicted. Reaching sixteen points, the speed can be verified to remain constant. A maximum of 256, one step per frame, may then be tried by the adventurous. For the lecturer: Checked by tests/verm1_steps.py: 8 steps in the first 64 frames of a game.

## Slide 11: CHANGED play_note: one function, any note
play_note: # a2 = MIDI note, a4 = milliseconds
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0 # channel
li a1, 0 # instrument
li a3, 255 # volume
call prg32_audio_note
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Replace eat_sound with play_note
2
The caller chooses note and duration: a2 and a4
3
The function fills in the other three arguments
UNDERSTAND NOW · the calling convention
Notes: play_note replaces eat_sound. The caller chooses the note and the duration, in a2 and a4; the function supplies channel, instrument and volume and calls prg32_audio_note. The choice of registers is deliberate: note and duration already sit where the runtime function expects them, so nothing needs to be moved. Designing a contract around the callee's interface saves instructions, a small but characteristic instance of interface design. UNDERSTAND NOW: the calling convention. For the lecturer: The arguments stay in the registers where prg32_audio_note expects them: a2 is the note and a4 the duration in both functions. Designing a contract around the callee saves moves.

## Slide 12: CHANGED step: remember the old head
la t0, head_i
lw t5, 0(t0) # t5 = ring index of the head
la t0, body_x
add t0, t0, t5
lbu s0, 0(t0) # one byte: the column of the head
la t0, old_x
sw s0, 0(t0) # remember where the head was
add s0, s0, t2
bgez s0, 1f
li s0, COLS-1 # off the left edge: wrap
1: li t4, COLS
blt s0, t4, 2f
li s0, 0
2: la t0, body_y
add t0, t0, t5
lbu s1, 0(t0)
la t0, old_y
sw s1, 0(t0)
add s1, s1, t3
bgez s1, 3f
li s1, ROWS-1
3: li t4, ROWS
blt s1, t4, 4f
li s1, 0
4:
1
Replace the same part of step
2
old_x, old_y: the cell the head is leaving
3
draw will repaint it in the colour of the body
UNDERSTAND NOW · arrays in memory
Notes: The beginning of step, with two stores added: before the head moves, its coordinates are written into old_x and old_y. That cell is about to cease being the head and become body, and draw will need to repaint it. UNDERSTAND NOW: arrays in memory. For the lecturer: Two stores are added to the code of Part 3: the lines that write old_x and old_y.

## Slide 13: CHANGED step: is there a cell to erase?
la t0, food_x
lw t1, 0(t0)
xor t1, t1, s0
la t0, food_y
lw t2, 0(t0)
xor t2, t2, s1
or s2, t1, t2 # s2 = 0 if the new head is on the food
la t0, length
lw t1, 0(t0)
bnez s2, 5f # not eating: the tail moves on
li t2, 255
bge t1, t2, 5f # the ring is full: no more growth
addi t1, t1, 1
sw t1, 0(t0) # eating: one cell longer, the tail stays
la t0, erase_on
sw zero, 0(t0) # ... so there is no cell to erase
j 6f
5: la t0, head_i
lw t2, 0(t0)
sub t2, t2, t1
addi t2, t2, 1
andi t2, t2, 255 # ring index of the tail
la t0, body_x
add t0, t0, t2
lbu t3, 0(t0)
la t0, body_y
add t0, t0, t2
lbu t4, 0(t0)
1
Eating: the tail stays, nothing to erase
2
erase_on = 0 says so to draw
UNDERSTAND NOW · arrays in memory
Notes: The branch taken on a meal. When the worm eats, the tail does not move, so there is no cell to erase, and erase_on is set to zero to record the fact. UNDERSTAND NOW: arrays in memory. For the lecturer: Two lines are added: the store of zero into erase_on.

## Slide 14: CHANGED step: note the tail, call the end
la t0, erase_x
sw t3, 0(t0) # remember the cell the tail leaves
la t0, erase_y
sw t4, 0(t0)
la t0, erase_on
li t5, 1
sw t5, 0(t0)
li t5, COLS
mul t4, t4, t5
add t4, t4, t3 # cell number of the tail = row * 40 + column
la t0, grid
add t0, t0, t4
sb zero, 0(t0) # the tail cell is free again
6: li t5, COLS
mul t4, s1, t5
add t4, t4, s0 # cell number of the new head
la t0, grid
add t0, t0, t4
lbu t1, 0(t0)
beqz t1, 7f # a free cell: go on
call game_is_over # the worm bit itself
j 9f
1
The tail leaves a cell: remember which one
2
erase_on = 1: draw must paint it black
3
The collision is now one call: game_is_over
UNDERSTAND NOW · arrays in memory
Notes: When the worm does not eat, the tail vacates a cell: its coordinates are saved in erase_x and erase_y, and erase_on is set to 1. Further on, the collision with the body is no longer handled inline: it has become a single call to game_is_over. UNDERSTAND NOW: arrays in memory. For the lecturer: The beginning is new, seven lines; the end is shorter than in Part 3, because the transition to OVER has become a function.

## Slide 15: CHANGED step: write the new head
7: li t1, 1
sb t1, 0(t0) # occupy the new cell
la t0, head_i
lw t1, 0(t0)
addi t1, t1, 1
andi t1, t1, 255 # the ring wraps after entry 255
sw t1, 0(t0)
la t0, body_x
add t0, t0, t1
sb s0, 0(t0) # write the new head into the ring
la t0, body_y
add t0, t0, t1
sb s1, 0(t0)
1
As in Part 3, up to the two sb
2
The end of the function is on the next slide
UNDERSTAND NOW · arrays in memory
Notes: The new head is written into the ring and into the map exactly as in Part 3. The slide appears only because the function continues on the next one. UNDERSTAND NOW: arrays in memory. For the lecturer: Unchanged lines, shown because the function continues.

## Slide 16: NEW step: something changed
la t0, dirty
li t1, 1
sw t1, 0(t0) # the screen must follow: a few cells
bnez s2, 9f
la t0, score
lw t1, 0(t0)
addi t1, t1, 1
sw t1, 0(t0)
call place_food
li a2, 72 # a short high note
li a4, 60
call play_note
9: lw s2, 0(sp)
lw s1, 4(sp)
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
dirty = 1: one step happened, draw has work
2
A meal: a point, new food, a short high note
3
li a2 and li a4, then call: arguments by contract
UNDERSTAND NOW · the calling convention
Notes: The new end of step. First dirty is set to 1, because a step has occurred and draw has work to do. Then, if the worm has eaten: one more point, new food, and a short high note, number 72 for 60 milliseconds, requested with two li instructions and a call, arguments passed by contract. UNDERSTAND NOW: the calling convention. For the lecturer: This replaces the end of step. Note 72 for 60 milliseconds: the sound of Part 2, through the new function.

## Slide 17: NEW game_is_over: the transition, in one place
game_is_over:
addi sp, sp, -16
sw ra, 12(sp)
la t0, state
li t1, OVER
sw t1, 0(t0) # PLAY --> OVER
la t0, dirty
li t1, 2
sw t1, 0(t0) # a new screen: draw everything
la t0, score
lw t1, 0(t0)
la t0, best
lw t2, 0(t0)
ble t1, t2, 1f
sw t1, 0(t0) # a new best score
1: li a2, 36 # a long low note
li a4, 400
call play_note
lw ra, 12(sp)
addi sp, sp, 16
ret
1
PLAY to OVER, and the best score, as in Part 3
2
dirty = 2: a new screen must be drawn
3
A long low note: 36, for 400 milliseconds
UNDERSTAND NOW · finite-state machines
Notes: game_is_over gathers in one place everything the transition from PLAY to OVER entails: the new state, the update of the best score, dirty set to 2 because an entire new screen must be drawn, and a long low note, number 36 for 400 milliseconds. A transition of the state machine merits a function of its own, so that its effects cannot be scattered or partially forgotten. UNDERSTAND NOW: finite-state machines. For the lecturer: A transition of the state machine deserves a function of its own: state, outputs and sound in one place.

## Slide 18: Run it: the sound of defeat
TRY IT
1
Build and run: the game looks exactly as after step 2
2
A meal sounds as before; biting yourself gives a long low note
3
In the debugger watch erase_x and erase_y follow the tail, one step behind
4
dirty stays at 1 or 2: nobody reads it yet
Expected result
No visible change: the screen is still drawn completely at every frame. The new variables are written and not yet used.
Notes: Build and run: the game looks exactly as it did after the second step. What changes can be heard: a low note on biting oneself. In the debugger, erase_x and erase_y can be seen to follow the tail one step behind, and dirty to hold 1 or 2: it is written, and nothing reads it yet. For the lecturer: This intermediate program is built and run by tests/verm1_steps.py: verm1_draw of Part 3 with step, play_note and game_is_over of Part 4.

## Slide 19: CHANGED draw: nothing, a little, or everything
verm1_draw:
la t0, dirty
lw t1, 0(t0)
beqz t1, 3f # nothing changed: nothing to draw
sw zero, 0(t0)
addi sp, sp, -16
sw ra, 12(sp)
li t2, 2
beq t1, t2, 1f
call draw_changes # one step: a few cells
j 2f
1: call draw_full # a new screen: everything
2: lw ra, 12(sp)
addi sp, sp, 16
3: ret
1
dirty = 0: return at once, no frame, no call
2
dirty = 1: a step happened, draw the changes
3
dirty = 2: a new screen, draw it all
4
The flag is cleared as soon as it is read
UNDERSTAND NOW · the frame buffer
Notes: The new verm1_draw reads dirty and clears it at once. If it was zero, the function returns immediately: no stack frame, no call, five machine instructions. If it was 1, a step has occurred and draw_changes is called. If it was 2, the state has changed and draw_full redraws everything. The most frequent case is the cheapest, which is the hallmark of a well-conceived optimisation. UNDERSTAND NOW: the frame buffer. For the lecturer: Replace verm1_draw. The frame is created only if there is something to do: the common case, nothing changed, costs five machine instructions.

## Slide 20: NEW draw_changes: three cells and the score
draw_changes:
addi sp, sp, -16
sw ra, 12(sp)
la t0, erase_on
lw t1, 0(t0)
beqz t1, 1f
la t0, erase_x
lw a0, 0(t0)
la t0, erase_y
lw a1, 0(t0)
li a2, BLACK
call draw_cell # the cell the tail has left
1: la t0, old_x
lw a0, 0(t0)
la t0, old_y
lw a1, 0(t0)
li a2, BODY
call draw_cell # the old head is now body
call draw_head
call draw_food
call draw_score
lw ra, 12(sp)
addi sp, sp, 16
ret
1
The cell the tail left, if any: black
2
The old head: body colour
3
Then the new head, the food, the score
4
The order matters: the head is drawn after the erase
UNDERSTAND NOW · the frame buffer
Notes: draw_changes paints at most three cells. If erase_on is set, the cell vacated by the tail is painted black. The old head is repainted in the colour of the body. Then the new head, the food and the score are drawn. The order matters: the head may enter exactly the cell the tail has just left, so the erasure must precede the drawing of the head. UNDERSTAND NOW: the frame buffer. For the lecturer: The head may enter the cell that the tail has just left: erasing first and drawing the head afterwards gives the right picture.

## Slide 21: NEW draw_full: a whole screen
draw_full:
addi sp, sp, -16
sw ra, 12(sp)
li a0, BLACK
call prg32_gfx_clear
li a0, 0
li a1, 0
la a2, title
call draw_text
call draw_score
la t0, state
lw t1, 0(t0)
li t2, TITLE
bne t1, t2, 1f
li a0, 132 # TITLE: only an invitation
li a1, 96
la a2, press_a
call draw_text
j 2f
1
The body of the old verm1_draw
2
The score is drawn on the title screen too
3
TITLE: the invitation, and nothing else
UNDERSTAND NOW · the frame buffer
Notes: draw_full is the body of the former verm1_draw: it clears the screen and draws the score, and in the TITLE state adds the invitation and returns. It is called once per change of state, not at every frame. UNDERSTAND NOW: the frame buffer. For the lecturer: Called once for each change of state.

## Slide 22: NEW draw_full: PLAY and OVER
1: call draw_worm # PLAY and OVER: the whole scene
call draw_food
la t0, state
lw t1, 0(t0)
li t2, OVER
bne t1, t2, 2f
li a0, 124
li a1, 96
la a2, game_over
call draw_text
2: lw ra, 12(sp)
addi sp, sp, 16
ret
1
The worm and the food, by their functions
2
OVER adds the two words
UNDERSTAND NOW · the frame buffer
Notes: The second half of draw_full: in PLAY and OVER it draws the worm and the food through their functions, and in OVER it adds the two words of the game-over screen. UNDERSTAND NOW: the frame buffer. For the lecturer: The second half of draw_full.

## Slide 23: NEW draw_head
draw_head:
addi sp, sp, -16
sw ra, 12(sp)
la t0, head_i
lw t1, 0(t0)
la t0, body_x
add t0, t0, t1
lbu a0, 0(t0)
la t0, body_y
add t0, t0, t1
lbu a1, 0(t0)
li a2, GREEN
call draw_cell
lw ra, 12(sp)
addi sp, sp, 16
ret
1
The head is entry head_i of the ring
2
One cell, bright green
UNDERSTAND NOW · the frame buffer
Notes: draw_head draws one cell in bright green, the entry head_i of the ring. It is a small function with a single responsibility, used by draw_changes. UNDERSTAND NOW: the frame buffer. For the lecturer: A small function used by draw_changes.

## Slide 24: NEW draw_food
draw_food:
addi sp, sp, -16
sw ra, 12(sp)
la t0, food_x
lw a0, 0(t0)
la t0, food_y
lw a1, 0(t0)
li a2, RED
call draw_cell
lw ra, 12(sp)
addi sp, sp, 16
ret
1
The three lines that were inside draw
2
Now they have a name, and two callers
UNDERSTAND NOW · the frame buffer
Notes: draw_food: the three lines formerly inside draw now have a name and two callers, the full drawing and the partial one. UNDERSTAND NOW: the frame buffer.

## Slide 25: UNCHANGED draw_text
draw_text: # a0 = x, a1 = y, a2 = address of the string
addi sp, sp, -16
sw ra, 12(sp)
li a3, WHITE
li a4, BLACK
call prg32_gfx_text8
lw ra, 12(sp)
addi sp, sp, 16
ret
1
The helper of Part 3, on a slide of its own
Notes: draw_text, the helper of Part 3, unchanged. It is shown on a slide of its own because in Part 3 it shared one with the game-over text. For the lecturer: Unchanged: it was shown together with the game-over text in Part 3.

## Slide 26: CHANGED init: ask for the first screen
.section .text
.global verm1_init
.global verm1_update
.global verm1_draw
verm1_init:
la t0, state
sw zero, 0(t0) # start on the title screen
la t0, prev_btn
sw zero, 0(t0)
la t0, dirty
li t1, 2
sw t1, 0(t0) # draw the whole title screen, once
ret
1
dirty = 2: the title screen must be drawn once
UNDERSTAND NOW · finite-state machines
Notes: verm1_init with three lines added: dirty starts at 2, because the title screen must be drawn once. UNDERSTAND NOW: finite-state machines. For the lecturer: Replace verm1_init: three lines are added.

## Slide 27: CHANGED update: a new state is a new screen
la t0, state
lw t1, 0(t0) # t1 = present state
li t2, PLAY
beq t1, t2, u_play
andi t3, s1, BTN_A # TITLE or OVER: wait for a new press of A
beqz t3, u_done
li t2, TITLE
beq t1, t2, u_start
sw t2, 0(t0) # OVER --A--> TITLE
la t0, dirty
li t1, 2
sw t1, 0(t0) # a new screen: draw everything
j u_done
u_start:
call new_game # TITLE --A--> PLAY
j u_done
u_play:
mv a0, s0
call play_update
u_done:
lw s1, 4(sp)
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
OVER to TITLE: dirty = 2
2
Three lines are added, after the store of the state
UNDERSTAND NOW · finite-state machines
Notes: In verm1_update, the transition from OVER back to TITLE now also sets dirty to 2: a new state requires a new screen. UNDERSTAND NOW: finite-state machines. For the lecturer: Replace the same part of verm1_update.

## Slide 28: CHANGED new_game: and here too
la t0, head_i
li t1, 2
sw t1, 0(t0) # the head is entry 2 of the ring
la t0, length
li t1, 3
sw t1, 0(t0)
la t0, dir
sw zero, 0(t0)
la t0, want
sw zero, 0(t0)
la t0, step_q8
sw zero, 0(t0)
la t0, score
sw zero, 0(t0)
call place_food
la t0, state
li t1, PLAY
sw t1, 0(t0)
la t0, dirty
li t1, 2
sw t1, 0(t0) # a new screen: draw everything
lw ra, 12(sp)
addi sp, sp, 16
ret
1
TITLE to PLAY: dirty = 2
2
Three lines are added, before the return
UNDERSTAND NOW · finite-state machines
Notes: The same in new_game, for the transition from TITLE to PLAY. This is the governing rule of the technique: every transition requests a full drawing, every step a partial one. Forgetting one produces the characteristic defect of incremental rendering, a screen that depicts a state no longer true. UNDERSTAND NOW: finite-state machines. For the lecturer: Every transition of the machine asks for a full drawing; every step asks for a partial one. Forgetting one of them is the typical bug of this technique: the screen shows a state that is no longer true.

## Slide 29: Run it: the finished Verm1
Score 004, seven cells
The end of a game
Expected: the same game as after step 3, pixel for pixel. If you see trails or holes, a change was not recorded: use the debugger.
Notes: The finished Verm1. It must be the same game as after the third step, pixel for pixel: the optimisation must be invisible. Trails or holes indicate that some change was not recorded, and the debugger should be used to find it, starting from the three variables that step writes. For the lecturer: Screenshots produced by tools/tests/verm1_check.py.

## Slide 30: Appendix: the functions that did not change
Eight parts of the file are those of Part 3: keep them as they are
They are on the next slides, so that this deck contains the whole program
update, new_game (first half), play_update (steering), step (lookup), place_food, draw_worm, draw_cell, .rodata
Notes: An appendix follows: the eight parts of the file unchanged since Part 3. They are included so that this deck contains the whole program, and they are to be kept as they stand. For the lecturer: Reference file for this part: verm1/verm1_part4.S (565 lines).

## Slide 31: UNCHANGED update: buttons and edges
verm1_update:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
sw s1, 4(sp)
call prg32_input_read
mv s0, a0 # s0 = buttons held in this frame
la t0, prev_btn
lw t1, 0(t0) # t1 = buttons held one frame ago
sw s0, 0(t0)
not t1, t1
and s1, s0, t1 # s1 = buttons pressed just now
1
The edge detector of Part 3
Notes: verm1_update: the reading of the buttons and the edge detector of Part 3.

## Slide 32: UNCHANGED new_game: the map and the worm
new_game:
addi sp, sp, -16
sw ra, 12(sp)
la t0, grid
li t1, COLS*ROWS
1: sb zero, 0(t0) # empty the grid, one byte per cell
addi t0, t0, 1
addi t1, t1, -1
bnez t1, 1b
li t1, 0 # i = 0, 1, 2: three cells in row 12
2: la t0, body_x
add t0, t0, t1
addi t2, t1, 3
sb t2, 0(t0) # columns 3, 4, 5
la t0, body_y
add t0, t0, t1
li t3, 12
sb t3, 0(t0)
la t0, grid+12*COLS
add t0, t0, t2
li t3, 1
sb t3, 0(t0) # mark the cell as occupied
addi t1, t1, 1
li t3, 3
blt t1, t3, 2b
1
The first half of new_game
Notes: The first half of new_game: the map is cleared and the worm laid down.

## Slide 33: UNCHANGED play_update: steering
play_update: # a0 = buttons held
addi sp, sp, -16
sw ra, 12(sp)
la t0, dir
lw t1, 0(t0) # t1 = direction of the last step
la t0, want
lw t2, 0(t0) # t2 = wanted direction, so far
andi t3, a0, BTN_RIGHT
beqz t3, 1f
li t2, DIR_RIGHT
1: andi t3, a0, BTN_DOWN
beqz t3, 2f
li t2, DIR_DOWN
2: andi t3, a0, BTN_LEFT
beqz t3, 3f
li t2, DIR_LEFT
3: andi t3, a0, BTN_UP
beqz t3, 4f
li t2, DIR_UP
4: xor t3, t2, t1 # opposite directions differ in bit 1 only
li t4, 2
beq t3, t4, 5f # a U-turn: ignore the request
sw t2, 0(t0)
5:
1
The masks and the U-turn rule of Part 2
Notes: The steering within play_update: the button masks and the rule forbidding the U-turn, from Part 2.

## Slide 34: UNCHANGED step: the table lookup
step:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp) # s0 = column of the new head
sw s1, 4(sp) # s1 = row of the new head
sw s2, 0(sp) # s2 = 0 when the worm eats
la t0, want
lw t1, 0(t0)
la t0, dir
sw t1, 0(t0) # the wanted direction is now the direction
slli t1, t1, 2 # table offset = direction * 4 bytes
la t0, dx
add t0, t0, t1
lw t2, 0(t0) # t2 = dx[direction]
la t0, dy
add t0, t0, t1
lw t3, 0(t0) # t3 = dy[direction]
1
The frame and the tables dx, dy
Notes: The beginning of step: the stack frame and the lookup of the direction in the tables dx and dy.

## Slide 35: UNCHANGED place_food
place_food:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
1: li a0, 0
li a1, COLS-1
call prg32_random_number
mv s0, a0 # s0 = a column
li a0, 0
li a1, ROWS-1
call prg32_random_number # a0 = a row
li t1, COLS
mul t2, a0, t1
add t2, t2, s0
la t0, grid
add t0, t0, t2
lbu t3, 0(t0)
bnez t3, 1b # on the worm: try again
la t0, food_x
sw s0, 0(t0)
la t0, food_y
sw a0, 0(t0)
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
A random free cell
Notes: place_food: a random cell, drawn again until a free one results.

## Slide 36: UNCHANGED draw_worm
draw_worm:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li s0, 0 # s0 = i: segment 0 is the head
1: la t0, length
lw t1, 0(t0)
bge s0, t1, 3f
la t0, head_i
lw t1, 0(t0)
sub t1, t1, s0
andi t1, t1, 255 # ring index of segment i
la t0, body_x
add t0, t0, t1
lbu a0, 0(t0)
la t0, body_y
add t0, t0, t1
lbu a1, 0(t0)
li a2, BODY
bnez s0, 2f
li a2, GREEN # the head is brighter
2: call draw_cell
addi s0, s0, 1
j 1b
3: lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Used by draw_full only, once per new screen
Notes: draw_worm, which traverses the ring backwards. It is now used only by draw_full, once per new screen.

## Slide 37: UNCHANGED draw_cell
draw_cell: # a0 = column, a1 = row, a2 = colour
addi sp, sp, -16
sw ra, 12(sp)
slli a0, a0, 3 # x = column * 8
slli a1, a1, 3
addi a1, a1, TOP # y = row * 8 + 8
mv a4, a2 # the colour is the fifth argument
li a2, CELL
li a3, CELL
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
1
From cells to pixels, since Part 2
Notes: draw_cell, from cells to pixels: the same function since Part 2.

## Slide 38: UNCHANGED .rodata
.section .rodata # constants: they stay in the cartridge file
title: .asciz "VERM1"
press_a: .asciz "PRESS A"
game_over: .asciz "GAME OVER"
dx: .word 1, 0, -1, 0 # right, down, left, up
dy: .word 0, 1, 0, -1
1
Strings and tables
Notes: The .rodata section: the strings and the direction tables.

## Slide 39: Run it: what you should see
On the screen
– the finished game: the score and the best score in digits, a worm that goes faster as the score grows, a short note for a meal and a long low one for the end.
What to press
– A starts a game; steer with the joystick
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 40: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --out verm1.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run verm1.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 41: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --architecture qemu \
--out verm1-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload verm1-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 42: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --architecture esp32c6 \
--out verm1-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run verm1-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 43: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix verm1; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 44: Make it yours
TRY IT
1
A pause: button B stops the game and writes PAUSE; B again resumes. A fourth state
2
A melody on the title screen: a table of notes in .rodata, one note every 15 frames
3
Bonus food: every fifth piece is yellow, worth three points, and disappears after 100 frames
4
Your own colours with prg32_palette_set, or your own rules: this is your game now
Expected result
The version you publish in Lecture 23 should have something that is yours. Change the title string, too.
Notes: Four ideas for making the game one's own. A pause on button B, which requires a fourth state. A melody on the title screen, read from a table of notes. Bonus food that is worth more and disappears after a time. One's own colours, or one's own rules. The version published in the next lecture should contain something of the author's, beginning with the title. For the lecturer: Pause: a state PAUSED with transitions on the edge of B (0x20), and dirty = 2 at both transitions. Melody: an index and a frame counter in .data; the table is read like dx.