## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 04
Representing Digital Information: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
04-Computer_Architecture-Digital_Information.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 04. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: analog and digital; bit, byte, word; hexadecimal; positional notation; a colour is a number; characters and strings; little-endian byte order; data structures; arrays in memory; algorithms. USE NOW: shifts as multiplications (Lecture 05) and, used without being studied in this course, the complete program, the PRG32 tools. UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The 2 listings of Lecture 04, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l04.S, 56 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l04.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l04.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: An array in memory, an element in a register
.section .data
scores: .word 32, 11, 34, 22 # four 32-bit words, 16 bytes
.section .text
la t0, scores # t0 = ADDRESS of element 0
li t1, 2 # index i = 2
slli t1, t1, 2 # offset = i * 4 bytes (shift left by 2)
add t0, t0, t1 # ADDRESS of element i
lw a0, 0(t0) # a0 = VALUE of scores[2] = 34
1
An array is a base address plus equal-sized elements
2
Element i of a word array is at base + 4 x i, because a word is four bytes
3
slli by 2 multiplies by four: a shift is a multiplication by a power of two
4
The high-level expression scores[i] is exactly these four instructions
USE NOW · shifts as multiplications → Lecture 05
UNDERSTAND NOW · arrays in memory
Notes: An array of four words, and the four instructions that read element 2. la loads the address of the first element. The index is multiplied by 4, the size of a word in bytes, with a shift to the left by 2: shifting by one position doubles a binary number. add forms the address of the element, and lw reads its value, 34. The expression scores[i] of a high-level language is exactly this. Note what is missing: nobody checks that the index is less than 4. UNDERSTAND NOW: arrays in memory. USE NOW: shifts as multiplications (studied in Lecture 05). For the lecturer: The shift-as-multiplication property is proved in Lecture 05 (properties of binary strings). Ask: what does lw read if i = 4? Whatever follows the array in memory: the machine does not check bounds.

## Slide 4: A probabilistic algorithm: is n prime?
is_probably_prime(n):
repeat 30 times:
a = random(2, n - 2)
if a^(n-1) mod n != 1:
return COMPOSITE # certain
return PROBABLY PRIME # almost certain
random_walk():
while t < t_final:
r = random(-1, 1)
x = x + r * u # a different path every run
y = y + r * v
t = t + 1
1
The first answer is always right; the second is right with overwhelming probability
2
Trading a tiny chance of error for a huge gain in speed is how real cryptography tests primes
3
A random walk gives a different result at every run: simulations average many of them
UNDERSTAND NOW · algorithms
Notes: Two examples of algorithms that use chance. The first tests whether a number is prime by trying random values: if a test fails, the number is certainly composite; if thirty tests pass, it is prime with overwhelming probability. Trading a tiny chance of error for a great gain in speed is how cryptography works in practice. The second is a random walk: the path is different at every run, and a simulation averages many runs. The listing is pseudo-code, not a language you can compile. UNDERSTAND NOW: algorithms. For the lecturer: The Fermat test shown here is the simplest; real libraries use Miller-Rabin, which closes its loopholes. Both examples are from the source slide.

## Slide 5: The complete program: l04.S (1 of 3)
# ARC12 Computer Architecture - Lecture 04: Representing Digital Information
# l04.S: an array in memory, an element in a register
#
# On the screen: four horizontal bars, one per element of the array (32, 11, 34, 22,
# four pixels per unit); element 2, the one the listing loads, is yellow.
# Build: python3 -m prg32 cartridge build l04.S --portable \
# --entry-prefix l04 --name l04 --out l04.prg32
.option norelax
.equ BLACK, 0x0000
.equ WHITE, 0xffff
.equ YELLOW, 0xffe0
.section .text
.global l04_init
.global l04_update
.global l04_draw
l04_init:
ret
l04_update:
ret
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l04.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 6: The complete program: l04.S (2 of 3)
l04_draw:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li a0, BLACK
call prg32_gfx_clear
li s0, 0 # index i, 0 to 3
1: la t0, scores # t0 = ADDRESS of element 0
mv t1, s0 # index i
slli t1, t1, 2 # offset = i * 4 bytes (shift left by 2)
add t0, t0, t1 # ADDRESS of element i
lw a2, 0(t0) # VALUE of scores[i]
slli a2, a2, 2 # width: four pixels per unit
li a4, WHITE
li t0, 2
bne s0, t0, 2f
li a4, YELLOW # scores[2] = 34: the element of the slide
2: li a0, 20 # x
slli a1, s0, 5
addi a1, a1, 30 # y = 30 + 32 * i
li a3, 16 # height
call prg32_gfx_rect
addi s0, s0, 1
li t0, 4
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l04.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: The complete program: l04.S (3 of 3)
blt s0, t0, 1b
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
.section .data
scores: .word 32, 11, 34, 22 # four 32-bit words, 16 bytes
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l04.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: Run it: what you should see
On the screen
– four horizontal bars, one per element of the array (32, 11, 34, 22, four pixels per unit); element 2, the one the listing loads, is yellow.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 9: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l04.S --portable \
--entry-prefix l04 --name l04 --out l04.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l04.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 10: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l04.S --portable \
--entry-prefix l04 --name l04 --architecture qemu \
--out l04-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l04-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 11: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l04.S --portable \
--entry-prefix l04 --name l04 --architecture esp32c6 \
--out l04-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l04-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 12: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l04; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 13: Exercises on PRG32
TRY IT
1
Change the bar of Lecture 02 to magenta, then to a dark grey of your choice: compute the RGB565 value by hand first
2
Print your name with prg32_gfx_text8. How many bytes does the string occupy?
3
Declare an array of four colours with .word and draw four bars, one per colour, reading each colour with lw
4
In PRG32-QT open the memory view on your string and on your array: find the terminating zero and check the byte order
Expected result
Four bars in four colours; in the memory view the string ends with 00 and each .word shows its least significant byte first.
Notes: Four exercises on the cartridge of Lecture 02. Compute an RGB565 value by hand before trying it: choose the three intensities, write the fields in binary, group by four. Print your name and count the bytes, including the terminator. Declare an array of colours with .word and read it with lw, as on the slide of the array. Finally look at the string and the array in the memory view of PRG32-QT: find the zero at the end, and check that each word shows its least significant byte first. For the lecturer: Dark grey example: red 8 of 31, green 16 of 63, blue 8 of 31 = 01000 010000 01000 = 0x4208, the GREY of the textbook lab.