## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 06
Number Representation: Real Numbers: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
06-Computer_Architecture-Number_Representation_Reals.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 06. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: fixed point; one's complement and excess-k; IEEE 754 floating point; the name RV32IMAC. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The 2 listings of Lecture 06, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l06.S, 47 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l06.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l06.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Three-eighths of a pixel, with integers only
.equ SPEED_Q8, 96 # 96 / 256 = 0.375 pixel per frame
ball_update:
la t0, ball_x_q8
lw t1, 0(t0) # position, in 1/256 of a pixel
addi t1, t1, SPEED_Q8 # add a fraction of a pixel
sw t1, 0(t0)
ret
ball_draw:
...
la t0, ball_x_q8
lw t1, 0(t0)
srai a0, t1, 8 # x in whole pixels: drop 8 bits
...
call prg32_gfx_rect
1
One pixel per frame is too fast, zero is too slow: the ball needs 0.375
2
The processor of the kit is RV32IMAC: integer instructions only, no floating point
3
Trick: store the position multiplied by 256, and divide by 256 only to draw
4
This is fixed point. Where does the trick come from, and when is it not enough?
UNDERSTAND NOW · fixed point
Notes: One pixel per frame is too fast, and zero is no movement at all: the ball needs 0.375 pixels per frame. The trick is to store the position multiplied by 256. ball_update adds 96 at each frame, and 96 divided by 256 is 0.375. ball_draw needs whole pixels, so it shifts the value right by 8 positions, that is, divides by 256, with srai. All the arithmetic is done with integer instructions. The suffix _q8 in the names is a reminder that the value carries eight fractional bits. UNDERSTAND NOW: fixed point. For the lecturer: Written for this lecture in the style of the textbook examples; the same idea is behind prg32_playfield_parallax(layer, x_q8, y_q8) in the PRG32 API. Run it with SPEED_Q8 = 96, then 16, then 1.

## Slide 4: The ball, bit by bit: Q24.8
ball_x_q8 = 0x00002A60 = 10848
0000 0000 0000 0000 0010 1010
integer part: 24 bits
0x00002A = 42 pixels
31
8
0110 0000
fraction: 8 bits
0x60 = 96/256 = 0.375
7
0
10848 / 256 = 42.375
Operation | In fixed point | RISC-V
add, subtract | as integers: the points are aligned | add, sub, addi
to whole pixels | shift right by f, keeping the sign | srai a0, t1, 8
multiply | multiply, then shift right by f | mul, then srai
UNDERSTAND NOW · fixed point
Notes: The ball seen bit by bit. The word 0x00002A60 is divided into 24 bits of integer part, 0x2A, that is 42 pixels, and 8 bits of fraction, 0x60, that is 96/256 = 0.375. As an integer the word is 10848, and 10848 divided by 256 is 42.375. The table gives the rules: addition and subtraction work as for integers, because the points are aligned; to obtain whole pixels, shift right by f; after a multiplication, shift right by f, because the product has twice the fractional bits. UNDERSTAND NOW: fixed point. For the lecturer: 42 x 256 = 10752; 10752 + 96 = 10848 = 0x2A60. After one more frame the value is 0x2AC0 (42.75), then 0x2B20 (43.125): the ball crosses a pixel boundary every two or three frames.

## Slide 5: Floating point is not the real numbers
0.1 has no finite binary expansion: it is stored approximately, like 0.8 in Lecture 05
Never test two floating-point results for equality: compare their difference with a tolerance
Addition is not associative: (a + b) + c can differ from a + (b + c)
Adding a very small number to a very large one can leave the large one unchanged
For money and for game positions, scaled integers are often the right tool
double a = 0.1 + 0.2;
// a == 0.3 ? false
// a = 0.30000000000000004
// better:
// fabs(a - 0.3) < 1e-9
UNDERSTAND NOW · IEEE 754 floating point
Notes: Floating-point numbers behave almost like the real numbers, and the "almost" causes real bugs. 0.1 has no finite binary expansion, so it is stored approximately, and 0.1 plus 0.2 is not exactly 0.3, as the code shows. Hence the rule: never test two floating-point results for equality; compare their difference with a tolerance. Addition is not even associative. For money and for positions in a game, scaled integers, that is fixed point, are often the right tool. UNDERSTAND NOW: IEEE 754 floating point. For the lecturer: The double-precision sum 0.1 + 0.2 is 0.30000000000000004. Try it in any language.

## Slide 6: The complete program: l06.S (1 of 3)
# ARC12 Computer Architecture - Lecture 06: Number Representation: Real Numbers
# l06.S: three-eighths of a pixel per frame, with integers only
#
# On the screen: a white square that crosses the screen slowly from the left: one
# pixel every 2.67 frames.
# Build: python3 -m prg32 cartridge build l06.S --portable \
# --entry-prefix l06 --name l06 --out l06.prg32
.option norelax
.equ SPEED_Q8, 96 # 96 / 256 = 0.375 pixel per frame
.section .text
.global l06_init
.global l06_update
.global l06_draw
l06_init:
ret
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l06.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: The complete program: l06.S (2 of 3)
l06_update:
ball_update:
la t0, ball_x_q8
lw t1, 0(t0) # position, in 1/256 of a pixel
addi t1, t1, SPEED_Q8 # add a fraction of a pixel
sw t1, 0(t0)
ret
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l06.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: The complete program: l06.S (3 of 3)
l06_draw:
ball_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0
call prg32_gfx_clear
la t0, ball_x_q8
lw t1, 0(t0)
srai a0, t1, 8 # x in whole pixels: drop 8 bits
li a1, 100
li a2, 8
li a3, 8
li a4, 0xffff
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
.section .data
ball_x_q8: .word 0 # Q24.8: 24 bits of pixels, 8 bits of fraction
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l06.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: Run it: what you should see
On the screen
– a white square that crosses the screen slowly from the left: one pixel every 2.67 frames.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 10: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l06.S --portable \
--entry-prefix l06 --name l06 --out l06.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l06.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 11: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l06.S --portable \
--entry-prefix l06 --name l06 --architecture qemu \
--out l06-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l06-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 12: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l06.S --portable \
--entry-prefix l06 --name l06 --architecture esp32c6 \
--out l06-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l06-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 13: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l06; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 14: Exercises: paper first, then PRG32
TRY IT
1
Write -6 on four bits in sign and magnitude, one's complement, two's complement and excess-8
2
Encode 10.5 and 0.15625 in IEEE 754 single precision; give the result in hexadecimal
3
Decode 0xBF800000
4
Run the ball with SPEED_Q8 = 96, 16 and 1. After how many frames does it move by one pixel in each case?
5
Give the ball a vertical speed too, and make it bounce: negate the speed with neg when it reaches an edge
Expected result
On paper: 0x41280000, 0x3E200000 and -1.0. On PRG32: the ball advances one pixel every 2.67, 16 and 256 frames; with the bounce it moves diagonally and stays on screen.
Notes: Five exercises. On paper: write minus 6 in the four encodings; encode 10.5 and 0.15625 in single precision; decode 0xBF800000. On PRG32: run the ball with three speeds and count after how many frames it moves by one pixel, then give it a vertical speed and make it bounce by changing the sign of the speed with neg at the edges. The results are in the green box; work them out before looking. For the lecturer: -6: 1110, 1001, 1010, 0010. 10.5 = 1010.1 = 1.0101 x 2^3: E = 130. 0.15625 = 0.00101 = 1.01 x 2^-3: E = 124. 0xBF800000: S = 1, E = 127, F = 0.