## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 01
PRG32 and PRG32-QT: Setting Up Your Workshop: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
01-Computer_Architecture-PRG32_and_PRG32-QT_Setup.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 01. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: the pieces of PRG32. USE NOW: the PRG32 tools, the PRG32-QT debugger, the complete program (used, not studied, in this course). UNDERSTAND LATER: the init, update, draw contract (Lecture 02); registers (Lecture 02). A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The 10 listings of Lecture 01, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l01.S, 57 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l01.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l01.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Download the installer for your system
Your system | File to download | Kind
Windows 10 or 11 | PRG32-QT-0.4.1-Windows-X64-Setup.exe | installer
macOS, Apple Silicon (M1 and later) | PRG32-QT-0.4.1-macOS-ARM64.dmg | disk image
macOS, Intel | PRG32-QT-0.4.1-macOS-Intel-X64.dmg | disk image
Linux, 64-bit PC | PRG32-QT-0.4.1-Linux-X64.deb | Debian package
Raspberry Pi OS, 64-bit | PRG32-QT-0.4.1-Raspberry-Pi-OS-ARM64.deb | Debian package
github.com/riscv-prg32/PRG32-QT, then Releases. Take the latest version.
USE NOW · the PRG32 tools
Notes: Find the row of your system and download that file from the Releases page of the PRG32-QT repository, always from the latest release. Windows has an installer, macOS a disk image (one for Apple Silicon, one for Intel), Linux and Raspberry Pi OS a Debian package. The number 0.4.1 is the version of October 2026: by the time you read this it may be higher, and the file names follow the same pattern. If you are not sure which Mac you have, the macOS slide tells you how to find out. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: From github.com/riscv-prg32/PRG32-QT, Releases, the latest one. 0.4.1 is the version of October 2026: the file names follow this pattern with the current number. The file SHA256SUMS-platforms.txt lists the checksums. Android and Android TV packages are on the same page.

## Slide 4: PRG32-QT on Windows
1
Download
The file ending in Windows-X64-Setup.exe, from the Releases page
2
Run it
If Windows shows a blue SmartScreen warning: More info, then Run anyway
3
Install
Accept the proposed folder: the installer brings everything the program needs
4
Start
PRG32, from the Start menu. If the firewall asks, allow it on private networks
USE NOW · the PRG32 tools
Notes: On Windows there are four moves: download the Setup file, run it, accept the proposed folder, and start PRG32 from the Start menu. Two warnings may appear, and both are expected. SmartScreen may show a blue box because the installer is not from the Microsoft Store: choose More info, then Run anyway. The firewall may ask for permission: allow it on private networks. PRG32-QT listens on port 8080 to receive cartridges from the tools, and you will use this in step 3. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The installer contains the Qt libraries and the compiler runtime: nothing else has to be installed. The firewall question appears because PRG32-QT listens on port 8080 for cartridges sent by the tools: step 3 uses it.

## Slide 5: PRG32-QT on macOS
1
Which Mac?
Apple menu, About This Mac: Chip Apple M... means ARM64; Processor Intel means X64
2
Install
Open the .dmg and drag PRG32 onto the Applications folder
3
First start
Right-click PRG32 and choose Open; or System Settings, Privacy and Security, Open Anyway
4
Allow
Accept incoming connections and local-network access when macOS asks
USE NOW · the PRG32 tools
Notes: On a Mac, first find out which processor you have: the Apple menu, About This Mac. "Chip Apple M..." means the ARM64 file; "Processor Intel" means the Intel one. Open the disk image and drag PRG32 onto Applications. At the first start macOS may refuse to open an application that does not come from the App Store: right-click it and choose Open, or use Privacy and Security in the System Settings. Then accept incoming connections and access to the local network, which the application needs to receive cartridges. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first-start step is needed if macOS says that the developer cannot be verified: the application is distributed outside the App Store. The two permissions are for the device interface on port 8080 and its announcement on the local network.

## Slide 6: PRG32-QT on Linux
# Debian 13, Ubuntu 25.04 and later, or another system with Qt 6.5 or newer
cd ~/Downloads
sudo apt install ./PRG32-QT-0.4.1-Linux-X64.deb
PRG32 &
# On older systems (Ubuntu 24.04 has Qt 6.4: too old): build from source
sudo apt install git cmake ninja-build g++ qt6-base-dev qt6-declarative-dev \
qt6-multimedia-dev qt6-websockets-dev
git clone https://github.com/riscv-prg32/PRG32-QT
cd PRG32-QT
./scripts/build-linux.sh
1
apt install with ./ installs the file and what it needs
2
The program is /usr/bin/PRG32
3
It needs Qt 6.5 or newer: check your distribution
4
Building from source needs a recent Qt as well
USE NOW · the PRG32 tools
Notes: On Linux the upper half of the listing installs the package: apt install with ./ before the file name installs the file together with what it depends on. The program is then /usr/bin/PRG32. The requirement to check is Qt 6.5 or newer: Debian 13 and Ubuntu 25.04 have it; Ubuntu 24.04 does not. The lower half is the alternative for older systems, building from source with the script in the repository. Lines that begin with # are comments: do not type them. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The package depends on the Qt 6 QML, Multimedia and WebSockets packages of the distribution. Where the system Qt is older than 6.5, install Qt with the online installer of qt.io and build with it. On Raspberry Pi OS use the ARM64 package, or scripts/build-raspbian.sh.

## Slide 7: Run it: your first cartridge, from the Store
TRY IT
1
Start PRG32-QT: the Setup screen appears, the same that the firmware shows on the kit
2
Choose Browse Store: the catalogue of the Cartridge Store is downloaded
3
Pick a game, download it, and choose Run Cartridge
4
Play it with the arrow keys, Z and X. Escape brings you back to Setup
5
Open Settings: look at the three performance profiles and at the layout choices
Expected result
A game from the Store runs on your laptop. This is level 1: from now on you can run any cartridge, and look inside it.
Notes: Your first run. Start PRG32-QT: the Setup screen is the same one the firmware shows on the kit. Choose Browse Store, pick a game, download it and choose Run Cartridge. Play with the arrow keys, Z and X; Escape brings you back. Then open Settings and look at the three profiles. The green box states what success looks like: a game from the Store runs on your laptop. If the catalogue stays empty, the problem is the network, not PRG32-QT. For the lecturer: The default Store is store.prg32.uniparthenope.it. If the list stays empty the laptop is not reaching the Internet, or a proxy is in the way: Settings shows the Store address.

## Slide 8: What you should see
The Setup menu
Browse Store
Settings
The same three screens on every system. If you are here, step 1 is done.
Notes: These are the three screens you should have seen: the Setup menu, the Store browser and Settings. They look the same on every operating system. Compare them with your own screen; if they match, level 1 is complete, and from now on you can run any cartridge and look inside it. If they do not, raise your hand now rather than later. For the lecturer: Screens from the PRG32 and PRG32-QT documentation (macOS).

## Slide 9: The toolchain on Windows
# 1. Install Git for Windows (git-scm.com) and Python 3 (python.org)
# 2. Run the ESP-IDF Tools Installer (dl.espressif.com/dl/esp-idf):
# - choose an ESP-IDF release 5.4 or newer
# - select the targets esp32c3 and esp32c6
# - optional: tick the QEMU RISC-V emulator
# 3. Open the shortcut "ESP-IDF PowerShell" that the installer created
# 4. In that window:
cd $HOME\Documents
git clone https://github.com/riscv-prg32/PRG32
cd PRG32
pip install pyaudio zeroconf
python -m prg32 doctor
1
Use the ESP-IDF PowerShell, never a plain terminal
2
On Windows the command is python, not python3
3
pip installs into the ESP-IDF environment: that is intended
4
doctor checks the installation: see the next slides
USE NOW · the PRG32 tools
Notes: On Windows the first three steps use graphical installers: Git, Python, and the ESP-IDF Tools Installer, in which you choose a release 5.4 or newer and the targets esp32c3 and esp32c6. The installer creates a shortcut called ESP-IDF PowerShell: always work in that window, never in a plain terminal. The five commands clone the PRG32 repository, install two Python packages and run the doctor. On Windows the interpreter is called python, not python3. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: From the README of PRG32. An alternative for those who prefer an editor: Visual Studio Code with the Espressif ESP-IDF extension, which installs the same toolchain. Avoid folders with spaces or accented letters in their path: old build tools do not like them.

## Slide 10: The toolchain on macOS
# 1. Homebrew (brew.sh), then the prerequisites
brew install git cmake ninja dfu-util ccache libusb python curl zip portaudio
# 2. ESP-IDF 5.4 for the two chips (a large download)
cd $HOME
git clone -b v5.4 --recursive https://github.com/espressif/esp-idf.git
cd esp-idf
./install.sh esp32c3,esp32c6
. ./export.sh
pip install pyaudio zeroconf
# 3. PRG32
cd $HOME
git clone https://github.com/riscv-prg32/PRG32
cd PRG32
python3 -m prg32 doctor
1
Homebrew first: it provides git, cmake, python
2
install.sh downloads the compilers: be patient
3
The dot before export.sh matters: it changes this terminal
4
Works on Apple Silicon and on Intel
USE NOW · the PRG32 tools
Notes: On macOS there are three blocks. Homebrew installs the prerequisites. Then ESP-IDF is cloned and install.sh downloads the compilers for the two chips: be patient, it is the long part. The line . ./export.sh begins with a dot and a space, and the dot matters: it makes the script change the terminal you are in, instead of a copy that disappears. The last block clones PRG32 and runs the doctor. The same commands work on Apple Silicon and on Intel. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: From the README of PRG32. git may first ask to install the Xcode command line tools: accept. The recursive clone and install.sh fetch a few gigabytes.

## Slide 11: The toolchain on Linux (Debian, Ubuntu)
# 1. Prerequisites
sudo apt update
sudo apt install -y git wget flex bison gperf python3 python3-venv python3-pip \
python3-zeroconf cmake ninja-build ccache libffi-dev libssl-dev dfu-util \
libusb-1.0-0 curl zip portaudio19-dev
# 2. ESP-IDF 5.4 for the two chips (a large download)
cd $HOME
git clone -b v5.4 --recursive https://github.com/espressif/esp-idf.git
cd esp-idf
./install.sh esp32c3,esp32c6
. ./export.sh
pip install pyaudio zeroconf
# 3. PRG32
cd $HOME
git clone https://github.com/riscv-prg32/PRG32
cd PRG32
python3 -m prg32 doctor
1
One long apt line: copy it whole
2
Steps 2 and 3 are the same as on macOS
3
Other distributions: the same packages, other names
4
For the kit only: sudo usermod -aG dialout $USER
USE NOW · the PRG32 tools
Notes: On Debian and Ubuntu the first block is one long apt command, split over three lines by the backslashes: copy it whole. Steps 2 and 3 are identical to those of macOS. On other distributions the packages are the same, with other names. The last callout concerns only those who have a kit: your user must belong to the group dialout to reach the serial port of the board, and you must log out and in again for the change to take effect. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: From the README of PRG32. The dialout group gives access to the serial port of the board: log out and in again after the command. It is not needed for PRG32-QT or QEMU.

## Slide 12: Every new terminal: switch ESP-IDF on
# macOS and Linux: in every new terminal, before anything else
. $HOME/esp-idf/export.sh
cd $HOME/PRG32
# save typing: add these two lines to ~/.zshrc or ~/.bashrc
alias get_idf=". $HOME/esp-idf/export.sh"
alias prg="python3 -m prg32"
# then, in a new terminal
get_idf
prg doctor
# Windows: open "ESP-IDF PowerShell" from the Start menu, then
cd $HOME\Documents\PRG32
1
export.sh acts on the terminal it runs in, and only that one
2
A new window is a new terminal: activate again
3
The aliases are a convenience, not a requirement
4
Run the prg32 commands from the PRG32 folder
USE NOW · the PRG32 tools
Notes: This slide is the daily routine, and it prevents the most common mistake of the first weeks. In every new terminal, before anything else, activate ESP-IDF with export.sh and move into the PRG32 folder. Two aliases save typing: get_idf activates, prg stands for python3 -m prg32. On Windows, opening ESP-IDF PowerShell does the same. Try it deliberately once: open a new terminal, run the doctor without activating, and read the error. Having seen it here, you will recognise it at once later. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The single most common mistake of the first weeks. Make the students close the terminal, open a new one and run doctor without activating: they must see the error once, here, and not during a tutorial.

## Slide 13: The doctor: is everything in place?
$ python3 -m prg32 doctor
[OK] idf.py found
[OK] riscv32-esp-elf-gcc found
[OK] partitions file found: .../PRG32/profiles/partitions_prg32.csv
[OK] partition cart0 parsed (offset=0x210000, size=131072)
...
# and when ESP-IDF is not active in this terminal:
[ERROR] idf.py missing (you must source ESP-IDF export.sh)
1
idf.py: ESP-IDF is active
2
riscv32-esp-elf-gcc: the RISC-V compiler is reachable
3
partitions: the PRG32 folder is complete
4
Any ERROR line says what to do: read it
USE NOW · the PRG32 tools
Notes: The doctor checks the installation and prints one line per check. [OK] idf.py found means that ESP-IDF is active. [OK] riscv32-esp-elf-gcc found means that the RISC-V compiler can be reached. The lines about partitions mean that the PRG32 folder is complete. A line that begins with [ERROR] says what is wrong and what to do: read it to the end before asking for help. When every line is OK, level 2 is done. The last lines of the listing show the error you get in a terminal where ESP-IDF is not active. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Messages of the doctor of October 2026. The four cartridge slots, cart0 to cart3, are regions of the flash memory of the board: 131072 bytes each. If doctor passes, level 2 is done.

## Slide 14: Build a cartridge from the examples
# in the PRG32 folder, ESP-IDF active
python3 -m prg32 cartridge build examples/games/pong/c/game.c \
--portable --entry-prefix pong_c --name pong --out pong.prg32
[OK] built pong.prg32 name=pong load=0x40800000
[INFO] code=3004 mem=3028 audio=0
# what did we build?
python3 -m prg32 cartridge summary pong.prg32
1
cartridge build: source in, .prg32 out
2
--entry-prefix: the name before _init, _update, _draw
3
--portable: runs on every host, not on one firmware only
4
A whole Pong: three thousand bytes
UNDERSTAND LATER · the init, update, draw contract → Lecture 02
USE NOW · the PRG32 tools
Notes: The command cartridge build takes a source file and writes a .prg32 file. Three options are worth understanding. --entry-prefix pong_c is the name that precedes _init, _update and _draw in the source. --portable makes a cartridge that runs on every host, not only on one firmware image. --out names the result. The tool answers with the size of the code: a whole game of Pong is about three thousand bytes. The source here is C, taken from the examples, so that you test the compiler without writing a program. USE NOW: the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: the init, update, draw contract (studied in Lecture 02). For the lecturer: Pong in C from the examples of the repository: it proves that the compiler works without typing a program. In Lecture 02 the source is yours, in assembly, and the command is the same. On Windows write python and put the command on one line.

## Slide 15: Send it to PRG32-QT
# PRG32-QT must be running on this computer
# 1. is it listening?
python3 -m prg32 runtime --url http://localhost:8080
# 2. upload the cartridge to slot cart0 and start it
python3 -m prg32 esp32c6 upload-and-run pong.prg32 \
--url http://localhost:8080 --slot cart0
{"loaded":false,"ok":true,"slot":"cart0","stored":true}
{"ok":true,"slot":"cart0"}
[OK] Finished upload and run on ESP32C6
1
PRG32-QT answers on port 8080, like a board
2
runtime prints its state: a quick connection test
3
upload-and-run stores the cartridge and starts it
4
The command says esp32c6: for the tool, PRG32-QT is a board
USE NOW · the PRG32 tools
Notes: PRG32-QT must be running. The first command, runtime, asks it for its state: if it answers, the connection works. The second, upload-and-run, stores the cartridge in slot cart0 and starts it; the game appears in the window of PRG32-QT. The command says esp32c6 because, for the tool, PRG32-QT behaves like a board that listens on port 8080. The same command with the address of a real board, http://192.168.4.1, sends the game there. Without the tools you can also import the file from the menu of PRG32-QT. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run for these slides on macOS. If localhost does not answer, read the address on the Setup screen of PRG32-QT and use it. Without the tools: in PRG32-QT import the file pong.prg32 and choose Run Cartridge. The same command with --url http://192.168.4.1 sends the game to a real board.

## Slide 16: Look inside: the debugger
1
In PRG32-QT open Settings and enable Run cartridges in RISC-V debug mode
2
Run the cartridge again: the game is on the left, the machine on the right
3
Press the pause button: the game freezes, and one instruction is highlighted in the listing
4
Press the step button a few times: the highlight moves, and some registers change value
5
Press Update, then Draw: the listing jumps to those two functions of the cartridge
6
Press the play button: the game goes on. Lower the speed to 0.1x and watch it in slow motion
UNDERSTAND LATER · registers → Lecture 02
USE NOW · the PRG32-QT debugger
Notes: Now open the machine. In Settings enable Run cartridges in RISC-V debug mode and run the cartridge again: the game is on the left, the machine on the right. Pause: one instruction is highlighted, the next to be executed. Step a few times: the highlight moves and some registers change. Update and Draw show those two functions of the cartridge. Resume, then lower the speed and watch the game in slow motion. You are not expected to understand the registers today; the point is that the debugger opens and obeys. USE NOW: the PRG32-QT debugger (used, not studied, in this course). UNDERSTAND LATER: registers (studied in Lecture 02). For the lecturer: A first look only: Lecture 02 explains what the registers are. The point today is that the debugger opens and responds. Debug mode stays on until you switch it off. Pause, resume and step are the three transport buttons of the debugger, drawn as on a video player: two bars, a triangle, a triangle with a bar. The slides and the tutorials call them Pause, Resume and Step.

## Slide 17: The machine, open
Assembly with the current instruction, the 32 registers, memory, and the counters of the frame
If you see this with your own cartridge, you are ready for the rest of the course.
UNDERSTAND LATER · registers → Lecture 02
USE NOW · the PRG32-QT debugger
Notes: This is what you should see: on the right the listing in assembly with the current instruction highlighted, the thirty-two registers, a window on memory and the counters of the frame. Every element of this picture will be explained in the coming lectures, starting with the registers in Lecture 02. If you see this screen with a cartridge that you built yourself, your workshop is complete. USE NOW: the PRG32-QT debugger (used, not studied, in this course). UNDERSTAND LATER: registers (studied in Lecture 02). For the lecturer: From the documentation of PRG32-QT.

## Slide 18: Level 3: the QEMU emulator
# libraries for the window of the emulator
brew install libgcrypt glib pixman sdl2 libslirp # macOS
sudo apt install -y libgcrypt20 libglib2.0-0 libpixman-1-0 \
libsdl2-2.0-0 libslirp0 # Linux
# the emulator itself (Windows: tick it in the ESP-IDF installer)
python $IDF_PATH/tools/idf_tools.py install qemu-riscv32
. $IDF_PATH/export.sh
# build the firmware for QEMU, stage a cartridge, run
python3 -m prg32 qemu build
python3 -m prg32 qemu upload pong.prg32
python3 -m prg32 qemu run
1
QEMU emulates a whole chip and runs the real firmware
2
qemu build compiles the firmware: several minutes
3
upload stages the cartridge: close QEMU first
4
QEMU opens on Setup: Run Cartridge, cart0. Type in the terminal
USE NOW · the PRG32 tools
Notes: Level 3 has three parts: the libraries that the emulator needs for its window, the emulator itself, and three commands of the tool. qemu build compiles the whole firmware, which takes several minutes the first time. qemu upload stages a cartridge into the flash image, and QEMU must be closed while it runs. qemu run starts the emulator, which opens on the Setup menu: choose Run Cartridge and then cart0. Remember to type in the terminal, not in the window with the picture. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: From the README and docs/usage/qemu.md of PRG32. Not run for these slides. The first build downloads components and compiles the whole firmware. If upload fails, run QEMU once so that the flash image exists, close it, and upload again. Since October 2026 the firmware starts on the Setup menu by default, on QEMU and on the board: choose Run Cartridge, then the slot. The keys go to the terminal that launched QEMU, not to the window with the picture.

## Slide 19: Level 4: the kit
# connect the board with a USB cable; ESP-IDF active, in the PRG32 folder
python3 -m prg32 esp32c6 build-and-flash
# the board starts and creates a Wi-Fi network
# name: PRG32 password: prg32game address: 192.168.4.1
# join it with your laptop, then
python3 -m prg32 esp32c6 upload-and-run pong.prg32 \
--url http://192.168.4.1 --slot cart0
# or let the board join the Wi-Fi of the classroom
python3 -m prg32 wifi set --ssid "NAME" --password "PASSWORD" --mode sta
1
build-and-flash writes the firmware: once per board. It starts on Setup
2
After that, games arrive over Wi-Fi: no more cables
3
The same upload command as for PRG32-QT, another address
4
Linux: your user must be in the group dialout
USE NOW · the PRG32 tools
Notes: Level 4 is the board. Connected by USB, build-and-flash compiles the firmware and writes it into the chip: once per board. The board then starts on the Setup menu and creates a Wi-Fi network called PRG32. Join it, and the upload command you already know works with the address 192.168.4.1: from then on, no cables. The last command makes the board join an existing network instead. On Linux your user must be in the group dialout. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: From the documentation of PRG32. Not run for these slides. If the serial port is not found pass it explicitly: COMx on Windows, /dev/ttyACM0 on Linux, /dev/cu.usbmodem... on macOS. A black screen after flashing usually means that the QEMU firmware was flashed instead of the board's, or that the display is wired to other pins than those of the firmware: since October 2026 the defaults are GPIO8 for DC and GPIO9 for RST (they were GPIO1 and GPIO0), and idf.py menuconfig changes them.

## Slide 20: The complete program: l01.S (1 of 3)
# ARC12 Computer Architecture - Lecture 01: PRG32 and PRG32-QT: Setting Up Your Workshop
# l01.S: a test pattern that proves the installation works
#
# On the screen: four vertical bars, red, green, blue and white, and the words PRG32
# OK.
# Build: python3 -m prg32 cartridge build l01.S --portable \
# --entry-prefix l01 --name l01 --out l01.prg32
.option norelax
.equ BLACK, 0x0000
.equ WHITE, 0xffff
.section .text
.global l01_init
.global l01_update
.global l01_draw
l01_init:
ret
l01_update:
ret
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l01.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 21: The complete program: l01.S (2 of 3)
l01_draw:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li a0, BLACK
call prg32_gfx_clear
li s0, 0 # bar number, 0 to 3
1: la t0, bars # the table of the four colours
slli t1, s0, 2 # 4 bytes per word
add t0, t0, t1
lw a4, 0(t0) # a4 = colour of bar s0
slli a0, s0, 6 # 64 * bar
addi a0, a0, 40 # x = 40 + 64 * bar
li a1, 40 # y
li a2, 48 # width
li a3, 100 # height
call prg32_gfx_rect
addi s0, s0, 1
li t0, 4
blt s0, t0, 1b
li a0, 124
li a1, 160
la a2, ok
li a3, WHITE
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l01.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 22: The complete program: l01.S (3 of 3)
li a4, BLACK
call prg32_gfx_text8
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
.section .rodata
bars: .word 0xf800, 0x07e0, 0x001f, 0xffff # red, green, blue, white
ok: .asciz "PRG32 OK"
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l01.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 23: Run it: what you should see
On the screen
– four vertical bars, red, green, blue and white, and the words PRG32 OK.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 24: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l01.S --portable \
--entry-prefix l01 --name l01 --out l01.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l01.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 25: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l01.S --portable \
--entry-prefix l01 --name l01 --architecture qemu \
--out l01-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l01-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 26: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l01.S --portable \
--entry-prefix l01 --name l01 --architecture esp32c6 \
--out l01-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l01-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 27: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l01; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 28: Before the next lecture
TRY IT
1
Finish the five checks of the Ready slide on your own laptop
2
Download three cartridges from the Store, and find in each the first instruction of update with the debugger
3
Build one of the other examples in examples/games, and run it
4
Close everything, restart the computer, and get back to a running cartridge without these slides
5
Optional: install QEMU and run the same cartridge there
Expected result
Your workshop survives a restart, and you can open it without help.
Notes: Homework. Complete the five checks. Download three cartridges from the Store and, in each, find the first instruction of update with the debugger. Build another example. The fourth task is the real test: close everything, restart the computer and get back to a running cartridge without these slides. If you can do it, you have understood activation, and your workshop is yours. For the lecturer: The fourth task is the real test: it shows who has understood the activation of ESP-IDF.