## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 03
History of Computing: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
03-Computer_Architecture-History_of_Computing.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 03. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: what informatics is; the von Neumann architecture; RISC and an open ISA. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: Boolean algebra (Lecture 08). A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
No listing in Lecture 03: this deck gives you the program to run
2
The complete program: code/l03.S, 94 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l03.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l03.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: The complete program: l03.S (1 of 5)
# ARC12 Computer Architecture - Lecture 03: History of Computing
# l03.S: the stored program: a program that reads one of its own instructions as data
#
# On the screen: a row of 32 lamps showing 0x00130313, the machine code of addi t1,
# t1, 1, and a green square: the word read is the one expected.
# Build: python3 -m prg32 cartridge build l03.S --portable \
# --entry-prefix l03 --name l03 --out l03.prg32
.option norelax
.equ BLACK, 0x0000
.equ GREY, 0x4208
.equ YELLOW, 0xffe0
.equ GREEN, 0x07e0
.equ RED, 0xf800
.section .text
.global l03_init
.global l03_update
.global l03_draw
l03_init:
ret
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l03.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 4: The complete program: l03.S (2 of 5)
l03_update:
ret
# One instruction of the program. For von Neumann's machine it is a number in
# the same memory as the data: the program can load it like any other word.
.option push
.option norvc # keep it 32 bits long: no compressed form
specimen:
addi t1, t1, 1
.option pop
ret
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l03.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 5: The complete program: l03.S (3 of 5)
l03_draw:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li a0, BLACK
call prg32_gfx_clear
la t0, specimen # the ADDRESS of an instruction ...
lw s0, 0(t0) # ... and the instruction, read as DATA
mv a0, s0
li a1, 60
call lamps32 # show its 32 bits
li t0, 0x00130313 # what the assembler should have produced
li a4, RED
bne s0, t0, 1f
li a4, GREEN # equal: instructions are numbers
1: li a0, 152
li a1, 100
li a2, 16
li a3, 16
call prg32_gfx_rect
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l03.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 6: The complete program: l03.S (4 of 5)
# lamps32: show the 32 bits of a word as a row of lamps, bit 31 on the left.
# a0 = the word, a1 = y of the row. A lamp is yellow for 1, grey for 0.
lamps32:
addi sp, sp, -32
sw ra, 28(sp)
sw s0, 24(sp)
sw s1, 20(sp)
sw s2, 16(sp)
mv s0, a0 # the word
mv s1, a1 # y
li s2, 0 # lamp number, 0 on the left
1: li t0, 31
sub t0, t0, s2 # lamp i shows bit 31 - i
srl t1, s0, t0 # bring that bit down to bit 0
andi t1, t1, 1 # keep it, clear all the others
li a4, GREY # lamp off
beqz t1, 2f
li a4, YELLOW # lamp on
2: slli a0, s2, 3
add a0, a0, s2 # 9 * i
addi a0, a0, 16 # x = 16 + 9 * i
mv a1, s1
li a2, 8
li a3, 8
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l03.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: The complete program: l03.S (5 of 5)
call prg32_gfx_rect
addi s2, s2, 1
li t0, 32
blt s2, t0, 1b
lw s2, 16(sp)
lw s1, 20(sp)
lw s0, 24(sp)
lw ra, 28(sp)
addi sp, sp, 32
ret
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l03.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: Run it: what you should see
On the screen
– a row of 32 lamps showing 0x00130313, the machine code of addi t1, t1, 1, and a green square: the word read is the one expected.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 9: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l03.S --portable \
--entry-prefix l03 --name l03 --out l03.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l03.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 10: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l03.S --portable \
--entry-prefix l03 --name l03 --architecture qemu \
--out l03-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l03-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 11: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l03.S --portable \
--entry-prefix l03 --name l03 --architecture esp32c6 \
--out l03-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l03-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 12: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l03; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 13: Exercises: paper first, then PRG32
TRY IT
1
Draw the four units of the von Neumann architecture and write, inside each, one thing of the program of Lecture 02 that lives or happens there
2
For each of these, say whether it is a new way of representing information or of prescribing operations: the abacus, the Jacquard loom, the Pascaline, Boole's algebra, the punched cards of the Analytical Engine, the stored program
3
Download two of the four retro games from the Store, or build them from examples/games; with the counters of the debugger find how many instructions each executes per frame, and compare
Expected result
Registers and ALU: addi executed. Memory: counter and the instructions themselves. Control unit: the fetch of each instruction. Input/output: the bar on the screen.
Notes: Three exercises. The first asks you to draw the four units and to place in each something from the program of Lecture 02: it checks that the architecture is not an abstract diagram for you. The second asks you to classify six inventions as ways of representing information or of prescribing operations; the stored program is the interesting case, because it unifies the two. The third is on the machine: use the counters of the debugger to compare how many instructions two games execute per frame. For the lecturer: Representing: abacus, Pascaline (digits as wheel positions), Boole's algebra. Prescribing: the Jacquard loom, the cards of the Analytical Engine, the stored program, which unifies the two: a program is itself represented information. The third exercise has no fixed answer: the counters depend on the game and on the moment.