## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 17
Verm1, Part 3: A Body, Rules and States: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Verm1 reference implementation contributed by Giuseppe Coviello
Code deck. The concepts, the figures and the questions are in the lecture deck:
17-Computer_Architecture-Verm1_Part_3.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 17. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: arrays in memory; finite-state machines; .text, .rodata, .data; latches and flip-flops; fixed point. USE NOW: the calling convention (Lecture 18) and, used without being studied in this course, the PRG32 tools, the PRG32-QT debugger. UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The 25 listings of Lecture 17, one per slide: read the code, then the numbered remarks beside it
2
The program is your verm1.S; the reference is verm1/verm1_part3.S, 435 lines, shown here region by region
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The reference program is ~/arc12/verm1/verm1_part3.S; tools/tests/verm1_check.py builds it and plays it with a scripted player, and verm1_steps.py runs the intermediate checkpoints. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The reference program is ~/arc12/verm1/verm1_part3.S; tools/tests/verm1_check.py builds it and plays it with a scripted player, and verm1_steps.py runs the intermediate checkpoints. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: The working loop, again
# 1. build the cartridge (from your PRG32 folder, toolchain active)
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --out ~/verm1/verm1.prg32
# 2. send it to PRG32-QT, running on the same computer
python3 -m prg32 esp32c6 upload-and-run ~/verm1/verm1.prg32 \
--url http://localhost:8080 --slot cart0
# or: in PRG32-QT, import the file verm1.prg32 and choose Run Cartridge
USE NOW · the PRG32 tools
Notes: The usual two commands. Today the file changes a great deal, so do not wait until the end to build: build and run after every slide entitled "Run it". If something breaks, the mistake is in the lines added since the last run. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The same two commands. Today the file changes a lot: build after every slide that says Run it, not only at the end.

## Slide 4: CHANGED Constants: a button, a colour, three states
.option norelax
.equ BLACK, 0x0000 # RGB565 colours
.equ WHITE, 0xffff
.equ GREEN, 0x07e0 # the head
.equ BODY, 0x03e0 # the body: a darker green
.equ RED, 0xf800 # the food
.equ CELL, 8 # a cell is 8 x 8 pixels
.equ COLS, 40
.equ ROWS, 24
.equ TOP, 8
.equ SPEED_Q8, 40 # 40/256 of a cell per frame
.equ BTN_LEFT, 0x01
.equ BTN_RIGHT, 0x02
.equ BTN_UP, 0x04
.equ BTN_DOWN, 0x08
.equ BTN_A, 0x10
.equ DIR_RIGHT, 0 # bit 0 = vertical, bit 1 = backwards
.equ DIR_DOWN, 1
.equ DIR_LEFT, 2
.equ DIR_UP, 3
.equ TITLE, 0 # the three states of the game
.equ PLAY, 1
.equ OVER, 2
1
BODY: a darker green, 0x03e0
2
BTN_A is bit 4 of the word of buttons
3
The states are numbers: 0, 1, 2
4
The .section and .global lines move to the next slide
UNDERSTAND NOW · finite-state machines
Notes: The new constants replace those of Part 2. BODY is a darker green for the segments behind the head. BTN_A is the mask of button A, bit 4 of the word of buttons. The three states are simply the numbers 0, 1 and 2, with names. The lines .section and .global, which used to close this block, move to the next slide. UNDERSTAND NOW: finite-state machines. For the lecturer: Replace the constants of Part 2.

## Slide 5: CHANGED .rodata: what stays in the file
.section .rodata # constants: they stay in the cartridge file
title: .asciz "VERM1"
press_a: .asciz "PRESS A"
game_over: .asciz "GAME OVER"
dx: .word 1, 0, -1, 0 # right, down, left, up
dy: .word 0, 1, 0, -1
1
Three strings and the two tables of Part 2
2
Read-only: the program never writes here
3
On the board this could stay in flash
UNDERSTAND NOW · .text, .rodata, .data
Notes: The read-only section: three strings, for the title, the invitation and the game over, and the two tables dx and dy of Part 2. The program never writes here. On the board this section could remain in flash; it is the part of the cartridge that would survive a power-off. UNDERSTAND NOW: .text, .rodata, .data. For the lecturer: Replace the .rodata of Part 2.

## Slide 6: CHANGED .data: what lives in RAM
.section .data # variables: they live in RAM
state: .word TITLE
prev_btn: .word 0 # the buttons one frame ago
dir: .word 0
want: .word 0
step_q8: .word 0
score: .word 0
best: .word 0 # lost when the power goes
food_x: .word 0
food_y: .word 0
head_i: .word 0 # ring index of the head
length: .word 0 # number of cells of the worm
body_x: .space 256 # the ring: one byte per segment
body_y: .space 256
grid: .space COLS*ROWS # one byte per cell: 1 = worm
1
head_x and head_y are gone: the head is in the ring
2
.space reserves bytes without naming each one
3
256 + 256 + 960 bytes: the worm and its world
4
best survives a game, not a power-off
UNDERSTAND NOW · .text, .rodata, .data
Notes: The section of variables. head_x and head_y have disappeared: the head now lives in the ring. The directive .space reserves a number of bytes without naming each one: 256 for body_x, 256 for body_y, 960 for the map. best holds the best score: it survives from one game to the next, but not a power-off, because it lives in RAM. A portable cartridge has no permanent memory of its own: an honest limit. UNDERSTAND NOW: .text, .rodata, .data. For the lecturer: Replace the .data of Part 2. Everything here is lost when the cartridge is unloaded: Lecture 16. A best score that survives needs permanent memory, which a portable cartridge does not have: an honest limit.

## Slide 7: CHANGED init: start on the title
.section .text
.global verm1_init
.global verm1_update
.global verm1_draw
verm1_init:
la t0, state
sw zero, 0(t0) # start on the title screen
la t0, prev_btn
sw zero, 0(t0)
ret
1
init only chooses the first state
2
The game itself is prepared by new_game
3
A leaf again: no frame
UNDERSTAND NOW · finite-state machines
Notes: verm1_init now does one thing only: it chooses the first state, TITLE. Preparing the game is the job of a new function, new_game, called when the player presses A. Delete from your file the old verm1_update, step and verm1_draw: the next slides replace them. Keep place_food, eat_sound and draw_cell. UNDERSTAND NOW: finite-state machines. For the lecturer: Replace verm1_init. Delete from your file verm1_update, step and verm1_draw of Part 2: the next slides replace them. Keep place_food, eat_sound and draw_cell.

## Slide 8: CHANGED update: buttons, and their edges
verm1_update:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
sw s1, 4(sp)
call prg32_input_read
mv s0, a0 # s0 = buttons held in this frame
la t0, prev_btn
lw t1, 0(t0) # t1 = buttons held one frame ago
sw s0, 0(t0)
not t1, t1
and s1, s0, t1 # s1 = buttons pressed just now
1
s0 = buttons now; prev_btn = buttons one frame ago
2
prev_btn is a register: it delays by one frame
3
now AND NOT before: 1 only where a press began
4
s0 and s1 must survive the calls: saved in the frame
USE NOW · the calling convention → Lecture 18
UNDERSTAND NOW · latches and flip-flops
Notes: The first half of the new verm1_update reads the buttons and computes their edges. s0 holds the buttons of this frame; prev_btn, in memory, holds those of the previous frame. The expression "now AND NOT before" gives a 1 only in the positions where a press has just begun, and the result goes into s1. Then prev_btn is updated. It is the edge detector of Lecture 13: a register that delays by one clock, and an AND gate with one input inverted. UNDERSTAND NOW: latches and flip-flops. USE NOW: the calling convention (studied in Lecture 18). For the lecturer: The edge detector of Lecture 13: a flip-flop and an AND gate with one inverted input. Here the flip-flop is a word of memory and the clock is the frame.

## Slide 9: CHANGED update: one branch per state
la t0, state
lw t1, 0(t0) # t1 = present state
li t2, PLAY
beq t1, t2, u_play
andi t3, s1, BTN_A # TITLE or OVER: wait for a new press of A
beqz t3, u_done
li t2, TITLE
beq t1, t2, u_start
sw t2, 0(t0) # OVER --A--> TITLE
j u_done
u_start:
call new_game # TITLE --A--> PLAY
j u_done
u_play:
mv a0, s0
call play_update
u_done:
lw s1, 4(sp)
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
The state is read first: it decides who looks at the inputs
2
TITLE and OVER react only to a new press of A
3
PLAY passes the held buttons to play_update
4
Named labels: u_play, u_start, u_done
UNDERSTAND NOW · finite-state machines
Notes: The second half is the transition table, line by line. The state is read first, and it decides who looks at the inputs. In TITLE a new press of A calls new_game. In OVER a new press of A stores TITLE. In PLAY the buttons that are held, the levels and not the edges, are passed to play_update, because steering must work while a button is kept down. The labels have names here, u_play, u_start, u_done, because numbers would be hard to follow. UNDERSTAND NOW: finite-state machines. For the lecturer: This is the rest of verm1_update: the transition table, line by line. OVER to TITLE only stores the new state; TITLE to PLAY calls new_game, which stores PLAY itself.

## Slide 10: CHANGED draw: what to show in each state
verm1_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, BLACK
call prg32_gfx_clear
li a0, 0
li a1, 0
la a2, title
call draw_text
la t0, state
lw t1, 0(t0)
li t2, TITLE
bne t1, t2, 1f
li a0, 132 # TITLE: only an invitation
li a1, 96
la a2, press_a
call draw_text
j 2f
1: call draw_score # PLAY and OVER: the whole scene
call draw_worm
la t0, food_x
lw a0, 0(t0)
la t0, food_y
lw a1, 0(t0)
li a2, RED
call draw_cell
1
The title line is always drawn
2
TITLE: only the invitation, PRESS A
3
PLAY and OVER: score, worm, food
4
x = 132 centres 7 characters of 8 pixels
UNDERSTAND NOW · finite-state machines
Notes: verm1_draw shows a different picture in each state. The title line is always drawn. In TITLE only the invitation PRESS A appears, centred: 132 is the x that centres seven characters of 8 pixels. In PLAY and OVER the function draws the score, the worm and the food. Note that draw changes nothing: its output depends only on the state and on the memory, as in a Moore machine. UNDERSTAND NOW: finite-state machines. For the lecturer: Replace verm1_draw. The output depends only on the state and on the memory: draw changes nothing.

## Slide 11: CHANGED draw: game over, and draw_text
la t0, state
lw t1, 0(t0)
li t2, OVER
bne t1, t2, 2f
li a0, 124
li a1, 96
la a2, game_over
call draw_text
2: lw ra, 12(sp)
addi sp, sp, 16
ret
draw_text: # a0 = x, a1 = y, a2 = address of the string
addi sp, sp, -16
sw ra, 12(sp)
li a3, WHITE
li a4, BLACK
call prg32_gfx_text8
lw ra, 12(sp)
addi sp, sp, 16
ret
1
OVER adds two words on top of the scene
2
draw_text: white on black, written once
3
It fills a3 and a4 and passes a0 to a2 through
UNDERSTAND NOW · finite-state machines
Notes: The end of verm1_draw: in the state OVER two words are written over the scene. A small helper, draw_text, fills in the two colour arguments, white on black, and passes the first three through, so that each call to draw text needs two lines less. Small helpers like this make a program shorter and easier to change. UNDERSTAND NOW: finite-state machines. For the lecturer: The end of verm1_draw, and a small helper that removes two lines from every text call.

## Slide 12: For now: four functions that do nothing
new_game: # temporary: only change the state
la t0, state
li t1, PLAY
sw t1, 0(t0)
ret
play_update: # temporary: nothing moves yet
ret
draw_score: # temporary
ret
draw_worm: # temporary
ret
1
Stubs: the names exist, so the program builds
2
new_game only changes the state
3
Steps 3 and 4 replace them one at a time
Notes: Four stubs: functions that exist only by name and return at once, except new_game, which just stores PLAY. Thanks to them the program builds and the machine can be tried before its parts are written. It is the method of the first lecture: start with returns that do nothing, then add one thing at a time. For the lecturer: Start with returns that do nothing, then add one thing at a time: the method of the first lecture. This intermediate program is built and run by tests/verm1_steps.py.

## Slide 13: Run it: a machine with nothing inside
TRY IT
1
Build and run: the title line and PRESS A in the middle of the screen
2
Press A: the invitation disappears. A red cell is in the top-left corner: the food, at column 0 of row 0
3
Nothing moves and the game cannot end: PLAY has no rules yet
4
In the debugger, find the variable state and watch it change from 0 to 1 when you press A
Expected result
Title screen, then an empty field with one red cell at the top left.
Notes: Run it. You see the title line and PRESS A. Press A: the invitation disappears and a red cell appears in the top-left corner, because the variables of the food are still zero. Nothing moves and the game cannot end: PLAY has no rules yet. In the debugger, find the variable state and watch it go from 0 to 1 when you press A: the machine works, and it is empty. For the lecturer: The food is at (0, 0) because food_x and food_y start at zero and the stub of new_game does not call place_food.

## Slide 14: NEW new_game: empty the map, lay the worm
new_game:
addi sp, sp, -16
sw ra, 12(sp)
la t0, grid
li t1, COLS*ROWS
1: sb zero, 0(t0) # empty the grid, one byte per cell
addi t0, t0, 1
addi t1, t1, -1
bnez t1, 1b
li t1, 0 # i = 0, 1, 2: three cells in row 12
2: la t0, body_x
add t0, t0, t1
addi t2, t1, 3
sb t2, 0(t0) # columns 3, 4, 5
la t0, body_y
add t0, t0, t1
li t3, 12
sb t3, 0(t0)
la t0, grid+12*COLS
add t0, t0, t2
li t3, 1
sb t3, 0(t0) # mark the cell as occupied
addi t1, t1, 1
li t3, 3
blt t1, t3, 2b
1
Replace the stub of new_game with this
2
960 bytes set to zero, one sb at a time
3
Three segments: columns 3, 4, 5 of row 12
4
Each one is written twice: in the ring and in the map
UNDERSTAND NOW · arrays in memory
Notes: The first half of the real new_game. A loop sets the 960 bytes of the map to zero, one sb at a time. Then the worm is laid down: three segments in columns 3, 4 and 5 of row 12. Each segment is written twice: its column and row in the ring, and a 1 in the map. The expression grid+12*COLS is computed by the assembler. Since each entry is one byte, the index is added to the base address without any shift. UNDERSTAND NOW: arrays in memory. For the lecturer: grid+12*COLS is computed by the assembler: the address of the first byte of row 12. sb stores one byte; the index is added to the base address, with no shift because each entry is one byte.

## Slide 15: NEW new_game: the variables, the food, PLAY
la t0, head_i
li t1, 2
sw t1, 0(t0) # the head is entry 2 of the ring
la t0, length
li t1, 3
sw t1, 0(t0)
la t0, dir
sw zero, 0(t0)
la t0, want
sw zero, 0(t0)
la t0, step_q8
sw zero, 0(t0)
la t0, score
sw zero, 0(t0)
call place_food
la t0, state
li t1, PLAY
sw t1, 0(t0)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
head_i = 2 and length = 3 describe the worm
2
Direction, timer and score start from zero
3
The last thing: the state becomes PLAY
UNDERSTAND NOW · arrays in memory
Notes: The second half sets the variables: head_i is 2 and length is 3, which together describe the worm just laid; direction, timer and score start from zero; the first food is placed. The last instruction stores PLAY in the state. The order is deliberate: the transition is complete only when everything is ready. UNDERSTAND NOW: arrays in memory. For the lecturer: The second half of new_game. The transition TITLE to PLAY is complete only when everything is ready: the state is stored last.

## Slide 16: NEW draw_worm: walk the ring backwards
draw_worm:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li s0, 0 # s0 = i: segment 0 is the head
1: la t0, length
lw t1, 0(t0)
bge s0, t1, 3f
la t0, head_i
lw t1, 0(t0)
sub t1, t1, s0
andi t1, t1, 255 # ring index of segment i
la t0, body_x
add t0, t0, t1
lbu a0, 0(t0)
la t0, body_y
add t0, t0, t1
lbu a1, 0(t0)
li a2, BODY
bnez s0, 2f
li a2, GREEN # the head is brighter
2: call draw_cell
addi s0, s0, 1
j 1b
3: lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Replace the stub of draw_worm with this
2
Segment i is entry head_i - i, AND 255
3
lbu loads one byte as an unsigned number
4
Segment 0 is the head: a brighter green
UNDERSTAND NOW · arrays in memory
Notes: draw_worm walks the ring backwards from the head: segment number i is entry head_i - i, masked with 255. Column and row are loaded with lbu, which reads one byte as an unsigned number, and passed to draw_cell. Segment 0, the head, is drawn in a brighter green than the others. The loop ends when i reaches the length. UNDERSTAND NOW: arrays in memory. For the lecturer: lbu and not lb: a column is a number from 0 to 39, never negative. With lb a byte of 200 or more would become negative: Lecture 05. Here both would work; lbu says what we mean.

## Slide 17: NEW draw_score: the marks of Part 2
draw_score:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li s0, 0 # s0 = i: one mark per point
1: la t0, score
lw t1, 0(t0)
bge s0, t1, 2f
slli a0, s0, 2
addi a0, a0, 56 # x = 56 + 4 * i
li a1, 1
li a2, 3
li a3, 6
li a4, WHITE
call prg32_gfx_rect
addi s0, s0, 1
j 1b
2: lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Replace the stub of draw_score with this
2
The loop of Part 2, now a function
3
It uses s0, so it saves and restores it
USE NOW · the calling convention → Lecture 18
Notes: draw_score is the loop that in Part 2 was inside verm1_draw, now a function of its own: one small mark for each point. It uses s0 as its counter, so it saves it at the beginning and restores it at the end. USE NOW: the calling convention (studied in Lecture 18). For the lecturer: The same loop that was inside verm1_draw in Part 2.

## Slide 18: One stub is left
play_update: # temporary: nothing moves yet
ret
1
play_update still does nothing
2
The worm exists, and stands still
Notes: Of the four stubs only one is left: play_update, which still does nothing. The worm exists in memory and on the screen, and stands still. For the lecturer: Only this stub remains from the previous four.

## Slide 19: Run it: a worm that stands still
TRY IT
1
Build and run, press A: a worm of three cells in row 12, columns 3 to 5, the head on the right
2
The food is now at a random cell: new_game calls place_food
3
In the debugger type the address of body_x in the Memory field: the first bytes are 03 04 05
4
Find grid + 12 x 40 + 3: three bytes at 01 in a sea of zeros
Expected result
Three green cells, the rightmost brighter; one red cell somewhere; nothing moves.
Notes: Run it and press A: a worm of three cells in row 12, with the brighter head on the right, and the food in a random cell. Now look at memory with the debugger. At the address of body_x the first bytes are 03 04 05. In the map, at row 12 times 40 plus 3, there are three bytes at 01 in a sea of zeros. You are looking at the two structures of the lecture deck, the ring and the map, filled. For the lecturer: To find the address of body_x: break at the start of draw_worm and step until la t0, body_x has run; t0 holds it. grid is 512 bytes after body_x; row 12 starts 480 bytes after grid.

## Slide 20: CHANGED play_update: your update of Part 2
play_update: # a0 = buttons held
addi sp, sp, -16
sw ra, 12(sp)
la t0, dir
lw t1, 0(t0) # t1 = direction of the last step
la t0, want
lw t2, 0(t0) # t2 = wanted direction, so far
andi t3, a0, BTN_RIGHT
beqz t3, 1f
li t2, DIR_RIGHT
1: andi t3, a0, BTN_DOWN
beqz t3, 2f
li t2, DIR_DOWN
2: andi t3, a0, BTN_LEFT
beqz t3, 3f
li t2, DIR_LEFT
3: andi t3, a0, BTN_UP
beqz t3, 4f
li t2, DIR_UP
4: xor t3, t2, t1 # opposite directions differ in bit 1 only
li t4, 2
beq t3, t4, 5f # a U-turn: ignore the request
sw t2, 0(t0)
5:
1
Replace the last stub with this and the next slide
2
The steering of Part 2, under a new name
3
The buttons arrive in a0: no call to read them
UNDERSTAND NOW · fixed point
Notes: play_update is your verm1_update of Part 2 under a new name: the four button tests and the U-turn rule. One difference: the buttons arrive as an argument in a0, so there is no call to read them. UNDERSTAND NOW: fixed point. For the lecturer: Take the body of the old verm1_update: remove the call to prg32_input_read and rename the function.

## Slide 21: CHANGED play_update: the timer
la t0, step_q8
lw t1, 0(t0)
addi t1, t1, SPEED_Q8 # add a fraction of a cell
li t2, 256
blt t1, t2, 6f # less than one whole cell: wait
sub t1, t1, t2
sw t1, 0(t0)
call step # one whole cell: move
j 7f
6: sw t1, 0(t0)
7: lw ra, 12(sp)
addi sp, sp, 16
ret
1
Exactly the timer of Part 2
2
One whole cell accumulated: call step
UNDERSTAND NOW · fixed point
Notes: The end of play_update is exactly the timer of Part 2: add the speed, and when a whole cell has accumulated call step. UNDERSTAND NOW: fixed point. For the lecturer: The end of play_update.

## Slide 22: CHANGED step: three registers to keep
step:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp) # s0 = column of the new head
sw s1, 4(sp) # s1 = row of the new head
sw s2, 0(sp) # s2 = 0 when the worm eats
la t0, want
lw t1, 0(t0)
la t0, dir
sw t1, 0(t0) # the wanted direction is now the direction
slli t1, t1, 2 # table offset = direction * 4 bytes
la t0, dx
add t0, t0, t1
lw t2, 0(t0) # t2 = dx[direction]
la t0, dy
add t0, t0, t1
lw t3, 0(t0) # t3 = dy[direction]
1
s0, s1: the cell of the new head
2
s2: zero when the worm eats
3
They must survive place_food: s registers
4
The table lookup is that of Part 2
USE NOW · the calling convention → Lecture 18
Notes: The beginning of step. Three registers must keep their values across the calls that follow: s0 and s1 for the cell of the new head, s2 for the result of the food test. So the frame saves ra and three s registers. The lookup of dx and dy is that of Part 2. USE NOW: the calling convention (studied in Lecture 18). For the lecturer: The frame has room for four words: ra and three saved registers.

## Slide 23: CHANGED step: where will the head be?
la t0, head_i
lw t5, 0(t0) # t5 = ring index of the head
la t0, body_x
add t0, t0, t5
lbu s0, 0(t0) # one byte: the column of the head
add s0, s0, t2
bgez s0, 1f
li s0, COLS-1 # off the left edge: wrap
1: li t4, COLS
blt s0, t4, 2f
li s0, 0
2: la t0, body_y
add t0, t0, t5
lbu s1, 0(t0)
add s1, s1, t3
bgez s1, 3f
li s1, ROWS-1
3: li t4, ROWS
blt s1, t4, 4f
li s1, 0
4:
1
The present head is entry head_i of the ring
2
One byte each for column and row: lbu
3
Add dx and dy, wrap as in Part 2
4
Nothing is written yet: first we must look
UNDERSTAND NOW · arrays in memory
Notes: Where will the head be? The present head is entry head_i of the ring: its column and row are loaded with lbu, dx and dy are added, and the result wraps at the edges as in Part 2. The new cell is now in s0 and s1. Nothing has been written: first the program must look. UNDERSTAND NOW: arrays in memory. For the lecturer: The new cell is only computed, in s0 and s1. Writing it comes after the collision test.

## Slide 24: CHANGED step: eat, or move the tail
la t0, food_x
lw t1, 0(t0)
xor t1, t1, s0
la t0, food_y
lw t2, 0(t0)
xor t2, t2, s1
or s2, t1, t2 # s2 = 0 if the new head is on the food
la t0, length
lw t1, 0(t0)
bnez s2, 5f # not eating: the tail moves on
li t2, 255
bge t1, t2, 5f # the ring is full: no more growth
addi t1, t1, 1
sw t1, 0(t0) # eating: one cell longer, the tail stays
j 6f
5: la t0, head_i
lw t2, 0(t0)
sub t2, t2, t1
addi t2, t2, 1
andi t2, t2, 255 # ring index of the tail
la t0, body_x
add t0, t0, t2
lbu t3, 0(t0)
la t0, body_y
add t0, t0, t2
lbu t4, 0(t0)
1
The comparator of Part 2 leaves its result in s2
2
Eating: length + 1, the tail stays where it is
3
Not eating: find the tail, entry head_i - length + 1
4
At 255 cells the worm stops growing
UNDERSTAND NOW · arrays in memory
Notes: Eat, or move the tail. The comparator of Part 2 leaves its result in s2: zero if the new head is on the food. If the worm eats, the length grows by one and the tail stays where it is. If not, the tail must leave: its entry is head_i - length + 1, and its column and row are loaded. Growing and not moving the tail are the same thing: that is the whole trick of Snake. UNDERSTAND NOW: arrays in memory. For the lecturer: Growing and not moving the tail are the same thing: this is the whole trick of Snake. t3 and t4 receive the column and row of the tail.

## Slide 25: NEW step: free the tail, test the head
li t5, COLS
mul t4, t4, t5
add t4, t4, t3 # cell number of the tail = row * 40 + column
la t0, grid
add t0, t0, t4
sb zero, 0(t0) # the tail cell is free again
6: li t5, COLS
mul t4, s1, t5
add t4, t4, s0 # cell number of the new head
la t0, grid
add t0, t0, t4
lbu t1, 0(t0)
beqz t1, 7f # a free cell: go on
la t0, state
li t1, OVER
sw t1, 0(t0) # the worm bit itself: PLAY --> OVER
la t0, score
lw t1, 0(t0)
la t0, best
lw t2, 0(t0)
ble t1, t2, 9f
sw t1, 0(t0) # a new best score
j 9f
1
Byte number = row x 40 + column: mul and add
2
Clear the tail's byte first, then test the head's
3
So the head may enter the cell the tail just left
4
Occupied: the state becomes OVER, best is updated
UNDERSTAND NOW · arrays in memory
Notes: Now the map. The number of a byte is row times 40 plus column, computed with mul and add. First the byte of the tail is cleared; then the byte of the new head is tested. The order matters: in the same step the tail moves away, so the head may enter the cell that the tail has just left. If the byte is 1 the worm has bitten itself: the state becomes OVER and the best score is updated. UNDERSTAND NOW: arrays in memory. For the lecturer: The order matters: freeing the tail before the test allows the worm to chase its own tail, as in the original game. mul needs the M extension of RISC-V, which the ESP32-C6 has.

## Slide 26: NEW step: write the new head
7: li t1, 1
sb t1, 0(t0) # occupy the new cell
la t0, head_i
lw t1, 0(t0)
addi t1, t1, 1
andi t1, t1, 255 # the ring wraps after entry 255
sw t1, 0(t0)
la t0, body_x
add t0, t0, t1
sb s0, 0(t0) # write the new head into the ring
la t0, body_y
add t0, t0, t1
sb s1, 0(t0)
bnez s2, 9f
la t0, score
lw t1, 0(t0)
addi t1, t1, 1
sw t1, 0(t0)
call place_food
call eat_sound
9: lw s2, 0(sp)
lw s1, 4(sp)
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Mark the cell in the map: t0 still points to it
2
head_i + 1, AND 255: the ring closes
3
Write column and row in the new entry
4
If s2 is zero: a point, new food, a sound
UNDERSTAND NOW · arrays in memory
Notes: If the cell is free, the new head is written: a 1 in the map, head_i plus 1 masked with 255, and column and row in the new entry of the ring. Then, if s2 is zero, the reward: a point, new food, a sound. After a collision the function skips all of this, so the screen shows the worm as it was before the fatal step. UNDERSTAND NOW: arrays in memory. For the lecturer: The end of step. After a collision the function jumps straight to label 9: nothing is written, and the screen shows the worm as it was before the fatal step.

## Slide 27: CHANGED place_food: not on the worm
place_food:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
1: li a0, 0
li a1, COLS-1
call prg32_random_number
mv s0, a0 # s0 = a column
li a0, 0
li a1, ROWS-1
call prg32_random_number # a0 = a row
li t1, COLS
mul t2, a0, t1
add t2, t2, s0
la t0, grid
add t0, t0, t2
lbu t3, 0(t0)
bnez t3, 1b # on the worm: try again
la t0, food_x
sw s0, 0(t0)
la t0, food_y
sw a0, 0(t0)
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Draw a cell at random, then look at the map
2
Occupied: draw again, until a free cell comes
3
The column waits in s0 during the second call
USE NOW · the calling convention → Lecture 18
Notes: place_food is corrected: it draws a random cell, looks at its byte in the map, and if the cell is occupied draws again, until a free one comes out. The column waits in s0 while the second random number is requested. The loop is short: even with the longest worm fewer than two attempts are needed on average. USE NOW: the calling convention (studied in Lecture 18). For the lecturer: Replace place_food of Part 2. The loop ends quickly as long as the worm is short: with 255 cells out of 960 the average is fewer than two attempts.

## Slide 28: Run it: Verm1, Part 3
After four meals: seven cells and four marks
The worm has bitten itself
Expected: the worm follows the head and grows; turning into the body ends the game; A returns to the title, A again starts a new game.
Notes: Run it: this is Verm1, Part 3. The worm follows the head and grows at every meal; turning into the body ends the game; A returns to the title, and A again starts a new game. The two screenshots come from the automatic test: seven cells and four marks after four meals, and the game-over screen. For the lecturer: Screenshots produced by tools/tests/verm1_check.py.

## Slide 29: Appendix: two functions that did not change
eat_sound and draw_cell are those of Part 2: keep them as they are
They are on the next two slides, so that this deck contains the whole program
The complete file is the sum of the slides marked NEW and CHANGED, plus these two
Notes: Two functions did not change with respect to Part 2: eat_sound and draw_cell. They are reprinted on the next two slides, marked UNCHANGED, so that this deck contains the whole program. The complete file is the sum of the slides marked NEW and CHANGED, plus these two. For the lecturer: Reference file for this part: verm1/verm1_part3.S (435 lines).

## Slide 30: UNCHANGED eat_sound
eat_sound:
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0 # channel
li a1, 0 # instrument
li a2, 72 # note: C5
li a3, 255 # volume
li a4, 60 # milliseconds
call prg32_audio_note
lw ra, 12(sp)
addi sp, sp, 16
ret
1
One note of 60 milliseconds, as in Part 2
Notes: eat_sound, as in Part 2: five arguments and a call to prg32_audio_note, for one note of 60 milliseconds.

## Slide 31: UNCHANGED draw_cell
draw_cell: # a0 = column, a1 = row, a2 = colour
addi sp, sp, -16
sw ra, 12(sp)
slli a0, a0, 3 # x = column * 8
slli a1, a1, 3
addi a1, a1, TOP # y = row * 8 + 8
mv a4, a2 # the colour is the fifth argument
li a2, CELL
li a3, CELL
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Column, row and colour in; one rectangle out
Notes: draw_cell, as in Part 2: column, row and colour come in, the cell coordinates are converted to pixels, and one rectangle is drawn.

## Slide 32: Run it: what you should see
On the screen
– a title screen; after A, a worm of three cells that grows by one at every meal; biting the body ends the game, and A returns to the title.
What to press
– A starts a game; steer with the joystick
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 33: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --out verm1.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run verm1.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 34: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --architecture qemu \
--out verm1-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload verm1-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 35: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --architecture esp32c6 \
--out verm1-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run verm1-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 36: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix verm1; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 37: Make it yours
TRY IT
1
Walls: the worm dies when it leaves the screen instead of wrapping
2
Start with a worm of five cells; then let the length at the start depend on the best score
3
Poison: a second, blue cell that makes the worm one cell shorter
4
On the game-over screen show the best score as marks on the second line
Expected result
Each change touches one or two functions. Keep a copy of the working Part 3: Part 4 starts from it.
Notes: Four changes of your own. Walls: the worm dies at the edge instead of wrapping. A longer worm at the start, perhaps depending on the best score. Poison: a second, blue cell that makes the worm one cell shorter. And the best score shown as marks on the game-over screen. Each touches one or two functions. Keep a copy of the working Part 3 first. For the lecturer: Walls: in step-head, replace each wrap with a jump to the code that stores OVER. Poison: move the tail twice in one step, clearing both bytes of the map, and never go below length 1.