## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 20
Buses and the Video Card: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
20-Computer_Architecture-Video_Card.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 20. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: the frame buffer; device controllers; buses and bandwidth; the video card; GPU and GPGPU. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The listing of Lecture 20: read the code, then the numbered remarks beside it
2
The complete program: code/l20.S, 32 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l20.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l20.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: One pixel, please
li a0, 100 # x
li a1, 50 # y
li a2, 0xf800 # red, in RGB565
call prg32_gfx_pixel # ... where does it go?
# what the runtime does, in principle:
li t0, 320
mul t1, a1, t0 # y * 320
add t1, t1, a0 # + x = position in the frame
la t2, framebuffer
add t2, t2, t1 # ADDRESS of that pixel
sb t3, 0(t2) # store its palette index (one byte)
1
The screen is an array in memory, one element per pixel: the frame buffer
2
Drawing a pixel is a store instruction at address base + y x 320 + x
3
Nothing appears until the frame is sent to the display: prg32_gfx_present
4
On a PC these two jobs, keeping the frame and sending it to the monitor, belong to the video card
UNDERSTAND NOW · the frame buffer
Notes: The first four lines are yours: x in a0, y in a1, a colour in a2, and a call to prg32_gfx_pixel. The second half shows, in principle, what the runtime does with them: it multiplies y by 320, adds x, adds the address of the frame buffer, and stores one byte there. The screen is an array in memory with one element per pixel, and drawing a pixel is a store. Nothing appears until the frame is sent to the display. On a PC, keeping the frame and sending it are the job of the video card. UNDERSTAND NOW: the frame buffer. For the lecturer: The second half is a sketch of the principle, not the source of the runtime: t3 stands for the palette index that the runtime derives from the RGB565 colour in a2. On the ESP32-C6 the PRG32 frame buffer is 320 x 200 bytes, one palette index per pixel (docs/hardware/ili9341.md).

## Slide 4: The complete program: l20.S (1 of 2)
# ARC12 Computer Architecture - Lecture 20: Buses and the Video Card
# l20.S: one pixel, please
#
# On the screen: a single red pixel at x = 100, y = 50 on a black screen. Look
# closely.
# Build: python3 -m prg32 cartridge build l20.S --portable \
# --entry-prefix l20 --name l20 --out l20.prg32
.option norelax
.section .text
.global l20_init
.global l20_update
.global l20_draw
l20_init:
ret
l20_update:
ret
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l20.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 5: The complete program: l20.S (2 of 2)
l20_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0
call prg32_gfx_clear
li a0, 100 # x
li a1, 50 # y
li a2, 0xf800 # red, in RGB565
call prg32_gfx_pixel # ... where does it go?
lw ra, 12(sp)
addi sp, sp, 16
ret
USE NOW · the complete program
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l20.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 6: Run it: what you should see
On the screen
– a single red pixel at x = 100, y = 50 on a black screen. Look closely.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 7: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l20.S --portable \
--entry-prefix l20 --name l20 --out l20.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l20.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 8: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l20.S --portable \
--entry-prefix l20 --name l20 --architecture qemu \
--out l20-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l20-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 9: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l20.S --portable \
--entry-prefix l20 --name l20 --architecture esp32c6 \
--out l20-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l20-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 10: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l20; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 11: Exercises: paper first, then PRG32
TRY IT
1
Compute the memory for one 4K frame in True Color, and the bytes per second at 60 frames per second
2
The PRG32 display bus runs at 27 MHz: how long does it take to send 20 rows of 320 pixels at 16 bits per pixel?
3
Draw a diagonal line pixel by pixel with prg32_gfx_pixel in a loop
4
Fill the screen once with prg32_gfx_clear and once with 64,000 calls to prg32_gfx_pixel: compare the frame rates
5
Change one palette entry with prg32_palette_set every frame and watch every pixel that uses it change at once
Expected result
On paper: 24,883,200 bytes per frame, about 1.5 GB per second; 102,400 bits, about 3.8 ms. On PRG32: palette cycling animates the screen without redrawing a single pixel.
Notes: Five exercises. Compute the memory of a 4K frame in True Color and the bytes per second at 60 frames. Compute how long the display bus of PRG32 takes to send 20 rows. Draw a diagonal line pixel by pixel. Fill the screen once with a single call and once with 64,000 calls, and compare the frame rates. Finally change one entry of the palette at every frame: all the pixels that use it change together, without being redrawn. For the lecturer: The last exercise shows why indexed colour was loved by game programmers: one store changes thousands of pixels. API calls from the textbook appendix (prg32_palette_set, prg32_gfx_clear, prg32_gfx_pixel).