## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 02
First Contact: RISC‑V Assembly on PRG32: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
02-Computer_Architecture-First_Contact_with_RISC-V_Assembly.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 02. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: registers, compute, move, jump; registers; the init, update, draw contract; arguments in a0 to a7; why ra is saved; address, value, load, store; the base instructions; pseudo-instructions; an instruction is a number; tracing by hand. USE NOW: the calling convention (Lecture 18); bit masks (Lecture 08) and, used without being studied in this course, the assembler directives, the PRG32 tools, the PRG32 runtime calls, the PRG32-QT debugger, the complete program. UNDERSTAND LATER: the stack (Lecture 18); addressing modes (Lecture 19); instruction formats (Lecture 19); hexadecimal (Lecture 04); two's complement (Lecture 05); fixed point (Lecture 06); Boolean algebra (Lecture 08); the adder (Lecture 09); from volts to bits (Lecture 10); latches and flip-flops (Lecture 13); the processor cycle (Lecture 19); the Verm1 project (Lecture 07). A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The 5 listings of Lecture 02, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l02.S, 60 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The program of this lecture is ~/arc12/code/l02.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l02.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Step 1: the smallest program that runs
# Assembly Lab 1: the smallest program that runs
.option norelax
.section .text
.global first_init
.global first_update
.global first_draw
first_init:
ret
first_update:
ret
first_draw:
ret
1
.option norelax keeps the layout of the cartridge predictable: every PRG32 example starts with it
2
.section .text says that what follows is executable code
3
.global makes a label visible to the firmware, which finds your functions by name
4
ret returns to the caller: three functions that do nothing, correctly
USE NOW · the assembler directives
Notes: The smallest program that runs. .option norelax, with which every PRG32 example begins, keeps the layout of the cartridge predictable by preventing the linker from rewriting instruction sequences. .section .text declares that executable code follows. Each .global exports a label beyond the file, so that the firmware can locate the function by name. Then come three functions, each consisting of the single instruction ret, which returns control to the caller. The result is a black screen, and it is a success: the framework has found the three entry points, invoked them, and regained control. These directives are used as given; the course does not study the assembler itself. USE NOW: the assembler directives (used, not studied, in this course). For the lecturer: Source: labs/05-asm-first-contact/step1_skeleton.S. Expected result: a black screen. The achievement is that the framework found the three functions, called them, and survived.

## Slide 4: Build it, run it
# 1. build a portable cartridge from one assembly file
python3 -m prg32 cartridge build step1_skeleton.S --portable \
--entry-prefix first --name step1 --out build/step1.prg32
# 2a. run it in QEMU on your laptop
python3 -m prg32 qemu upload build/step1.prg32
python3 -m prg32 qemu run
# 2b. or send it to a board, or to PRG32-QT, over the network
python3 -m prg32 esp32c6 upload-and-run build/step1.prg32 \
--url http://192.168.4.1 --slot cart0
USE NOW · the PRG32 tools
Notes: Two commands that will be typed hundreds of times. cartridge build turns the assembly file into a cartridge: --entry-prefix first gives the prefix of the three entry points, --out the name of the output. The cartridge is then executed: in QEMU with qemu upload followed by qemu run, or on a board or on PRG32-QT with upload-and-run and the address of the host, which for PRG32-QT on the student's own laptop is http://localhost:8080. The same cartridge file serves all three hosts. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Source: labs/run.sh. With PRG32_HOME set, the whole sequence is: labs/run.sh 05-asm-first-contact/step1_skeleton.S first . The cartridge file is byte-for-byte the same for QEMU, the board and PRG32-QT.

## Slide 5: Step 2: say hello
first_draw:
addi sp, sp, -16 # prologue: a 16-byte frame
sw ra, 12(sp) # save the return address
li a0, BLACK
call prg32_gfx_clear
li a0, 32 # x
li a1, 40 # y
la a2, title # address of the string
li a3, WHITE # foreground
li a4, BLACK # background
call prg32_gfx_text8
lw ra, 12(sp) # epilogue: restore ra
addi sp, sp, 16 # release the frame
ret
.section .rodata
title:
.asciz "HELLO PRG32"
Screenshot: this step, built and run on PRG32
The first argument goes in a0, the second in a1, and so on. li loads a number; la loads the address of a label.
USE NOW · the PRG32 runtime calls
UNDERSTAND NOW · arguments in a0 to a7
Notes: The second step writes to the screen. first_draw is best read in three parts. The first two lines open a stack frame and save ra, because the function is about to make calls. Two calls follow: prg32_gfx_clear, with the colour in a0, and prg32_gfx_text8, with five arguments in a0 to a4: x, y, the address of the string, foreground colour and background colour. The two ways of loading a register should be distinguished: li loads a numerical constant, la the address of a label. The last three lines restore ra, release the frame and return. The string itself is data, placed in the read-only section .rodata. UNDERSTAND NOW: arguments in a0 to a7. USE NOW: the PRG32 runtime calls (used, not studied, in this course). For the lecturer: Source: labs/05-asm-first-contact/step2_hello.S. The .equ lines (BLACK 0x0000, WHITE 0xffff) are omitted on the slide.

## Slide 6: Step 3: a value that survives between frames
first_update:
# A leaf function: it calls nothing,
# so it needs no stack frame.
la t0, counter # t0 = ADDRESS of counter
lw t1, 0(t0) # t1 = VALUE stored there (load)
addi t1, t1, 1 # one tick per frame (modify)
sw t1, 0(t0) # write it back (store)
ret
.section .data
counter: .word 0
1
counter is a label: it names a location in memory, in the .data section, holding one 32-bit word
2
la puts the ADDRESS of that location in t0
3
lw reads the VALUE at that address into t1; sw writes it back
4
The processor computes only in registers: load, modify, store
UNDERSTAND NOW · address, value, load, store
Notes: The third step preserves a value from one frame to the next. Registers do not retain their contents between successive invocations of update, so the value must reside in memory. counter is a label naming a location in the .data section that holds one word. The four instructions constitute the pattern underlying every variable: la places the address of the location in t0; lw loads the value into t1; addi modifies it; sw writes it back. Load, modify, store: the defining idiom of a load-store architecture. Nothing changes on the screen yet: the counter advances, but nothing draws it. UNDERSTAND NOW: address, value, load, store. For the lecturer: Source: labs/05-asm-first-contact/step3_counter.S. Nothing visible changes yet: the counter ticks but nobody draws it. Ask the class how they could prove that it is ticking (answer: the debugger of PRG32-QT, or the next step).

## Slide 7: Step 4: make the counter visible
la t0, counter
lw t1, 0(t0)
andi a2, t1, 255 # width = counter modulo 256
li a0, 32 # x
li a1, 60 # y
li a3, 8 # height
li a4, GREEN # .equ GREEN, 0x07e0
call prg32_gfx_rect
Screenshot: this step, built and run on PRG32
The bar grows from 0 to 255 pixels, then starts again. andi with 255 keeps only the low eight bits of the counter.
USE NOW · bit masks → Lecture 08
Notes: The fourth step renders the counter visible as a green bar. The value is loaded, and andi a2, t1, 255 retains only its eight least significant bits, so the width runs from 0 to 255 and then begins again. The remaining registers carry the arguments of prg32_gfx_rect: x, y, width, height and colour. These eight lines contain the seeds of three later lectures: 255 written as 0xFF (positional notation, Lecture 04), andi used as a mask (Boolean algebra, Lecture 08), and 0x07e0 denoting green (the encoding of colour, Lecture 04). It is worth remembering where each was first encountered. USE NOW: bit masks (studied in Lecture 08). For the lecturer: Source: labs/05-asm-first-contact/step4_bar.S (the lines added to first_draw). Three future lectures hide in these eight lines: 255 = 0xFF (positional notation), andi as a bit mask (Boolean algebra), 0x07e0 as a colour (information encoding).

## Slide 8: The complete program: l02.S (1 of 3)
# ARC12 Computer Architecture - Lecture 02: First Contact: RISC-V Assembly on PRG32
# l02.S: the four steps of the lecture in one file
#
# On the screen: HELLO PRG32 and, under it, a green bar that grows by one pixel per
# frame and starts again at 256.
# Build: python3 -m prg32 cartridge build l02.S --portable \
# --entry-prefix first --name first --out first.prg32
.option norelax
.equ BLACK, 0x0000
.equ WHITE, 0xffff
.equ GREEN, 0x07e0
.section .text
.global first_init
.global first_update
.global first_draw
first_init: # step 1: a function that returns
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l02.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: The complete program: l02.S (2 of 3)
first_update: # step 3: a value that survives between frames
# A leaf function: it calls nothing, so it needs no stack frame.
la t0, counter # t0 = ADDRESS of counter
lw t1, 0(t0) # t1 = VALUE stored there (load)
addi t1, t1, 1 # one tick per frame (modify)
sw t1, 0(t0) # write it back (store)
ret
first_draw: # step 2: say hello
addi sp, sp, -16 # prologue: a 16-byte frame
sw ra, 12(sp) # save the return address
li a0, BLACK
call prg32_gfx_clear
li a0, 32 # x
li a1, 40 # y
la a2, title # address of the string
li a3, WHITE # foreground
li a4, BLACK # background
call prg32_gfx_text8
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l02.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 10: The complete program: l02.S (3 of 3)
la t0, counter # step 4: make the counter visible
lw t1, 0(t0)
andi a2, t1, 255 # width = counter modulo 256
li a0, 32 # x
li a1, 60 # y
li a3, 8 # height
li a4, GREEN
call prg32_gfx_rect
lw ra, 12(sp) # epilogue: restore ra
addi sp, sp, 16 # release the frame
ret
.section .rodata
title:
.asciz "HELLO PRG32"
.section .data
counter: .word 0
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l02.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 11: Run it: what you should see
On the screen
– HELLO PRG32 and, under it, a green bar that grows by one pixel per frame and starts again at 256.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 12: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l02.S --portable \
--entry-prefix first --name l02 --out l02.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l02.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 13: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l02.S --portable \
--entry-prefix first --name l02 --architecture qemu \
--out l02-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l02-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 14: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l02.S --portable \
--entry-prefix first --name l02 --architecture esp32c6 \
--out l02-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l02-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 15: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix first; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 16: Exercises on PRG32
TRY IT
1
Change the title string and its colour to yellow (0xffe0); run it again
2
Make the bar grow twice as fast, then four times as fast, changing one instruction only
3
Make the bar shrink instead of grow. What happens when the counter passes zero?
4
In PRG32-QT, single-step first_update and write down t0 and t1 after each instruction
5
Draw a second bar, in red, whose width is the counter modulo 64
Expected result
For exercise 3 the counter goes 0, then 0xFFFFFFFF: with andi 255 the bar jumps to 255 and shrinks. Keep the observation: Lecture 05 explains it.
Notes: Five exercises on the student's own cartridge, each the seed of a later lecture. Change the text and its colour. Make the bar grow two or four times as fast by modifying a single instruction. Make it shrink, and observe what happens when the counter passes zero: the bar jumps to its full width, a phenomenon that Lecture 05 explains through two's complement. Single-step first_update and record the registers after each instruction. Draw a second bar whose width is the counter modulo 64. In every case the outcome should be predicted before the program is run. For the lecturer: Hints: addi t1, t1, 2 or slli before andi for exercise 2; addi t1, t1, -1 for exercise 3; andi a2, t1, 63 for exercise 5. Each exercise is a seed for a later lecture.