## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 21
Input and Output: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
21-Computer_Architecture-Input_Output.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 21. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: polling, interrupts, DMA; CRT and LCD displays; keyboard and mouse; printers. USE NOW: the complete program, the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The listing of Lecture 21: read the code, then the numbered remarks beside it
2
The complete program: code/l21.S, 63 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. The program of this lecture is ~/arc12/code/l21.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l21.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Read the world, once per frame
steer_update:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
call prg32_input_read # a0 = one bit per button
mv s0, a0 # keep it in a saved register
andi t0, s0, 0x10 # button A
beqz t0, 1f
li a0, 0 # channel
li a1, 0 # instrument
li a2, 69 # note: A4, 440 Hz
li a3, 255 # volume
li a4, 120 # milliseconds
call prg32_audio_note
1: andi t0, s0, 0x01 # LEFT: s0 survived the call
beqz t0, 2f
... # move left
2: ...
1
Each button is a switch on one input pin of the chip: pressed or released, one bit
2
The runtime reads the pins and packs them into one word: a decoded representation (Lecture 11)
3
Your game asks once per frame: this is polling
4
A keyboard has a hundred keys, a mouse moves in two dimensions, a display has thousands of pixels: how do they talk to a processor?
UNDERSTAND NOW · polling, interrupts, DMA
Notes: The warm-up: a function that reads the input once per frame. prg32_input_read returns in a0 a word with one bit per button; the code copies it into s0, a callee-saved register, because the word must survive the call that plays a note, and in a temporary it would be lost. Each button is then tested with andi and a mask: 0x10 for A, 0x01 for LEFT. Behind each bit lies a switch on an input pin of the chip, and the runtime gathers the pins into one word, a decoded representation in the sense of Lecture 11. The program asks, once per frame, and this mode of operation has a name, polling. The other devices are less simple, and the lecture examines them. UNDERSTAND NOW: polling, interrupts, DMA. For the lecturer: From textbook chapter 6, lab 06 and the sound example of the capstone chapter (examples/asm_capstone/audio_note_event.S). Built as a cartridge and run on the PRG32-QT headless runner (tools/tests): the marker moves with LEFT also while A plays the note, because the mask is kept in s0, a saved register; in t0 it would be lost at the call. The pins are memory-mapped GPIO registers (Lecture 15), configured as inputs, that is, with their output buffers in high impedance (Lecture 14).

## Slide 4: The complete program: l21.S (1 of 3)
# ARC12 Computer Architecture - Lecture 21: Input and Output
# l21.S: read the world, once per frame
#
# On the screen: a yellow square in the middle of the screen. LEFT moves it to the
# left; A plays a note, and the square keeps moving while the note sounds.
# Build: python3 -m prg32 cartridge build l21.S --portable \
# --entry-prefix l21 --name l21 --out l21.prg32
.option norelax
.section .text
.global l21_init
.global l21_update
.global l21_draw
l21_init:
ret
l21_update:
steer_update:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l21.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 5: The complete program: l21.S (2 of 3)
call prg32_input_read # a0 = one bit per button
mv s0, a0 # keep it in a saved register
andi t0, s0, 0x10 # button A
beqz t0, 1f
li a0, 0 # channel
li a1, 0 # instrument
li a2, 69 # note: A4, 440 Hz
li a3, 255 # volume
li a4, 120 # milliseconds
call prg32_audio_note
1: andi t0, s0, 0x01 # LEFT: s0 survived the call
beqz t0, 2f
la t1, marker_x
lw t2, 0(t1)
addi t2, t2, -2
sw t2, 0(t1)
2: lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l21.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 6: The complete program: l21.S (3 of 3)
l21_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0
call prg32_gfx_clear
la t0, marker_x
lw a0, 0(t0)
li a1, 100
li a2, 16
li a3, 16
li a4, 0xffe0
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
.section .data
marker_x: .word 152
USE NOW · the complete program
Notes: One page of the complete program, reproduced exactly as it appears in the repository. It should be read from the top. The header states what the program displays and how it is built; the three entry points, init, update and draw, follow, and the data sections close the file. Lines already met in the listings of the lecture carry the same comments here, so that each fragment can be located within the whole. USE NOW: the complete program (used, not studied, in this course). For the lecturer: code/l21.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: Run it: what you should see
On the screen
– a yellow square in the middle of the screen. LEFT moves it to the left; A plays a note, and the square keeps moving while the note sounds.
What to press
– LEFT moves the square; A plays a note
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 8: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l21.S --portable \
--entry-prefix l21 --name l21 --out l21.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l21.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 9: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l21.S --portable \
--entry-prefix l21 --name l21 --architecture qemu \
--out l21-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l21-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 10: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l21.S --portable \
--entry-prefix l21 --name l21 --architecture esp32c6 \
--out l21-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l21-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 11: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l21; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 12: Exercises: paper first, then PRG32
TRY IT
1
A keyboard has 104 keys: how many bits does the key code need? How many rows and columns could the matrix have?
2
A page of 8 by 11 inches at 600 dots per inch, one bit per dot: how much memory does the printer need for the bitmap?
3
Move a pointer on the PRG32 screen with the joystick, as a mouse would: keep x and y, clamp them to the screen
4
Make button A act only once per press (edge detection, Lecture 13)
5
Draw a seven-segment score with rectangles, using the transcoder table of Lecture 11
Expected result
On paper: 7 bits, for example 8 by 13; about 4 MB. On PRG32: a pointer that stays on screen and a button that fires once per press.
Notes: Five exercises. Determine how many bits the code of a 104-key keyboard requires, and propose a suitable matrix of rows and columns. Compute the memory a printer needs for the bitmap of a page at 600 dots per inch. Move a pointer on the screen with the joystick, keeping it within the screen by clamping as in Lecture 05. Make button A act only once per press, by edge detection as in Lecture 13. And draw a score with seven-segment digits, using the table of Lecture 11. For the lecturer: 8 x 600 = 4,800 by 11 x 600 = 6,600 dots: 31,680,000 bits = 3.96 MB.