## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 23
Verm1 on the Cartridge Store: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Verm1 reference implementation contributed by Giuseppe Coviello
Code deck. The concepts, the figures and the questions are in the lecture deck:
23-Computer_Architecture-Verm1_On_The_Cartridge_Store.pptx
UNDERSTAND LATER
USE NOW
UNDERSTAND NOW
Notes: This is the code deck of Lecture 23. Where the lecture deck develops the concepts, this deck contains everything that is written and executed: each listing with its commentary, the complete program of the lecture, the output it is expected to produce, and the procedure for testing it on each of the three hosts. The two decks are meant to be read together: the concepts explain the code, and the code gives the concepts an observable consequence. Learning status: UNDERSTAND NOW, by the end of this lecture you explain it, trace it and apply it on your own; USE NOW, you follow and use the recipe today; how it works inside is explained later, or is not part of the course; UNDERSTAND LATER, recognise the name and what it is for; a later lecture explains it. A slide without a badge is context: a story, an example, a question, an exercise. Learning status of this lecture. UNDERSTAND NOW: packaging and publishing; the portable cartridge. USE NOW: the PRG32 tools (used, not studied, in this course). UNDERSTAND LATER: nothing. A slide without a badge is context: a story, an example, a question, an exercise.

## Slide 2: In this deck
1
The 8 listings of Lecture 23, one per slide: read the code, then the numbered remarks beside it
2
The files of the bundle: manifest, metadata, colophon, icon, and one cartridge per architecture
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: The contents of the deck, in the order of the slides. The program of the lecture is a complete source file that can be built and executed as it stands. The recommended approach is to run it first, observe its behaviour, and then return to the individual listings to understand how each part contributes to that behaviour. tools/tests/verm1_store.py builds the two cartridges, attaches the metadata and packs the bundle; nothing is uploaded. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. tools/tests/verm1_store.py builds the two cartridges, attaches the metadata and packs the bundle; nothing is uploaded. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Build for the kit and for QEMU
cd ~/PRG32 # your PRG32 folder, toolchain active
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 \
--architecture esp32c6 --out ~/verm1/verm1-esp32c6.prg32
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 \
--architecture qemu --out ~/verm1/verm1-qemu.prg32
1
The command of every lecture, with one more option
2
--architecture names the target of the file
3
The names follow a rule: game-architecture.prg32
4
The finished Verm1 is about 6 kilobytes of code
USE NOW · the PRG32 tools
UNDERSTAND NOW · the portable cartridge
Notes: The build command of every lecture, with one additional option: --architecture names the target for which the file is produced, first esp32c6 and then qemu. The output files follow a naming rule: the name of the game, a hyphen, the architecture. The source is identical for both. The size reported by the builder is worth noting: the entire finished game amounts to about six kilobytes of code. UNDERSTAND NOW: the portable cartridge. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The builder answers: built verm1-esp32c6.prg32 name=verm1 load=0x40800000, and code=6216 for the reference game. Six kilobytes: less than this slide as a picture.

## Slide 4: Check: is it portable?
python3 -m prg32 cartridge summary ~/verm1/verm1-esp32c6.prg32
{
...
"import_model": "abi-table",
...
}
1
summary prints what the file declares about itself
2
abi-table: the cartridge reaches the runtime through a table of functions
3
So it does not depend on one build of the firmware: it is portable
4
The Store accepts portable cartridges
UNDERSTAND NOW · the portable cartridge
Notes: cartridge summary prints what a cartridge file declares about itself. One line is decisive: import_model must be abi-table. It means that the cartridge reaches the runtime's functions through a table, not through the fixed addresses of a particular firmware image. Such a cartridge is portable: it continues to work when the firmware is updated, because the table, not the addresses, is the interface. This is the stable-interface principle first met in Lecture 01. The Store accepts portable cartridges, and the check is repeated on the second file. UNDERSTAND NOW: the portable cartridge. For the lecturer: A non-portable cartridge is linked against the addresses of one firmware image and breaks at the next update. The table is the ABI of PRG32: prg32_gfx_rect and the others are entries of it. Repeat the check on the QEMU file.

## Slide 5: manifest.json: who is this game?
{
"abi": "prg32-metadata-1.0",
"id": "it.uniparthenope.arc12.verm1",
"title": "Verm1",
"version": "1.0.0",
"summary": "A hungry worm on a 40 by 24 grid: a tribute to Snake.",
"description": "Verm1 (say \"vermone\") is the course-long project of ...",
"authors": [{"name": "Your Name"}],
"license": "MIT",
"tags": ["arcade", "snake", "assembly", "education"],
"assets": {"icon": "icon.png"},
"architectures": [
{"id": "esp32c6", "file": "verm1-esp32c6.prg32"},
{"id": "qemu", "file": "verm1-qemu.prg32"}
]
}
1
id: a name that is unique in the world, and for ever
2
version: three numbers, 1.0.0 for a first release
3
summary: one line for the shelf; description: a paragraph
4
architectures: which file serves which target
UNDERSTAND NOW · packaging and publishing
Notes: The manifest is a JSON file describing the game, whose fields should be read one by one. id is a globally unique name. version consists of three numbers. title is what the player reads. summary is a one-line description for the shelf, description a paragraph. Authors, licence and tags follow. At the end, assets names the icon and architectures states which cartridge file serves which target. The file is created with a text editor in the folder of the game. UNDERSTAND NOW: packaging and publishing. For the lecturer: Create the file in ~/verm1 with a text editor. The description is cut on the slide. The abi line says which version of the metadata format this is.

## Slide 6: colophon.json: credits and controls
{
"abi": "prg32-colophon-1.0",
"title": "Verm1",
"subtitle": "A tribute to Snake, in RISC-V assembly",
"version": "1.0.0",
"release_date": "2026-12-18",
"developer": {"name": "Your Name"},
"authors": [
{"role": "game design", "name": "Your Name"},
{"role": "programming", "name": "Your Name"}
],
"license": "MIT",
"copyright": "Copyright 2026 Your Name",
"acknowledgements": [
"Giuseppe Coviello, reference implementation of Verm1",
"ARC12 Computer Architecture, University of Naples Parthenope",
"The PRG32 community"
],
"controls": [
{"input": "JOYSTICK", "action": "Steer the worm"},
{"input": "A", "action": "Start, and return to the title after game over"}
],
"start_prompt": "Press A to play"
}
1
The colophon is the credits page of the cartridge
2
Roles and names: give credit to everyone
3
controls: what each input does, for the player
4
acknowledgements: whom you thank; the reference game you started from stays there
UNDERSTAND NOW · packaging and publishing
Notes: The colophon is the credits page of the cartridge; the word comes from printing, where it denotes the note at the end of a book recording who made it. It lists roles and names, the controls, that is, what each input does for the player, and the acknowledgements, in which the reference game from which the student began remains cited. The placeholder name is replaced throughout and the date set. UNDERSTAND NOW: packaging and publishing. For the lecturer: Colophon is the printers' word for the note at the end of a book that says who made it. Replace Your Name everywhere, and set the release date.

## Slide 7: metadata.json, and attach
# metadata.json = manifest.json WITHOUT the "assets" and "architectures" entries
python3 -m prg32 store attach-metadata ~/verm1/verm1-esp32c6.prg32 \
--metadata ~/verm1/metadata.json --icon ~/verm1/icon.png \
--colophon ~/verm1/colophon.json --architecture esp32c6 \
--out ~/verm1/verm1-esp32c6.prg32
python3 -m prg32 store attach-metadata ~/verm1/verm1-qemu.prg32 \
--metadata ~/verm1/metadata.json --icon ~/verm1/icon.png \
--colophon ~/verm1/colophon.json --architecture qemu \
--out ~/verm1/verm1-qemu.prg32
1
Copy the manifest and delete two entries: assets, architectures
2
attach writes title, icon and credits inside the cartridge
3
A cartridge copied by hand still says what it is
4
Once per file, with its own architecture
UNDERSTAND NOW · the portable cartridge
Notes: metadata.json is prepared first: a copy of the manifest without the two entries assets and architectures, which concern the bundle rather than an individual cartridge. store attach-metadata then writes metadata, icon and colophon into the cartridge, once per file, each with its own architecture. The program itself is untouched; the information is appended after it. Henceforth a cartridge copied by hand still declares what it is and who made it. UNDERSTAND NOW: the portable cartridge. For the lecturer: The tool answers: wrote verm1-esp32c6.prg32 legacy=6316 blocks=3. The three blocks are the metadata, the icon and the colophon, appended after the program; the program itself is untouched. Careful: giving the full manifest to --metadata makes the tool fail, because of the assets entry.

## Slide 8: Read it back
python3 -m prg32 store inspect-metadata ~/verm1/verm1-esp32c6.prg32
{
...
"id": "it.uniparthenope.arc12.verm1",
"license": "MIT",
"runtime": { "architecture": "esp32c6", ... },
"summary": "A hungry worm on a 40 by 24 grid: a tribute to Snake.",
"title": "Verm1",
"version": "1.0.0"
},
...
"trailer_present": true,
"unknown_blocks": []
}
1
Never trust a write you have not read back
2
Check id, title, version and architecture
3
trailer_present: the papers are in the file
4
Run the cartridge once more: it must still work
UNDERSTAND NOW · the portable cartridge
Notes: A write that has not been read back should never be trusted. store inspect-metadata prints what the cartridge contains: identifier, title, version and architecture are checked, together with trailer_present being true. The cartridge is then run once more and must behave exactly as before. Reading back what was written is a habit cultivated throughout the course, from the memory view of the debugger to this command. UNDERSTAND NOW: the portable cartridge. For the lecturer: Output abridged. Reading back what was written is the habit of the whole course: the memory view of the debugger, and now this.

## Slide 9: Pack
python3 -m prg32 store pack-bundle \
--manifest ~/verm1/manifest.json --out ~/verm1/verm1-1.0.0.zip
Bundle: ~/verm1/verm1-1.0.0.zip
manifest.json 0.7 KB
icon.png 0.1 KB
verm1-esp32c6.prg32 7.8 KB
verm1-qemu.prg32 7.8 KB
Total: 16.4 KB
1
The tool reads the manifest and collects the files it names
2
A missing or misnamed file stops it here, not at the Store
3
The name carries the version: verm1-1.0.0.zip
4
Your whole game, for two machines: 16 kilobytes
UNDERSTAND NOW · packaging and publishing
Notes: store pack-bundle reads the manifest, collects the files it names and produces a ZIP file whose name carries the version. If a file is missing or misnamed, the tool stops here, on the student's computer, rather than later at the Store, so that errors are caught where they are cheapest to correct. The listing it prints shows the manifest, the icon and the two cartridges: the entire game, for two machines, occupies about sixteen kilobytes. UNDERSTAND NOW: packaging and publishing. For the lecturer: Real output for the reference game, from tools/tests/verm1_store.py. The files must be in the same folder as the manifest.

## Slide 10: Run it: test the bundle, not your folder
TRY IT
1
Unzip verm1-1.0.0.zip into an empty folder
2
In PRG32-QT import verm1-esp32c6.prg32 from that folder and run it: title, icon and credits must be yours
3
Upload verm1-qemu.prg32 to QEMU and play one game
4
If you have a kit, upload the ESP32-C6 file and play with the real joystick
5
Ask a colleague to do the same on another computer: the first user who is not you
Expected result
The game runs from the files in the bundle, on every target you declared, on a computer that is not yours.
Notes: The bundle is tested, not the working folder. It is unzipped into an empty folder and used from there: the ESP32-C6 cartridge is imported into PRG32-QT to verify that title, icon and credits are the author's; the other is uploaded to QEMU and a game played; on a kit, the real joystick is tried. A colleague is then asked to repeat the procedure on another computer. This catches the classic error of a bundle built before the last correction. For the lecturer: Testing the packaged files, and not the ones in the working folder, catches the classic mistake: a bundle built before the last fix.

## Slide 11: Publish
# 1. sign in to the Store and create a token on the Tokens page
# 2. keep it in the environment of your shell: never in a file, never in Git
export PRG32_STORE_URL="https://store.prg32.uniparthenope.it"
export PRG32_STORE_TOKEN="paste-your-token-here"
# 3. submit
python3 -m prg32 store publish-bundle ~/verm1/verm1-1.0.0.zip \
--store-url "$PRG32_STORE_URL" --token "$PRG32_STORE_TOKEN"
1
The token is you: whoever has it publishes in your name
2
It is a secret: not in the source, not in a screenshot
3
The submission is pending until an editor approves it
4
Lost or shown by mistake: revoke it and make a new one
UNDERSTAND NOW · packaging and publishing
Notes: Three actions. The author signs in to the Store and creates a token, keeps it in an environment variable of the shell, and submits the bundle with store publish-bundle. The token stands for its owner: whoever holds it publishes in the owner's name. It is therefore a secret, and belongs neither in the source, nor in any file under version control, nor in a screenshot. A token that is lost or accidentally exposed is revoked and replaced. This is the only step not executed for these slides, since it requires a personal account. UNDERSTAND NOW: packaging and publishing. For the lecturer: This is the only step that was not run for these slides: it needs a personal account. Do it live with a volunteer, with the volunteer's own token, and never project the token.

## Slide 12: Run it: what you should see
On the screen
– Verm1, started from the files of the bundle: on each host the title, the icon and the credits are those of the manifest.
What to press
– A starts a game; steer with the joystick
The frame written by the automatic test on PRG32-QT
Notes: The expected behaviour of the program, and the input it requires. The outcome should be predicted before the program is run: any discrepancy between prediction and screen is information about one's model of the machine, and is worth explaining before it is corrected. The image was produced by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 13: Test it on PRG32-QT
# 1. start PRG32-QT on this computer
# 2. unzip the bundle into an empty folder
mkdir ~/verm1-test && cd ~/verm1-test && unzip ~/verm1/verm1-1.0.0.zip
# 3. in PRG32-QT: import verm1-esp32c6.prg32 from that folder, Run Cartridge
# or, from the PRG32 folder:
python3 -m prg32 esp32c6 upload-and-run ~/verm1-test/verm1-esp32c6.prg32 \
--url http://localhost:8080 --slot cart0
# 4. the title, the icon and the credits must be those of your manifest
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
USE NOW · the PRG32 tools
Notes: The most direct route: PRG32-QT on one's own computer, in four steps, each with its command. PRG32-QT presents itself to the tools as a board listening on port 8080, which is why the upload command names the esp32c6. With debug mode enabled, execution can be halted at any instruction and the registers and memory inspected. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 14: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. read back what the cartridge for QEMU declares
python3 -m prg32 store inspect-metadata ~/verm1-test/verm1-qemu.prg32
# 3. with QEMU closed, stage it into the flash image
python3 -m prg32 qemu upload ~/verm1-test/verm1-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
USE NOW · the PRG32 tools
Notes: The same program on the emulator. QEMU executes the actual firmware on an emulated chip, so the cartridge must be built for the qemu architecture and staged while QEMU is not running. The firmware starts on its Setup menu, from which Run Cartridge and the slot are selected. Keyboard input is read by the terminal from which QEMU was launched, not by the window that displays the image. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 15: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. send the cartridge of the bundle for the board, and start it
python3 -m prg32 esp32c6 upload-and-run ~/verm1-test/verm1-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
# 4. play one whole game with the real joystick and speaker
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
USE NOW · the PRG32 tools
Notes: The same program on the physical kit. The firmware is written once, over USB; thereafter cartridges are transferred over Wi-Fi with the same upload command used for PRG32-QT, addressed to the board. This is the only host not exercised by the automatic tests, so observations made on the board are particularly valuable and should be reported. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 16: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix verm1; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
USE NOW · the PRG32 tools
Notes: The five most frequent symptoms, their meaning, and the corrective action. The error message should be read in full before anything is changed: in nearly every case it names the cause. When asking for help, the command and the complete message should be reported verbatim. USE NOW: the PRG32 tools (used, not studied, in this course). For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 17: Your release
TRY IT
1
Choose your id and your title, write the manifest and the colophon for your variant of Verm1
2
Draw your icon
3
Build, attach, inspect, pack: produce your bundle and pass the checklist with a colleague as reviewer
4
If you want your game on the shelf: publish it, and send the link to the class
Expected result
A bundle of your own game, reviewed by a colleague against the checklist.
Notes: The release. The student chooses an identifier and a title, writes the manifest and the colophon of their variant, and draws the icon. The cartridge is then built, the metadata attached, inspected and packed, and the checklist completed with a colleague acting as reviewer. The bundle is the deliverable of the project. Publication itself is optional and personal: those who wish their game to stand on the shelf publish it and share the link with the class. For the lecturer: Publication is optional and personal; the bundle is the deliverable of the project.