## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 00
Course Introduction: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
00-Computer_Architecture-Course_Introduction.pptx
Notes: This is the code deck of Lecture 00. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
No listing in Lecture 00: this deck gives you the program to run
2
The complete program: code/l00.S, 46 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l00.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l00.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Before the next lecture: we install everything together
TRY IT
1
Bring your laptop, charged, with the right to install programs on it
2
Download the PRG32-QT installer for your system: github.com/riscv-prg32/PRG32-QT, Releases
3
At home, on a good connection, start the long download: ESP-IDF, following the README of github.com/riscv-prg32/PRG32 for your system
4
If something fails, do not fight it alone: bring the error message, we solve it in class
5
Send your address for the shared folder and fill in the Sorting Hat questionnaire
Expected result
You arrive at Lecture 01 with the downloads done. In two hours everyone leaves with PRG32-QT running and a cartridge built on their own laptop.
Notes: Homework for the next lecture, which is a hands-on installation. Bring your laptop, charged, on which you are allowed to install software. Download the installer of PRG32-QT for your system. At home, on a good connection, start the long download of ESP-IDF, following the README of PRG32. If something fails, do not lose an evening on it: bring the exact error message and it will be solved in class. The expected result is stated at the bottom: after Lecture 01 everyone has PRG32-QT running and a cartridge built on their own machine. For the lecturer: Lecture 01 is the installation, step by step, for Windows, macOS and Linux. The only thing that cannot be done in class is the download of ESP-IDF: a few gigabytes per student.

## Slide 4: The complete program: l00.S (1 of 2)
# ARC12 Computer Architecture - Lecture 00: Course Introduction
# l00.S: the first program of the course, to read before you can write it
#
# On the screen: the word ARC12 in white on a blue screen, and under it HELLO, RISC-V.
# Build: python3 -m prg32 cartridge build l00.S --portable \
# --entry-prefix l00 --name l00 --out l00.prg32
.option norelax
.equ BLUE, 0x001f # a colour is a 16-bit number (Lecture 04)
.equ WHITE, 0xffff
.section .text
.global l00_init
.global l00_update
.global l00_draw
l00_init: # called once, when the cartridge starts
ret
l00_update: # called once per frame: nothing changes here
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l00.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 5: The complete program: l00.S (2 of 2)
l00_draw: # called once per frame: paint the screen
addi sp, sp, -16 # a function that calls others saves ra
sw ra, 12(sp)
li a0, BLUE
call prg32_gfx_clear # fill the screen with one colour
li a0, 140 # x, in pixels
li a1, 88 # y
la a2, line1 # the ADDRESS of the text
li a3, WHITE # foreground
li a4, BLUE # background
call prg32_gfx_text8
li a0, 104
li a1, 104
la a2, line2
li a3, WHITE
li a4, BLUE
call prg32_gfx_text8
lw ra, 12(sp)
addi sp, sp, 16
ret
.section .rodata # constants: two strings, each ending with a zero byte
line1: .asciz "ARC12"
line2: .asciz "HELLO, RISC-V"
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l00.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 6: Run it: what you should see
On the screen
– the word ARC12 in white on a blue screen, and under it HELLO, RISC-V.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 7: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l00.S --portable \
--entry-prefix l00 --name l00 --out l00.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l00.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 8: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l00.S --portable \
--entry-prefix l00 --name l00 --architecture qemu \
--out l00-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l00-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 9: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l00.S --portable \
--entry-prefix l00 --name l00 --architecture esp32c6 \
--out l00-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l00-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 10: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l00; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.