## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 07
Verm1, Part 1: A Head That Crosses the World: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Verm1 reference implementation contributed by Giuseppe Coviello
Code deck. The concepts, the figures and the questions are in the lecture deck:
07-Computer_Architecture-Verm1_Part_1.pptx
Notes: This is the code deck of Lecture 07. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 8 listings of Lecture 07, one per slide: read the code, then the numbered remarks beside it
2
The program is your verm1.S; the reference is verm1/verm1_part1.S, 78 lines, shown here region by region
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The reference program is ~/arc12/verm1/verm1_part1.S; tools/tests/verm1_check.py builds it and plays it with a scripted player, and verm1_steps.py runs the intermediate checkpoints. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The reference program is ~/arc12/verm1/verm1_part1.S; tools/tests/verm1_check.py builds it and plays it with a scripted player, and verm1_steps.py runs the intermediate checkpoints. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Build and run
# 1. build the cartridge (from your PRG32 folder, toolchain active)
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --out ~/verm1/verm1.prg32
# 2. send it to PRG32-QT, running on the same computer
python3 -m prg32 esp32c6 upload-and-run ~/verm1/verm1.prg32 \
--url http://localhost:8080 --slot cart0
# or: in PRG32-QT, import the file verm1.prg32 and choose Run Cartridge
Notes: Make a folder called verm1 in your home directory and keep in it one file, verm1.S, that will grow from part to part. The first command builds the cartridge; the second sends it to PRG32-QT running on the same computer and starts it. These two commands are identical in every tutorial. If localhost does not answer, use the address shown on the Setup screen of PRG32-QT. As an alternative you can import the file from the menu of PRG32-QT. For the lecturer: Make a folder ~/verm1 and keep one file in it, verm1.S, that grows from part to part. PRG32-QT listens on port 8080 and shows its address on the Setup screen: use that address if localhost does not answer. The same cartridge runs on QEMU (python3 -m prg32 qemu upload, then qemu run) and on the board (--url http://192.168.4.1).

## Slide 4: Step 1: three functions that return
# verm1.S - my Verm1
.option norelax
.section .text
.global verm1_init
.global verm1_update
.global verm1_draw
verm1_init:
ret
verm1_update:
ret
verm1_draw:
ret
1
Type it, build it, run it: a black screen is the right answer
2
The prefix verm1 is the name you pass to --entry-prefix
3
init runs once; update and draw run once per frame
4
From now on: add one thing, run, look. Never two things at once
Notes: Step 1 is the skeleton of Lecture 02 with the prefix verm1: three global labels and three functions that only return. Type it, build it, run it. The right result is a black screen: it proves that the tools work and that the firmware finds your functions. If the build fails here, the problem is the installation, not your program, and it must be solved before going on. The last callout is the rule of the whole project: add one thing, run, look. Never two things at once. For the lecturer: The skeleton of Lecture 02. If the build fails here the problem is the installation, not the program: solve it before going on.

## Slide 5: Constants: colours and the grid
.option norelax
.equ BLACK, 0x0000 # RGB565 colours
.equ WHITE, 0xffff
.equ GREEN, 0x07e0
.equ CELL, 8 # a cell is 8 x 8 pixels
.equ COLS, 40 # 320 / 8 cells across
.equ ROWS, 24 # 192 / 8 cells down
.equ TOP, 8 # the top 8 pixels are the title line
.equ SPEED_Q8, 40 # 40/256 of a cell per frame (Q24.8)
.section .text
.global verm1_init
.global verm1_update
.global verm1_draw
1
Colours are RGB565 numbers: 0x07e0 is pure green
2
320 pixels across, 8 per cell: 40 columns
3
The top 8 pixels hold the title; 192 are left: 24 rows
4
.equ gives a name to a number: no memory is used
Notes: These lines replace the beginning of the skeleton. Each .equ gives a name to a number and uses no memory: the assembler simply substitutes the number. Three colours in RGB565. Then the geometry: a cell is 8 by 8 pixels, so the 320 pixels of the width hold 40 columns; the top 8 pixels are reserved for the title, and the remaining 192 hold 24 rows. SPEED_Q8 is the speed in fixed point and will be used in step 3. Constants with names make the program readable and easy to change. For the lecturer: Replace the skeleton's first lines with these. SPEED_Q8 is used in step 3.

## Slide 6: Variables and a string
.section .rodata
title: .asciz "VERM1"
.section .data
head_x: .word 5 # column of the head, 0 .. COLS-1
head_y: .word 12 # row of the head, 0 .. ROWS-1
step_q8: .word 0 # fraction of a step, in 1/256
1
.rodata holds constants: the title ends with a zero byte
2
.data holds variables: one 32-bit word each
3
The initial values are only a start: init will set them again
Notes: This goes at the end of the file. The section .rodata holds what never changes: the title, a string that .asciz ends with a zero byte. The section .data holds the variables, one 32-bit word each: the column of the head, its row, and the fraction of a step accumulated so far. The initial values written here are only a start: init will set them again explicitly. For the lecturer: Put this at the end of the file. step_q8 is used in step 3.

## Slide 7: init: put the head in its place
verm1_init:
la t0, head_x
li t1, 5
sw t1, 0(t0) # the head starts in column 5 ...
la t0, head_y
li t1, 12
sw t1, 0(t0) # ... of row 12
la t0, step_q8
sw zero, 0(t0) # no fraction of a step yet
ret
1
la takes an ADDRESS, sw stores a VALUE there
2
init sets the start explicitly: never trust what memory contained
3
zero is the register that always reads 0
4
A leaf function: no calls, so no stack frame
Notes: verm1_init puts the head in its place. For each variable the pattern is the same: la loads the address, li loads the value, sw stores the value at the address. The fraction step_q8 is set to zero by storing the register zero directly. The function calls nothing, so it is a leaf and needs no stack frame. Why set values that .data already contains? Because init may be called again to restart the game: never trust what memory contained.

## Slide 8: draw: title and head
verm1_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, BLACK
call prg32_gfx_clear
li a0, 0 # x
li a1, 0 # y
la a2, title # address of the string
li a3, WHITE
li a4, BLACK
call prg32_gfx_text8
la t0, head_x
lw a0, 0(t0)
slli a0, a0, 3 # x = column * 8
la t0, head_y
lw a1, 0(t0)
slli a1, a1, 3
addi a1, a1, TOP # y = row * 8 + 8
li a2, CELL # width
li a3, CELL # height
li a4, GREEN
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Clear, write the title, draw one rectangle: three calls
2
Arguments travel in a0 to a4, in order
3
slli by 3 multiplies by 8: cell to pixel
4
draw makes calls, so it saves ra in a stack frame
Notes: verm1_draw makes three calls: clear the screen, write the title, draw the head. It therefore saves ra in a stack frame at the beginning and restores it at the end, as in Lecture 02. Look at how the cell becomes pixels: the column is loaded into a0 and shifted left by 3; the row is loaded into a1, shifted and increased by TOP. The remaining arguments are width, height and colour. Arguments travel in a0 to a4, in the order in which the function expects them. For the lecturer: prg32_gfx_text8(x, y, string, foreground, background); prg32_gfx_rect(x, y, width, height, colour).

## Slide 9: Run it: a head on the grid
The title and the head. After step 3 the head will be moving: this picture was taken 64 frames into the finished Part 1
Expected now: the word VERM1 at the top left and a green square standing still in column 5, row 12.
Notes: Build and run. You should see the word VERM1 at the top left and a green square standing still in column 5 of row 12. The screenshot on the slide was taken later, from the finished Part 1, so its head is further to the right: do not worry about the difference. If your square is in the wrong place, check the two shifts and the addition of TOP before anything else. For the lecturer: Screenshot produced by tools/tests/verm1_check.py from verm1/verm1_part1.S.

## Slide 10: update: accumulate, step, wrap
verm1_update:
la t0, step_q8
lw t1, 0(t0)
addi t1, t1, SPEED_Q8 # add a fraction of a cell
li t2, 256
blt t1, t2, 2f # less than one whole cell: wait
sub t1, t1, t2 # one cell done: keep the remainder
sw t1, 0(t0)
la t0, head_x
lw t3, 0(t0)
addi t3, t3, 1 # one cell to the right
li t4, COLS
blt t3, t4, 1f
li t3, 0 # past the right edge: back to column 0
1: sw t3, 0(t0)
ret
2: sw t1, 0(t0)
ret
1
Add the speed to the fraction; below 256, wait
2
At 256: subtract it, keep the rest, move one cell
3
Column 40 does not exist: back to column 0
4
Two exits: each stores what it changed
Notes: Read verm1_update in two halves. First the timer: load step_q8, add the speed, compare with 256. If it is less, jump to label 2, store the fraction and return: nothing moves in this frame. Otherwise subtract 256, keeping the remainder, and store it. Then the step: load head_x, add 1, compare with COLS; if the column has reached 40 it becomes 0, and the head comes back from the left. The labels 1: and 2: are local labels: 1f means "the next label 1 forward". For the lecturer: blt compares signed numbers, which is right here: every value is small and positive. Local labels 1: and 2: are referred to as 1f and 2f, 'the next 1 or 2 forward'.

## Slide 11: Run it: the head crosses the world
TRY IT
1
Build and run: the head moves to the right, about five cells per second
2
Wait for the right edge: the head leaves at column 39 and returns at column 0
3
Change SPEED_Q8 to 8, then to 128, then to 256: predict the speed before you run
4
Change the starting row in init and the colour of the head
Expected result
The head crosses the forty columns in 256 frames, about eight and a half seconds at thirty frames per second, for ever.
Notes: Run it. The head moves to the right at about five cells per second, leaves at column 39 and returns at column 0. Then experiment with the speed: before each run, predict what you will see. With 8 the head is slow; with 128 it takes a step every two frames; with 256, one step per frame. Try a larger value and discover a limit of this program: update takes at most one step per frame. For the lecturer: With SPEED_Q8 = 256 the head moves one cell per frame; larger values still give one step per frame, because update takes at most one step: a limit worth discovering.

## Slide 12: What the listing shows: your code, as the assembler left it
verm1_update:
auipc t0, 0x0 # la t0, step_q8 is two instructions:
addi t0, t0, ... # t0 = address of step_q8
lw t1, 0(t0)
addi t1, t1, 40 # SPEED_Q8 is gone: only the number is left
addi t2, zero, 256 # li t2, 256
blt t1, t2, ...
sub t1, t1, t2
sw t1, 0(t0)
...
c.addi t3, 1 # addi t3, t3, 1 in a 16-bit form
...
c.jr ra # ret
1
Names are gone: labels became addresses, constants became numbers
2
Pseudo-instructions are expanded: la is auipc plus addi, li is addi from zero, ret is a jump to ra
3
Some instructions start with c.: the compressed 16-bit forms of the same instructions
4
The cartridge is loaded at address 0x40800000: every address you see starts there
Notes: The debugger does not show your source: it shows what the assembler produced. Names have disappeared: labels have become addresses and SPEED_Q8 has become the number 40. Pseudo-instructions are expanded: la is auipc followed by addi, li is an addi from zero, ret is a jump to ra. Some instructions begin with c.: they are the compressed, 16-bit forms of the same instructions, the C in RV32IMAC. Recognising your own program in this listing is a skill that grows with practice. For the lecturer: Disassembly of verm1_update from verm1/verm1_part1.S (objdump, rv32imac), abridged; the exact offsets depend on the build. Instruction formats and compressed instructions are the subject of Lecture 19.

## Slide 13: Run it: what you should see
On the screen
– the word VERM1 at the top left and a green head that crosses the grid from left to right, about five cells per second, and comes back in from column 0.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 14: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --out verm1.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run verm1.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 15: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --architecture qemu \
--out verm1-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload verm1-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 16: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --architecture esp32c6 \
--out verm1-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run verm1-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 17: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix verm1; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 18: Make it yours
TRY IT
1
Make the head move to the left: which instruction changes, and which comparison detects the edge?
2
Make it move downwards instead, wrapping from row 23 to row 0
3
Draw a second cell, in a darker green, one column behind the head: a first hint of a body
4
Write your own name next to the title, in a colour you computed by hand in RGB565
Expected result
Each change is a few lines. Keep a copy of the working Part 1 before you experiment: Part 2 starts from it.
Notes: Four changes to make the program yours, each of a few lines. Make the head move to the left: the addition becomes a subtraction, and the edge is detected on the sign of the result. Make it move downwards. Draw a second, darker cell behind the head. Write your name beside the title in a colour computed by hand. Before experimenting, keep a copy of the working Part 1: Part 2 starts from it. For the lecturer: Moving left: addi t3, t3, -1, then bgez t3 to skip the wrap, else li t3, COLS-1. The comparison is on the sign: Lecture 05. Darker green: 0x03e0.