## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 08
Elements of Boolean Algebra: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
08-Computer_Architecture-Boolean_Algebra_1.pptx
Notes: This is the code deck of Lecture 08. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 3 listings of Lecture 08, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l08.S, 107 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l08.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l08.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Is LEFT pressed?
call prg32_input_read # a0 = all the buttons, one bit each
mv t0, a0 # keep our own copy
andi t3, t0, 0x01 # keep only bit 0: LEFT
beqz t3, 1f # zero: LEFT is not pressed
addi t2, t2, -2 # move left
1:
andi t3, t0, 0x02 # keep only bit 1: RIGHT
beqz t3, 2f
addi t2, t2, 2 # move right
2:
1
prg32_input_read returns all the buttons at once: one bit per button
2
andi with 0x01 keeps bit 0 and forces every other bit to zero
3
The result is non-zero exactly when LEFT is pressed
4
andi is thirty-two AND gates working side by side: what is an AND, exactly?
Notes: prg32_input_read returns all the buttons at once in a0, one bit per button. andi t3, t0, 0x01 keeps bit 0 and forces every other bit to zero; the result is different from zero exactly when LEFT is pressed, and beqz skips the movement otherwise. The same pattern, with 0x02, tests RIGHT. The constant used with andi is called a mask. The last callout asks the question of the lecture: andi is thirty-two AND gates working side by side, so what is an AND? For the lecturer: From textbook chapter 6 (State and Input) and lab 06-asm-state-and-input. The constant used with andi is called a mask.

## Slide 4: One bit per button
LEFT 0x01, RIGHT 0x02, UP 0x04, DOWN 0x08: bits 0 to 3
A 0x10, B 0x20, START / SELECT 0x40: bits 4 to 6
Holding RIGHT and A together gives 0x12 = 0001 0010
Each lamp of the lab is one bit of the mask: lit when the bit is 1
Every question about the joystick is a Boolean expression over these variables
Lab 06, step 1: seven lamps, one per button bit
Notes: The value returned by the buttons is a word in which each bit has a meaning: bit 0 is LEFT, bit 1 RIGHT, bit 2 UP, bit 3 DOWN, bits 4 and 5 are A and B, bit 6 is START. If you hold RIGHT and A together you get 0x12, that is 0001 0010. In the picture each lamp is one bit of this word. Every question you can ask about the joystick, such as "is LEFT pressed but not RIGHT?", is a Boolean expression over these seven variables. For the lecturer: Button constants from prg32.h (PRG32_BTN_*). Player two uses the same layout in higher bits.

## Slide 5: Bitwise instructions: the algebra on a whole register
Instruction | Operation | a = 1100 1010, b = 0000 1111 | In C
and t0, a, b | bit by bit AND | 0000 1010 | a & b
or t0, a, b | bit by bit OR | 1100 1111 | a ¦ b
xor t0, a, b | bit by bit XOR | 1100 0101 | a ^ b
not t0, a | complement every bit | 0011 0101 | ~a
Each instruction applies one gate to every bit position at once. not is a pseudo-instruction: xori with -1, that is, with all ones.
Notes: and, or, xor and not apply one gate to every pair of corresponding bits of two registers, all positions at once. The third column works out an example on eight bits: with a equal to 1100 1010 and b equal to 0000 1111, AND gives 0000 1010, OR gives 1100 1111, XOR gives 1100 0101. The last column shows the same operators in C. not is a pseudo-instruction: it is xori with minus 1, because minus 1 in two's complement is all ones. For the lecturer: Each instruction applies the same gate to all thirty-two pairs of bits at once (eight shown). The immediate forms andi, ori and xori take a 12-bit constant; not is the pseudo-instruction xori t0, a, -1, because -1 is all ones.

## Slide 6: Four things to do with a mask
Goal | Law used | Instruction (bit 4 = button A) | Effect on the other bits
Test a bit | x . 1 = x, x . 0 = 0 | andi t1, t0, 0x10 | forced to 0 in the result
Set a bit to 1 | x + 1 = 1, x + 0 = x | ori t0, t0, 0x10 | unchanged
Clear a bit to 0 | x . 0 = 0, x . 1 = x | andi t0, t0, ~0x10 | unchanged
Toggle a bit | x xor 1 = x', x xor 0 = x | xori t0, t0, 0x10 | unchanged
Notes: The four standard uses of a mask, each resting on a law of the algebra. To test a bit, AND with a mask that has 1 in that position: x AND 1 is x, x AND 0 is 0. To set it to 1, OR with the same mask. To clear it, AND with the complemented mask. To toggle it, XOR with the mask. In the last three cases the other bits are unchanged, and this is the whole point: a mask acts on the bits you choose and leaves the rest alone. For the lecturer: The identity and null-element laws are exactly what makes a mask work: a 1 in the mask lets the bit through (AND) or forces it (OR); a 0 does the opposite. ~0x10 is 0xFFFFFFEF, which the assembler encodes as the immediate -17.

## Slide 7: De Morgan at the joystick
# "idle" when NEITHER LEFT NOR RIGHT is pressed
andi t3, t0, 0x03 # 0x03 = LEFT | RIGHT: keep both bits
beqz t3, idle # all zero: (LEFT + RIGHT)' is true
# the long way: test each button, the result is the same
andi t3, t0, 0x01
bnez t3, moving # LEFT pressed: not idle
andi t3, t0, 0x02
bnez t3, moving # RIGHT pressed: not idle
j idle # LEFT' . RIGHT'
1
A mask with two bits tests two buttons in one instruction
2
The result is zero only if both bits are zero: NOT (LEFT OR RIGHT)
3
By De Morgan this equals (NOT LEFT) AND (NOT RIGHT): the long way below
4
The algebra tells you that the two programs are equivalent, and which is cheaper
Notes: De Morgan in a program. The player is idle when neither LEFT nor RIGHT is pressed. The short version uses a mask with two bits, 0x03: the result is zero only if both bits are zero, that is NOT (LEFT OR RIGHT). The long version tests each button separately: (NOT LEFT) AND (NOT RIGHT). The second law of De Morgan says that the two are the same condition. Two instructions instead of five: simplifying an expression is useful in software as well as in hardware. For the lecturer: (x + y)' = x' . y'. Two instructions instead of five: minimisation is not only for hardware.

## Slide 8: One lamp per bit: shifting and masking
# s0 = bit number, 0 to 6
la t0, buttons
lw t1, 0(t0) # t1 = the button mask
srl t1, t1, s0 # bring bit number s0 down to bit 0
andi t1, t1, 1 # keep it, clear all the others
li a4, GREY # lamp off
beqz t1, 1f
li a4, YELLOW # lamp on
1: call prg32_gfx_rect
Screenshot: this step, built and run on PRG32
Shift, then mask with 1: the standard way to read bit number n of a word.
Notes: How to read bit number n of a word when n is in a register: shift the word right by n positions, so that the bit you want arrives in position 0, then mask with 1. Here s0 holds the number of the lamp, srl shifts the button word, andi isolates the bit, and the colour is chosen accordingly: grey for off, yellow for on. Shift and mask is one of the most common idioms in low-level programming. For the lecturer: Source: textbook lab 06-asm-state-and-input, step1_lamps.S (inside lamp_loop). srl is a logical shift right (Lecture 05).

## Slide 9: The complete program: l08.S (1 of 6)
# ARC12 Computer Architecture - Lecture 08: Elements of Boolean Algebra
# l08.S: one lamp per button, a marker that moves, and De Morgan at the joystick
#
# On the screen: seven lamps, one per button (LEFT on the left), lit while the button
# is held; a white marker that LEFT and RIGHT move; a square that is green when
# neither LEFT nor RIGHT is pressed and red otherwise.
# Build: python3 -m prg32 cartridge build l08.S --portable \
# --entry-prefix l08 --name l08 --out l08.prg32
.option norelax
.equ BLACK, 0x0000
.equ WHITE, 0xffff
.equ GREY, 0x4208
.equ YELLOW, 0xffe0
.equ GREEN, 0x07e0
.equ RED, 0xf800
.section .text
.global l08_init
.global l08_update
.global l08_draw
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l08.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 10: The complete program: l08.S (2 of 6)
l08_init:
ret
l08_update:
addi sp, sp, -16
sw ra, 12(sp)
call prg32_input_read # a0 = all the buttons, one bit each
mv t0, a0 # keep our own copy
la t1, buttons
sw t0, 0(t1) # remember them for draw
la t1, marker_x
lw t2, 0(t1)
andi t3, t0, 0x01 # keep only bit 0: LEFT
beqz t3, 1f # zero: LEFT is not pressed
addi t2, t2, -2 # move left
1:
andi t3, t0, 0x02 # keep only bit 1: RIGHT
beqz t3, 2f
addi t2, t2, 2 # move right
2:
sw t2, 0(t1)
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l08.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 11: The complete program: l08.S (3 of 6)
# "idle" when NEITHER LEFT NOR RIGHT is pressed
li t4, 1 # idle = 1
andi t3, t0, 0x03 # 0x03 = LEFT | RIGHT: keep both bits
beqz t3, 3f # all zero: (LEFT + RIGHT)' is true
li t4, 0 # idle = 0
3: la t1, idle
sw t4, 0(t1)
lw ra, 12(sp)
addi sp, sp, 16
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l08.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 12: The complete program: l08.S (4 of 6)
l08_draw:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li a0, BLACK
call prg32_gfx_clear
li s0, 0 # s0 = bit number, 0 to 6
1: la t0, buttons
lw t1, 0(t0) # t1 = the button mask
srl t1, t1, s0 # bring bit number s0 down to bit 0
andi t1, t1, 1 # keep it, clear all the others
li a4, GREY # lamp off
beqz t1, 2f
li a4, YELLOW # lamp on
2: slli a0, s0, 5
addi a0, a0, 48 # x = 48 + 32 * bit
li a1, 40
li a2, 24
li a3, 24
call prg32_gfx_rect
addi s0, s0, 1
li t0, 7
blt s0, t0, 1b
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l08.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 13: The complete program: l08.S (5 of 6)
la t0, marker_x # the marker
lw a0, 0(t0)
li a1, 100
li a2, 16
li a3, 16
li a4, WHITE
call prg32_gfx_rect
la t0, idle # the result of De Morgan's test
lw t1, 0(t0)
li a4, RED
beqz t1, 3f
li a4, GREEN
3: li a0, 152
li a1, 150
li a2, 16
li a3, 16
call prg32_gfx_rect
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l08.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 14: The complete program: l08.S (6 of 6)
.section .data
buttons: .word 0
marker_x: .word 152
idle: .word 1
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l08.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 15: Run it: what you should see
On the screen
– seven lamps, one per button (LEFT on the left), lit while the button is held; a white marker that LEFT and RIGHT move; a square that is green when neither LEFT nor RIGHT is pressed and red otherwise.
What to press
– LEFT and RIGHT move the marker; try A and B too
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 16: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l08.S --portable \
--entry-prefix l08 --name l08 --out l08.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l08.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 17: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l08.S --portable \
--entry-prefix l08 --name l08 --architecture qemu \
--out l08-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l08-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 18: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l08.S --portable \
--entry-prefix l08 --name l08 --architecture esp32c6 \
--out l08-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l08-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 19: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l08; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 20: Exercises: paper first, then PRG32
TRY IT
1
Prove the second De Morgan law, (x + y)' = x' . y', with a truth table
2
Simplify with the algebra: x . y + x . y' . z + x' . y, naming the law used at each step
3
Write the mask and the instruction that test whether A and B are pressed together
4
Change the lamp program so that the lamps show the complement of the buttons (lit when released)
5
Convert a letter from upper to lower case and back using one bitwise instruction (hint: ASCII, Lecture 04)
Expected result
On PRG32: all seven lamps lit at rest, each one going dark while its button is held. For the letter: xori with 0x20 toggles bit 5.
Notes: Five exercises. Prove the second law of De Morgan with a truth table. Simplify an expression, naming the law at each step. Write the mask and the test for "A and B pressed together": note that testing for a non-zero result would mean A or B. Change the lamps so that they show the complement of the buttons. And convert a letter between upper and lower case with one instruction, remembering from Lecture 04 that the two differ in one bit. For the lecturer: Exercise 2: x y + x y' z + x' y = y (x + x') + x y' z = y + x y' z = y + x z. Exercise 3: andi t1, t0, 0x30 then compare with 0x30 (li t2, 0x30; beq t1, t2, both): testing for non-zero would mean A OR B.