## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 12
Verm1, Part 2: Steering, Food and a Score: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Verm1 reference implementation contributed by Giuseppe Coviello
Code deck. The concepts, the figures and the questions are in the lecture deck:
12-Computer_Architecture-Verm1_Part_2.pptx
Notes: This is the code deck of Lecture 12. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 15 listings of Lecture 12, one per slide: read the code, then the numbered remarks beside it
2
The program is your verm1.S; the reference is verm1/verm1_part2.S, 231 lines, shown here region by region
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The reference program is ~/arc12/verm1/verm1_part2.S; tools/tests/verm1_check.py builds it and plays it with a scripted player, and verm1_steps.py runs the intermediate checkpoints. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The reference program is ~/arc12/verm1/verm1_part2.S; tools/tests/verm1_check.py builds it and plays it with a scripted player, and verm1_steps.py runs the intermediate checkpoints. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: The working loop, again
# 1. build the cartridge (from your PRG32 folder, toolchain active)
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --out ~/verm1/verm1.prg32
# 2. send it to PRG32-QT, running on the same computer
python3 -m prg32 esp32c6 upload-and-run ~/verm1/verm1.prg32 \
--url http://localhost:8080 --slot cart0
# or: in PRG32-QT, import the file verm1.prg32 and choose Run Cartridge
Notes: The same two commands as in Part 1: build the cartridge, then upload it to PRG32-QT and run it. Keep PRG32-QT open for the whole session, with the debug mode enabled if you want the debugger at hand: step 4 uses it. For the lecturer: The same two commands of Part 1. PRG32-QT must be running, with Run cartridges in RISC-V debug mode enabled in Settings if you want the debugger.

## Slide 4: CHANGED Constants: buttons and directions
.option norelax
.equ BLACK, 0x0000 # RGB565 colours
.equ WHITE, 0xffff
.equ GREEN, 0x07e0
.equ RED, 0xf800
.equ CELL, 8 # a cell is 8 x 8 pixels
.equ COLS, 40
.equ ROWS, 24
.equ TOP, 8
.equ SPEED_Q8, 40 # 40/256 of a cell per frame
.equ BTN_LEFT, 0x01 # one bit per button
.equ BTN_RIGHT, 0x02
.equ BTN_UP, 0x04
.equ BTN_DOWN, 0x08
.equ DIR_RIGHT, 0 # a direction is a 2-bit code:
.equ DIR_DOWN, 1 # bit 0 = vertical
.equ DIR_LEFT, 2 # bit 1 = backwards
.equ DIR_UP, 3
.section .text
.global verm1_init
.global verm1_update
.global verm1_draw
1
New colour: RED, for the food
2
Each button is one bit of a word: a mask selects it
3
A direction is a number from 0 to 3: two bits
4
The codes are not arbitrary: see the lecture deck
Notes: Add these lines to the constants of Part 1. RED is the colour of the food. The four BTN_ constants are masks: each has a single bit at 1, the bit of that button in the word returned by the runtime. The four DIR_ constants are the codes of the directions, numbers from 0 to 3, that is two bits. The comments say what each of the two bits means, and the lecture deck, in the slide "A code chosen with care", explains why the codes were chosen in this way. For the lecturer: Add the lines from RED and from BTN_LEFT to DIR_UP to the constants of Part 1.

## Slide 5: CHANGED Data: two tables and five new variables
.section .rodata
title: .asciz "VERM1"
dx: .word 1, 0, -1, 0 # right, down, left, up
dy: .word 0, 1, 0, -1
.section .data
head_x: .word 5
head_y: .word 12
dir: .word 0 # direction of the last step
want: .word 0 # direction asked by the player
step_q8: .word 0
score: .word 0
food_x: .word 20
food_y: .word 12
1
dx and dy: four words each, one per direction
2
They are constants, so they live in .rodata
3
dir is the direction of the last step, want the one asked for
4
score, food_x, food_y: used in step 3
Notes: Replace the data of Part 1 with these. In .rodata there are two tables of four words, dx and dy: for each direction code, the change of column and the change of row. They never change, so they live with the constants. In .data there are five new variables: dir, the direction of the last step; want, the direction the player has asked for; and score, food_x and food_y, which are used in step 3. For the lecturer: Replace the data of Part 1 with this. The initial values are enough for step 2: init is completed in step 3.

## Slide 6: CHANGED update: from buttons to a wish
verm1_update:
addi sp, sp, -16
sw ra, 12(sp)
call prg32_input_read # a0 = one bit per button
la t0, dir
lw t1, 0(t0) # t1 = direction of the last step
la t0, want
lw t2, 0(t0) # t2 = wanted direction, so far
andi t3, a0, BTN_RIGHT
beqz t3, 1f
li t2, DIR_RIGHT
1: andi t3, a0, BTN_DOWN
beqz t3, 2f
li t2, DIR_DOWN
2: andi t3, a0, BTN_LEFT
beqz t3, 3f
li t2, DIR_LEFT
3: andi t3, a0, BTN_UP
beqz t3, 4f
li t2, DIR_UP
4: xor t3, t2, t1 # opposite directions differ in bit 1 only
li t4, 2
beq t3, t4, 5f # a U-turn: ignore the request
sw t2, 0(t0) # remember it for the next step
5:
1
andi keeps one bit: zero means not pressed
2
Each pressed button overwrites the wish in t2
3
xor of wish and direction: 2 means opposite
4
A U-turn is not stored: the old wish survives
Notes: This replaces the beginning of verm1_update. After the call to prg32_input_read, t1 receives the current direction and t2 the current wish. Then four identical blocks: andi isolates one button; if the result is zero the next instruction is skipped; otherwise the wish in t2 is overwritten with that direction. Finally the rule: the XOR of wish and direction is compared with 2; if they are equal the request is a U-turn and the sw is skipped, so the old wish survives. update now makes a call, so it has a stack frame. For the lecturer: This replaces the beginning of verm1_update. update now calls a function, so it needs a stack frame. With two buttons pressed the last test wins: UP beats LEFT beats DOWN beats RIGHT. The player's wish is stored in want and becomes the direction only at the next step: so two quick presses cannot fold the worm onto itself.

## Slide 7: CHANGED update: the timer calls step
la t0, step_q8
lw t1, 0(t0)
addi t1, t1, SPEED_Q8 # add a fraction of a cell
li t2, 256
blt t1, t2, 6f # less than one whole cell: wait
sub t1, t1, t2
sw t1, 0(t0)
call step # one whole cell: move
j 7f
6: sw t1, 0(t0)
7: lw ra, 12(sp)
addi sp, sp, 16
ret
1
The fixed-point timer of Part 1, unchanged
2
Moving is now a function of its own: step
3
Labels 6 and 7: numbers 1 to 5 are used above
Notes: The rest of verm1_update is the fixed-point timer of Part 1, unchanged: add the speed, and when a whole cell has accumulated subtract 256. The only difference is what happens then: instead of moving head_x directly, the code calls a new function, step. The local labels here are 6 and 7 because the numbers from 1 to 5 are already used in the first half of the function. For the lecturer: This is the rest of verm1_update. The lines that moved head_x in Part 1 are gone: they become the function step.

## Slide 8: NEW step: look the movement up
step:
addi sp, sp, -16
sw ra, 12(sp)
la t0, want
lw t1, 0(t0)
la t0, dir
sw t1, 0(t0) # the wanted direction is now the direction
slli t1, t1, 2 # table offset = direction * 4 bytes
la t0, dx
add t0, t0, t1
lw t2, 0(t0) # t2 = dx[direction]: -1, 0 or +1
la t0, dy
add t0, t0, t1
lw t3, 0(t0) # t3 = dy[direction]
1
The wish becomes the direction, once per step
2
A word is 4 bytes: offset = code shifted left by 2
3
address of table + offset: the word to load
4
No branch: the code selects, like a multiplexer
Notes: The first half of step. The wish becomes the direction: this happens once per step, not once per frame, so two quick presses cannot fold the worm back on itself. Then the lookup: the code of the direction is shifted left by 2, because each entry of a table is a word of four bytes, and added to the address of dx; the word loaded is the change of column, minus 1, 0 or plus 1. The same offset serves for dy. There is no branch: the code selects the value, as a multiplexer would. For the lecturer: A table in read-only memory addressed by a code is a ROM: Lecture 11. The alternative is four branches; the table is shorter, and changing the rules means changing data, not code.

## Slide 9: NEW step: move and wrap, both ways
la t0, head_x
lw t4, 0(t0)
add t4, t4, t2
bgez t4, 1f
li t4, COLS-1 # off the left edge: wrap
1: li t5, COLS
blt t4, t5, 2f
li t4, 0 # off the right edge: wrap
2: sw t4, 0(t0) # t4 = new column
la t0, head_y
lw t6, 0(t0)
add t6, t6, t3
bgez t6, 3f
li t6, ROWS-1
3: li t5, ROWS
blt t6, t5, 4f
li t6, 0
4: sw t6, 0(t0) # t6 = new row
1
Add dx: the column can now go below 0
2
bgez tests the sign: negative means off the left
3
The same for the row, with ROWS
4
t4 and t6 keep the new cell for the next slide
Notes: The second half moves the head and handles the edges, in both directions. The column plus dx can now become minus 1: bgez tests the sign, and a negative column is replaced by the last column. If instead it has reached COLS, it becomes 0. The same is done for the row with ROWS. Note the last callout: t4 and t6 still hold the new column and row, and the next piece of code will use them. For the lecturer: In Part 1 only the right edge existed. A negative column is a signed number: bgez and blt are the signed comparisons of Lecture 05.

## Slide 10: For now: close the function
lw ra, 12(sp) # temporary end of step:
addi sp, sp, 16 # Step 3 will replace these three lines
ret
1
Type these three lines after the wrap
2
They restore ra and return: step is complete
3
Step 3 puts the food test before them
Notes: Three temporary lines that restore ra, release the frame and return, so that step is complete and the program can run now. This is a habit of the tutorials: when a function will be finished later, close it provisionally and test what you have. In step 3 you will insert the test for the food before these lines. For the lecturer: A temporary ending, so that the program can run now. This intermediate program is built and run by tests/verm1_steps.py.

## Slide 11: Run it: you are driving
TRY IT
1
Build and run: the head still starts to the right, from column 5 of row 12
2
Hold DOWN: the head turns at its next step and goes down, wrapping from row 23 to row 0
3
While it goes right, hold LEFT: nothing happens. The U-turn is refused
4
Hold DOWN and then LEFT: two turns, and now the head goes left
Expected result
Holding DOWN from the start for 64 frames brings the head to column 5, row 22: ten steps, all downwards.
Notes: Run it: you are driving. The head starts to the right as before. Hold DOWN and it turns at its next step. While it goes right, hold LEFT: nothing happens, because the U-turn is refused. To go left you need two turns, DOWN and then LEFT. The green box gives a precise check: holding DOWN from the start for 64 frames brings the head to column 5 of row 22, ten steps down. For the lecturer: Checked on the PRG32-QT headless runner: DOWN held 64 frames gives (5, 22); LEFT held 64 frames gives (15, 12), as if nothing had been pressed.

## Slide 12: CHANGED init: a complete start
verm1_init:
addi sp, sp, -16
sw ra, 12(sp)
la t0, head_x
li t1, 5
sw t1, 0(t0)
la t0, head_y
li t1, 12
sw t1, 0(t0)
la t0, dir
sw zero, 0(t0) # moving right
la t0, want
sw zero, 0(t0)
la t0, step_q8
sw zero, 0(t0)
la t0, score
sw zero, 0(t0)
call place_food
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Every variable gets its starting value
2
init now calls a function: it needs a stack frame
3
The first food is placed here
Notes: verm1_init is replaced by a complete version: every variable receives its starting value, including the direction, the wish and the score, and the first food is placed by calling place_food. Because it now makes a call, init too has a stack frame that saves ra. For the lecturer: Replace verm1_init.

## Slide 13: NEW place_food: a random cell
place_food:
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0
li a1, COLS-1
call prg32_random_number # a0 = a column, 0 .. 39
la t0, food_x
sw a0, 0(t0)
li a0, 0
li a1, ROWS-1
call prg32_random_number # a0 = a row, 0 .. 23
la t0, food_y
sw a0, 0(t0)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
prg32_random_number(min, max): both included
2
Arguments in a0 and a1, result in a0
3
A column from 0 to 39, a row from 0 to 23
4
The food may fall on the head: Part 3 fixes it
Notes: place_food asks the runtime for two random numbers. The contract of prg32_random_number is: minimum in a0, maximum in a1, both included, result in a0. The first call gives a column from 0 to 39, the second a row from 0 to 23, and each is stored in its variable. One defect is left on purpose: the food may fall exactly on the head. Part 3, when the worm has a body, will correct it. For the lecturer: The random numbers come from the runtime: on the board from the hardware generator of the ESP32-C6. Two runs of the game are different.

## Slide 14: CHANGED step: is the head on the food?
la t0, food_x
lw t1, 0(t0)
xor t1, t1, t4 # 0 if same column
la t0, food_y
lw t2, 0(t0)
xor t2, t2, t6 # 0 if same row
or t1, t1, t2 # 0 only if both are equal
bnez t1, 5f # not on the food
la t0, score
lw t1, 0(t0)
addi t1, t1, 1
sw t1, 0(t0)
call place_food
call eat_sound
5: lw ra, 12(sp)
addi sp, sp, 16
ret
1
Replace the temporary ending with this
2
xor is 0 when two numbers are equal
3
or of the two results: 0 only if both are equal
4
Eating: one more point, new food, a sound
Notes: This replaces the temporary ending of step. It is a comparator built from instructions: xor of the food's column and the head's column is 0 when they are equal; the same for the rows; or of the two results is 0 only if both are equal. If the result is not zero, the function ends. Otherwise the worm has eaten: the score is increased by one, new food is placed, and a sound is played. It is the AND of XNORs of Lecture 11, written with two xor and one or. For the lecturer: A comparator for equality is a row of XOR gates followed by an OR: Lecture 11. Here it is two xor and one or. The registers t4 and t6 still hold the new column and row; after the calls they are no longer needed, which is why it is safe to keep them in temporaries.

## Slide 15: NEW eat_sound: one note
eat_sound:
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0 # channel
li a1, 0 # instrument
li a2, 72 # note: C5
li a3, 255 # volume
li a4, 60 # milliseconds
call prg32_audio_note
lw ra, 12(sp)
addi sp, sp, 16
ret
1
Five arguments, a0 to a4, then the call
2
Note 72 is C5 in MIDI numbering
3
Sound comes last: the game worked without it
Notes: eat_sound plays one note. prg32_audio_note takes five arguments, in a0 to a4: channel, instrument, note, volume and duration in milliseconds. Note 72 is the C of the fifth octave in MIDI numbering. The last callout repeats a principle of PRG32: sound comes last. The game worked without it, and it is added when everything else is solid. For the lecturer: prg32_audio_note(channel, instrument, note, volume, milliseconds). On PRG32-QT the note is played by the computer; on the board by the amplifier and its speaker.

## Slide 16: CHANGED draw: the score as marks
verm1_draw:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li a0, BLACK
call prg32_gfx_clear
li a0, 0
li a1, 0
la a2, title
li a3, WHITE
li a4, BLACK
call prg32_gfx_text8
li s0, 0 # s0 = i: one mark per point
1: la t0, score
lw t1, 0(t0)
bge s0, t1, 2f
slli a0, s0, 2
addi a0, a0, 56 # x = 56 + 4 * i
li a1, 1
li a2, 3
li a3, 6
li a4, WHITE
call prg32_gfx_rect
addi s0, s0, 1
j 1b
2:
1
s0 counts the marks: it must survive the calls
2
So s0 is saved in the frame, with ra
3
One small rectangle per point, 4 pixels apart
4
The loop ends when s0 reaches the score
Notes: The beginning of the new verm1_draw: after the title, a loop draws one small rectangle for each point of the score, 4 pixels apart. The counter of the loop is in s0, not in a t register, because it must survive the calls to prg32_gfx_rect: a function may destroy the temporaries, but preserves the s registers. In exchange your own function must save s0 in its frame and restore it at the end. This convention is studied in Lecture 18. For the lecturer: Replace the beginning of verm1_draw. A t register may be destroyed by any call; an s register is preserved, provided that we save and restore it ourselves: the convention, met in Lecture 02, is studied in Lecture 18. Digits arrive in Part 4, when division is available.

## Slide 17: CHANGED draw: food and head
la t0, food_x
lw a0, 0(t0)
la t0, food_y
lw a1, 0(t0)
li a2, RED
call draw_cell
la t0, head_x
lw a0, 0(t0)
la t0, head_y
lw a1, 0(t0)
li a2, GREEN
call draw_cell
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
1
The same three lines twice: column, row, colour
2
draw_cell does the conversion to pixels
3
The head is drawn last: it covers the food
Notes: The rest of verm1_draw: the same three lines twice, first for the food and then for the head: load the column, load the row, load the colour, and call draw_cell. The order matters: the head is drawn last, so that it covers the food if they are in the same cell. Then s0 and ra are restored and the function returns. For the lecturer: This is the rest of verm1_draw: it replaces the rectangle of Part 1.

## Slide 18: NEW draw_cell: from cells to pixels
draw_cell: # a0 = column, a1 = row, a2 = colour
addi sp, sp, -16
sw ra, 12(sp)
slli a0, a0, 3 # x = column * 8
slli a1, a1, 3
addi a1, a1, TOP # y = row * 8 + 8
mv a4, a2 # the colour is the fifth argument
li a2, CELL
li a3, CELL
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
1
The arithmetic of Part 1, written once
2
The colour arrives in a2 and must leave in a4
3
Move it first: a2 is about to be overwritten
Notes: draw_cell gathers in one function the arithmetic that Part 1 had inside draw: column times 8, row times 8 plus TOP. Its contract is written in the comment on its first line: column in a0, row in a1, colour in a2. One subtlety: prg32_gfx_rect wants the colour in a4, and a2 is about to be overwritten with the width, so the colour must be moved first. Writing the contract of a function in a comment is part of the job. For the lecturer: A function with a contract: a0 = column, a1 = row, a2 = colour. Writing the contract in a comment is part of the job.

## Slide 19: Run it: Verm1, Part 2
The head, the food, and two marks after the title: two points
Expected: a red cell somewhere; steer the head onto it; a note sounds, a mark appears next to VERM1, the food moves.
Notes: Run it. You should see a red cell somewhere. Steer the head onto it: a note sounds, a mark appears next to the title, and the food moves to another cell. The screenshot shows the game after two bites, with two marks. It was produced by the automatic test, in which a scripted player steers the head to the food twice. For the lecturer: Screenshot produced by tools/tests/verm1_check.py: a scripted player steers the head to the food twice.

## Slide 20: Run it: what you should see
On the screen
– a head that you steer, a red cell of food that moves when it is eaten, a note, and one mark per point next to VERM1.
What to press
– steer with the joystick; a U-turn is refused
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 21: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --out verm1.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run verm1.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 22: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --architecture qemu \
--out verm1-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload verm1-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 23: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/verm1/verm1.S --portable \
--entry-prefix verm1 --name verm1 --architecture esp32c6 \
--out verm1-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run verm1-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 24: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix verm1; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 25: Make it yours
TRY IT
1
Make button A a brake: while it is held, the timer does not advance
2
Give two points for a piece of food eaten in the top row
3
Draw the head in a different colour for each direction, using a third table of four colours
4
Change the encoding so that RIGHT = 0, LEFT = 1, DOWN = 2, UP = 3: what does the U-turn rule become?
Expected result
Each change is a few lines. Keep a copy of the working Part 2 before you experiment: Part 3 starts from it.
Notes: Four changes of your own. Make button A a brake that stops the timer while it is held. Give two points for food eaten in the top row. Draw the head in a different colour for each direction, with a third table indexed like dx. And change the encoding of the directions: with RIGHT 0, LEFT 1, DOWN 2 and UP 3, what does the U-turn rule become? Keep a copy of the working Part 2 before experimenting. For the lecturer: Brake: andi with BTN_A (0x10) at the start of the timer, branch to the exit. Colour table: four .word in .rodata, indexed like dx. New encoding: opposites differ in bit 0, so the test is XOR = 1.