## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 15
Memory: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Code deck. The concepts, the figures and the questions are in the lecture deck:
15-Computer_Architecture-Memory.pptx
Notes: This is the code deck of Lecture 15. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 2 listings of Lecture 15, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l15.S, 95 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l15.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l15.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Read the same memory as a word and as bytes
la t0, value
lw t1, 0(t0) # the whole word t1 = 0x12345678
lbu t2, 0(t0) # the byte at address A t2 = 0x78
lbu t3, 1(t0) # the byte at address A+1 t3 = 0x56
lbu t4, 3(t0) # the byte at address A+3 t4 = 0x12
.section .data
value: .word 0x12345678
1
A word of thirty-two bits occupies four consecutive addresses: memory is addressed byte by byte
2
The byte at the lowest address is 0x78, the least significant: little-endian order
3
lw fetches four bytes in one operation; lbu fetches one
4
What is a memory made of, and what happens between the processor and the memory when lw runs?
Notes: value is a word that contains 0x12345678. lw loads all of it into t1. Then three lbu instructions load single bytes, at the address of the word, at that address plus 1 and plus 3: they give 0x78, 0x56 and 0x12. Two facts follow. A word occupies four consecutive addresses, because memory is addressed byte by byte. And the byte at the lowest address is the least significant: the little-endian order. Open the memory view of PRG32-QT at the address in t0 and you see 78 56 34 12. For the lecturer: Run it in PRG32-QT and open the memory view at the address in t0: the bytes appear as 78 56 34 12. The byte-order slide of Lecture 04 becomes an experiment.

## Slide 4: Aligned and unaligned words
A word that starts at an address multiple of its size is aligned on the word boundary: multiples of 4 for 32-bit words
An aligned word is fetched with a single memory access
An unaligned word straddles two memory words: two accesses are needed
RISC-V: the assembler aligns .word data for you, and instructions must always be aligned
– a load or store to a misaligned address is, depending on the processor, done more slowly or refused with an exception
The directive .balign 4 forces alignment after a string or a byte
.section .data
name: .asciz "PRG32" # 6 bytes
.balign 4 # skip 2
score: .word 0 # aligned
Notes: A word is aligned when it starts at an address that is a multiple of its size: a multiple of 4 for 32-bit words. An aligned word is fetched with a single access; an unaligned one straddles two memory words. In RISC-V the assembler aligns .word data for you, and a load from a misaligned address is, depending on the processor, slower or refused. The code on the right shows the typical case: after a string of six bytes, .balign 4 skips two bytes so that the next word is aligned. For the lecturer: The original deck: the MC68000 does not allow unaligned words, Intel x86 allows them at the cost of two accesses. The RISC-V specification leaves the choice to the implementation: correct programs keep their data aligned.

## Slide 5: Fetching a word: lw t1, 0(t0)
Step | What happens | Where
1 | the address, t0 + 0, is computed by the ALU and placed in MA | processor
2 | MA drives the address bus | address bus
3 | the control unit raises read enable | control lines
4 | the memory decodes the address and puts the four bytes of the word on the data bus | memory, data bus
5 | the datum on the data bus is latched in MB | processor
6 | MB is copied into the destination register t1 | processor
sw is symmetrical: the datum goes into MB, write enable is raised, and the memory stores what it finds on the data bus.
Notes: The six steps of lw t1, 0(t0). The ALU computes the address and puts it in MA. MA drives the address bus. The control unit raises read enable. The memory decodes the address and puts the word on the data bus. The datum is captured in MB. MB is copied into t1. A store is symmetrical: the address goes to MA, the datum to MB, write enable is raised, and the memory stores what it finds on the data bus. The access time is what elapses between the second and the fifth step. For the lecturer: A store, sw t1, 0(t0), is symmetrical: address in MA, datum in MB, write enable raised, and the memory latches the datum. The access time is the time between step 2 and step 5.

## Slide 6: Where things live on the ESP32-C6 (simplified)
Address range begins with | What is there | Reached by
0x4000... | ROM: the code that starts the chip | instruction fetch
0x4080... | SRAM: 512 KB for data, stack and cartridges loaded in RAM | lw, sw, instruction fetch
0x4200... | external flash, seen through a cache: firmware and constants | lw, instruction fetch
0x6000... | peripheral registers: GPIO, SPI, I2S, timers, Wi-Fi | lw, sw
One address space for everything. Writing a word to a peripheral register with sw is how a RISC-V program lights a pixel or reads a button.
Notes: A simplified map of the addresses of the ESP32-C6. Addresses that begin with 0x4000 are the ROM with the code that starts the chip; 0x4080 is the SRAM, where your cartridge is loaded; 0x4200 is the external flash with the firmware; 0x6000 are the registers of the peripherals. The same thirty-two address lines reach everything, and the same lw and sw operate everything. The cartridge address you saw in the debugger, 0x40800000, is the beginning of the RAM. For the lecturer: Simplified from the ESP32-C6 technical reference manual; check the manual before relying on an address. The point for the students: the same thirty-two address lines reach ROM, RAM, flash and every device, and the same lw and sw operate them.

## Slide 7: The complete program: l15.S (1 of 5)
# ARC12 Computer Architecture - Lecture 15: Memory
# l15.S: the same memory read as a word and as bytes
#
# On the screen: five rows of lamps. The first is the word 0x12345678 read with lw.
# The other four are the bytes at addresses A, A+1, A+2, A+3 read with lbu: 0x78,
# 0x56, 0x34, 0x12. The lowest address holds the least significant byte: little-
# endian.
# Build: python3 -m prg32 cartridge build l15.S --portable \
# --entry-prefix l15 --name l15 --out l15.prg32
.option norelax
.equ BLACK, 0x0000
.equ GREY, 0x4208
.equ YELLOW, 0xffe0
.section .text
.global l15_init
.global l15_update
.global l15_draw
l15_init:
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l15.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: The complete program: l15.S (2 of 5)
l15_update:
ret
l15_draw:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li a0, BLACK
call prg32_gfx_clear
call prg32_console_clear
la t0, value
lw a0, 0(t0) # the whole word
call prg32_console_hex32
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l15.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: The complete program: l15.S (3 of 5)
la t0, value
lw a0, 0(t0) # the whole word: 0x12345678
li a1, 20
call lamps32
li s0, 0 # byte number, 0 to 3
1: la t0, value
add t0, t0, s0 # address A + s0: one byte further each time
lbu a0, 0(t0) # the byte at that address, zero-extended
slli a1, s0, 4
slli t1, s0, 3
add a1, a1, t1 # 24 * s0
addi a1, a1, 60 # y = 60 + 24 * byte number
call lamps32
addi s0, s0, 1
li t0, 4
blt s0, t0, 1b
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l15.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 10: The complete program: l15.S (4 of 5)
# lamps32: show the 32 bits of a word as a row of lamps, bit 31 on the left.
# a0 = the word, a1 = y of the row. A lamp is yellow for 1, grey for 0.
lamps32:
addi sp, sp, -32
sw ra, 28(sp)
sw s0, 24(sp)
sw s1, 20(sp)
sw s2, 16(sp)
mv s0, a0 # the word
mv s1, a1 # y
li s2, 0 # lamp number, 0 on the left
1: li t0, 31
sub t0, t0, s2 # lamp i shows bit 31 - i
srl t1, s0, t0 # bring that bit down to bit 0
andi t1, t1, 1 # keep it, clear all the others
li a4, GREY # lamp off
beqz t1, 2f
li a4, YELLOW # lamp on
2: slli a0, s2, 3
add a0, a0, s2 # 9 * i
addi a0, a0, 16 # x = 16 + 9 * i
mv a1, s1
li a2, 8
li a3, 8
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l15.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 11: The complete program: l15.S (5 of 5)
call prg32_gfx_rect
addi s2, s2, 1
li t0, 32
blt s2, t0, 1b
lw s2, 16(sp)
lw s1, 20(sp)
lw s0, 24(sp)
lw ra, 28(sp)
addi sp, sp, 32
ret
.section .data
value: .word 0x12345678
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l15.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 12: Run it: what you should see
On the screen
– five rows of lamps. The first is the word 0x12345678 read with lw. The other four are the bytes at addresses A, A+1, A+2, A+3 read with lbu: 0x78, 0x56, 0x34, 0x12. The lowest address holds the least significant byte: little-endian.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 13: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l15.S --portable \
--entry-prefix l15 --name l15 --out l15.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l15.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 14: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l15.S --portable \
--entry-prefix l15 --name l15 --architecture qemu \
--out l15-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l15-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 15: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l15.S --portable \
--entry-prefix l15 --name l15 --architecture esp32c6 \
--out l15-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l15-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 16: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l15; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 17: Exercises: paper first, then PRG32
TRY IT
1
A memory of 4 KiB words of 16 bits: how many address lines, how many data lines, how many bits in all?
2
Write the bytes stored, in order of address, by .word 0xDEADBEEF and by .asciz "Ciao" on a little-endian machine
3
List the steps of sw t1, 8(t0) on the processor-memory interface
4
In PRG32-QT, find your counter variable in the memory view and watch its four bytes change frame by frame
5
Store a word with sw and read it back with four lbu instructions; rebuild it with shifts and ors and check that it matches
Expected result
On paper: 12 address lines, 16 data lines, 65,536 bits. On PRG32: the lowest byte of the counter changes every frame, the next one every 256 frames.
Notes: Five exercises. Compute address lines, data lines and total bits of a memory of 4 KiB words of 16 bits. Write, in order of address, the bytes stored by a word and by a string on a little-endian machine. List the steps of a store on the processor-memory interface. In PRG32-QT find your counter in the memory view and watch its four bytes change. And store a word, read it back as four bytes, rebuild it with shifts and ORs, and check that it matches. For the lecturer: 0xDEADBEEF: EF BE AD DE. "Ciao": 43 69 61 6F 00. Exercise 5: slli by 8, 16 and 24, then or.