## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 02
First Contact: RISC-V Assembly on PRG32: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Notes: This is the code deck of Lecture 02. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 5 listings of Lecture 02, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l02.S, 60 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l02.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l02.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Step 1: the smallest program that runs
# Assembly Lab 1: the smallest program that runs
.option norelax
.section .text
.global first_init
.global first_update
.global first_draw
first_init:
ret
first_update:
ret
first_draw:
ret
1
.option norelax keeps the layout of the cartridge predictable: every PRG32 example starts with it
2
.section .text says that what follows is executable code
3
.global makes a label visible to the firmware, which finds your functions by name
4
ret returns to the caller: three functions that do nothing, correctly
Notes: The smallest program that runs. .option norelax is a line with which every PRG32 example starts: it keeps the layout of the cartridge predictable. .section .text says that code follows. Each .global makes a label visible outside the file, so that the firmware can find the function by name. Then three functions, each made of the single instruction ret, which returns to the caller. The result is a black screen, and it is a success: the framework found your three functions, called them, and got control back. For the lecturer: Source: labs/05-asm-first-contact/step1_skeleton.S. Expected result: a black screen. The achievement is that the framework found the three functions, called them, and survived.

## Slide 4: Build it, run it
# 1. build a portable cartridge from one assembly file
python3 -m prg32 cartridge build step1_skeleton.S --portable \
--entry-prefix first --name step1 --out build/step1.prg32
# 2a. run it in QEMU on your laptop
python3 -m prg32 qemu upload build/step1.prg32
python3 -m prg32 qemu run
# 2b. or send it to a board, or to PRG32-QT, over the network
python3 -m prg32 esp32c6 upload-and-run build/step1.prg32 \
--url http://192.168.4.1 --slot cart0
Notes: Two commands that you will type hundreds of times. cartridge build turns the assembly file into a cartridge: --entry-prefix first is the prefix of your three functions, --out the name of the result. Then you run it: in QEMU with qemu upload and qemu run, or on a board or PRG32-QT with upload-and-run and the address of the host. For PRG32-QT on your own laptop the address is http://localhost:8080. The cartridge file is the same for all three. For the lecturer: Source: labs/run.sh. With PRG32_HOME set, the whole sequence is: labs/run.sh 05-asm-first-contact/step1_skeleton.S first . The cartridge file is byte-for-byte the same for QEMU, the board and PRG32-QT.

## Slide 5: Step 2: say hello
first_draw:
addi sp, sp, -16 # prologue: a 16-byte frame
sw ra, 12(sp) # save the return address
li a0, BLACK
call prg32_gfx_clear
li a0, 32 # x
li a1, 40 # y
la a2, title # address of the string
li a3, WHITE # foreground
li a4, BLACK # background
call prg32_gfx_text8
lw ra, 12(sp) # epilogue: restore ra
addi sp, sp, 16 # release the frame
ret
.section .rodata
title:
.asciz "HELLO PRG32"
Screenshot: this step, built and run on PRG32
The first argument goes in a0, the second in a1, and so on. li loads a number; la loads the address of a label.
Notes: The second step writes on the screen. Read first_draw in three parts. The first two lines make room on the stack and save ra. Then two calls: prg32_gfx_clear with the colour in a0, and prg32_gfx_text8 with five arguments in a0 to a4: x, y, the address of the string, foreground, background. Note the two ways of loading: li loads a number, la loads the address of a label. The last three lines restore ra, release the stack and return. The string itself is data, in the section .rodata. For the lecturer: Source: labs/05-asm-first-contact/step2_hello.S. The .equ lines (BLACK 0x0000, WHITE 0xffff) are omitted on the slide.

## Slide 6: Step 3: a value that survives between frames
first_update:
# A leaf function: it calls nothing,
# so it needs no stack frame.
la t0, counter # t0 = ADDRESS of counter
lw t1, 0(t0) # t1 = VALUE stored there (load)
addi t1, t1, 1 # one tick per frame (modify)
sw t1, 0(t0) # write it back (store)
ret
.section .data
counter: .word 0
1
counter is a label: it names a location in memory, in the .data section, holding one 32-bit word
2
la puts the ADDRESS of that location in t0
3
lw reads the VALUE at that address into t1; sw writes it back
4
The processor computes only in registers: load, modify, store
Notes: The third step keeps a value from one frame to the next. Registers do not survive between calls of update, so the value must live in memory. counter is a label: it names a location in the section .data that holds one word. The four instructions are the pattern of every variable: la puts the address of the location in t0; lw loads the value into t1; addi changes it; sw stores it back. Load, modify, store. Nothing changes on the screen yet: the counter ticks, but nobody draws it. For the lecturer: Source: labs/05-asm-first-contact/step3_counter.S. Nothing visible changes yet: the counter ticks but nobody draws it. Ask the class how they could prove that it is ticking (answer: the debugger of PRG32-QT, or the next step).

## Slide 7: Step 4: make the counter visible
la t0, counter
lw t1, 0(t0)
andi a2, t1, 255 # width = counter modulo 256
li a0, 32 # x
li a1, 60 # y
li a3, 8 # height
li a4, GREEN # .equ GREEN, 0x07e0
call prg32_gfx_rect
Screenshot: this step, built and run on PRG32
The bar grows from 0 to 255 pixels, then starts again. andi with 255 keeps only the low eight bits of the counter.
Notes: The fourth step makes the counter visible as a green bar. The value is loaded, and andi a2, t1, 255 keeps only its low eight bits, so the width goes from 0 to 255 and then starts again. The other registers are the arguments of prg32_gfx_rect: x, y, width, height and colour. Eight lines, and three later lectures are hidden in them: 255 written as 0xFF, andi used as a mask, and 0x07e0 that means green. Remember where you first saw them. For the lecturer: Source: labs/05-asm-first-contact/step4_bar.S (the lines added to first_draw). Three future lectures hide in these eight lines: 255 = 0xFF (positional notation), andi as a bit mask (Boolean algebra), 0x07e0 as a colour (information encoding).

## Slide 8: The complete program: l02.S (1 of 3)
# ARC12 Computer Architecture - Lecture 02: First Contact: RISC-V Assembly on PRG32
# l02.S: the four steps of the lecture in one file
#
# On the screen: HELLO PRG32 and, under it, a green bar that grows by one pixel per
# frame and starts again at 256.
# Build: python3 -m prg32 cartridge build l02.S --portable \
# --entry-prefix first --name first --out first.prg32
.option norelax
.equ BLACK, 0x0000
.equ WHITE, 0xffff
.equ GREEN, 0x07e0
.section .text
.global first_init
.global first_update
.global first_draw
first_init: # step 1: a function that returns
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l02.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: The complete program: l02.S (2 of 3)
first_update: # step 3: a value that survives between frames
# A leaf function: it calls nothing, so it needs no stack frame.
la t0, counter # t0 = ADDRESS of counter
lw t1, 0(t0) # t1 = VALUE stored there (load)
addi t1, t1, 1 # one tick per frame (modify)
sw t1, 0(t0) # write it back (store)
ret
first_draw: # step 2: say hello
addi sp, sp, -16 # prologue: a 16-byte frame
sw ra, 12(sp) # save the return address
li a0, BLACK
call prg32_gfx_clear
li a0, 32 # x
li a1, 40 # y
la a2, title # address of the string
li a3, WHITE # foreground
li a4, BLACK # background
call prg32_gfx_text8
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l02.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 10: The complete program: l02.S (3 of 3)
la t0, counter # step 4: make the counter visible
lw t1, 0(t0)
andi a2, t1, 255 # width = counter modulo 256
li a0, 32 # x
li a1, 60 # y
li a3, 8 # height
li a4, GREEN
call prg32_gfx_rect
lw ra, 12(sp) # epilogue: restore ra
addi sp, sp, 16 # release the frame
ret
.section .rodata
title:
.asciz "HELLO PRG32"
.section .data
counter: .word 0
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l02.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 11: Run it: what you should see
On the screen
– HELLO PRG32 and, under it, a green bar that grows by one pixel per frame and starts again at 256.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 12: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l02.S --portable \
--entry-prefix first --name l02 --out l02.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l02.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 13: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l02.S --portable \
--entry-prefix first --name l02 --architecture qemu \
--out l02-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l02-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 14: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l02.S --portable \
--entry-prefix first --name l02 --architecture esp32c6 \
--out l02-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l02-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 15: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix first; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 16: Exercises on PRG32
TRY IT
1
Change the title string and its colour to yellow (0xffe0); run it again
2
Make the bar grow twice as fast, then four times as fast, changing one instruction only
3
Make the bar shrink instead of grow. What happens when the counter passes zero?
4
In PRG32-QT, single-step first_update and write down t0 and t1 after each instruction
5
Draw a second bar, in red, whose width is the counter modulo 64
Expected result
For exercise 3 the counter goes 0, then 0xFFFFFFFF: with andi 255 the bar jumps to 255 and shrinks. Keep the observation: Lecture 05 explains it.
Notes: Five exercises on your own cartridge; each is the seed of a later lecture. Change the text and its colour. Make the bar grow two or four times as fast by changing one instruction. Make it shrink, and observe what happens when the counter passes zero: the bar jumps to its full width, and Lecture 05 will explain why. Single-step first_update and write down the registers. Draw a second bar whose width is the counter modulo 64. Predict first, then run. For the lecturer: Hints: addi t1, t1, 2 or slli before andi for exercise 2; addi t1, t1, -1 for exercise 3; andi a2, t1, 63 for exercise 5. Each exercise is a seed for a later lecture.