## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 10
Introduction to Electronics and Digital Electronics: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Notes: This is the code deck of Lecture 10. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 1 listing of Lecture 10, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l10.S, 58 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l10.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l10.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: One button, one bit
call prg32_input_read # a0 = one bit per button
andi t3, a0, 0x01 # bit 0: LEFT
beqz t3, 1f # 0: not pressed
... # 1: pressed
1:
# on the kit:
# LEFT is a switch between pin GPIO18 and ground
# pressed -> the pin is at 0 volts
# released -> the pin is at 3.3 volts
1
Since the first labs a pressed button has been a 1 in a register
2
On the board the button is a piece of metal that joins a pin of the chip to ground
3
Pressed means 0 volts on the pin, and yet the program reads 1
4
What is a volt, why is the released pin at 3.3 V, and who decides that 0 V is a bit?
Notes: In your program a pressed button is a 1. On the board the button LEFT is a switch between a pin of the chip, GPIO18, and ground. When it is pressed the pin is at 0 volts; when it is released the pin is at 3.3 volts. So pressed means 0 volts, and yet the program reads 1. The four callouts turn this into the questions of the lecture: what is a volt, why is the released pin at 3.3 V, and who decides that 0 V is a bit? The last section answers them. For the lecturer: Wiring from the PRG32 hardware documentation: every button is a switch to GND, and the firmware enables the internal pull-up of each input. The runtime inverts the level when it builds the mask (prg32_controller.c): pressed pin low, bit high. The last section of the lecture answers the four callouts.

## Slide 4: From the finger to the bit
Step | What happens | Where it is explained
1 | the finger closes the switch between GPIO18 and ground | this lecture: the circuit
2 | the pin falls from 3.3 V to 0 V, in well under a microsecond | this lecture: R x C
3 | the input buffer sees a voltage below 0.825 V: a logic 0 | this lecture: logic levels
4 | the level is sampled into a flip-flop of the input register | Lecture 13: sequential machines
5 | the firmware reads that register with a load instruction | Lecture 15: memory-mapped input/output
6 | it inverts the bit and packs it with the others into a0 | Lecture 08: masks; Lecture 21: input devices
7 | your program tests it: andi t3, a0, 0x01 | Lecture 02: first contact
Notes: The whole journey in seven steps. The finger closes the switch; the pin falls to 0 V in less than a microsecond; the input buffer sees a voltage below its threshold, a logic 0; the level is captured in a flip-flop; the firmware reads it with a load instruction, inverts it and packs it with the others; your program tests it with andi. The right column says where each step is explained: three in this lecture, the others in lectures you have attended or will attend. Seven layers lie between a finger and a bit. For the lecturer: The contacts of a real switch bounce for a few milliseconds when they close: reading the buttons once per frame, every few tens of milliseconds, hides the bounce (Lecture 21).

## Slide 5: The kit as a circuit
A breadboard: holes joined in rows underneath, so that components connect without soldering
Two long buses carry the supply: 3.3 V and ground; a separate bus carries 5 V for the audio amplifiers
Every part shares the same ground: without a common reference, the voltages of two parts mean nothing to each other
The buttons go from a pin to ground; the display and the amplifiers receive digital signals from other pins
An output pin can light an LED through a resistor; an input pin only listens
The PRG32 kit on a breadboard (PRG32 hardware documentation)
Notes: The kit seen as a circuit. A breadboard has holes joined in rows underneath, so components connect without soldering. Two long buses carry the supply, 3.3 V and ground, and a separate one carries 5 V for the audio amplifiers. Every part shares the same ground: without a common reference the voltages of two parts would mean nothing to each other. Buttons go from a pin to ground; the display and the amplifiers receive digital signals. Never connect a pin that is driven high directly to ground. For the lecturer: Diagram from the PRG32 repository (docs/hardware/images). A pin of the ESP32-C6 can source some tens of milliamperes: an LED needs its series resistor, as computed earlier. Never join a pin driven high directly to ground.

## Slide 6: The complete program: l10.S (1 of 3)
# ARC12 Computer Architecture - Lecture 10: Introduction to Electronics and Digital Electronics
# l10.S: one button, one bit: from the finger to a register
#
# On the screen: a large square, grey while LEFT is released and yellow while it is
# pressed. On the kit LEFT is a switch between GPIO18 and ground.
# Build: python3 -m prg32 cartridge build l10.S --portable \
# --entry-prefix l10 --name l10 --out l10.prg32
.option norelax
.equ BLACK, 0x0000
.equ GREY, 0x4208
.equ YELLOW, 0xffe0
.section .text
.global l10_init
.global l10_update
.global l10_draw
l10_init:
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l10.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: The complete program: l10.S (2 of 3)
l10_update:
addi sp, sp, -16
sw ra, 12(sp)
call prg32_input_read # a0 = one bit per button
andi t3, a0, 0x01 # bit 0: LEFT
la t0, pressed
sw t3, 0(t0) # 0: not pressed, 1: pressed
lw ra, 12(sp)
addi sp, sp, 16
ret
# on the kit:
# LEFT is a switch between pin GPIO18 and ground
# pressed -> the pin is at 0 volts
# released -> the pin is at 3.3 volts
# the runtime inverts the level: in the program, pressed is 1
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l10.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: The complete program: l10.S (3 of 3)
l10_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, BLACK
call prg32_gfx_clear
la t0, pressed
lw t1, 0(t0)
li a4, GREY
beqz t1, 1f
li a4, YELLOW
1: li a0, 120
li a1, 60
li a2, 80
li a3, 80
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
.section .data
pressed: .word 0
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l10.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: Run it: what you should see
On the screen
– a large square, grey while LEFT is released and yellow while it is pressed. On the kit LEFT is a switch between GPIO18 and ground.
What to press
– press and release LEFT
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 10: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l10.S --portable \
--entry-prefix l10 --name l10 --out l10.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l10.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 11: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l10.S --portable \
--entry-prefix l10 --name l10 --architecture qemu \
--out l10-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l10-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 12: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l10.S --portable \
--entry-prefix l10 --name l10 --architecture esp32c6 \
--out l10-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l10-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 13: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l10; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 14: Exercises: paper first, then the kit
TRY IT
1
A blue LED drops 3.0 V: which resistor gives 2 mA from 3.3 V? What power does the resistor dissipate?
2
A divider with R1 = 10 kΩ and R2 = 20 kΩ on 3.3 V: compute Vout. Is it read as 0, as 1, or undefined by an input of the kit?
3
Draw a three-input NAND in CMOS and count its transistors
4
Check the NOR drawing for the four input combinations, marking which transistors conduct
5
On PRG32, run the lamps cartridge and bridge a button pin to ground with a wire: explain what you see, and what would happen with the pull-up disabled
Expected result
On paper: 150 Ω and 0.6 mW; Vout = 2.2 V, in the undefined band. On the kit: the lamp lights exactly as if the button were pressed.
Notes: Five exercises. Size the resistor of a blue LED and compute the power it dissipates. Compute the output of a divider and say how an input of the kit would read it: compare it with the two thresholds. Draw a NAND with three inputs and count the transistors. Check the NOR on the drawing. And on the kit, with the lamps cartridge running, bridge a button pin to ground with a wire: explain what you see, and what would happen without the pull-up. For the lecturer: Exercise 1: (3.3 - 3.0) / 0.002 = 150 Ω; P = 0.3 x 0.002 = 0.6 mW. Exercise 2: 3.3 x 20 / 30 = 2.2 V, between 0.825 and 2.475. Exercise 3: three pMOS in parallel, three nMOS in series: six transistors. The lamps cartridge is step 1 of textbook lab 06.