## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 11
Combinational Machines: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Notes: This is the code deck of Lecture 11. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 2 listings of Lecture 11, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l11.S, 50 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l11.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l11.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Choose one of four colours
# a0 = selector, 0 to 3 result: a4 = the selected colour
la t0, palette # four words: the data inputs
slli t1, a0, 2 # selector * 4 bytes
add t0, t0, t1 # address of the selected word
lw a4, 0(t0) # the selected input reaches the output
.section .rodata
# red, green, blue, yellow
palette: .word 0xf800, 0x07e0, 0x001f, 0xffe0
1
The same selector always gives the same colour: the result depends only on the present inputs
2
Nothing is remembered from one use to the next
3
In hardware this is a multiplexer: four data inputs, two selection bits, one output
4
A processor contains dozens of them. How are they built?
Notes: a0 holds a number from 0 to 3. The four instructions are the array access of Lecture 04: load the address of the table, multiply the selector by 4, add, and load the selected word. The same selector always gives the same colour, and nothing is remembered from one use to the next. This behaviour, outputs that depend only on the present inputs, defines the machines of today. In hardware this particular one is a multiplexer: four data inputs, two selection bits, one output. For the lecturer: The array access of Lecture 04, read as a circuit. In the processor the selection is done by gates in well under a nanosecond; here it takes four instructions.

## Slide 4: In the processor: which register is written?
addi t1, t1, 1 = 0x00130313
000000000001
31
20
00110
19
15
000
14
12
00110
rd = 6
11
7
0010011
6
0
decoder 5-to-32
0
x0
0
x1
0
x2
0
x3
0
x4
0
x5
1
x6
0
x7
0
x8
0
x9
0
x10
0
x11
0
x12
0
x13
0
x14
0
x15
0
x16
0
x17
0
x18
0
x19
0
x20
0
x21
0
x22
0
x23
0
x24
0
x25
0
x26
0
x27
0
x28
0
x29
0
x30
0
x31
The five bits of rd are a code word: thirty-two registers, ceil(log2 32) = 5
A 5-to-32 decoder turns them into thirty-two write-enable lines: only x6, that is t1, receives the result
Two more selections, on rs1 and rs2, choose which registers are read
Notes: A decoder at work in the processor. The instruction addi t1, t1, 1 contains a 5-bit field, rd, with the number of the destination register: 00110, that is 6, the register t1. A 5-to-32 decoder turns those five bits into thirty-two write-enable lines, of which only the sixth is active: only that register receives the result. The same instruction contains two more register numbers, which select the registers to be read. For the lecturer: The instruction of Lecture 02. Grey fields are not involved. The write enable of x0 is simply not connected: x0 always reads zero. Reading uses multiplexers, shown in a few slides.

## Slide 5: In the processor: register or constant?
register file
value of rs1
register file
value of rs2
immediate from the
instruction, sign-extended
MUX
ALU
A
0
1
B
selection: 0 for add, 1 for addi
result
add t2, t0, t1 and addi t2, t0, 5 use the same adder
A multiplexer in front of the ALU chooses the second operand: a register or the constant
It is a multiplexer on words: thirty-two one-bit multiplexers sharing one selection line
Reading a register is a multiplexer too: 32 words in, 5 selection bits (rs1), one word out
Notes: A multiplexer at work in the processor. add t2, t0, t1 adds two registers; addi t2, t0, 5 adds a register and a constant taken from the instruction. Both use the same adder. A multiplexer in front of the second input of the ALU chooses between the value of a register and the constant: its selection line is 0 for add and 1 for addi. It is a multiplexer on whole words: thirty-two one-bit multiplexers with a common selection line. Reading a register is a multiplexer too. For the lecturer: In the textbook datapath of Patterson and Hennessy the selection signal is called ALUSrc. A gate applied to every bit of a word with a common control is a word gate (porta di parola).

## Slide 6: A parity network in seven instructions
# a0 = one byte result: a0 = 1 if the number of 1 bits is odd
srli t0, a0, 4
xor a0, a0, t0 # fold eight bits onto four
srli t0, a0, 2
xor a0, a0, t0 # fold four bits onto two
srli t0, a0, 1
xor a0, a0, t0 # fold two bits onto one
andi a0, a0, 1 # keep the parity bit
1
Each xor combines the upper half of the bits with the lower half
2
Three levels for eight bits: the software version of a tree of XOR gates
3
The same value appended to the byte makes its total parity even
Notes: A parity network in software, for one byte. Each pair of instructions shifts the value right and combines it with itself by XOR: the first fold brings eight bits onto four, the second four onto two, the third two onto one. The last instruction keeps only the lowest bit, which is the parity. In hardware the same three levels are a tree of seven XOR gates. Trace it by hand with 0x53, which has four 1s, and with 0x13, which has three. For the lecturer: Written for this lecture. Trace it with 0x53 = 0101 0011 (four 1s, result 0) and with 0x13 = 0001 0011 (three 1s, result 1). In hardware the three levels are a tree of seven XOR gates.

## Slide 7: RISC-V instructions and the ALU
Instruction | funct3 | ALU operation | Unit that produces the result
add, sub | 000 | sum or difference | adder / subtractor (one more bit, in funct7, chooses)
sll | 001 | shift left | shifter
slt, sltu | 010, 011 | set if less than | subtractor, then the sign rules
xor | 100 | bitwise XOR | XOR gates
srl, sra | 101 | shift right | shifter (funct7 chooses logical or arithmetic)
or | 110 | bitwise OR | OR gates
and | 111 | bitwise AND | AND gates
funct3 is a 3-bit code inside the instruction: the ALU multiplexer is driven by decoding it.
Notes: How an instruction chooses the operation. The 3-bit field funct3 of the instruction is a compact code: 000 for sum or difference, 001 for shift left, 100 for XOR, 110 for OR, 111 for AND. A small decoder turns it into the selection lines of the multiplexer of the ALU. Where two instructions share a value, such as add and sub, one more bit elsewhere in the instruction distinguishes them. A code, a decoder, a multiplexer: the whole lecture in one table. For the lecturer: funct3 is the 3-bit field of the instruction seen in Lecture 02 (bits 14 to 12). Three bits, eight code words: a compact code that a small decoder turns into the selection lines of the ALU multiplexer.

## Slide 8: The complete program: l11.S (1 of 3)
# ARC12 Computer Architecture - Lecture 11: Combinational Machines
# l11.S: a multiplexer in software: a selector chooses one of four colours
#
# On the screen: four horizontal bars, red, green, blue and yellow from the top: bar k
# is drawn in the colour that the selector k chooses in the table.
# Build: python3 -m prg32 cartridge build l11.S --portable \
# --entry-prefix l11 --name l11 --out l11.prg32
.option norelax
.section .text
.global l11_init
.global l11_update
.global l11_draw
l11_init:
ret
l11_update:
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l11.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: The complete program: l11.S (2 of 3)
l11_draw:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
li a0, 0
call prg32_gfx_clear
li s0, 0 # the selector, 0 to 3
bars:
mv a0, s0 # a0 = selector, 0 to 3
la t0, palette # four words: the data inputs
slli t1, a0, 2 # selector * 4 bytes
add t0, t0, t1 # address of the selected word
lw a4, 0(t0) # the selected input reaches the output
li a0, 20
slli a1, s0, 5
addi a1, a1, 20 # y = 20 + 32 * selector
li a2, 200
li a3, 16
call prg32_gfx_rect
addi s0, s0, 1
li t0, 4
blt s0, t0, bars
lw s0, 8(sp)
lw ra, 12(sp)
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l11.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 10: The complete program: l11.S (3 of 3)
addi sp, sp, 16
ret
.section .rodata
# red, green, blue, yellow
palette: .word 0xf800, 0x07e0, 0x001f, 0xffe0
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l11.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 11: Run it: what you should see
On the screen
– four horizontal bars, red, green, blue and yellow from the top: bar k is drawn in the colour that the selector k chooses in the table.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 12: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l11.S --portable \
--entry-prefix l11 --name l11 --out l11.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l11.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 13: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l11.S --portable \
--entry-prefix l11 --name l11 --architecture qemu \
--out l11-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l11-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 14: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l11.S --portable \
--entry-prefix l11 --name l11 --architecture esp32c6 \
--out l11-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l11-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 15: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l11; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 16: Exercises: paper first, then PRG32
TRY IT
1
Synthesise segment g of the seven-segment transcoder with a Karnaugh map, using the don't-cares
2
Build a 3-to-8 decoder from two 2-to-4 decoders with enable and one inverter
3
Implement F = sum of m(1, 2, 4, 7) with one multiplexer of 8 inputs. Which function is it?
4
Write a comparator in assembly: a0 = 1 if a0 and a1 are equal, using xor and sltiu only
5
Draw a seven-segment digit on PRG32: a table of ten bytes, one per digit, and seven rectangles lit by testing its bits
Expected result
On PRG32: a large digit that counts from 0 to 9, one step per second, drawn from seven rectangles.
Notes: Five exercises. Synthesise segment g with a map, using the don't-cares. Build a 3-to-8 decoder from two 2-to-4 decoders with enable and one inverter. Implement a function with one multiplexer by putting its truth table on the data inputs, and recognise the function. Write a comparator in assembly with only xor and sltiu. And draw a seven-segment digit on PRG32: a table of ten bytes, one per digit, and seven rectangles lit by testing its bits: a transcoder in software. For the lecturer: Exercise 3: put 0, 1, 1, 0, 1, 0, 0, 1 on the data inputs: it is the three-input XOR, the sum bit of the full adder. Exercise 4: xor a0, a0, a1 then sltiu a0, a0, 1 (the pseudo-instruction seqz). Exercise 5 is a software transcoder followed by seven bit tests: the table is the truth table of this lecture, one row per byte.