## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 14
Elementary Machines: Registers and Buses: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Notes: This is the code deck of Lecture 14. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 2 listings of Lecture 14, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l14.S, 94 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l14.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l14.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Send a byte one bit at a time
# a0 = the byte to send, most significant bit first
li t0, 8 # eight bits to go
1: srli t1, a0, 7 # bring bit 7 down to bit 0
andi t1, t1, 1 # t1 = the bit to put on the wire
... # drive the data line with t1,
... # then pulse the clock line
slli a0, a0, 1 # shift left: the next bit moves up
addi t0, t0, -1
bnez t0, 1b
1
The display and the sound chip of the kit are connected by a few wires, not by thirty-two
2
A word must therefore travel one bit after another: a serial transfer
3
The loop is a shift register in software: shift, take one bit, repeat
4
The ESP32-C6 has hardware that does exactly this, millions of times per second
Notes: The loop sends a byte one bit at a time, most significant bit first. At each turn the byte is shifted right by 7 and masked with 1, which isolates its top bit; that bit would be put on a data line and a clock line pulsed; then the byte is shifted left by one, so that the next bit moves into the top position. After eight turns the whole byte has gone. The loop is a shift register in software. The chip of the kit contains hardware that does the same thing, millions of times per second. For the lecturer: Written for this lecture. On the kit the display uses SPI and the amplifier I2S: both are serial buses driven by shift registers inside the chip. The two elided lines would write to memory-mapped GPIO registers (Lecture 15).

## Slide 4: Buses on the PRG32 kit
Connection | Kind | Lines | What travels on it
inside the ESP32-C6 | parallel | 32 data lines, address and control | instructions, data and register transfers
display (ILI9341) | serial, SPI | clock, data out, chip select, data/command | every pixel of every frame, bit by bit
sound amplifier | serial, I2S | bit clock, word select, data | audio samples, 22,050 per second
joystick and buttons | one wire per button | one input pin each | a decoded representation: one line per button
USB to the laptop | serial, differential pair | two data wires | the firmware and the debug console
Notes: The buses of the kit. Inside the chip the bus is parallel. The display is connected by SPI, a serial bus with a clock, a data line, a chip select and a line that distinguishes data from commands: every pixel of every frame travels on it bit by bit. The amplifier is connected by I2S, another serial bus, which carries 22,050 audio samples per second. The buttons use one wire each: a decoded representation. USB, serial as well, carries the firmware and the debug console. For the lecturer: From the hardware description of the PRG32 repository (docs/hardware). Chip select is the CS of the small memory on the previous slide: several devices can share the same serial bus because only the selected one listens.

## Slide 5: Shifts in RISC-V: a shift register in one instruction
slli and srli move all the bits of a register by a given number of positions, filling with zeros
srai fills with copies of the sign bit (Lecture 05)
sll, srl and sra take the amount from a second register
In hardware a shift by any amount in one step is done by a barrel shifter: layers of multiplexers, not a chain of flip-flops
The shifter is one of the units of the ALU of Lecture 11
# parallel to serial, LSB first
andi t1, a0, 1 # take bit 0
srli a0, a0, 1 # next bit
# serial to parallel, MSB first
slli a1, a1, 1 # make room
or a1, a1, t1 # insert bit
Notes: The shift instructions move all the bits of a register in a single step: slli and srli fill with zeros, srai with copies of the sign bit; sll, srl and sra take the number of positions from a register. In hardware this is not a chain of flip-flops, which would need one clock pulse per position, but a barrel shifter, a combinational network of layers of multiplexers, and it is one of the units of the ALU. The code on the right shows the two conversions between parallel and serial. For the lecturer: A true shift register needs n clock pulses for n positions; the barrel shifter of the ALU is combinational and does it within one clock period.

## Slide 6: The complete program: l14.S (1 of 6)
# ARC12 Computer Architecture - Lecture 14: Elementary Machines: Registers and Buses
# l14.S: a byte sent one bit at a time, and rebuilt at the other end
#
# On the screen: top row: the eight bits of 0xA5 in the order in which they leave,
# most significant first (lit, dark, lit, dark, dark, lit, dark, lit). Bottom row: the
# byte rebuilt by the receiver. A green square says that it is equal to the byte sent.
# Build: python3 -m prg32 cartridge build l14.S --portable \
# --entry-prefix l14 --name l14 --out l14.prg32
.option norelax
.equ BLACK, 0x0000
.equ GREY, 0x4208
.equ YELLOW, 0xffe0
.equ GREEN, 0x07e0
.equ RED, 0xf800
.equ BYTE, 0xA5 # the byte to send: 1010 0101
.section .text
.global l14_init
.global l14_update
.global l14_draw
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: The complete program: l14.S (2 of 6)
l14_init:
ret
l14_update:
ret
# lamp: a0 = position 0 to 7, a1 = y, a2 = bit
lamp:
li a4, GREY
beqz a2, 1f
li a4, YELLOW
1: slli a0, a0, 5
addi a0, a0, 36 # x = 36 + 32 * position
li a2, 24
li a3, 24
tail prg32_gfx_rect
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: The complete program: l14.S (3 of 6)
l14_draw:
addi sp, sp, -32
sw ra, 28(sp)
sw s0, 24(sp)
sw s1, 20(sp)
sw s2, 16(sp)
sw s3, 12(sp)
li a0, BLACK
call prg32_gfx_clear
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: The complete program: l14.S (4 of 6)
li s0, BYTE # a0 of the slide: the byte to send
li s1, 0 # the receiver's shift register
li s2, 0 # how many bits have gone
1: srli t1, s0, 7 # bring bit 7 down to bit 0
andi s3, t1, 1 # s3 = the bit to put on the wire
mv a0, s2 # ... here the wire is a lamp:
li a1, 40 # position = the order of sending
mv a2, s3
call lamp
slli s1, s1, 1 # receiver: make room (serial to parallel)
or s1, s1, s3 # insert the bit
slli s0, s0, 1 # sender: shift left, the next bit moves up
andi s0, s0, 255 # (keep eight bits)
addi s2, s2, 1
li t0, 8 # eight bits to go
blt s2, t0, 1b
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 10: The complete program: l14.S (5 of 6)
li s2, 0 # show the byte that the receiver rebuilt
2: li t0, 7
sub t0, t0, s2
srl a2, s1, t0
andi a2, a2, 1
mv a0, s2
li a1, 100
call lamp
addi s2, s2, 1
li t0, 8
blt s2, t0, 2b
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 11: The complete program: l14.S (6 of 6)
li a4, RED # is it the byte that was sent?
li t0, BYTE
bne s1, t0, 3f
li a4, GREEN
3: li a0, 152
li a1, 150
li a2, 16
li a3, 16
call prg32_gfx_rect
lw s3, 12(sp)
lw s2, 16(sp)
lw s1, 20(sp)
lw s0, 24(sp)
lw ra, 28(sp)
addi sp, sp, 32
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l14.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 12: Run it: what you should see
On the screen
– top row: the eight bits of 0xA5 in the order in which they leave, most significant first (lit, dark, lit, dark, dark, lit, dark, lit). Bottom row: the byte rebuilt by the receiver. A green square says that it is equal to the byte sent.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 13: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l14.S --portable \
--entry-prefix l14 --name l14 --out l14.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l14.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 14: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l14.S --portable \
--entry-prefix l14 --name l14 --architecture qemu \
--out l14-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l14-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 15: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l14.S --portable \
--entry-prefix l14 --name l14 --architecture esp32c6 \
--out l14-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l14-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 16: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l14; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 17: Exercises: paper first, then PRG32
TRY IT
1
Draw a 4-bit serial-in, parallel-out shift register with D flip-flops, and fill in its contents over four clock pulses for the input 1, 0, 1, 1
2
Three registers share a common bus: write the enable and load signals needed to copy register B into register A
3
Complete the warm-up: write the loop that receives eight bits from a line and rebuilds the byte
4
On PRG32, show a byte as eight lamps and shift it left by one position every half second
5
Make the bit that leaves on the left come back in on the right (a rotation): a ring counter
Expected result
On PRG32: a pattern of lamps that walks to the left and, in the last exercise, goes round for ever.
Notes: Five exercises. Draw a 4-bit serial-in, parallel-out shift register and follow its content over four clock pulses. Write the enable and load signals that copy one register into another on a common bus. Complete the warm-up with the receiving loop. On PRG32, show a byte as eight lamps and shift it every half second. Finally make the bit that leaves on one side come back on the other: a rotation, also called a ring counter. For the lecturer: Exercise 3: slli a1, a1, 1 then or with the received bit, eight times. Exercise 5: srli t1, a0, 7; andi t1, t1, 1; slli a0, a0, 1; or a0, a0, t1; andi a0, a0, 255.