## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 16
Permanent Memory: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Notes: This is the code deck of Lecture 16. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 1 listing of Lecture 16, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l16.S, 82 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l16.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l16.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Switch the kit off and on again
.section .rodata # part of the cartridge file
title: .asciz "HIGH SCORE" # stored in flash: it survives
.section .data # copied into RAM at start
best: .word 0 # lives in RAM: it is lost
game_update:
...
la t0, best
lw t1, 0(t0)
ble a0, t1, 1f # new score not better: skip
sw a0, 0(t0) # remember the best score ... in RAM
1: ...
1
After a power cycle the title is still there, but the best score is 0 again
2
The cartridge is a file in flash memory: non-volatile
3
The variable lives in SRAM: volatile
4
To keep a score for ever it must be written to a permanent memory: which ones exist?
Notes: The title is in the section .rodata, which is part of the cartridge file: the file is stored in flash memory and survives. The best score is a variable in the section .data, which is copied into RAM when the cartridge starts: it lives in SRAM and is lost. So after a power cycle the title is there and the score is 0 again. To keep a score for ever it must be written into a permanent memory, and the lecture presents the ones that exist. Note where each section of a program lives. For the lecturer: Written for this lecture. On PRG32 persistent scores are handled by the Cartridge Store service; the point here is where each section of a program lives.

## Slide 4: The complete program: l16.S (1 of 4)
# ARC12 Computer Architecture - Lecture 16: Permanent Memory
# l16.S: what stays in the file and what lives in RAM
#
# On the screen: the title HIGH SCORE and two bars: the score of this run, which grows
# while A is held and falls back to zero when A is released, and the best score, which
# never goes down. Restart the cartridge: the title is still there, the best score is
# zero again.
# Build: python3 -m prg32 cartridge build l16.S --portable \
# --entry-prefix l16 --name l16 --out l16.prg32
.option norelax
.equ BLACK, 0x0000
.equ WHITE, 0xffff
.equ GREEN, 0x07e0
.equ YELLOW, 0xffe0
.section .text
.global l16_init
.global l16_update
.global l16_draw
l16_init:
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l16.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 5: The complete program: l16.S (2 of 4)
l16_update:
game_update:
addi sp, sp, -16
sw ra, 12(sp)
call prg32_input_read
andi t2, a0, 0x10 # button A
la t0, score
lw a0, 0(t0)
addi a0, a0, 1 # A held: one more point per frame
bnez t2, 2f
li a0, 0 # A released: the run is over
2: sw a0, 0(t0)
la t0, best
lw t1, 0(t0)
ble a0, t1, 1f # new score not better: skip
sw a0, 0(t0) # remember the best score ... in RAM
1: lw ra, 12(sp)
addi sp, sp, 16
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l16.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 6: The complete program: l16.S (3 of 4)
l16_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, BLACK
call prg32_gfx_clear
li a0, 20
li a1, 20
la a2, title # read from .rodata: it is always there
li a3, WHITE
li a4, BLACK
call prg32_gfx_text8
la t0, score
lw a2, 0(t0)
andi a2, a2, 255 # width = score, at most 255 pixels
li a0, 20
li a1, 60
li a3, 12
li a4, GREEN
call prg32_gfx_rect
la t0, best
lw a2, 0(t0)
andi a2, a2, 255
li a0, 20
li a1, 100
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l16.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: The complete program: l16.S (4 of 4)
li a3, 12
li a4, YELLOW
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
.section .rodata # part of the cartridge file
title: .asciz "HIGH SCORE" # stored in flash: it survives
.section .data # copied into RAM at start
best: .word 0 # lives in RAM: it is lost
score: .word 0
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l16.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 8: Run it: what you should see
On the screen
– the title HIGH SCORE and two bars: the score of this run, which grows while A is held and falls back to zero when A is released, and the best score, which never goes down. Restart the cartridge: the title is still there, the best score is zero again.
What to press
– hold A, release it, then restart the cartridge
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 9: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l16.S --portable \
--entry-prefix l16 --name l16 --out l16.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l16.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 10: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l16.S --portable \
--entry-prefix l16 --name l16 --architecture qemu \
--out l16-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l16-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 11: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l16.S --portable \
--entry-prefix l16 --name l16 --architecture esp32c6 \
--out l16-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l16-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 12: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l16; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 13: Exercises
TRY IT
1
A disk turns at 7,200 revolutions per minute: what is its average latency?
2
A cache answers in 1 ns and the memory in 50 ns: what is the average access time with 95% of hits?
3
List where each of these lives on the PRG32 kit: the boot code, the firmware, a cartridge, the variable counter, the register t0
4
Find the specifications of the storage of your laptop or phone: technology, capacity, interface
5
On PRG32, time two loops that sum a large array: one in order, one jumping by a large step. Is there a difference, and why might there not be on this chip?
Expected result
Latency: half a revolution, about 4.2 ms. Average access time: 0.95 x 1 + 0.05 x 51 = 3.5 ns.
Notes: Five exercises. Compute the average latency of a disk at 7,200 revolutions per minute: half a revolution. Compute the average access time of a cache with 95% of hits. Say where five things live on the kit: the boot code, the firmware, a cartridge, a variable, a register. Find the specifications of the storage of your own laptop or phone. And measure on PRG32 two loops over a large array, one in order and one in jumps: is there a difference, and why might there not be on this chip? For the lecturer: 60 / 7200 = 8.33 ms per revolution. Exercise 3: ROM, flash, flash (or RAM once loaded), SRAM, a flip-flop register in the processor. Exercise 5: the SRAM of the ESP32-C6 has no cache in front of it, so the access pattern matters little; on a laptop the difference is large.