## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 19
Instructions and Interrupts: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Notes: This is the code deck of Lecture 19. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 2 listings of Lecture 19, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l19.S, 112 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l19.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l19.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Four words in memory
address machine code what you wrote
0x000 0x0002A303 lw t1, 0(t0)
0x004 0x00130313 addi t1, t1, 1
0x008 0x0062A023 sw t1, 0(t0)
0x00C 0x00008067 ret
1
This is first_update of Lecture 02 as it sits in memory: four numbers, four addresses apart
2
How does the processor know that the first is a load and the second an addition?
3
Which steps does it take for each of them?
4
And while it runs them, how does it notice that a button was pressed or a timer expired?
Notes: Four words of memory, four addresses apart: this is first_update, the function that increments a counter. On the left the addresses, in the middle the machine code, on the right what you wrote. The processor has only the middle column. Three questions organise the lecture. How does it know that the first word is a load and the second an addition? Which steps does it take for each? And while it executes them, how does it notice that a button was pressed or a timer expired? For the lecturer: The la that precedes these instructions is omitted, and the encodings are the uncompressed 32-bit ones: with the C extension the assembler may choose 16-bit forms for some of them. Addresses are relative to the start of the function.

## Slide 4: Decoding by hand
0x006283B3
add t2, t0, t1
0000000
funct7
add, not sub
31
25
00110
rs2
x6 = t1
24
20
00101
rs1
x5 = t0
19
15
000
funct3
add
14
12
00111
rd
x7 = t2
11
7
0110011
opcode
register-register
6
0
0x0002A303
lw t1, 0(t0)
000000000000
immediate
offset 0
31
20
00101
rs1
x5 = t0
19
15
010
funct3
a word
14
12
00110
rd
x6 = t1
11
7
0000011
opcode
load
6
0
Notes: Two instructions decoded by hand. Write the eight hexadecimal digits in binary; cut off the last seven bits, the opcode, which tells you the format; then cut the remaining fields. For 0x006283B3 the opcode says register to register, the fields give x7, x5 and x6, and funct3 with funct7 say addition: add t2, t0, t1. For 0x0002A303 the opcode says load, the immediate is 0, the base is x5, the destination x6: lw t1, 0(t0). Do it once with pencil and paper. For the lecturer: Method: write the eight hexadecimal digits in binary, cut off the last seven bits (the opcode), look up the format, then cut the fields. The decoders of Lecture 11 do the same thing in a fraction of a nanosecond.

## Slide 5: The fetch phase, transfer by transfer
Step | Register transfer | Meaning
1 | MA := PC | the address of the instruction goes to the memory address register
2 | read enable; MB := M[MA] | the memory puts the instruction on the data bus; it is latched in the buffer
3 | D := MB | the instruction is copied into the decoding register
4 | PC := PC + 4 | the PC now points to the next instruction
Notes: The fetch phase in four register transfers, using the registers of the model of Lecture 18. The content of the PC goes to MA, the memory address register. The memory is read and the word arrives in MB, the buffer. The word is copied into D, the decoding register. The PC is increased by 4, because an instruction occupies four bytes, so that it points to the next one. Each row is a transfer on the internal bus, commanded by the control unit. For the lecturer: Fase fetch. PC, D, MA and MB are the registers of the reference model of Lecture 18; the transfers travel on the internal bus. In the original deck the machine had 16-bit words and the PC advanced by 2; in RV32 a word is four bytes, so the PC advances by 4 (by 2 after a compressed instruction).

## Slide 6: The rest of the cycle for two instructions
Phase | add t2, t0, t1 | lw t1, 0(t0)
decode | O1 := R[t0]; O2 := R[t1] | O1 := R[t0]; O2 := 0 (the immediate)
execute | U := O1 + O2 | U := O1 + O2 (an address)
memory | - | MA := U; read enable; MB := M[MA]
write back | R[t2] := U | R[t1] := MB
The same ALU adds two registers for add and forms an address for lw. The control unit, by decoding the opcode, decides which transfers happen.
Notes: The other four phases, side by side for two instructions. For add, decoding reads the two registers into the operand registers of the ALU, execution adds them, the memory phase is skipped, and the sum is written in t2. For lw, the second operand is the immediate, the sum is an address, the memory phase reads the word at that address, and the word read is written in t1. The same adder serves both: only the commands of the control unit differ. For the lecturer: O1, O2 and U are the registers of the ALU. The same adder computes a sum for add and an address for lw: only the control signals differ. A store ends at the memory phase; a branch ends at execute, by choosing the next PC.

## Slide 7: A trap handler, in outline
trap_entry:
addi sp, sp, -16
sw t0, 0(sp) # software context: save what we use
sw t1, 4(sp)
csrr t0, mcause # why are we here?
bgez t0, exception # top bit 0: an exception
... # top bit 1: find the device, serve it
lw t0, 0(sp) # restore the context
lw t1, 4(sp)
addi sp, sp, 16
mret # MIE := MPIE, PC := mepc
1
The interrupted program must not notice: every register the handler touches is saved and restored
2
mcause read as a signed number is negative for interrupts: bgez separates the two families
3
mret is the only way back: it re-enables interrupts and reloads the PC in one step
4
The firmware of the kit contains exactly such a routine; your cartridge is interrupted many times per frame
Notes: A handler in outline. It makes room on the stack and saves the registers it is going to use: the software part of the context. It reads mcause with csrr and tests its sign: the top bit is the sign bit, so bgez separates exceptions from interrupts with one instruction. After serving the event it restores the registers, releases the stack and executes mret. The interrupted program must not notice anything: one register left dirty here is a bug that appears at random, anywhere. For the lecturer: An outline, not the PRG32 source: a real handler saves all the caller-saved registers, usually on a separate stack reached through mscratch. csrr t0, mcause is the pseudo-instruction for csrrs t0, mcause, zero.

## Slide 8: The complete program: l19.S (1 of 6)
# ARC12 Computer Architecture - Lecture 19: Instructions and Interrupts
# l19.S: four words in memory: a function read back as machine code
#
# On the screen: four rows of 32 lamps, the machine code of lw t1, 0(t0) / addi t1,
# t1, 1 / sw t1, 0(t0) / ret, and beside each a green square: the word in memory is
# the one decoded by hand in the lecture.
# Build: python3 -m prg32 cartridge build l19.S --portable \
# --entry-prefix l19 --name l19 --out l19.prg32
.option norelax
.equ BLACK, 0x0000
.equ GREY, 0x4208
.equ YELLOW, 0xffe0
.equ GREEN, 0x07e0
.equ RED, 0xf800
.section .text
.global l19_init
.global l19_update
.global l19_draw
l19_init:
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l19.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 9: The complete program: l19.S (2 of 6)
l19_update:
ret
# The function of Lecture 02, kept in its uncompressed 32-bit forms.
.option push
.option norvc
sample:
lw t1, 0(t0) # 0x0002A303
addi t1, t1, 1 # 0x00130313
sw t1, 0(t0) # 0x0062A023
ret # 0x00008067
.option pop
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l19.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 10: The complete program: l19.S (3 of 6)
l19_draw:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
sw s1, 4(sp)
li a0, BLACK
call prg32_gfx_clear
li s0, 0 # which instruction, 0 to 3
1: la t0, sample
slli t1, s0, 2 # instructions are 4 bytes apart
add t0, t0, t1
lw s1, 0(t0) # the instruction, fetched as a datum
mv a0, s1
slli a1, s0, 5
addi a1, a1, 30 # y = 30 + 32 * s0
call lamps32
la t0, expected # compare with the encoding worked out by hand
slli t1, s0, 2
add t0, t0, t1
lw t2, 0(t0)
li a4, RED
bne s1, t2, 2f
li a4, GREEN
2: li a0, 306
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l19.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 11: The complete program: l19.S (4 of 6)
slli a1, s0, 5
addi a1, a1, 30
li a2, 8
li a3, 8
call prg32_gfx_rect
addi s0, s0, 1
li t0, 4
blt s0, t0, 1b
lw s1, 4(sp)
lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l19.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 12: The complete program: l19.S (5 of 6)
# lamps32: show the 32 bits of a word as a row of lamps, bit 31 on the left.
# a0 = the word, a1 = y of the row. A lamp is yellow for 1, grey for 0.
lamps32:
addi sp, sp, -32
sw ra, 28(sp)
sw s0, 24(sp)
sw s1, 20(sp)
sw s2, 16(sp)
mv s0, a0 # the word
mv s1, a1 # y
li s2, 0 # lamp number, 0 on the left
1: li t0, 31
sub t0, t0, s2 # lamp i shows bit 31 - i
srl t1, s0, t0 # bring that bit down to bit 0
andi t1, t1, 1 # keep it, clear all the others
li a4, GREY # lamp off
beqz t1, 2f
li a4, YELLOW # lamp on
2: slli a0, s2, 3
add a0, a0, s2 # 9 * i
addi a0, a0, 16 # x = 16 + 9 * i
mv a1, s1
li a2, 8
li a3, 8
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l19.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 13: The complete program: l19.S (6 of 6)
call prg32_gfx_rect
addi s2, s2, 1
li t0, 32
blt s2, t0, 1b
lw s2, 16(sp)
lw s1, 20(sp)
lw s0, 24(sp)
lw ra, 28(sp)
addi sp, sp, 32
ret
.section .rodata
expected: .word 0x0002A303, 0x00130313, 0x0062A023, 0x00008067
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l19.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 14: Run it: what you should see
On the screen
– four rows of 32 lamps, the machine code of lw t1, 0(t0) / addi t1, t1, 1 / sw t1, 0(t0) / ret, and beside each a green square: the word in memory is the one decoded by hand in the lecture.
What to press
– nothing: the program runs by itself
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 15: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l19.S --portable \
--entry-prefix l19 --name l19 --out l19.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l19.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 16: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l19.S --portable \
--entry-prefix l19 --name l19 --architecture qemu \
--out l19-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l19-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 17: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l19.S --portable \
--entry-prefix l19 --name l19 --architecture esp32c6 \
--out l19-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l19-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 18: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l19; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 19: Exercises: paper first, then PRG32
TRY IT
1
Decode 0x00A28293 and 0x40628333 by hand: format, fields, assembly
2
Encode sub t0, t1, t2 and sw a0, 8(sp)
3
Write the register transfers of the whole cycle for sw t1, 0(t0) and for beq t0, t1, target
4
Draw the pipeline diagram for six instructions on a four-stage pipeline: when does the sixth complete?
5
In PRG32-QT set a breakpoint in first_update, step, and compare the machine code shown with your decoding of the warm-up
Expected result
On paper: addi t0, t0, 10 and sub t1, t0, t1. On PRG32-QT: the four words of the warm-up, or their compressed equivalents.
Notes: Five exercises. Decode two words by hand, with format, fields and assembly. Encode sub t0, t1, t2 and sw a0, 8(sp): the inverse path. Write the register transfers of the whole cycle for a store and for a branch. Draw the pipeline diagram of six instructions on four stages and say when the sixth finishes. And in PRG32-QT stop in first_update, step, and compare the machine code shown with your decoding of the warm-up. For the lecturer: 0x00A28293: imm 10, rs1 x5, funct3 000, rd x5, opcode 0010011. 0x40628333: funct7 0100000, rs2 x6, rs1 x5, funct3 000, rd x6, opcode 0110011. sub t0, t1, t2 = 0x407302B3. sw a0, 8(sp) = 0x00A12423. Six instructions on four stages complete at cycle 9.