## Slide 1
ARC12 COMPUTER ARCHITECTURE · LECTURE 21
Input and Output: the code
Code deck: every listing explained, the complete program, and how to test it on PRG32-QT, on QEMU and on the board
Prof. Raffaele Montella, PhD
University of Naples “Parthenope” · A.Y. 2026/27
raffaelemontella.it · raffaele.montella@uniparthenope.it
Notes: This is the code deck of Lecture 21. The lecture deck holds the concepts; this one holds everything you type and run: the listings with their explanation, the complete program, what it shows, and the way to test it on each of the three hosts.

## Slide 2: In this deck
1
The 1 listing of Lecture 21, one per slide: read the code, then the numbered remarks beside it
2
The complete program: code/l21.S, 63 lines, printed in full
3
What you should see when it runs, checked on the PRG32-QT headless runner
4
How to test it, step by step: on PRG32-QT, on QEMU, on the board
5
The exercises: change the program, predict, run
Notes: What the deck contains, in the order of the slides. The program of the lecture is a file that you can build and run as it is: start from there, and come back to the listings to understand each part. The program of this lecture is ~/arc12/code/l21.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. For the lecturer: Get the code once: git clone https://github.com/riscv-prg32/computer-architecture-with-prg32 ~/arc12. The program of this lecture is ~/arc12/code/l21.S; tools/tests/cartridges/run.py builds it, runs it on PRG32-QT with scripted input and checks the pixels of the frame. Every listing on these slides is read by the build from a tested file, or checked by tools/tests: see its README.

## Slide 3: Read the world, once per frame
steer_update:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
call prg32_input_read # a0 = one bit per button
mv s0, a0 # keep it in a saved register
andi t0, s0, 0x10 # button A
beqz t0, 1f
li a0, 0 # channel
li a1, 0 # instrument
li a2, 69 # note: A4, 440 Hz
li a3, 255 # volume
li a4, 120 # milliseconds
call prg32_audio_note
1: andi t0, s0, 0x01 # LEFT: s0 survived the call
beqz t0, 2f
... # move left
2: ...
1
Each button is a switch on one input pin of the chip: pressed or released, one bit
2
The runtime reads the pins and packs them into one word: a decoded representation (Lecture 11)
3
Your game asks once per frame: this is polling
4
A keyboard has a hundred keys, a mouse moves in two dimensions, a display has thousands of pixels: how do they talk to a processor?
Notes: A function that reads the input once per frame. prg32_input_read returns in a0 a word with one bit per button; the code copies it into s0, a saved register, because the word must survive the call that plays a note. Then each button is tested with andi and a mask: 0x10 for A, 0x01 for LEFT. Behind each bit there is a switch on an input pin of the chip. The program asks, once per frame, and this way of proceeding has a name: polling. The other devices are less simple. For the lecturer: From textbook chapter 6, lab 06 and the sound example of the capstone chapter (examples/asm_capstone/audio_note_event.S). Built as a cartridge and run on the PRG32-QT headless runner (tools/tests): the marker moves with LEFT also while A plays the note, because the mask is kept in s0, a saved register; in t0 it would be lost at the call. The pins are memory-mapped GPIO registers (Lecture 15), configured as inputs, that is, with their output buffers in high impedance (Lecture 14).

## Slide 4: The complete program: l21.S (1 of 3)
# ARC12 Computer Architecture - Lecture 21: Input and Output
# l21.S: read the world, once per frame
#
# On the screen: a yellow square in the middle of the screen. LEFT moves it to the
# left; A plays a note, and the square keeps moving while the note sounds.
# Build: python3 -m prg32 cartridge build l21.S --portable \
# --entry-prefix l21 --name l21 --out l21.prg32
.option norelax
.section .text
.global l21_init
.global l21_update
.global l21_draw
l21_init:
ret
l21_update:
steer_update:
addi sp, sp, -16
sw ra, 12(sp)
sw s0, 8(sp)
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l21.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 5: The complete program: l21.S (2 of 3)
call prg32_input_read # a0 = one bit per button
mv s0, a0 # keep it in a saved register
andi t0, s0, 0x10 # button A
beqz t0, 1f
li a0, 0 # channel
li a1, 0 # instrument
li a2, 69 # note: A4, 440 Hz
li a3, 255 # volume
li a4, 120 # milliseconds
call prg32_audio_note
1: andi t0, s0, 0x01 # LEFT: s0 survived the call
beqz t0, 2f
la t1, marker_x
lw t2, 0(t1)
addi t2, t2, -2
sw t2, 0(t1)
2: lw s0, 8(sp)
lw ra, 12(sp)
addi sp, sp, 16
ret
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l21.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 6: The complete program: l21.S (3 of 3)
l21_draw:
addi sp, sp, -16
sw ra, 12(sp)
li a0, 0
call prg32_gfx_clear
la t0, marker_x
lw a0, 0(t0)
li a1, 100
li a2, 16
li a3, 16
li a4, 0xffe0
call prg32_gfx_rect
lw ra, 12(sp)
addi sp, sp, 16
ret
.section .data
marker_x: .word 152
Notes: One page of the complete program, exactly as it is in the repository. Read it from the top: the header says what the program shows and how to build it; the three functions init, update and draw follow, then the data. Lines that you met in the listings of the lecture have the same comments here. For the lecturer: code/l21.S, as built and run by the tests. The comments are part of the program: read them with the code.

## Slide 7: Run it: what you should see
On the screen
– a yellow square in the middle of the screen. LEFT moves it to the left; A plays a note, and the square keeps moving while the note sounds.
What to press
– LEFT moves the square; A plays a note
The frame written by the automatic test on PRG32-QT
Notes: What the program shows when it runs, and what to press. Predict before you run: if the screen differs from this picture, the difference is information. The picture was written by the automatic test, not drawn by hand. For the lecturer: The picture is the frame that the headless runner of PRG32-QT produced in the test of this program. On QEMU and on the board the game area is the same 320 by 200 pixels, between the two status bands.

## Slide 8: Test it on PRG32-QT
# 1. start PRG32-QT on this computer (it listens on port 8080)
# 2. in the PRG32 folder, with ESP-IDF active: build the cartridge
python3 -m prg32 cartridge build ~/arc12/code/l21.S --portable \
--entry-prefix l21 --name l21 --out l21.prg32
# 3. send it to PRG32-QT and start it
python3 -m prg32 esp32c6 upload-and-run l21.prg32 \
--url http://localhost:8080 --slot cart0
# 4. look, press, compare with the previous slide
1
PRG32-QT must be running: it answers on port 8080, like a board
2
Build once, from the PRG32 folder, with ESP-IDF active in the terminal
3
upload-and-run stores the cartridge in slot cart0 and starts it
4
Enable debug mode in Settings to stop the program and read registers and memory
Notes: The quickest way: PRG32-QT on your own computer. Four steps, each with its command. PRG32-QT behaves like a board on port 8080, which is why the upload command says esp32c6. With debug mode enabled you can stop at any instruction and read registers and memory. For the lecturer: Run by the tests: the cartridge of this slide is built with this command and executed on the headless runner of PRG32-QT. Without the toolchain: import the .prg32 file in PRG32-QT and choose Run Cartridge. Keys: arrows or WASD for the joystick, Z or J for A, X or K for B, Enter for Start, Escape to go back to Setup.

## Slide 9: Test it on QEMU
# 1. once: build the firmware for QEMU (several minutes)
python3 -m prg32 qemu build
# 2. build the cartridge for the emulated chip
python3 -m prg32 cartridge build ~/arc12/code/l21.S --portable \
--entry-prefix l21 --name l21 --architecture qemu \
--out l21-qemu.prg32
# 3. with QEMU closed, stage the cartridge into its flash image
python3 -m prg32 qemu upload l21-qemu.prg32
# 4. start the emulator; on Setup choose Run Cartridge, then cart0
python3 -m prg32 qemu run
1
The emulator runs the real firmware on an emulated chip: build it once
2
The cartridge is built for the architecture qemu: the same source, another file
3
Stage the cartridge with QEMU closed, then start it and choose Run Cartridge
4
The keys go to the terminal: arrows or WASD, Z or J for A, X or K for B
Notes: The same program on the emulator. QEMU runs the real firmware on an emulated chip, so the cartridge must be built for the architecture qemu. Stage the cartridge while QEMU is closed. The firmware opens on the Setup menu: choose Run Cartridge and the slot. Remember that the keyboard is read by the terminal, not by the window with the picture. For the lecturer: Checked by the tests up to the staging: the cartridge is built for the architecture qemu and accepted into the flash image of the emulator. What the emulator then shows is not checked automatically: Espressif QEMU needs its window. Since October 2026 the firmware starts on Setup: choose Run Cartridge, then cart0.

## Slide 10: Test it on the board
# 1. once per board: write the firmware through the USB cable
python3 -m prg32 esp32c6 build-and-flash
# 2. join the Wi-Fi network of the board: PRG32, password prg32game
# 3. build the cartridge for the board
python3 -m prg32 cartridge build ~/arc12/code/l21.S --portable \
--entry-prefix l21 --name l21 --architecture esp32c6 \
--out l21-esp32c6.prg32
# 4. send it over Wi-Fi and start it
python3 -m prg32 esp32c6 upload-and-run l21-esp32c6.prg32 \
--url http://192.168.4.1 --slot cart0
1
The firmware is written once per board, through the USB cable
2
The board creates the Wi-Fi network PRG32: join it with your computer
3
The same upload command as for PRG32-QT, with the address of the board
4
A black screen: check the wiring of the display against the firmware
Notes: The same program on the kit. The firmware is written once, through USB; after that cartridges travel over Wi-Fi. The upload command is the one used for PRG32-QT with the address of the board. This is the only host that the automatic tests do not run: try it, and report what you see. For the lecturer: Not run by the tests: there is no board on the test machine. The cartridge for the architecture esp32c6 is built by the tests; the steps are those of the PRG32 documentation. If the serial port is not found pass it explicitly. To use the Wi-Fi of the classroom: python3 -m prg32 wifi set --ssid NAME --password PASSWORD --mode sta.

## Slide 11: If it does not work
You see | It means | Do this
missing entry point | the prefix is not the one in the source | --entry-prefix l21; check the three .global lines
idf.py: command not found | ESP-IDF is not active in this terminal | run export.sh, or open the ESP-IDF PowerShell
upload: connection refused | the host is not listening at that address | start PRG32-QT; use the address on its Setup screen
a black screen, or the menu again | a function does not return, or ra was not saved | debug mode: step through init, update, draw
QEMU ignores the keys | the keyboard goes to the terminal | click the terminal that launched QEMU
Notes: The five most common symptoms, what each means, and what to do. Read the message before changing anything: it nearly always names the cause. For the lecturer: The first three rows cover most cases. When asking for help, paste the command and the whole message as text. docs/usage/troubleshooting.md of the PRG32 repository has the complete list.

## Slide 12: Exercises: paper first, then PRG32
TRY IT
1
A keyboard has 104 keys: how many bits does the key code need? How many rows and columns could the matrix have?
2
A page of 8 by 11 inches at 600 dots per inch, one bit per dot: how much memory does the printer need for the bitmap?
3
Move a pointer on the PRG32 screen with the joystick, as a mouse would: keep x and y, clamp them to the screen
4
Make button A act only once per press (edge detection, Lecture 13)
5
Draw a seven-segment score with rectangles, using the transcoder table of Lecture 11
Expected result
On paper: 7 bits, for example 8 by 13; about 4 MB. On PRG32: a pointer that stays on screen and a button that fires once per press.
Notes: Five exercises. How many bits does the code of a keyboard with 104 keys need, and what matrix could it have? How much memory does a printer need for the bitmap of a page at 600 dots per inch? Move a pointer on the screen with the joystick, keeping it inside the screen. Make button A act only once per press, by detecting the edge. And draw a score with seven-segment digits, using the table of Lecture 11. For the lecturer: 8 x 600 = 4,800 by 11 x 600 = 6,600 dots: 31,680,000 bits = 3.96 MB.